## Slide 1: Prin 2009 Bologna RU - Status
Mauro Villa

## Slide 2: Prin 2009 BO Goals
Digital readout architectures for pixel chips
  Space resolution 50 um, time resolution 100 ns
  Efficiency >98% with 100 Mhit/s rate on 1 cmq
Online tracking system
  Continue the study on the AM systems (+PI+MI)
  Push the system to its limit (bandwidths)
  AM roads processing (tracking/fitting/TSP)

## Slide 3: Pixel chip architecture

## Slide 5: The 3D MAPS projects
Apsel-VI
  MATRIX 96x128(2 sub-m. 48 x128)
  5.2 x 10 mm (incl. scr. line)
  Rows divided in:
    4 sparsifiers
    32 rows for each sparsifier
    8 zones for each sparsifier (Wzone= 4 pixels)
SuperPix1
  MATRIX 32x128 (2 sub-m. 16x128)
  3.5 x 10 mm (inc. scr. Line)
  Rows divided in:
    4 sparsifiers
    32 rows for each sparsifier
    8 zones for each sparsifier (Wzone= 4 pixels)

## Slide 8: Stratix Firmware building blocks
VME Memory
32 D32
+ EPMCs
Register
File
EPMC
Regs
Clock
Manager
Main
FSM
Data
Processing
8 Hit streams
6 AM Hit streams
Spy
buffer
Spy
buffer
Roads
Spy
buffer
AM
L1Accept
Post
Processing
Event
Out
S-Link out
From epmc or simu
From TTC or simu
Stratix

## Slide 9: Latenza e Rate
Scrittura disabilitata
Configurazione finale
Latenza AM ≈ 0.8 ms
Hit EDRO → AMB
Road AMB → EDRO

## Slide 10: HW Hit generation in EDRO  AM  EDRO  ROS
Test system in Bologna: sample run
HW hit generation to
exercise the system at low and high rates
DAQ rates 1Hz 62 kHz stable
depending on event size
TDAQ Rate
Mean size ≈ 500 words
Mean roads ≈ 90
TDAQ rate: 28 kHz
AM roads
Evt length
Online histograms
Comparison with offline analysis: on 100k events, 9M HW roads, 99% matched in simulation (missing roads due to event mixing, wrong data transfer or cuts), 0.1% missing End-Events.
No TDAQ errors

## Slide 11: Firmware e Software
SOFTWARE
HIT
ATLAS
EDRO
AMB
DISCO
HIT
ROAD
Simulazione
Lettura
Controllo
EDRO
AMB
Confronto
Qualità del Run:
Errori
Istogrammi
Grafici
Gen

## Slide 12: Evoluzione Firmware
Purezza = Road corrette individuate / totali individuate
Vecchia Versione
Nuova Versione
Efficienza = Road corrette individuate / totali attese
Pur 100%
Eff 100%

## Slide 13: Installazione
Ottobre, CERN:
Installazione in ATLAS
Test dati reali
Banca pattern di prova
Test di trasmissione hit e stabilità
EDRO
AMB

## Slide 14: Not implemented
Prin program describes track cleaning by a Data Organizer, a Tree Search Processor and a Track fitter (BO+MI+PI).
No time to develop the data organizer, no track fitting. The TSP has been superseeded by the next generation of AM chips (don’t care bits).

## Slide 15: Prin-related papers/presentations
F. Giorgi – The Front-End chip for the SVT detector – Elba 2012
F. Giorgi - A fast digital readout architecture for vertically integrated pixel sensors WIT 2012 (poster np)
A. Gabrielli – Development and simulation results-… IPRD2010
A. Gabrielli – High efficiency readout circuits … (NIM 2011)
A. Annovi – The EDRO Board connected to the Associative Memory … TIPP2011
M. Villa - Online tracking applications of the general purpose EDRO Board ... WIT 2012 (poster np)

## Slide 16: Summary
Digital readout architectures for pixel chips
  PRIN goals reached; readout architectures fully developed, simulated and ready to be submitted
Online tracking system
  2 out of 3 PRIN goals reached;
  Last one superseed by new AM chips

## Slide 18: Vertical Slice
Particella (alto pT)
Prototipo 2012:
AMB
EDRO
HIT
PATTERN
ROAD = Regione che contiene tutte le tracce di un Pattern

## Slide 19: La scheda EDRO
Altera Stratix II FPGA
Riceve/genera e organizza le hit
Strip/pixel colpito → coordinate reali
Comunica con la AMB
EDRO
AMB
AMChip
8 hit stream
6 hit bus
Road
Stratix
Gen
DAQ
Road + hit
ATLAS
o
Simu
VME
CPU

## Slide 20: Memorie Associative
AMChip basato sulle CAM
Correlazione tra hit -> pattern a bassa risoluzione in parallelo
Banca (50k - 100k) pattern (6-8 layer) → road

## Slide 21: I Primi Test
Scopo: testare passo a passo, scheda per scheda durante lo sviluppo
Bologna, Pisa
Sviluppo firmware EDRO e AM
Hit generate nella EDRO
Hit e road salvate su disco
Simulazione
Confronto dei risultati

## Slide 22: Latenza e Rate
Scrittura disabilitata
Configurazione finale
Latenza AM ≈ ms
Hit EDRO → AMB
Road AMB → EDRO

## Slide 23: Test Vertical Slice
Bologna, Pisa, CERN
Test prototipo completo
Hit generate da programma e salvate
Inviate da PC
Risultati su disco
Simulazione prende hit e road da file diversi
Confronto risultati

## Slide 24: Test Vertical Slice
Corretta trasmissione hit
Match tra road trovate e simulate
Purezza 100%
Efficienza 100%