## Slide 1: Concept of compact electron positron factory with beam energy from 0.5 GeV to 2 GeV (Super phi-tau-charm factory)
Bogomyagkov
Budker Institute of Nuclear Physics
Novosibirsk
26-31 May 2013
Workshop on Tau-Charm at High Luminosity

## Slide 2: Requirements
Beam energy from 0.5 to 2.1 GeV
Peak luminosity is 1035 cm-2s-1 at 2 GeV and within as wide as possible energy range
Circumference 366 m to fit in the existent tunnel of VEPP4-M
Conform as much as possible to existent infrastructure
Longitudinal polarization at some energy points
Energy calibration by Compton backscattering
  (~(5  10)10-5)

## Slide 3: Details
Two rings with Crab Waist collision scheme and single interaction point
Sub-mm y at IP and large x
No X chromaticity correction section in IR
Wigglers to control emittance
Highly effective positron source (50 Hz top-up injection)
Longitudinal polarization at 2 GeV

## Slide 4: Super-c-tau: scientific case

D
Ds


## Slide 5: Super-phi-tau-c: scientific case
Charmonia
Spectroscopy, BFs
Light hadron spectroscopy
J/ rare decays
…
Charm
Spectroscopy
(Semi)leptonic decays
Rare decays
Mixing
CP violation
…
Tau
Spectral functions, BFs
Lorentz structure
CP violation
LFV decays
…
Phi
K meson physics
…

## Slide 6: Crab Waist
Large Piwinski’s angle (z/x∙) – to decrease the overlapping area
Low y – luminosity increase
Crab waist – to suppress betatron resonances (sextupoles in phase with IP)
(P.Raimondi 2006)

## Slide 7: Main ring scheme
R45 m
Damping wigglers

## Slide 8: Facility scheme
R=45 m

## Slide 9: Site

## Slide 10: Parameters
Energy | 2.0 GeV | 1.5 GeV | 1.0 GeV | 0.5 GeV
Circumference | 368 m |  |  | 
Beta IP hor/ver | 20 cm / 0.6 mm |  |  | 
Emittance hor/ver with ibs @ 0.5% coupling | 3.1 nm 16 pm | 2.7 nm 14 pm | 5.5 nm 26 pm | 18 nm 89 pm
Crossing angle | 2x30 mrad |  |  | 
Bunch length | 8 mm | 8 mm | 8 mm | 8 mm
Energy spread | 1·10-3 | 1.4·10-3 | 3.3·10-3 | 9.9·10-3
RF frequency | 700 MHz |  |  | 
Harmonic number | 864 |  |  | 
Particles in bunch | 3.25·1010 | 3.11·1010 | 3.78·1010 | 3.53·1010
Number of bunches | 418 |  |  | 
Total beam current | 1.8 A | 1.7 A | 2.1 A | 1.9 A
Beam-beam parameter | 0.095 | 0.13 | 0.17 | 0.17
Luminosity | 1·1035 | 1·1035 | 0.98·1035 | 0.36·1035
2 cm / 0.76 mm
10 nm
10 mm
C-Tau
7·1010
1.7 A

## Slide 11: Optical functions: FF
IP: y=0.6 mm, x=20 cm

## Slide 12: Optical functions: CELL
x=y=
Non interleaved sextupoles
x=1.5 nm
Compact
Based on diffraction limited ring

## Slide 13: Optical functions: RING

## Slide 14: Final focus
QD0
Detector Yoke
QF1
Anti Solenoid
e-
e+
Cryostat
Compensation Solenoid

## Slide 15: Final focus

## Slide 16: QD0 quadrupole
SC iron yoke twin aperture magnet
Excitation current 8.5 kA·turns
Single aperture 2 cm
Gradient 10.7 kGs/cm
Length 20 cm

## Slide 17: Energy acceptance
Energy acceptance is 1.2%
Qx=26.54, Qy=25.576

## Slide 18: Dynamic aperture

## Slide 19: Injection facility

## Slide 20: Conclusion
The lattice, meeting all main requirements (600 m y, chromatic correction, momentum bandwidth, luminosity optimization for wide energy range, fits in the tunnel of VEPP-4M etc. ) is ready.
FF quadrupoles are reasonable.
Prototype of the damping wiggler is ready.
Detailed machine design and beam dynamics simulation is in progress.
It is possible to increase beam energy up to 2.5 GeV. The limitations are FF quadrupoles and some dipoles.

## Slide 21: ESTIMATION OF LONGITUDINAL POLARIZATION AT PhiCT-FACTORY -1 S.A. Nikitin
What energy?
1.8 GeV (τ -lepton production threshold) up to 2.1 GeV (upper limit of PhiCT factory ) is reasonable
LP increases sensitivity of experiments on search of CP violence in τ -lepton decays in several times
Yu.A. Tikhonov. Super c-tau factory (Status Report)/BINP Internal Report (2012)
Maximum of the τ+τ- production cross section at E b ≈ 2.2 GeV
LP scheme must be oriented to 2-2.1 GeV
What injector?
Electron-positron linac with energy up to 2.1 GeV
Electrons from a photo-gun source are longitudinally polarized.
Spins are rotated downstream of the gun to match beam polarization in the collider
Continuous mode injection
Radiative polarization time scaling
Sokolov-Ternov polarization build-up time , K – curvature in units of R-1
Current version of PhiCT factory without LP inserts:
τ0 =0.39 h (23 min) at E=2 GeV
τ0 =0.70 h (42 min) at E=1.777 GeV
Generally, radiative relaxation time of polarization is given by known formula
- an axis of polarization; - a spin-orbit coupling function; - a velocity vector ( )

## Slide 22: ESTIMATION OF LONGITUDINAL POLARIZATION AT PhiCT-FACTORY -2
Siberian Snake estimation
Siberian Snake using solenoid rotates spin around velocity at azimuth of 1800 opposite to IP
Betatron coupling is localized over insert with solenoid and matching/compensating quads
Radiative relaxation time , ν=a, νx – horizontal betatron tune
Estimation ( betatron factor B(ν, νx) 1, far from spin resonances ν νx=k):
τr =34 sec at E=2 GeV
τr =1.2 hours at E=1.0 GeV
Depolarization time is very small as compared with luminosity beam lifetime τl=3-8 min 
Siberian Snake variant is fully unsatisfying (see next point). At E ≤ 1GeV the situation becomes contrary.
Kinetics of polarization under continuous injection
SuperB CDR, arXive:0709.0451

## Slide 23: ESTIMATION OF LONGITUDINAL POLARIZATION AT PhiCT-FACTORY -3 LP scheme with restoration of vertical polarization in arcs

/2 solenoid
/2 solenoid
Bend magnet
Bend magnet
Due to vertical polarization in arcs the depolarization effect is sufficiently suppressed in comparison with Siberian Snake case. Similar schemes was considered earlier for VEPP-4 and SuperB. The -bend is included in the matching optic sections upstream and downstream of Crab Waist FF. Solenoid inserts are at edges of arcs with regular structure. Coupling is localized over these inserts using special quads. Nominal energy can be chosen near 2.1 GeV (a ≈ 4.77)
Polarized e-beam
from 2.1 GeV linac
spin “back”
spin in plane

## Slide 24
ESTIMATION OF LONGITUDINAL POLARIZATION AT PhiCT-FACTORY -4 Equilibrium polarization extent
Betatron term
Dispersion of spin
rotation in bend magnets
A and B coefficients found using transport matrix elements for several points at the solenoid inserts;
βx,1, the beta-x value at input of the insert;
<|h|2>, the Courant-Snyder’s invariant averaged over the arcs
D=-π for π/2 spin rotation angle in bend magnets from solenoid rotator to IP
Spin tune n0=n=ga
Term with D is determinative far from nx±n0=k resonances where the first term in d2 matters
Working point nx may be close to half integer values so avoid half integer n0 (as well as integer)!
Very preliminary estimate (only D term used):
E=2.05 GeV, =19.3,n0=4.65, τ0=20 min, τr=7 min, τl=3 min, P=67%
Estimate of spin-orbit coupling and relaxation time in LP scheme with “restoration”
S. Nikitin/SB-NOTE-ACC- 2008- 001:

## Slide 25: ESTIMATION OF LONGITUDINAL POLARIZATION AT PhiCT-FACTORY -5 Combined restoration scheme tunable over energy
S. Nikitin/Preprint Budker INP 2009-2
Advantages of combined scheme:
Longitudinal polarization at IP and vertical polarization in arcs are attained not only at a single energy value but over a certain energy range by retuning spin rotation angles in solenoids (1,2)
Polarization axis chromaticity n/  is reduced in every point of working energy region  integer spin resonances ν0=k become more narrow
No hard requirement to 1,2 taken separately

## Slide 26: ESTIMATION OF LONGITUDINAL POLARIZATION AT PhiCT-FACTORY -6 Summary
Longitudinal Polarization at PhiCT factory can be obtained at the beam energy range from 1.8 to 2.1 GeV for studies of CP violence in tau-lepton decays experiments.
Source of polarized particles: continuous injection of polarized electrons from 2.1 GeV linac.
Siberian Snake-based LP scheme is unsatisfactory at the top of PhiCT energy range because of very small depolarization time. But it looks fine at 1 GeV (τr=1.2 hour). Polarization experiments at the threshold of baryon production?
Quick estimation of the LP scheme with restoration of vertical polarization in arcs gives more 60% polarization at E=2.05 GeV. It needs high luminosity (beam life time is 3 min) . -bend of matching section must be increased from 13 (current version) to 19.3 
Another variant, the combined restoration scheme, has sufficient advantages. It is reasonable to consider.

## Slide 27: Chromaticity from CRAB sextupole