## Slide 1: LNF NEMO group
oceanografia
Orlando Ciaffoni, Marco Cordelli, Roberto Habel, Agnese Martini, Luciano Trasatti

## Slide 2
RFID
PORFIDO
Physical Oceanography by
Outreach

## Slide 3
NEMO FASE II Optical module

## Slide 4
Optical Module with PORFIDO probe schematic
FCM
FCM

## Slide 5
PORFIDO
RFID communication through glass
Very little interference with detector
Very little bandwidth to-from shore
Very little power
continuous data taking
data rate controlled from shore

## Slide 6
Radio Frequency Identification (RFID
RFID .
Radio Frequency Identification
developed for access control
sensors added
Reader (inside OM)
.
Notes: Prova

## Slide 7
Tag - WISP
RF powered (no batteries)
thermometer and accelerometer on board
open architecture

## Slide 8
WISP potted in a marine two component epoxy.

## Slide 9
two capacitors, square copper pads, 25x25 mm2
cut the wings

## Slide 10
much more stable
immune to the presence of metal
decrease the reader RF power by a factor of 10.
dimensions decreased to the size of the reader (70x40 mm2)).

## Slide 11
PORFIDO on the OM,

## Slide 12
LNS pressure test
40 MPa, equivalent to 4000 m depth in sea water
Pressure Test

## Slide 13
no interference with the PM tube and with the electronic boards inside the Optical Module.
RF Interference test

## Slide 14
4 PORFIDO probes on the Phase 2 tower - working

## Slide 15
PORFIDO for DOM

## Slide 16
Salinity sensor with 1 ppM sensitivity
2 inductances coupled by seawater
no electrodes in water
testing
Power!  Energy Harvesting
Prototype before summer
Developments
- 24 bit AFE (ADC) driven by WISP
Thermometer 0.001 ˚C using PT 100
working

## Slide 17
Where do you put the temperature probe?
OM 1.5 W
Sea current 0.5 cm/s
One thousandth of a degree
Open problems

## Slide 18
Where do you put the temperature probe?
Open problems

## Slide 19
Where do you put the temperature probe?
Open problems
One more hole

## Slide 20
hole

## Slide 21
- Stability absolute or relative? NO Instruments
sold with precision guaranteed > 1 year
Relative calibration – on which time scale?
Pressure
Technological development with good oceanographic data
What else can you do with 24 bits?
Open problems 2

## Slide 22
How many PORFIDO probes?
4 towers as far as possible
< every floor (20 m) – 4 /tower
total 32
Distributed in time?
Open problems 3

## Slide 23
Cost
Reader Thingmagic – 1 k€ ea./ 10 pcs
CAEN Reader – access to software
Temp sensors PT100 IDRONAUT .8 k€ /1 piece
Too much – a few for calib
32 PORFIDO probes
Readers 30 k€
PT100 5 k€
Chips, PCB, resin, etc. 15 k€
Small pressure chamber 5 k€
Total 55 k€

## Slide 24
ANTARES temp 1 year

## Slide 25
ANTARES temp 3 days