## Slide 1: Progress in the installation of the Compton line
C. Vaccarezza

## Slide 2: Outline
The Compton source
Nov 2012- May 2013: work done
Commissioning plan
Eli-NP: the sinergy
Summary

## Slide 3: The La y ou t
A. Zolla

## Slide 4: Thomson Source Parameter List
Laser
Electron Beam
Wavelength 800 nm
Compressed pulse energy 5 J
Pulse duration/bandwidth 3 -12 (80) ps/nm
Rep.Rate 10 Hz
Beam quality M2 <1.5
Energy stability 10%
Pointing stability < 2 µm
Synchronization with SPARC photoinjector clock < 1 ps
Bunch charge 0.2-1.0 nC
Energy 28-150 MeV
Length 15-20 ps
εn x,y 1-5 µ rad
Energy spread 0.1-0.2 %
Spot size at IP 5-20 µm
Rep.Rate 10 Hz

## Slide 5: Some pictures

## Slide 6: More on the photon beamline
R. Sorchetti

## Slide 7: In detail:
Dipole delivery completion by Sep. 2012
The solenoid delivery by the end of Nov. 2012
The Interaction Chamber part. by the end of Dec 2012
Interaction Chamber completion by Mid April 2013
Photon beamline completed by April 2012 w mirror chamber modifications complying the int. chmb.
on going:
  Solenoid magnet & PS water cooling
  Mirror mounting

## Slide 8: Diagnostic equipment:
6 Flag+pump stations
7 BPMs
1 BCM

## Slide 9: Compact BPM for Thomson beamline
A. Stella, V. Lollo

## Slide 10: HFM2 operating mode
For the first experiments the source has been optimized for applications in medical imaging, mammography in particular.
Highest X-ray flux at about 20 keV, with a relative radiation energy spread < 20% and keeping as low as possible the high harmonics contribution.

## Slide 11: The Beats2 experiment
M. Gambaccini

## Slide 12: The Thomson Interaction laser
Spectra of the collected radiation for pulses of duration 3, 6, 9, and 12 ps.
for
Spectral–angular (integrated in the azimuthal angle φ) distribution of the collected radiation for the optimized parameters w = 15 μm and duration T = 6 ps, where ϑM = 8 mrad
and

## Slide 13: The nominal case injector : 30MeV, 840pC
2007 measured beams
εx,y= 2.7 mm-mrad (at first TW Cavity entrance)
120 MV/m
(S2)=90°
(S1)=0°
t [ps]
Int.
Measured Laser-profile
εth=1.2 mm-mrad (norm. σx= 1 mm)
σt = 6.5 psec
Qbunch = 840 pC
σx,y = 0.57 mm
Energy Spread Correction
11.0 MV/m
2.0 MV/m
Off
sol. embedded
sol. embedded
z [m]
εx [mm-mrad]
0
12
6
3 mm-rad
emittance
A.Bacci

## Slide 14: e- beam at IP
E=30MeV
Q=840 pC
Elegant output
120 kp
E=150 MeV
Q=840 pC
Rms beam sizes at IP
& Twiss parameters of the 150 MeV beam
Rms beams sizes evolution along the transfer line & longitudinal tunability" of the beam waist at IP.

## Slide 15: Source spectra simulations
q=1 mrad
q=6 mrad
Spettro
Ee=30 MeV
Ntot=1,69 109
Dw/w (FWHM)=10.5 %
Dw/w rms=5.2 %
div (FWHM)= 22 mrad
div rms= 5.3 mrad
V.Petrillo

## Slide 16: The Low-Charge Case injector: 30MeV, 350pC
120 MV/m
(S2)=92°
13.2 MV/m
0.2 MV/m
(S1)=-26°
5.5 MV/m
(S3)=100°
sol. embedded
sol. embedded
Energy Spread Correction by a proper Acc.Gradient, Phase injection and
phase slippage on the first TW cavity
εth=1.2 mm-mrad (norm. σx= 1 mm)
σt = 16 psec, rise-time= 1psec
Qbunch = 350 pC
σx,y = 0.300 mm

## Slide 17: SL-Thomson: e beam for commissioning
Q=350pC
E=30 MeV
With triplet only
Tstep code simulation

## Slide 18: SL-Thomson: e beam for commissioning
Q=350pC
E=30 MeV
With
solenoid
Tstep code simulation

## Slide 19: Commissioning:
90 MeV – 160 pC e- beam (Comb or THz exp)
  Down to dumper w flags
  Quads alignement check on this orbit
  BPM first reference orbit
  Response matrix iterations for lattice optimization
30 MeV low charge transport and optimization
= 1÷1.5 month (May)
Photon beam transport & optimization
Synchronization & Collision
= 1 month (June)
  Al-window
    Kapton window
      Carbon fiber window

## Slide 20: Beats2

## Slide 21: At first:
18keV
18keV
Al properties: (http://henke.lbl.gov/tmp/xray3931.html

## Slide 22: Next:
Kapton (limited lifetime)
Cycloparaphenylene: C18H28B2O4
(structure footprint? Check @ Elettra)
18keV
18keV

## Slide 23: Beats2 apparatus
Filter holders/Collimators
Flux measure
X beam monitor
Banco ottico per allineamento oggetti test
e apparati di imaging X in assorbimento e
In contrasto di fase
Monitor fascio X
e portafiltri
M. Gambaccini

## Slide 24: ELI-NP sinergy:
The study of the electron distribution after the scattering is relevant for:
  Informations about the scattering-quantum model validation
  Electron longitudinal phase space
  deterioration
  Eventual transverse cooling
24
Target position

## Slide 25
Electron energy distribution at varying laser time duration.
Simulation made with CAIN.
Thomson SPARC-LAB at 150 MeV
Photon distribution vs electron energy for a0 = 0.083 and
Dt=0.083ps
Initial condition,
No collisions
1 collision
2 collisions
courtesy of V. Petrillo

## Slide 26
G Funct, typical of random walk
Diffusion in the phase space
Electron energy distribution at varying laser time duration. Simulation with CAIN
SL-Thomson case ELI-np case
Dt=0.083ps
Electron distribution vs electron energy for the a0 = 0.083
Dt=1.66ps
Dt=6.66ps
a0 = 0.046
ELI simulated beam
Electron distribution, 2
Dt=0.33ps
Dt=3.33ps
Dt=8.33ps
Initial
final
courtesy of V. Petrillo

## Slide 27
Thomson SPARC-LAB data, 150 MeV
Red: CAIN
Blue: master eq.
P is the electron distribution
Chapman-Kolmogorov master-equation for Markov process
Submitted to NJP
courtesy of V. Petrillo

## Slide 28: Summary
The e- beamline installation has been completed and the comissioning will start next week jointly w «2 colors FEL» and «THz» exp.
The photon beamline mirror mounting will proceed in parallel to set the high power photon beam transport.
Synchronization optimization and collisions soon after.
The first part of the BEATS2 exp. will provide the source characterization besides
The electron distribution study after the collision will provide information for the ELI-NP scaling.
The second part of the BEATS2 exp. will deal w the source efficiency for the medical imaging.