## Slide 1: Nuclear emulsions in FIRST: a first look
Giovanni De Lellis, Lucia Consiglio, Adele Lauria, Maria Cristina Montesi
University Federico II and INFN, Naples, Italy

## Slide 2: Nuclear emulsion as sensitive media for charged particles
50 micron
Microscopic Image
Recorded as silver grains
along the line particle passed through
Resolution of 0.3 micron
After the passage of charged particles through the emulsion layer, a latent image is produced
After a physical/chemical process known as development, Ag grains become visible with an optical microscope
AgBr crystal, size 0.2 micron
Is the elementary detection element
30-40 grains/100 microns for MIP
Nuclear emulsions used for
more than 100 years in Particle
Physics

## Slide 3: OPERA emulsions
Plastic Base (205 microns)
Emulsion Layer
Emulsion Layer (45 microns)
OPERA industrial emulsions from FujiFilm
The AgBr density in the OPERA emulsions is higher in respect to the commercial films
Special R&D for OPERA: the double pouring procedure
150 microns
Emulsions are continuously sensitive detector
ALL charged particle: cosmic rays,
natural radioactivity etc recorded as a
latent images. They can be partially
erased by a “refreshing” procedure
applied just before the detector assembling
Before refreshing
>30 tracks/mm^2 bg
After refreshing
~1 tracks/mm^2 bg

## Slide 4
EU: ESS (European Scanning System)
Japan: SUTS (Super Ultra Track Selector)
• Scanning speed/system: 75cm2/h
• High speed CCD camera (3 kHz), Piezo-controlled objective lens
• FPGA Hard-coded algorithms
• Scanning speed/system: 20cm2/h
• Customized commercial optics and mechanics
• Asynchronous DAQ software
Emulsion Scanning Stations
Both systems demonstrate:
• ~0.3 m spatial resolution
• ~2 mrad angular resolution
• ~95% base track detection efficiency

## Slide 5
CMOS camera 1280×1024 pixel 256 gray levels 376 frames/sec (Mikrotron MC1310)
XY stage (Micos) 0.1 μm nominal precision
Emulsion Plate
Z stage (Micos) 0.05 μm nominal precision
Illumination system, objective (Oil 50× NA 0.85) and optical tube (Nikon)

## Slide 6
16 Tomographic Images taken through 44-micron Emulsion Layer
Movable stage
Principle of scanning emulsion
(European)

## Slide 7
What the microscope CCD sees in one film..

## Slide 8: Data (images) processing and motion control flow in the ESS
280×365μm2
Tomographic sequences Z axis moving, 2D images spanning emulsion thickness
Move XYZ to next view
Process/save data
Next field of view, Z at top, new cycle
DAQ cycle (185 ms)
Camera
2D Images (peak 452 MB/s, avg. 97 MB/s)
Image Processor board (Matrox Odyssey)
Binarized 2D Images
Host PC (Dual Pentium Workstation) Running WinXP
3D microtracks
XYZ Motion Commands
Motion Controller (National Instruments FlexMotion)
Motors (VEXTA Nanostep)
Power
Functional blocks

## Slide 9: Kinematical measurements 1.Momentum measurement by multiple coulomb scattering
P =
13.6 (MeV/c)

X0
x
1/P(GeV/c)-1
0.8GeV/c pion : P =0.79(GeV/c), dP/P =11%
1.5GeV/c pion : P =1.53(GeV/c), dP/P =16%
P(GeV/c)

## Slide 10: Exposure of an Emulsion Cloud Chamber (ECC) to 400 MeV/u Carbon ions
ECC structure: 219 emulsion films (300 µm thick) and 219 Lexan plates 1 mm thick (73 consecutive “cells”)
Lexan:  = 1.15 g/cm3 and electron density =
3.6 x 1023/cm3, e.g. Water 3.3 x 1023/cm3
Cell structure
LEXAN
LEXAN
LEXAN
R0
R1
R2
R0: sensitive to m.i.p.
R1: insensitive to m.i.p., sensitive to protons
R2: sensitive to He
12C

## Slide 11: Carbon exposure at HIMAC (NIRS-Chiba)

## Slide 12: Vertex reconstruction More than 2000 vertices detected and analyzed
C
3 cm
i.p. of He tracks

## Slide 13: Charge separation
G. De Lellis et al., Journal of Instrumentation 2 (2007) P06004

## Slide 14: Charge changing cross-section

## Slide 15: Emulsions in FIRST: Schematic view
Bricks

## Slide 16: Bricks

## Slide 17: Brick structure: 61 films and 55 lead plates
Particles
6 consecutive films
61
56
55
54
53
52
1
2
55 1mm thick lead plates
interleaving emulsion films

## Slide 18: Track slopes expected in emulsion
beamline
a ≈ 16.5 cm
b
α
brick 1
(b+l)/a ≤ tg(α) ≤ (b+2l)/a
brick 2
b/a ≤ tg(α) ≤ (b+l)/a
tg(α) > 1  α > 45 degrees
Typical values in high energy physics: tg(α) < 0.6
L = 13 cm
X
Y
Z
tg(α) = dx/dz

## Slide 19: Dedicated study on Large angle track detection
tg(theta)
ε
72 degrees!

## Slide 20
Scanning of 4 emulsion films (slope ≤ 2)
Tracks angular distribution of films 61÷58
Peak signal selection
Brick 1: preliminary results

## Slide 21: Scanning of brick 2
3 most upstream films
brick rotated by 180 degrees w.r.t. the other one

## Slide 22
Brick 2: preliminary results
274 trks/cm2 (nseg>=2)
Contribution from cosmic-rays included
Scanning of 3 emulsion films (slope ≤ 2)
Tracks angular distribution of films 61÷59

## Slide 23
Films transported from Gran Sasso to CERN
Brick assembled at CERN
Cosmic-ray integrated during the transportation of the brick from CERN to GSI and from GSI to Gran Sasso
Brick disassembled and film developed at Gran Sasso
Cosmic-ray angular distribution
Cosmic-rays taken with the films inside the
brick in the same geometrical configuration
as for the beam at GSI, with the brick rotated
by 90 degrees to minimize the flux

## Slide 24: Conclusions
Scanning of very large angle tracks is now routinely done
First look at the films exposed at GSI in Summer 2011
To be done:
Define tracks by the first 6 consecutive films
Analysis of the films interleaved with lead to measure the properties of these tracks and try the particle identification (proton/alpha)