## Slide 1: The Gamma-400 MISSION
Valter Bonvicini
INFN – Trieste, Italy
On behalf of the Gamma-400 Collaboration
12th LNF Mini-workshop series: INFN-Space/3
Laboratori Nazionali di Frascati, 18-19 September 2013

## Slide 2: Outline
Introduction
GAMMA-400 mission:
  “Baseline” (original Russian) project:
    The B1 configuration
  Italian proposals:
    The B2 configuration
Physics with GAMMA-400
  Photons
  Electrons
  Nuclei
Conclusions

## Slide 3: GAMMA-400 Collaboration

## Slide 4: The GAMMA-400 project
Mission is approved by ROSCOSMOS (launch currently scheduled by November 2018)
GAMMA-400:
  Scientific payload mass: 4100 kg
  Power budget: 2000 W
  Telemetry downlink capability: 100 GB/day
  Lifetime: 10 years
  Orbit (initial parameters): apogee 300000 km, perigee 500 km, orbital period 7 days, inclination 51.8 °
  Gamma-400 will be installed onboard the platform “Navigator” manufactured by Lavochkin and launched by a “Proton-M” rocket

## Slide 5: GAMMA-400 orbit

## Slide 6: GAMMA-400 “baseline”: the B1 version
Original Russian design focused on:
  High energy gamma-rays (10 GeV - 3 TeV)
  High energy electrons (e- and e+)
Science objectives (from Russian proposal):
  “To study the nature and features of weakly interacting massive particles, from which the dark matter consists”
  “To study the nature and features of variable gamma-ray activity of astrophysical objects from stars to galactic clusters”
  “To study the mechanisms of generation, acceleration, propagation, and interaction of cosmic rays in galactic and intergalactic spaces”

## Slide 7: Gamma-400 “baseline”: the B1 version
Gamma-ray energy range | 10 – 3000 GeV
Multilayer converter | Si-W, 10 layers, 100 x 100 cm2 , 0.84 X0
Calorimeter CC1 | CsI-Si, 5 layers, 80 x 80 cm2, 3 X0
Calorimeter CC2 | 1024 BGO bars (25 x25 x 250 mm3), 80 x 80 cm2, 22 X0
Angular resolution (@ 100 GeV) | 0.01 – 0.02°
Energy resolution (@ 100 GeV) | 1 – 2%
Proton rejection | 105

## Slide 8: GAMMA-400: Italian proposal
Availability for a revision of the design that could enhance the performance and science capability of the project during the last years, a great deal of effort has been deployed by the Italian collaboration in order to significantly improve the scientific characteristics of the GAMMA-400 mission. The guidelines of this work have been:
  to define the best configuration for a dual instrument for photons (30 MeV - > 300 GeV) and cosmic rays (electrons > 1 TeV and high-energy cosmic-ray nuclei, p and He spectra close to the “knee” region (1014 – 1015 eV): E version.
  to agree upon a jointly defined dual instrument that, taking into account the currently available financial resources, optimizes the scientific performance and improves them with respect to the B1 version: this new “baseline” version, called B2, has been agreed upon by both (Russian and Italian) sides during a collaboration meeting held in Moscow in February 2013.

## Slide 9: The new B2 version
Original Russian proposal (2011)
Jointly agreed Russian-Italian proposal (2013)

## Slide 10: The new B2 version
B2 over B1 improvements:
Introduction of the highly segmented
homogeneous calorimeter with CsI
cubes  improved energy resolution,
extended GF with lateral particle
impingement, nuclei capability
Increase of the planar dimensions of
the calorimeter (from 80 cm x 80 cm
to 100 cm x 100 cm)  larger Aeff
Si strip detector pitch of the 2 CC1
layers decreased from 0.5 mm to
0.1 mm

## Slide 11: Converter/Tracker
Homogeneous Si-W Tracker
4 towers ( 50 cm x 50 cm each);
8 W/Si-x/Si-y planes + 2 Si-x/Si-y planes (no W);
Thickness of each plane 0.1 X0
Each sensor  9.7 cm x 9.7 cm from 6” wafers;
Sensors arranged in ladders (5 detectors/ladder), 1 ladder  50 cm;
Read-out pitch 240 µm (capacitive charge division), 384 strips/ladder
Implant pitch:
  Either 120 µm (one strip every 2 is read-out)
  Or 80 µm (one strip every 3 is read-out)
2000 silicon detectors;
153600 readout channels, 2400 front-end ASICs (64 channels/ASIC)

## Slide 12: Converter/Tracker: FE electronics
Front-end ASIC: architecture similar to TAA1 used in AGILE, with sparse read-out (only triggered ASICs are read-out).
Configuration: CSA, shaping amplifier, S/H and MUX. Each channel has a comparator with adjustable (via a DAC) threshold for trigger.
The ASIC should be designed in a “modern” technology: AMS 0.35 µm CMOS is well known (reliability) and offers excellent noise performance!

## Slide 13: Converter/Tracker: FE electronics
Preliminary specs for the GAMMA-400 Tracker front-end ASIC:
  128 channels
  Self-triggerable
  Power dissipation < 0.5 mW/channel
  S/N > 20 @ Cdet = 60 pF
  Dynamic range  25 fC
Contacts with IDE AS (Norway) already established, preliminary project done.

## Slide 14: Calorimeter
0.1 mm

## Slide 15: Calorimeter

## Slide 16: Calorimeter
Minimum 2 photodiodes are needed on each CsI crystal to cover the HUGE (1 MIP  107 MIP) dynamic range, hence:
A front-end electronics with large dynamic range and sensitivity down to 1-MIP signals is needed:
CASIS 1.2 ASIC, developed by the Trieste group

## Slide 17: Calorimeter

## Slide 18: Calorimeter

## Slide 19: Calorimeter

## Slide 20: Calorimeter

## Slide 21: Calorimeter

## Slide 22: Calorimeter

## Slide 23: Calorimeter
Preliminary!

## Slide 24: Calorimeter

## Slide 25: Calorimeter
FE Electronics: next step, CASIS1.2B
The final version of the FE ASIC includes a 12-bit ADC/channel (design submitted on August 30th, 2013 to Europractice)
ASICs are expected by November 2013

## Slide 26: B2 configuration: performance
Effective area (m2) of the G-400 instrument with B2 configuration. Left panel: variation of the effective area with energy for normal incidence and flat area distribution (Blue: G-400, Green: Fermi-LAT total, Red: Fermi-LAT front). Right panel: variation of effective area of G-400 at 100 GeV with polar angle for flat area distribution.
Preliminary!
Preliminary!

## Slide 27: B2 configuration: performance
Variation of angular resolution (68% fraction) of the G-400 instrument with B2 configuration with energy for normal incidence and flat area distribution, and comparison with Fermi-LAT. (Blue: G-400, Green: Fermi-LAT total, Red: Fermi-LAT front)
Preliminary!

## Slide 28: B2 configuration: performance
Variation of energy resolution (68% fraction) of the G-400 instrument with B2 configuration with energy for normal incidence and flat area distribution, and comparison with Fermi-LAT. (Blue: G-400, Green: Fermi-LAT total, Red: Fermi-LAT front)
Preliminary!

## Slide 29: Physics with GAMMA-400

## Slide 30: Physics with GAMMA-400
Possible scenarios in indirect dark matter search in -rays

## Slide 31: Physics with GAMMA-400
arXiv:1205.1045
arXiv:1206.1616
+
Gamma-400 ideal for looking for spectral DM-induced
features, like searching for –ray lines! If Weniger is right, the 130 GeV line should be seen with 10  significance (L. Bergström et al., arXiv:1207.6773v1 [hep-ph])
L. Bergström, , Stockholm 2012

## Slide 32: Physics with GAMMA-400

## Slide 33: Physics with GAMMA-400
Electron spectrum

## Slide 34: Physics with GAMMA-400
Cosmic-ray acceleration and propagation

## Slide 35: Physics with GAMMA-400
Nuclei
Knee structure
Structures in the GeV - TeV
region recently discovered for
p and He
Current spectral measurements
in the knee region are only
indirect

## Slide 36: Conclusions
The Gamma-400 mission represents a unique opportunity to perform simultaneous measurements of photons, electrons and nuclei with unprecedented accuracy.
  Pointing strategy without Earth occultation/large FOV
  High resolution converter/tracker providing excellent PSF
  Excellent energy resolution from the deep, homogenous calorimeter
Gamma-400 can provide in-depth investigations on some of the most challenging physics items, such as DM search, CR origin, production and acceleration to the highest energies…

## Slide 37: Back-up slides

## Slide 38: Gamma-400: scientific goals
Dark matter studies at GeV energies, resolving the Galactic Center and providing excellent sensitivity for searches in spheroidal galaxies (several times better than Fermi-LAT)
Cosmic-ray acceleration in SNR and galactic diffusion resolved with unprecedented detail in both space and spectra.
  Excellent sensitivity to neutral pion emission below 200 MeV.

## Slide 39: Scientific goals: low-energy s
Cosmic rays and low-energy s

## Slide 40: Scientific goals: electrons

## Slide 41: Scientific goals: nuclei

## Slide 42: Converter/Tracker
Homogeneous Si-W Tracker
25 W/Si-x/Si-y planes
Thickness of each plane 0.03X0
4 towers ( 50 cm x 50 cm each)
Single-sided,  120 µm pitch
microstrip detectors
Each sensor  9.7 cm x 9.7 cm
Sensors arranged in ladders (5
detectors/ladder)
Capacitive charge division readout
(1 strip every 2)
5000 silicon detectors
384000 readout channels

## Slide 43: Gamma-400 and Fermi: Aeff & PSF
Effective area
PSF
Black line: Fermi front+back
Blue line: Fermi front
Red solid line: G-400 120 x 120 cm2
Red dashed line: G400 100 x 100 cm2
Black line: Fermi front
Blue line: Fermi front + back
Red line: Gamma-400

## Slide 44: Calorimeter
Homogeneous cubic calorimeter
Symmetric, to maximize GF
Total mass < 1600 kg
Very large dynamic range
Finely segmented in all directions
1 RM x 1 RM x 1 RM CsI(Tl) cubic
crystals
Few mm gaps between crystals
Detail of a calorimeter plane:
Blue: crystals
Grey: Al support
Green: photodetectors
Brown: readout cables

## Slide 45: Calorimeter details
 | Cubes | Cubes | Cubes | Cubes
NNN | 202020 | 202019 | 212118 | 323232
L (cm) | 3.6* | 3.6* | 3.6* | 2.2
Crystal volume (cm3) | 46.7 | 46.7 | 46.7 | 10.6
Gap (cm) | 0.3 | 0.4 | 0.3 | 0.3
Mass (Kg) | 1683 | 1599 | 1578 | 1574
N.Crystals | 8000 | 7600 | 7497 | 32768
Size (cm3) | 78.078.078.0 | 80.080.076.0 | 81.981.981.9 | 80.080.080.0
Depth (R.L.) “ (I.L.) | 393939 1.81.81.8 | 393937 1.81.81.7 | 414133 1.91.91.6 | 383838 1.81.81.8
Planar GF (m2sr) (fiducial**) | 1.721.721.72 | 1.811.721.72 | 1.911.531.53 | 1.891.891.89
(* one Moliere radius)
(** within a reduced perimeter of size (N-1)*L )

## Slide 46: Russian vs. Italian design

## Slide 47: Tracker geometry

## Slide 48: Sensitivity – 48 hrs
Galactic center
Extragalactic
Black line: Fermi front+back
Blue line: Fermi front
Red solid line: G-400 120 x 120 cm2
Red dashed line: G400 100 x 100 cm2

## Slide 49: Sensitivity – 1 month
Black line: Fermi front+back
Blue line: Fermi front
Red solid line: G-400 120 x 120 cm2
Red dashed line: G400 100 x 100 cm2
Galactic center
Extragalactic

## Slide 50: Calorimeter summary

## Slide 51: Electrons – counts estimation

## Slide 52: Protons and He – counts estimation

## Slide 53: B2: electron count estimation

## Slide 54: B2: p and He count estimation

## Slide 55: B2: heavy nuclei count estimation