Efficient C++ Coding
How modern C++ improves your code
Francesco Giacomini – INFN-CNAF
ESC'13, 2013-10-22

---
A bit of C++ history
Invented in 1979 (“C with classes”), standardized in 1998

---
Sources about C++11
- The standard
  - a document close to the final text is freely available at http://www.open-std.org/jtc1/sc22/wg21/docs/papers/2011/n3242.pdf
- Official documents available at the C++ standard committee's site
  http://www.open-std.org/jtc1/sc22/wg21/docs/papers/
- The C++11 FAQ by B. Stroustrup
  http://www.stroustrup.com/C++11FAQ.html
- The boost libraries
  http://www.boost.org/
- GoingNative
  http://channel9.msdn.com/Events/GoingNative/2013
- For an introduction to C++98
  https://www.cnaf.infn.it/~giaco/c++/introduction_to_c++.pdf

---
Efficiency
- For the computer → performance
- For the developer → productivity
- For the reader → maintainability

---
The Core Language
To the Standard Library

---
>>
#include <vector>
#include <complex>
std::vector<std::complex<double>> v; // error in C++98, ok in C++11
std::vector<std::complex<double> > v; // ok in both C++98 and C++11
Note the space

---
Initializer lists
In C++98 initializing data structures is often burdensome
In C++11 the operation is much simpler
std::vector<int> v;
v.push_back(1);
v.push_back(2);
v.push_back(3);
v.push_back(4);
v.push_back(5);
std::map<int, std::string> ids;
ids.insert(std::make_pair(23, "Andrea"));
ids.insert(std::make_pair(49, "Camilla"));
ids.insert(std::make_pair(96, "Ugo"));
ids.insert(std::make_pair(72, "Elsa"));
std::vector<int> const v = {1, 2, 3, 4, 5};
std::map<int, std::string> const ids = {
  {23, "Andrea"},
  {49, "Camilla"},
  {96, "Ugo"},
  {72, "Elsa"}
};
Favor const-correctness
→ thread-safety
%

---
Initializer lists
- Implemented with std::initializer_list<T>
  - E.g. {1, 2, 3, 4, 5} has type std::initializer_list<int>
  - Consider it a read-only container
    - Availability of size(), begin(), end(), iterators, etc.
  - Elements must be uniform
void f(std::initializer_list<int> l)
{
  for (std::initializer_list<int>::const_iterator b = begin(l), e = end(l); b != e; ++b) {
    std::cout << *b << '\n';
  }
}
template<typename T>
class vector
{
  vector(std::initializer_list<T> l) { … };
};

---
Uniform initialization syntax
- Use braces {} for all kinds of initializations
  - initializer lists
  - normal constructors
  - aggregates (available in C++98 as well)
vector<int> v {1, 2, 3}; // calls vector<int>::vector(initializer_list<int>)
vector<int> v = {1, 2, 3}; // idem
complex<double> c(1.0, 2.0); // calls complex<double>::complex(double, double);
complex<double> c {1.0, 2.0}; // idem
complex<double> c = {1.0, 2.0}; // idem
struct X {
  int i_, j_;
};
X x {1, 2}; // x.i_ == 1, x.j_ == 2
X x = {1, 2}; // idem

---
Uniform initialization syntax
Additional advantage: prevention of narrowing
int c(1.5); // ok, but truncation, c == 1
int c = 1.5; // idem
int c{1.5}; // error
int c{1.}; // error, floating → integer is always considered narrowing
char c(7); // ok, c == 7
char c(256); // ok, but c == 0 (assuming a char has 8 bits)
char c{256}; // error, the bit representation of 256 doesn't fit in a char
Beware: initializer-list constructors are favored over other constructors
vector<int> v{2}; // calls vector<int>::vector(initializer_list<int>)
        // v.size() == 1, v[0] == 2
vector<int> v(2); // calls vector<int>::vector(size_t)
        // v.size() == 2, v[0] == v[1] == 0

---
auto
std::map<std::string, int> m;
std::map<std::string, int>::iterator iter = begin(m);
Why should I tell the compiler what the type of iter is? it must know!
std::map<std::string, int> m;
auto iter = begin(m);
The auto type specifier signifies that the type of a variable being declared shall be deduced from its initializer

---
auto
auto a; // error, no initializer
auto i = 0; // i has type int
auto d = 0.; // d has type double
auto const e = 0.; // e has type double const
auto const& g = 0.; // g has type double const&
auto f = 0.f; // f has type float
auto c = "ciao";	// c has type char const*
auto p = new auto(1); // p has type int*
auto int i; // OK in C++98, error in C++11
template<typename T, typename U>
void op(T t, U u)
{
  …
  ??? s = t * u; // what's the type of s?
  …
}
template<typename T, typename U>
void op(T t, U u)
{
  …
  auto s = t * u;
  …
}

---
range for
std::vector<Account> v;
for (std::vector<Account>::const_iterator b = begin(v), e = end(v); b != e; ++b) {
  print(*b);
}
for (std::vector<Account>::iterator b = begin(v), e = end(v); b != e; ++b) {
  update(*b);
}
std::vector<Account> v;
for (Account a: v) { // or, rather, Account const&
  print(a);
}
for (auto u: v) { // or, rather, auto const&
  print(u);
}
for (auto& u: v) {
  update(u);
}
C++11: simplified syntax to iterate on a sequence

---
range for
- A range can be:
  - an array
    - e.g. int a[10];
  - a class C such that C::begin() and C::end() exist
    - e.g. std::vector<int>, std::string
  - a class C such that begin(C) and end(C) exist
- Instead of an explicit for loop consider the use of an algorithm (such as for_each or find_if), possibly with a lambda function (see later)
for_each(begin(v), end(v), print);
for_each(begin(v), end(v), update);

---
nullptr
nullptr is a literal denoting the null pointer
f(int);
f(int*);
f(0); // calls f(int)
f(nullptr); // calls f(int*)
int* p = nullptr;
int* q = 0; // still valid and p == q
nullptr is not an integer
int i = nullptr; // error
NULL was not a solution
// stddef.h
#ifdef (__cplusplus)
#define NULL 0

---
In-class member initializers
Allow to specify the initialization expression of a non-static data member when it is declared
struct C
{
  int i_;
  C(): i_(5) {}
  C(int i): i_(i) {}
};
C c1; // c1.i_ == 5
C c2(3); // c2.i_ == 3
struct C
{
  int i_ = 5;
  C() {}
  C(int i): i_(i) {}
};
C c1; // c1.i_ == 5
C c2(3); // c2.i_ == 3
the initialization in the constructor
takes precedence
Simplifies the initialization of objects, especially in presence of multiple constructors, that need to be kept in sync

---
In-class member initializers
Beware side effects in the initializer
double global_d;
std::string get_string() { return "hello, world!"; }
double get_double() { global_d = 3.; return 1.;}
class A
{
  int i_ = 5;
  std::string s_ = get_string();
  double d_ = get_double(); // ignored!
public:
  A(): d_(2.) {}
};
A a;
// a.i_ == 5, a.s_ == "hello, world!", a.d_ == 2., global_d == 0
side effect

---
Delegating constructors
A constructor can delegate to another constructor
class C
{
  std::string k_;
  int v_;
  void init(std::string const& k, int v)
  {
    k_ = k;
    v_ = v;
    // validate k_ and v_
  }
public:
  C(std::string const& k, int v) { init(k, v); }
  C(int v) { init("default", v); }
};
class C
{
  std::string k_;
  int v_;
public:
  C(std::string const& k, int v)
    : k_(k), v_(v)
  {
    // validate k_ and v_
  }
  C(int v): C("default", v) {}
};
- No need of an auxiliary function
- Favor initialization over assignment

---
Inheriting constructors
Re-use constructors defined in a base class
struct B
{
  void f(int);
  void f(double);
  B(int);
  B(double);
};
struct D1: B // C++98
{
  using B::f;
  void f(int); // prefer this to B::f(int)
  D1(int);
  D1(double d): B(d) {} // forward to B::B(double)
};
struct D2: B // C++11
{
  using B::B; // re-use B's constructors
  D2(int); // prefer this to B::B(int)
};

---
Deleted functions
Prevent the compiler from implicitly generating functions not explicitly declared
// a non-copyable class in C++98
struct C
{
  C() {}
private:
  C(C const&);
  C& operator=(C const&);
};
C c;
C c1(c); // error (at compile or link time)
C c2;
c2 = c; // error (at compile or link time)
// a non-copyable class in C++11
struct C
{
  C() {}
  C(C const&) = delete;
  C& operator=(C const&) = delete;
};
C c;
C c1(c); // error (at compile time)
C c2;
c2 = c; // error (at compile time)
copy constructor and copy assignment
operator can even be public
declare, but don't define, the copy constructor
and the copy assignment operator as private
void f(double);
f(1.); // ok
f(1); // ok, calls f passing double(1)
void f(int) = delete;
f(1); // error
The mechanism is more general:
any function can be deleted

---
Defaulted functions
- Explicitly tell the compiler that the default implementation of a special member function is ok
  - To force the generation of the function
  - As a documentation feature
struct C
{
// the implicitly-generated default constructor,
// copy constructor and copy assignment operator
// are ok
};
C c;
C c1(c);
C c2; c2 = c;
struct C
{
  C() = default;
  C(C const&) = default;
  C& operator=(C const&) = default;
};
C c;
C c1(c);
C c2; c2 = c;
tell it with comments
tell it with code
Remember that the default constructor is generated only if no other constructor is present

---
long long
- A longer integer, at least 64 bits
  - signed and unsigned
long long i1 = 4611686018427387903;
auto i2 = 1LL; // i2 has type long long
unsigned long long i3 = 4611686018427387903;
auto i4 = 1ULL; // i4 has type unsigned long long

---
Exception specification
- Dynamic exception specifications are deprecated
  - still supported, but can be removed from a future revision of the standard
  - they were practically useless, if not harmful, anyway
- A noexcept specification has been introduced
- noexcept tells the compiler that a function
  - doesn't throw, or
  - is not able to manage possible exceptions → better to terminate
- noexcept can depend on a constant expression, to make the function conditionally non-throwing
void f() throw(std::runtime_exception, my_exception);
void f() noexcept;

---
Raw string literals
- A string literal that doesn't recognize C++ escape sequences (e.g. '\n', '\\', '\"', …)
- Address readability difficulties introduced, e.g., with regular expressions and XML text
cout << "\\\\\""; // prints \\" (3 characters)
cout << R"(\\")"; // idem, but easier
cout << "\n"; // prints a newline
cout << R"(\n)"; // prints \n (2 characters)
// how to print )" (2 characters)
cout << R"()")"; // error
cout << R"*+()")*+"; // ok
an (almost) arbitrary sequence of characters

---
User-defined literals
C++98 foresees literals only for built-in types
C++11 supports literals for user-defined types as well
123 // int
123U // unsigned int
123L // long int
12.3 // double
12.3F // float
12.3L // long double
'h' // char
"hello" // char[6]
// for example
123s // seconds
12us // microseconds
42.1km // kilometers
23.3m2 // squared meters
"hi"s // as an std::string
.5i // imaginary
10101000b // binary
Speed v1 = 9.8m / 1s; // ok
Speed v2 = 100m / 1s2; // error
Speed v3 = 100 / 1s; // error
Acceleration a = v1 / 1s; // ok
Improve type safety, with no runtime overhead

---
User-defined literals
UD literals are mapped to the corresponding types via literal operators
std::complex<double> operator "" i(long double d)
{
  return {0, d};
}
std::string operator "" s(char const* chars, size_t size)
{
  return std::string(chars, size);
}
- Certain suffixes (those not starting with _) are actually reserved for future standardization
- Namespaces help prevent suffix clashes

---
enum class
- enum in C++98 has several issues:
  - absence of strong scoping
  - implicit conversion to integer
  - inability to specify the underlying type
enum E1 { red };
enum E2 { red }; // error
enum Color { red, green, blue };
int c = red; // ok
void f(int);
f(green); // ok
sizeof(Color); // 4 (!) bytes on my machine

---
enum class
- enum class in C++11 addresses the enum issues:
  - strong scoping
  - no implicit conversion to integer
  - ability to specify the underlying type
enum class E1 { red };
enum class E2 { red }; // ok
enum class Color { red, green, blue };
int c = red; // error
void f(int);
f(green); // error
f(Color::green); // error
void g(Color);
g(green); // error
g(Color::green); // ok
enum class Color: char { red, green, blue };
sizeof(Color); // 1 (on any machine!)

---
Static assertions
Check that a certain constant boolean expression is satisfied during compilation, otherwise fail with the specified message
static_assert(sizeof(long) >= 8, "64-bit code generation required for this library.");
- A static assertion declaration can appear practically anywhere in the code
- There is no effect, hence no overhead, at runtime

---
constexpr
- Generalize the concept of constant expressions, extending it to include
  - calls to “sufficiently simple” functions
    - more flexibility in C++14
  - objects of user-defined types constructed from “sufficiently simple” constructors
- A way to guarantee that an initialization is computed at compile time
  - favor const-correctness
  - performance benefit
- constexpr functions can be called also at run-time

---
factorial at compile time
// general case
template<int N>
struct Factorial // C++98
{
  static const int value = N * Factorial<N-1>::value;
};
// basic case
template<>
struct Factorial<1>
{
  static const int value = 1;
};
constexpr int factorial(int N) // C++11
{
  return N > 1 ? N * factorial(N - 1) : 1;
}
constexpr int f1 = Factorial<10>::value;
constexpr int f2 = factorial(10);
static_assert(f1 == f2, "Factorial<10>::value == factorial(10)");

---
constexpr
struct Complex
{
  double real;
  double imag;
  constexpr Complex(double r, double i): real(r), imag(i) {}
};
constexpr Complex c {12.3, 4.56}; // ok, initialized at compile time
constexpr double r = c.real; // ok, initialized at compile time
constexpr Complex operator "" i(long double d) { return {0, d}; }
void f(Complex c)
{
  constexpr double r1 = c.real; // error, can't evaluate at compile time
  double r2 = c.real; // ok
  constexpr Complex c1 = 2i; // ok
}
constexpr implies const

---
Lambda expressions
- A concise way to create simple anonymous function objects
- Useful to pass actions/callbacks to algorithms, threads, frameworks, …
vector<int> v = {-2, -3, 4, 1};
sort(v.begin(), v.end()); // default sort, v == {-3, -2, 1, 4}
struct abs_compare
{
  bool operator()(int l, int r) const { return abs(l) < abs(r); }
};
sort(v.begin(), v.end(), abs_compare()); // C++98, v == {1, -2, -3, 4}
sort(v.begin(), v.end(), [](int l, int r) { return abs(l) < abs(r); }); // C++11

---
What is a function object?
- A function object (aka functor) is an instance of a class that has overloaded operator()
- A function object can then be used as if it were a function
- A function object, being an instance of a class, can have state
struct Incrementer
{
  int operator()(int i) const
  { return ++i; }
};
Incrementer inc;
int r = inc(3); // r == 4
class Add_n {
  int n_;
public:
  Add_n(int n): n_(n) {}
  int operator()(int i) const
  { return n_ + i; }
};
Add_n s(5);
int r = s(3); // r == 8

---
Lambda expressions
- The evaluation of a lambda expression produces a closure, which consists of:
  - the code of the body of the lambda
  - the environment in which the lambda is defined
    - the variables that are referenced in the body need to be captured and are stored in the generated function object
double min_salary = …;
find_if(
  begin(employees),
  end(employees),
  [=](Employee const& e) { return e.salary() < min_salary; }
);
[] // capture nothing
[&] // capture all by reference
[=] // capture all by value
[=, &i] // capture all by value, but i by reference

---
Copy vs move
String s1("...");
String s2(s1); // (1)
String get_string();
String s3(get_string()); // (2)
- In (1) the deep copy is necessary, because s1 still esists after the copy
- In (2) the deep copy is a waste, because the temporary created by get_string() is immediately destroyed after the construction of s3
- Named objects are called lvalues
  - and you can take their address
- Temporary objects are called rvalues
  - and you can't take their address

---
Copy vs move
class String {
  char* s_; // null-terminated
public:
  String(char const* s) {
    size_t size = strlen(s) + 1;
    s_ = new char[size];
    memcpy(s_, s, size);
  }
  ~String() { delete [] s_; }
  // copy
  String(String const& other) {
    size_t size = strlen(other.s_) + 1;
    s_ = new char[size];
    memcpy(s_, other.s_, size);
  }
};
class String {
  char* s_; // null-terminated
public:
  String(char const* s) {
    size_t size = strlen(s) + 1;
    s_ = new char[size];
    memcpy(s_, s, size);
  }
  ~String() { delete [] s_; }
  // copy
  String(String const& other) {
    size_t size = strlen(other.s_) + 1;
    s_ = new char[size];
    memcpy(s_, other.s_, size);
  }
};
String get_string();
class String {
  char* s_; // null-terminated
public:
  String(char const* s) {
    size_t size = strlen(s) + 1;
    s_ = new char[size];
    memcpy(s_, s, size);
  }
  ~String() { delete [] s_; }
};
class String {
  char* s_; // null-terminated
public:
  String(char const* s) {
    size_t size = strlen(s) + 1;
    s_ = new char[size];
    memcpy(s_, s, size);
  }
  ~String() { delete [] s_; }
  // copy
  String(String const& other) {
    size_t size = strlen(other.s_) + 1;
    s_ = new char[size];
    memcpy(s_, other.s_, size);
  }
  // move
  String(??? other): s_(other.s_) {
    other.s_ = nullptr;
  }
};
String get_string();
String s1("...");
String s1("...");
String s2(s1);
s1
s_
s2
s_
String s1, s2;
String s3(get_string());
tmp
s_
s3
s_

---
rvalue references
- In C++98 there is no way to overload functions specifically for rvalue (i.e. temporary) arguments
- C++11 introduces rvalue references (T&&)
class String
{
  // move constructor
  String(String&& other)
    : s_(other.s_)
  {
    other.s_ = nullptr;
  }
};
String s1;
String s2(s1); // calls String::String(String const&)
String s3(get_string()); // calls String::String(String&&)
lvalues can be explicitly transformed into rvalues
String s2(std::move(s1)); // I don't care about s1 anymore
s1.size(); // undefined

---
Special functions
- A class in C++11 has now 5 special member functions
  - plus the default constructor
class C
{
  T(T const&); // copy constructor
  T& operator=(T const&); // copy assignment
  T(T&&); // move constructor, new in C++11
  T& operator=(T&&); // move assignment, new in C++11
  ~T(); // destructor
};
- Rule of thumb: if you need to declare any one of these functions, declare them all
  - consider =delete, =default
class C // non-copyable, movable
{
  T(T const&) = delete;
  T& operator=(T const&) = delete;
  T(T&&) = default;
  T& operator=(T&&) = default;
  ~T() = default;
};

---
Move in the standard lib
namespace std
{
  template<typename T, …>
  class vector
  {
  public:
    vector(vector&& other);
    vector& operator=(vector&& other);
    void push_back(T&& value);
    iterator insert(iterator position, T&& value);
    …
  };
}
vector<string> read_from_file(std::string const& filename);
string get_another_string();
vector<string> v(read_from_file("strings.txt"));
v.push_back(get_another_string());
move semantics applied to the container
move semantics applied to the elements
steal from the temporary returned by the function

---
Reminder on exception safety
- Different levels of exception safety guarantees:
  - No guarantee – if an exception occurs, anything can happen
  - Basic – if an exception occurs, at least object invariants are preserved → no resources are leaked, the object is correctly destructible, etc., but the original object value may not be preserved
  - Strong – if an exception occurs, the original object value is preserved
  - No throw – if an exception occurs, it is swallowed and managed directly by the implementation, without any visible effect
- In general the higher the level of safety, the higher the overhead
  - strive to provide at least the basic guarantee
  - the no throw guarantee (→ noexcept) enables significant optimizations, e.g. in the standard library

---
Example for copy assignment
class String {
  char* s_; // null-terminated
public:
  String(String const& other)
  {
    size_t size = strlen(s) + 1;
    s_ = new char[size];
    memcpy(s_, s, size);
  }
  String& operator=(String const& other)
  {
    String tmp(other);
    *this = std::move(tmp);
    return *this;
  }
  String& operator=(String&& other) noexcept
  {
    delete [] s_;
    s_ = nullptr;
    s_ = other.s_;
    other.s_ = nullptr;
    return *this;
  }
};
- The copy constructor can throw because new can throw
  - if the memory allocation fails
- The copy assignment can throw because the copy constructor can throw
  - but if it throws the original value is preserved → strong exception safety guarantee
- The move assignment provides the no throw guarantee → marked as noexcept
- Also the move constructor can be marked noexcept
- Note that the move assignment is not protected against self-assignment
  - s = std::move(s)
  - but at least it doesn't crash

---
Passing by value
- Perceived as inefficient → pass by const&
- In fact compilers are allowed to do copy elision in some circumstances
  - they are good at it and getting better
- General advice: pass sink arguments by value and move them into destination
  - i.e. arguments that would in any case be copied within the function body
class runtime_error
{
  String msg_;
public:
  runtime_error(String msg)
  : msg_(std::move(msg))
  {
  }
};
String s;
// pass an lvalue
runtime_error e1(s);
// pass a temporary
runtime_error e2(get_string());
	by const& + copy	by value / + move
pass lvalue	1 copy	1 copy / + 1 move
pass rvalue	1 copy	1 move
For a POD: move == copy

---
Return value optimization
- Copy elision applies also to return values
  - (U)RVO → (Unnamed) Return Value Optimization
  - NRVO → Named Return Value Optimization
- If the compiler is not able to elide the copy, it tries first to move the return value into destination and only copies it as a last resort
String urvo()
{
  return {}; // returns an unnamed default-constructed String
}
String nrvo()
{
  String result;
  return result; // returns a named default-constructed String
}
String s1 = urvo();
String s2 = nrvo();

---
De-virtualization
- Virtual functions have a cost
  - indirect call through a pointer kept in the virtual table
- If the compiler can determine the exact dynamic type of an object, it can call the function directly
  - and possibly inline it
struct B {
  virtual int fun() { return 31; }
};
struct D: B {
  int fun() { return 42; }
};
struct E: D {
};
int main()
{
  B* b = new D;
  b->fun();
}
here the compiler can easily see that b is actually a D
and call directly, and inline, D::fun()

---
De-virtualization
- The compiler however may not see enough code or not able to prove what the dynamic type of an object is
- The compiler can be helped telling it either
  - that a virtual function cannot be overridden any more, or
  - that an entire class cannot be derived from
here the compiler can prove that d->fun() cannot be overridden
and statically determine to call, and inline, D1::fun()
struct B {
  virtual int f() { return 31; }
};
struct D1: B {
  int f() final { return 42; }
};
struct D2 final: B {
};
// in another translation unit
int f(D1* d) { return d->f(); }
int f(D2* d) { return d->f(); }
here the compiler can prove that d->fun() cannot be overridden
and statically determine to call, and inline, B::fun()

---
De-virtualization
- Consider static polymorphism
  - no virtual functions → no need to de-virtualize
struct D1 {
  int f() { return 42; }
};
struct D2 {
  int f() { return 31; }
};
template<typename B>
int f(B* b) { return b->f(); }
f(new D1); // calls f<D1>(D1* b)
f(new D2); // calls f<D2>(D2* b)
struct B {
  virtual int f() = 0;
};
struct D1: B {
  int f() { return 42; }
};
struct D2: B {
  int f() { return 31; }
};
int f(B* b) { return b->f(); }
f(new D1);
f(new D2);

---
Trailing return type
That auto specifier in place of the return type of a function means that the declarator of that function shall include a trailing return type
template<typename T, typename U>
??? op(T t, U u)
{
  return t * u;
}
what's the type of the returned value?
template<typename T, typename U>
auto op(T t, U u) -> decltype(t * u)
{
  return t * u;
}
auto here means “to be specified later”
t and u are not known until after their declaration
This form can be used for any function
auto op(double d, double e) -> double
{
  return d * e;
}

---
Type aliases
- A more powerful typedef
  - enable template typedef
// can be used in place of the usual typedef
typedef vector<Employee> Employees;
using Employees = vector<Employee>; // equivalent, probably preferable
Employees employees;
template <class T, size_t N> class array; // C++11 fixed-size array
array<int, 100> a1; // an array of 100 ints
template<class T> using array_100 = array<T, 100>; // N is bound to 100
array_100<int> a2; // an array of 100 ints
template<size_t N> using int_array = array<int, N>; // T is bound to int
int_array<100> a3; // an array of 100 ints
static_assert(is_same<array<int, 100>, array_100<int>>::value, "different types");
static_assert(is_same<array<int, 100>, int_array<100>>::value, "different types");

---
Variadic templates
- Provide templates with the ability to accept any number of template arguments
  - How to implement a type-safe printf?
  - How to build a tuple?
    - A tuple is a heterogeneous, fixed-size collection of values
printf("Hello, %s.\n", "Francesco"); // 2 args
printf("The value of %s is %g.\n", std::string("pi"), 3.14); // 3 args
std::tuple<int, Employee, string> r {
    12345, Employee("Giacomini"), string("INFN")
}; // 3 elements
std::tuple<Point, Length, Color, Thickness> l {
    Point(1.,2.), 12mm, Red, .1in
}; // 4 elements

---
Variadic templates
Use of recursion: general case + one or more basic cases
// general case
template<typename T, typename... R>
void print(T value, R... rest)
{
  cout << value << ' ';
  print(rest...);
}
// basic case
template<typename T>
void print(T t)
{
  cout << t;
}
print(1, 2.9, "hello", '\n'); // T = int, R = {double, char const*, char}
print(2.9, "hello", '\n'); // T = double, R = {char const*, char}
print('\n'); // basic case, T = char
Template type parameter pack
Function parameter pack
Recursive call
Parameter expansion

---
Memory model
- Finally C++ has a memory model that contemplates a multi-threaded execution of a program
- A thread is a single flow of control within a program
  - Every thread can potentially access every object and function in the program
  - The interleaving of each thread's instructions is undefined
Thread 1	Thread 2
y = 1; / r1 = x;	x = 1; / r2 = y;
Execution 1	Execution 2	Execution 3
y = 1; / r1 = x; / x = 1; / r2 = y; / // r1 == 0, r2 == 1	x = 1; / r2 = y; / y = 1; / r1 = x; / // r1 == 1, r2 == 0	y = 1; / x = 1; / r2 = y; / r1 = x; / // r1 == 1, r2 == 1

---
Memory model
- C++ guarantees that two threads can update and access separate memory locations without interfering with each other
- For all other situations updates and accesses have to be properly synchronized
  - atomics, locks, memory fences
- If updates and accesses to the same location by multiple threads are not properly synchronized, there is a data race
  - undefined behavior
- Data races can be made visible by transformations applied by the compiler or by the processor for performance reasons
Thread 1	Thread 2
y = 1; / r1 = x;	x = 1; / r2 = y;
Thread 1	Thread 2
r1 = x; / y = 1; / // r1 == 0	r2 = y; / x = 1; / // r2 == 0

---
The Standard Library
To the Core Language

---
Overview of changes
- Adoption of new language features in the library
  - examples
- New data structures
- New algorithms
- New libraries

---
Use of constexpr
namespace std {
  template<> class complex<double>
  {
  public:
    constexpr complex(double re = 0.0, double im = 0.0);
    constexpr double real();
    constexpr double imag();
    …
  };
}
constexpr std::complex c{1., 2.};
constexpr double re = c.real();
constexpr double im = c.imag();

---
= default, = delete
namespace std {
  template<typename T> class shared_ptr
  {
    public:
      // copyable, let the compiler implement the functions
      shared_ptr(shared_ptr const&) noexcept = default;
      shared_ptr& operator=(shared_ptr const&) noexcept = default;
    …
  };
  class error_category
  {
  public:
    // not copyable
    error_category(error_category const&) = delete;
    error_category& operator=(error_category const&) = delete;
    …
  };
}

---
Containers
- C++ containers belong to two broad categories
  - sequence: elements are strictly in a linear order and the order is under the control of the developer
    - vector, deque, list, forward_list, array
  - associative: the order of the elements is under the control of the container itself, based on a key
    - set, multiset, map, multimap, unordered_set, unordered_multiset, unordered_map, unordered_multimap

---
forward_list
std::list
- std::forward_list
  - more space-efficient, but less functionality
 next
        prev
 next
        prev
 next
        prev
 next
 next
 next
 next
 next

---
array
- Fixed-size container of homogeneous elements
  - storage is contiguous
  - no space overhead with respect to a C array
std::array<int, 4> a {1, 2, 3, 4};
std::array<int, 4> b; // {0, 0, 0, 0}
std::array<int, 4> c {1, 2} // {1, 2, 0, 0}
std::array<int, 4> d {1, 2, 3, 4, 5}; // error
std::array<int> e {1, 2}; // error (size is mandatory)
a[2] = 5; // {1, 2, 5, 4}
std::cout << a.size(); // prints 4
auto beg = a.begin(); // iterator to the first element
auto end = a.end(); // iterator to one after the last element
int* p = a.data(); // p points to a[0]

---
Unordered containers
- Also known as hash containers
  - map, multimap, set, multiset
- Similar to their ordered counterparts, but:
  - elements are not ordered
  - no need of a less-than operator being defined
  - need of a hash function, possibly user defined
  - lookup is O(1), instead of O(log N)
std::unordered_map<int, std::string> ids = {
  {23, "Andrea"},
  {49, "Camilla"},
  {96, "Ugo"},
  {72, "Elsa"}
};

---
tuple
- A tuple is an ordered, heterogeneous, fixed-size collection of values
  - a generalization of std::pair
  - an unnamed struct of unnamed members
  - members are accessible with an index
std::tuple<Point, Length, Color, Thickness> l {Point(1.,2.), 12mm, Red, .1in};
auto r = make_tuple(12345, Employee("Giacomini"), std::string("INFN"));
// r has type std::tuple<int, Employee, std::string>
Point p = std::get<0>(l);
auto s = std::get<2>(r); // s has type std::string
auto d = std::get<3>(r); // compilation error
int i; Employee e; std::string s;
tie(i, e, s) = r; // i == 12345, e == Employee("Giacomini"), s = std::string("INFN")

---
Algorithms
all_of, any_of, none_of, for_each, find, find_if, find_if_not, find_end, find_first_of, adjacent_find, count, count_if, mismatch, equal, is_permutation, search, search_n, copy, copy_n, copy_if, copy_backward, move, move_backward, swap, swap_ranges, iter_swap, transform, replace, replace_if, replace_copy, replace_copy_if, fill, fill_n, generate, generate_n, remove, remove_if, remove_copy, remove_copy_if, unique, unique_copy, reverse, reverse_copy, rotate, rotate_copy, random_shuffle, shuffle, is_partitioned, partition, stable_partition, partition_copy, partition_point, sort, stable_sort, partial_sort, partial_sort_copy, is_sorted, is_sorted_until, nth_element, lower_bound, upper_bound, equal_range, binary_search, merge, inplace_merge, includes, set_union, set_intersection, set_difference, set_symmetric_difference, push_heap, pop_heap, make_heap, sort_heap, is_heap, is_heap_until, min, max, minmax, min_element, max_element, minmax_element, lexicographical_compare, next_permutation, prev_permutation

---
Algorithms
std::array<int, 6> a {3, 5, 4, 2, 8, 9};
std::all_of(
  begin(a), // from here...
  end(a), // ... to here
  [] (int i) { return i < 10; } // if less than 10
); // returns true
std::vector<int> v;
copy_if(
  begin(a), // from here...
  end(a), // ... to here
  back_inserter(v), // push_back to v...
  [] (int i) { return i % 2; } // ... if odd
); // v == {3, 5, 9}
std::is_sorted(begin(a), end(a)); // returns false
is_sorted(
  begin(v),
  end(v),
  [] (int i, int j) { i % 3 < j % 3; } // compare mod 3
); // returns false

---
Numeric operations
accumulate, inner_product, partial_sum, adjacent_difference, iota
std::array<int, 6> a; // a = {0, 0, 0, 0, 0, 0}
std::iota(begin(a), end(a), 3); // a = {3, 4, 5, 6, 7, 8}

---
Regular expressions
- A form of pattern-matching often used in text processing
  - think grep
std::regex e(R"(^([A-Z]{3}) *([A-Z]{3}) *(\d{2}[A-Z]\d{2}) *([A-Z]\d{3}) *([A-Z])$)");
std::string fmt(R"(\1\2\3\4\5)");
regex_replace("RSS MRA 70A01 H501 S", e, fmt); // returns "RSSMRA70A01H501S"
Note the use of raw string literals
to avoid excessive escaping of \ characters
std::regex e(R"(^[A-Z]{3} *[A-Z]{3} *\d{2}[A-Z]\d{2} *[A-Z]\d{3} *[A-Z]$)");
regex_match("RSS MRA 70A01 H501 S", e); // returns true
regex_match("RSS MRA 70A01 6501 S", e); // returns false
beginning of line
0 or more spaces
3 letters
end of line
3 letters
0 or more spaces
0 or more spaces
0 or more spaces
2 digits
1 letter
2 digits
3 digits
1 letter
1 letter

---
Random number generation
- Generators/engines
  - generate uniformly distributed unsigned integers according to specific properties
  - linear congruential, mersenne twister, …
- Distributions
  - generate values that are distributed according to an associated mathematical probability density function or according to an associated discrete probability function
  - uniform int, uniform real, bernoulli, binomial, normal, …
std::default_random_engine e; // a typedef for one of the engines
std::uniform_int_distribution<> d(1, 6);
d(e); // returns an integer between 1 and 6

---
bind
A mechanism to transform an n-ary callable entity into an m-ary callable entity
char f(int i, double d); // function
auto h = std::bind(f, 1, 2.);
h(); // calls f(1, 2.)
auto g = std::bind(f, std::placeholders::_1, 1.);
g(3); // 3 is passed as _1 to f; calls f(3, 1.)
struct T { char operator()(int); }; // function object
T t;
auto j = std::bind(t, 1);
j(); // calls t(1)
struct S { char foo(int k); }; // member function
S s;
auto k = std::bind(&S::foo, s, _1);
k(1); // calls s.foo(1)
g has type std::_Bind<char (*(std::_Placeholder<1>, double))(int, double)> (in gcc)

---
bind
Useful for callbacks, operators/predicates/comparators to algorithms, …
default_random_engine e;
uniform_int_distribution<> d(1, 6);
d(e); // generates a random int
auto gen = bind(d, e);
gen(); // calls d(e)
// generate 1000 numbers between 1 and 6 and store them into v
vector<int> v(1000);
generate_n(begin(v), v.size(), gen);
generate_n(begin(v), v.size(), bind(d, e)); // with bind
generate_n(begin(v), v.size(), [&] { return d(e); }); // with lambda
// check that all of them are less than 10
all_of(begin(v), end(v), [] (int i) { return i < 10; }); // with lambda
all_of(begin(v), end(v), bind(less<int>(), _1, 10)); // with bind

---
function
A uniform wrapper that can hold any callable entity with a given signature
char foo(int); // function
struct S { char foo(int); }; S s; // member function
struct T { char operator()(int); }; T t; // function object
auto bf = bind(foo, _1); // std::_Bind<char (*(std::_Placeholder<1>))(int)>
auto bs = bind(&S::foo, s, _1); // std::_Bind<std::_Mem_fn<char (S::*)(int) const> … >
auto bt = bind(t, _1); // std::_Bind<T (std::_Placeholder<1>)>
std::function<char(int)> ff = bf;
std::function<char(int)> fs = bs;
std::function<char(int)> ft = bt;
ff(1); fs(1); ft(1); // callable like a function
char g(std::function<char(int)> f) { cout << f(1); } // pass it to a function
std::map<int, std::function<char(int)>> int_to_f_map; // store in a data structure

---
Smart pointers: unique_ptr
- unique_ptr<T>, unique_ptr<T[]>
  - strict ownership
    - owns the object it points to and deletes it when it goes out of scope
  - movable, not copiable
  - replaces auto_ptr
  - supports a custom deleter
{
  unique_ptr<C> p(new C(…));
  C c = *p; // use like a pointer
  p->f(); // use like a pointer
  v.push_back(std::move(p));
  *p; // error
} // p automatically delete'd
{
  unique_ptr<C[]> q(new C[N]);
  q[i] = C();
} // q automatically delete []'d
{
  unique_ptr<char> p((char*)malloc(N), free);
} // the pointer will be deleted using free

---
Smart pointers: shared_ptr
{
  shared_ptr<C> p(make_shared<C>(…)); // or
  auto p = make_shared<C>(…);
  C c = *p; // use like a pointer
  p->f(); // use like a pointer
  v.push_back(p);
  *p; // ok
} // the pointer is automatically deleted
{
  shared_ptr<FILE> f(
    fopen("main.cpp", "r"),
    fclose // custom deleter
  );
  fread(…, f.get());
} // fclose is automatically called
- shared_ptr<T>
  - shared ownership
    - the last that goes out of scope deletes the object
  - movable and copiable
  - reference counted
  - supports a custom deleter
- if possible, use make_shared<> instead of direct new
  - faster (it saves an allocation)
  - exception safe
- no shared_ptr<T[]> yet

---
ratio
- Exact representation of any finite rational number with a numerator and denominator representable by compile-time constants
  - arithmetic operations
  - comparisons
typedef ratio<5, 3> x;
static_assert(x::num == 5 && x::den == 3, "x == 5/3");
typedef ratio<10, 6> y;
static_assert(y::num == 5 && y::den == 3, "y == 5/3");
static_assert(ratio_equal<x, y>::value == true, "5/3 == 10/6");
typedef ratio_divide<x, y>::type z;
static_assert(z::num == 1 && z::den == 1, "5/3 / 10/6 == 1");

---
ratio and SI
Convenience typedefs
namespace std {
  typedef ratio<1, 1000000000000000000> atto;
  typedef ratio<1, 1000000000000000> femto;
  …
  typedef ratio<1, 1000000> micro;
  typedef ratio<1, 1000> milli;
  typedef ratio<1, 100> centi;
  typedef ratio<1, 10> deci;
  typedef ratio< 10, 1> deca;
  typedef ratio< 100, 1> hecto;
  typedef ratio< 1000, 1> kilo;
  typedef ratio< 1000000, 1> mega;
  …
  typedef ratio< 1000000000000000, 1> peta;
  typedef ratio<1000000000000000000, 1> exa;
}

---
chrono (time utilities)
Duration
namespace std { namespace chrono {
template <class Representation, class Period = ratio<1>> class duration;
// convenience typedefs
typedef duration<int64_t, nano> nanoseconds;
typedef duration<int64_t> seconds;
typedef duration<int, ratio<60>> minutes;
…
}}
minutes m1(3);
minutes m2(2);
minutes m3 = m1 + m2;
microseconds us1(3);
microseconds us2(2);
microseconds us3 = us1 - us2;
microseconds us4 = m3 + us3;
minutes m4 = m3 + us3; // error; to force use a duration_cast
us3 < us1; // true

---
chrono (time utilities)
- Clocks and time points
  - various clocks: system (wall-clock), steady (non decreasing), high resolution (with the shortest tick period)
chrono::system_clock::time_point start = chrono::system_clock::now();
this_thread::sleep_for(chrono::seconds(1));
cout << (chrono::system_clock::now() - start).count() << '\n';
// prints 1000131 (microseconds) on my machine with gcc
start = chrono::system_clock::now();
this_thread::sleep_until(start + chrono::seconds(1));
cout << (chrono::system_clock::now() - start).count() << '\n';

---
?