## Slide 1
Matthias Hoek
on behalf of the PANDA Cherenkov Group
The PANDA Barrel DIRC
PSHP 2013, Frascati, 11.-13. November 2013

## Slide 2
FAIR & PANDA Experiment
Barrel DIRC Design
Pattern Reconstruction
Technical Challenges
Prototyping
Conclusions
Overview

## Slide 3
Facility for Antiproton and Ion Research (FAIR)
GSI
Secondary beams
  Broad range of radioactive beams up to 1.5 – 2 GeV/u
  Antiprotons 3 – 30 GeV
HESR
PANDA
5·1010 antiprotons
• 1.5 to 15 GeV/c
High luminosity mode Dp/p ≈ 10-4 with stochastic cooling L = 1032 cm-2s-1
High precision mode (<8.9GeV/c) Dp/p ≈ 10-5 with electron cooling L = 1031 cm-2s-1
Primary beams
  Heavy Ion Beams
  30 GeV protons (2·1013s-1)

## Slide 4
Physics Goals of PANDA
Precision Hadron Spectroscopy
Exotic States
(Glueballs, Hybrids)
In-Medium Modifications
Nucleon Structure
Hypernuclei
Non-perturbative QCD
Excellent PID required
Notes: Some physics book results
General PANDA physics goals (Map?)
Final states for some key channels

## Slide 5
PANDA DIRC Detectors
Barrel DIRC
(22˚- 140˚)
Beam
Endcap Disk DIRC
(5˚- 22˚)
EMC
GEM
Notes: Picture of TS + geometrical acceptance

## Slide 6
PANDA DIRC Detectors
Barrel DIRC
(22˚-140˚)
Beam
Endcap Disk DIRC
(5˚ -22˚)
Barrel DIRC
PID Goal: 3s p/K separation up to 3.5GeV/c
Endcap Disk DIRC
Novel design
PID Goal: 3s p/K separation up to 4GeV/c
p/K Cherenkov angle difference at 3.5 GeV/c in fused silica ~8.5mrad
Kaon distribution of the radiative decay J/y → K+K- g
Notes: Picture of TS + geometrical acceptance
This radiative decay is a benchmark channel for glue balls;

## Slide 7
Barrel DIRC Base Design
250cm
100cm
Radiator bars (80pcs)
17mm32mm2400mm
Syn. fused silica
Photon detection
& Electronics
15000 channels
MCP-PMTs
Fast TDC + ADC FEE
Focussing optics
High-refractive index lens
30cm
Expansion Volume
Mineral oil
Performance Goals
qc single photon resolution 8-10mrad
20 detected photons per track (b=1)
Timing resolution ~100ps
Simulated hit pattern
N-LaK 33
Notes: General design + numbers
15k readout channels
Timing
Rates

## Slide 8
Barrel DIRC Design Options
Narrow bars
& segmented expansion volume
Plate & Prisms
One fused silica prism per sector (5 bars)
Higher photon yield
More ambiguities in reconstruction
Fused silica prism
1 plate per sector (16cm)
Similar to Belle II iTOP
Less surfaces
Needs timing information
X-Y hit pattern
X (cm)
Y (cm)
Notes: Bars or plates

## Slide 9
Barrel DIRC Pattern Reconstruction (Bar)
Use BaBar-like reconstruction approach
Generate Look-up table
The ambiguity background is spread around the true peak
Photon arrival time information is used to reduce the ambiguity background
Does not work for plate configuration
Reconstructed
Cherenkov angle
for 50 tracks
(with time cut)
See H. Kumawat’s talk @ DIRC2013

## Slide 10
Approach inspired by BELLE II
Use photon hit time per pixel & generate PDFs (needs simulation)
Barrel DIRC Pattern Reconstruction (Plate)
1 GeV/c Pion
1 GeV/c Kaon
p+
K+
3.5 GeV/c, 22˚
X-Y
X-T
T-Y
p/K separation at 3.5 GeV/c possible even w/o focussing
See H. Kumawat’s talk @ DIRC2013
2 GeV/c muon, 35˚

## Slide 11
Barrel DIRC Technical Challenges
Radiator
Production of large fused silica bars or plates
Strict mechanical tolerances on shape with optical finish and long sharp edges
Few potential vendors worldwide
Photon Detection
Single photon detection
Spatial resolution ~ few mm
Operation in 1T field
Fast rise time
High-rate capability 0.2 MHz/cm2
Fast Frontend
Electronics
High-precision timing
Fast high-bandwidth pre-amplifiers
Radiation hardness
Trigger-less DAQ
Large data volume
Notes: Radiator
FEE
Photon Detector

## Slide 12
~30 bar and plate prototypes from different vendors
  Different fabrication process and bulk materials
Characterise bar surfaces and shape with lasers
  Bulk transmission
  Internal reflection coefficient
Sensitive to surface roughness and subsurface damage
  RMS roughness (indirect) with 1-2Å precision
Barrel DIRC Radiator
See G. Kalicy’s talk @ DIRC2013
Notes: Surface properties
Bar geometry

## Slide 13
Barrel DIRC Photon Detection – 3 years ago

## Slide 14
MCP-PMT is preferred sensor technology
ALD technique improves lifetime
  6C/cm2 reached
Meets most PANDA requirements
Barrel DIRC Photon Detection
See A. Lehmann’s talk @ DIRC2013
Notes: MCP-PMTs life time development

## Slide 15
Barrel DIRC Frontend Electronics
MCP-PMT
connector
NINO
PADIWA
Pre-amplifier
Card (16ch)
Discriminator
Card (16ch)
LVDS output+ slow control
Current feedback amplifier (THS3201)
NINO ASIC
(8 ch)
MCP-PMT
connector
Pre-amplifier
(MMIC)
FPGA
(Lattice MachXO2)
LVDS output
FPGA programming interface
Power supply
(+5V)
DAQ system based on TRBv3 board (developed at GSI)
  High-resolution TDC (<10ps) based on FPGAs
  LVDS input signals
Precise timing
  amplitude information (ToT)
Compare different technologies
  ASIC: NINO chip (ALICE TOF)
  FPGA: PADIWA (GSI)
Charge (pC)
Notes: FEE development
TRB system + NINO Frontend card

## Slide 16
Prototypes in test experiments
2009 – GSI
  Proton beam, E~2GeV
  Oil tank
2011 – CERN T9
  Mixed hadron beam, p<15GeV/c
  Oil tank
2012 – CERN T9
  Fused silica prism
  3x3 Planacon MCP-PMT matrix
  896 readout channels
  Fused silica plate
Barrel DIRC Protypes
CERN T9 (2012)
See G. Kalicy’s talk @ DIRC2013
Notes: Test beam results from CERN 2012
Pattern with prism attached
Look at Greg’s talk!

## Slide 17
2012 Analysis in progress
  3D tracking to be added
  Improve timing/position calibration
  Plate reconstruction in preparation
Preliminary results indicate sufficient performance
Barrel DIRC Prototypes
10 GeV/c, 60˚
Number of detected photons
Expected: Qc=824mrad, sQc≈9mrad
See G. Kalicy’s talk @ DIRC2013
Qc=825mrad
sQc≈ 11mrad
Notes: Test beam results from CERN 2012
Pattern with prism attached
Look at Greg’s talk!

## Slide 18
2013 – MAMI B, 855 MeV electron beam
Test frontend electronics
  Timing resolution
  Time walk correction
  Thresholds
Barrel DIRC Prototypes
33˚
NINO
PADIWA
w/o correction
Walk correction
Time (ns)
frequency
Notes: MAMI 2013 results
Picture of our prototype
Image
Timing results

## Slide 19
Barrel DIRC is a key component of the PANDA PID system
Challenging R&D program
  Radiator production
  Compact expansion volume
  Lens system
  Photon detection in strong magnetic field
  Fast frontend electronics
Sophisticated prototypes to verify performance
  Decision on radiator geometry in 2014
TDR ready end of 2014
Installation planned for 2017
Conclusions
PANDA Cherenkov Group
JINR Dubna | FAU Erlangen-Nürnberg | JLU Gießen | U. Glasgow |
GSI Darmstadt | HIM Mainz | JGU Mainz | SMI OeAW Vienna