## Slide 1
Vincenzo Rizi
CETEMPS,
Dipartimento di Scienze Fisiche e Chimiche,
Università Degli Studi dell’Aquila,
L’Aquila, Italy
vincenzo.rizi@aquila.infn.it
Raman LIDARs for Pierre Auger Observatory: field experiences and results.
AtmoHEAD 2014 - Padova Italy, 19-21 May, 2014

## Slide 2
SORRY!

## Slide 3
OUTLINE
The different Raman LIDARS at Pierre Auger Observatory
Performances and constrains
Aerosol observations
Some results and comments

## Slide 4
Primary issue.
Is the Raman LIDAR useful to the High Energy Astroparticle Detectors?
YES
Why?

## Slide 5
atmosphere as a calorimeter
fluorescence detector concept
E: shower energy
T: atmospheric optical transmission
UHECR (Ultra High Energy Cosmic Rays)
energy deposit in the atmosphere
fluorescence (UV range)
fluorescence detector
Fluorescence yield
Detector calibration

## Slide 6
http://apcauger.in2p3.fr/Public/Presentation/

## Slide 7
s range along the line of sight
It can be easily estimated with sufficient precision ...
The absorption can be neglected …
Total atmospheric (optical) transmission
High variability …
direct measurements

## Slide 8
LIDAR ARCHITECTURE
TRANSMITTER
RADIATION SOURCE
RECEIVER
LIGHT COLLECTION AND DETECTION
SYSTEM CONTROL AND DATA ACQUISITION

## Slide 9
TRANSMITTER
It provides laser pulses that meet certain requirements depending on application needs (e.g., wavelength, pulse duration time, pulse energy, repetition rate, divergence angle, etc).
Transmitter consists of lasers, collimating optics, diagnostic equipment.

## Slide 10
RECEIVER
It collects and detects returned photons
It consists of telescopes, filters, collimating optics, photon detectors, discriminators, etc.
The receiver can spectrally distinguish the returned photons.

## Slide 11
SYSTEM CONTROL AND DATA ACQUISITION
It records returned data and corresponding time of flight, and provides the coordination to transmitter and receiver.
It consists of multi-channel scaler which has very precise clock so can record time precisely, discriminator, computer and software.

## Slide 12
detector
Interaction between
radiation and object
radiation
source
signal
propagation
Data acquisition and analysis
radiation
propagation

## Slide 13
detector
Interaction between
radiation and object
radiation
source
signal
propagation
Data acquisition and analysis
radiation
propagation

## Slide 14
Lidar system efficiency and geometry factor
Emitted laser photon number
Laser photon transmission through medium
Probability of a transmitted photon to be scattered
Scattered photon transmission through medium
Probability of a scattered photon to be collected

## Slide 15
In general, the interaction between the light photons and the particles is a scattering process.
The expected photon counts are proportional to the product of the
(1) transmitted laser photon number,
(2) probability that a transmitted photon is scattered,
(3) probability that a scattered photon is collected,
(4) light transmission through medium, and
(5) overall system efficiency.
Background photon counts and detector noise also contribute to the expected photon counts.

## Slide 16
A PARTIAL REPRESENTATION
(a physics-ological drama)

## Slide 17
LIDAR PHYSICAL PROCESS
Interaction between light and objects
Scattering (elastic & inelastic): Mie, Rayleigh, Raman
…
Light propagation in atmosphere or medium: transmission/extinction
Extinction = Scattering + Absorption

## Slide 18
back-scattering
extinction
scattering
LIDAR
aerosol
back-scattering
aerosol extinction

## Slide 19
Back-scattering cross sections
Physical process | Back-scattering cross section
Mie (aerosol) scattering | 10-8  10-10 cm2 sr-1
Rayleigh scattering | 10-27 cm2 sr-1
Raman scattering | 10-30 cm2 sr-1
laser
receiver

## Slide 20
Example ...o=355nm
~21nm
~32nm
~53nm

## Slide 21
LIDAR … aerosol devoted

## Slide 22
Aerosol lidar
i.e., tropospheric aerosols
backscattering increase

## Slide 23
Raman aerosol lidar
Rayleigh/Mie signal
N2 Raman/anelastic signal
i.e., tropospheric aerosol
more backscattering
more attenuation
no backscattering
o
o+N2

## Slide 24
capability of detecting low light levels
suppression of cross-talking between the different
channels (i.e, suppression of the strong elastically
backscattered light in Raman channels)
Main characteristics

## Slide 25
Real Raman signal in presence of a cloud
cloud transmission
cloud backscattering
Nitrogen Raman
Air/aerosol Rayleigh
1/2 hour
measurements
nighttime
Sept. 2001

## Slide 27
Raman LIDAR signals

## Slide 28
ADVANTAGES of Raman LIDAR technique:
A major drawback of backscatter LIDARs is that it is not possible to independently invert the optical parameters of interest, namely, the aerosol extinction (i.e., attenuation) and the aerosol backscatter (equivalently to the mean reflectivity in the observation volume) without introducing correlating hypotheses between these two parameters.
This limitation is, however, superseded by Raman LIDARs, i.e., systems combining the elastic channel and one inelastic (nitrogen or oxygen) Raman channel.
WHY … a Raman LIDAR system? 1/2

## Slide 29
DISADVANTAGES of Raman LIDAR technique at AUGER:
Limited measurement time period.
It needs long acquisitions ( 30 min)
WHY … a Raman LIDAR system? 2/2

## Slide 30
The standard atmospheric Raman lidar are usually deployed where the aerosols are abundant!
Within AUGER observatories, we are facing the sensitivity limits of the Raman lidar sampling.
This is improving the understanding of the technique.

## Slide 31
The different Raman LIDARS at Pierre Auger Observatory

## Slide 32: AUGER Atmospheric monitoring
Laser facilities
LIDAR
at each eye
Understanding fluorescence data requires monitoring atmospheric conditions
Weather stations
& Radiosondes
FRAM, HAM
APF
Star monitor

## Slide 33
Aug. 2006 to Jun. 2007
RAMAN LIDAR (located at Los Leones: 35.32S, 69.30W, 1416m a.s.l.),
remotely operated, with the primary goal of measuring (at the best) the
vertical profile of the aerosol optical depth.
In spite of some problems, one year of observations allows to characterize the aerosols climatology over the site.
V.R.
# 1

## Slide 34
WHERE … was the RAMAN LIDAR located?
expected a high degree of horizontal homogeneity in the atmospheric properties

## Slide 35
F. Molina Campos
V.R.

## Slide 36
AUGER RAMAN
LIDAR
in the dry or semi-arid pampa
V.R.

## Slide 37
O2
N2
RAMAN
receiver
Optical fiber
from telescope
Elastic
DAQ
The RAMAN CORNER
Laser
telescope
small cost!
V.R.
V.R.
V.R.
V.R.
V.R.

## Slide 38
The measurements cover a period from 15/08/2006 to 24/06/2007
(179 homogeneous measurements of aerosol extinction and backscatter coefficients).
WHEN … the RAMAN LIDAR measurements?
Thanks to
La difunta correa

## Slide 39
Planetary Boundary Layer
Entrainment zone
An example of RAMAN LIDAR data
The aerosol extinction, backscatter and lidar ratio profiles measured on May 18, 2007 (about 48000 laser shots) in the period 19:26-20:06LT. The error bars indicate the propagated statistical indetermination
WHAT … is the RAMAN LIDAR measuring?

## Slide 40
winter aerosol backscatter coefficient profile

## Slide 41
summer aerosol backscatter coefficient profile
longer extension in vertical of the aerosols

## Slide 43
PBL monthly mean values

## Slide 44
The PBL thickness (sPBL) shows low values in fall/winter and enlarges in spring/summer.
The extension of the entrainment region (h) is reduced during late spring/summer (… the free troposphere is more stable than in autumn/winter, and the vertical mixing is damped)

## Slide 45
VAOD and INT monthly mean values (at about 5km)
summer
autumn
winter
spring

## Slide 46
The Raman (monthly mean) VAODs and INT:
Low values during late fall and early winter
High values in summer
Relative high content of aerosols in late winter and early spring (diffuse regional meteorological pattern? Increased occurence of dust storms? …)

## Slide 47
SEM images of two samples of coarse aerosols between 2.5-10m size.
Left: sample collected on 1 June 2008, concentration 4.6g/m3.
Right: sample collected on 14 August 2008, concentration 13.6g/m3
Instituto de Física Rosario (IFIR)
Universidad Nacional de Rosario
WHO … are these aerosols?

## Slide 48
The black circles showed in each figure correspond to filter pores, while the aerosol particles are showed in white or gray tones. The scale on the bottom of image shows a 1 micrometer reference for the particle size. The mineral dust particles are irregular and relatively large, they are made mainly of SiO2, and other oxides of metal elements like Al, Ca, Mg and Fe.

## Slide 49
Sept. 2010 to July 2011
RAMAN LIDAR (located at 37.9228N, 102.6109W and 1198m a.s.l. in Prowers County, Colorado, about 15 km south of Lamar, Colorado, USA).
remotely operated, with the primary goal of measuring (at the best) the
vertical profile of the aerosol optical depth to be compared with simultaneous side scattering technique.
# 2

## Slide 50
The Raman LIDAR system: the side pictures show the 3 channel LIDAR receiver, the telescope, and the laser transmitter (UV mirrors, and beam expander).

## Slide 53
Left: The VAODs data versus time as measured with the AMT (black dots) and the Raman LIDAR (blue squares) at 6 km a.g.l. Right: VAODs measured with the AMT versus Raman LIDAR for hours observed with both instruments. The diagonal is shown in black, a fit to the black dots in red.

## Slide 54
May 2013 to …
RAMAN LIDAR (located at 35°16'50.65"S, 69°20'12.26"O and 1379m a.s.l. in Central Raman LIDAR Facility (previous Central Laser Facility) at AUGER observatory
remotely operated, with the primary goal of measuring (at the best) the
vertical profile of the aerosol optical depth to be the benchmark of the measurements carried with FD telescopes and the central laser.
# 3

## Slide 55
The Raman LIDAR at C(R)LF

## Slide 56
Nev DeWitt Pierrat, Blake Knoll (CSM)
Batteries
Thermal
Reservoir
(2000 L Water)
Weather
Station
Microwave
Link
Raman LIDAR
Storage and
future expansion
Laser,
Beam Switching,
Robotic Calibration
Insulation

## Slide 57
STATUS and PERFORMANCES of the Raman LIDAR:
opto-mechanics highly stable;
sampling from boundary layer to free troposphere;
one vertical profile of AOD and aerosol backscatter in 12’ or 24’.
UPGRADE of the Raman LIDAR:
capability to measure the H2O mixing ratio profile;
better detection of the (weak) Raman backscatterings;
(this LIDAR and analysis methods benchmarked against EARLINET)

## Slide 58
PERFORMANCES of the Raman LIDAR
Raman LIDAR operation in CLF
Raman data taken before and after FD shifts, 24 min (evening) 12 min (morning), since end of July.
After each Raman run:
- data are copied to LNGS/INFN/Italy and CSM/USA
- a program computes preliminary VAOD values and generates preliminary VAOD plots, all is available after few seconds;
- off-line, more refined analysis after few days on http://atmoforum.aquila.infn.it/osservatorio/

## Slide 59
Clean and dirty nights along a FD shift.
PERFORMANCES of the Raman LIDAR
aerosol day to day variability

## Slide 60
Clean

## Slide 61
Dirty

## Slide 62
EVOLUTION of the Raman LIDAR

## Slide 63
Raman LIDAR
equipments raw costs
Solid state Nd:YAG laser 40000$
High power mirrors 900$
Beam expander 1500$
Silica window 6000$
Telescope parabolic mirror 3000$
Optical fiber 1500$ Interference filters, beam splitters 18000$
Photomultipliers 3900$
High voltage power supply 4500$
Data Acquisition system 8600$ Optical parts (lenses, etc.) 2200$
Opto-mechanical parts (optical tables, holders, etc.) 6200$
TOTAL 96300$

## Slide 64
THANK YOU!