## Slide 1
ASY-EOS 2015
International Workshop on
Nuclear Symmetry Energy and Reaction Mechanisms
FARCOS:
a new telescope array for correlations and spectroscopy
A. Trifiró1, L. Acosta2 , R. Andolina7, L. Auditore1, C. Boiano3, G. Cardella4, A. Castoldi3,5, M. D’Andrea4, E. De Filippo4, S. De Luca1, D. Dell’Aquila9, L. Francalanza9, E. Geraci4,7, B. Gnoffo4, C. Guazzoni3,5, G. Lanzalone6,8, I. Lombardo9, N. Martorana6,7, T. Minniti1, S. Norella1, A. Pagano4, E.V. Pagano6,7, M. Papa4, S. Pirrone4, G. Politi4,7, F. Porto6,7, L. Quattrocchi1, F. Rizzo6,7, E. Rosato9, P. Russotto4, G. Saccà4, M. Trimarchi1, G. Verde4,10, M. Vigilante9.
1 Dipartimento di Fisica e Scienze della Terra, Università di Messina & INFN Gruppo Collegato di Messina, Messina, Italy
2 Instituto de Física, Universidad Nacional Autónoma de México, México D.F. 01000, Mexico
3 INFN Sezione di Milano, Milano, Italy
4 INFN Sezione di Catania, Catania, Italy
5 Politecnico di Milano, Dipartimento di Elettronica, Informazione e Bioingegneria, Milano, Italy
6 INFN Laboratori Nazionali del Sud, Catania, Italy
7 Dipartimento di Fisica e Astronomia, Università di Catania, Catania, Italy
8 Università Kore Enna, Enna, Italy
9 INFN-Sezione di Napoli & Dipartimento di Fisica, Università di Napoli Federico II, Napoli, Italy
10 Institute de Physique Nucléaire d’Orsay, Orsay, France

## Slide 2
(2+)
9.56 MeV
(4+)
10.150 MeV
(?)
11.230 MeV
theoretical
(4+)
11.760 MeV
Vcm
Vcm
10Be
α
6He
α
6He
Lab Frame
Emitting Source Frame
α
α
n
n
10Be:
possible molecular state
M. Freer et al., Phys. Rev. Lett. 96, 042501 (2006)

## Slide 3
High energy and angular resolution (θ,φ)
Wide dynamic range of identification
  -MeV to GeV
Pulse-shape capabilities
-Low identification thresholds
High Modularity
Flexibility
-Electronics integrated, reconfigurable
-Copuling with 4π array, magnetic spectrometers,
neutron detectors, etc..
Portability
-Campaign in several facilities around the world
Features planned for FARCOS array

## Slide 4
1°stage:
1 square (0.3x62x62 mm3) DSSSD 32+32 strips
2° stage:
1 square (1.5x62x62 mm3) DSSSD 32+32 strips
3° stage:
4 60x32x32mm3
CsI(Tl) crystals
photodiodes
FARCOS (Fentomscopy ARray for Correlation and Spettroscopy)

## Slide 5
Pre-Amplification Stage
Mesytec MPR-32
NPA prototype
Test of Silicon Detectors
Analogue acquisition based on 16 channels NIM-CAEN Amplifiers
and VME CAEN 64 channels QDC
Digital acquisition of PAC signals with aliasing filter and AAA
Amplifier [1] and SIS3301 ADC boards [2] for digitizing of 64 channels.
Digital acquisition of PAC signals with GET [3] electronics;
[1] Boiano et al., A 16-Channel Programmable Antialiasing Amplifier, 2010 IEEE
[2] SiS33001SiS330/ 651801/00 MHz VME FADCs - User Manual, Struck Innovative System GmbH, Germany, 2004
[3] S. Anvar et al. and AT-TPC collaboration, 2011 IEEE
Amplification and Acquisition Systems
Net-Instruments

## Slide 6
µTCA Crate
µTCA Backplane
µTCA Backplane
ASAD
AGET
AGET
AGET
AGET
ASAD
AGET
AGET
AGET
AGET
ASAD
AGET
AGET
AGET
AGET
ASAD
AGET
AGET
AGET
AGET
COBO
Gb Eth
RAM
FPGA CPU
ASAD
AGET
AGET
AGET
AGET
ASAD
AGET
AGET
AGET
AGET
ASAD
AGET
AGET
AGET
AGET
ASAD
AGET
AGET
AGET
AGET
COBO
Gb Eth
RAM
FPGA CPU
ASAD
AGET
AGET
AGET
AGET
ASAD
AGET
AGET
AGET
AGET
ASAD
AGET
AGET
AGET
AGET
ASAD
AGET
AGET
AGET
AGET
COBO
Gb Eth
RAM
FPGA CPU
DETECTOR ARRAY
MUTANT A
RAM
FPGA CPU
MUTANT B
RAM
Gb Eth
FPGA CPU
Multiplicities
Trigger / TS
1 Gb Ethernet per COBO
10 Gb Switch µTCA MCH
10 Gb Ethernet
DAQ Network Switch
DAQ Workstations
General Electronics for TPCs
132 channels for each telescope
New front-end electronics planned for FARCOS array
AGET
PA
Shaper
SCA
Pulser

## Slide 7
Test of Silicon Detectors
Mixed
alpha
source
3MeV protons
FWHM = 0.5%
300µm
Junction side
3MeV protons
FWHM = 1.2%
300µm
ohmic side

## Slide 8
Test of CsI(Tl) Detectors
Charge Sensitive
Preamplifiers
based on
CHIMERA ones
Mixed α source
Energy (channel)
α+Pb @ 62AMeV

## Slide 9: The FARCOS prototype (4 modules) was coupled to the 4π detector CHIMERA at LNS during the InKiIsSy experiment (see E. De Filippo Talk): 124Xe+64Zn @ 35 AMeV reaction was studied in order to disentangle Isospin against Size effects in Projectile Like Fragments dynamical fission
16°<θlab<44°

## Slide 10
α
3He
p
t
d
ECsI(ch)
ESi(1500µm) (ch)
Z=8

## Slide 11
Ring8 - UP
Ring8 - BOTTOM
Information on Neutrons
CsI(Tl)
CsI(Tl)

## Slide 12
Estimated efficiency ≈ 3%
Information on Neutrons
Yeld of Neutrons (a.u.)
(n,px) reaction
in CsI(Tl)
(n,dx) reaction
in CsI(Tl)
(n,αx) reaction
in CsI(Tl)

## Slide 13
High energy and angular resolution (θ,φ)
Wide dynamic range of identification
  -MeV to GeV
Pulse-shape capabilities
-Low identification thresholds
High Modularity
Flexibility
-Electronics integrated, reconfigurable
-Copuling with 4π array, magnetic spectrometers,
neutron detectors, etc..
Portability
-Campaign in several facilities around the world
Features of FARCOS array

## Slide 14
(2+)
9.56 MeV
(4+)
10.150 MeV
(?)
11.230 MeV
theoretical
(4+)
11.760 MeV
d=250mm
Δθ=0.5o
Vcm
Vcm
10Be
α
6He
α
6He
Lab Frame
Emitting Source Frame
α
α
n
n
10Be:
possible molecular state
M. Freer et al., Phys. Rev. Lett. 96, 042501 (2006)
● center of each pixel

## Slide 15
Physics Cases
Particle-Particle Correlation Function  Esym
Cluster states (α-conjugate, boson condensates,…)
Invariant mass spectroscopy
Femtoscopy: space time probes of emitting source
Study of isospin effects on reaction mechanisms
and on IMF production
…
Possible Coupling of Farcos to other apparata:
Chimera
Indra
Must2
Fazia
Magnex
… … …
G. Verde
G. Verde

## Slide 16
A. Trifiró1, L. Acosta2 , R. Andolina7, L. Auditore1, C. Boiano3, G. Cardella4, A. Castoldi3,5, M. D’Andrea4, E. De Filippo4, S. De Luca1, D. Dell’Aquila9, L. Francalanza9, E. Geraci4,7, B. Gnoffo4, C. Guazzoni3,5, G. Lanzalone6,8, I. Lombardo9, N. Martorana6,7, T. Minniti1, S. Norella1, A. Pagano4, E.V. Pagano6,7, M. Papa4, S. Pirrone4, G. Politi4,7, F. Porto6,7, L. Quattrocchi1, F. Rizzo6,7, E. Rosato9, P. Russotto4, G. Saccà4, M. Trimarchi1, G. Verde4,10, M. Vigilante9.
1 Dipartimento di Fisica e Scienze della Terra, Università di Messina & INFN Gruppo Collegato di Messina, Messina, Italy
2 Instituto de Física, Universidad Nacional Autónoma de México, México D.F. 01000, Mexico
3 INFN Sezione di Milano, Milano, Italy
4 INFN Sezione di Catania, Catania, Italy
5 Politecnico di Milano, Dipartimento di Elettronica, Informazione e Bioingegneria, Milano, Italy
6 INFN Laboratori Nazionali del Sud, Catania, Italy
7 Dipartimento di Fisica e Astronomia, Università di Catania, Catania, Italy
8 Università Kore Enna, Enna, Italy
9 INFN-Sezione di Napoli & Dipartimento di Fisica, Università di Napoli Federico II, Napoli, Italy
10 Institute de Physique Nucléaire d’Orsay, Orsay, France