## Slide 1: The italian neutron sources suite and a close look to the BTF at LNF
Paolo Valente – INFN Roma & LNF
Helium Replacement in Italy - HeRe in Italy
ENEA Frascati, December 2nd–3rd, 2013

## Slide 2: Outlook
The Italian neutron facilities:
  [Research] reactors and radio-sources
  Accelerator driven
A closer look to BTF at LNF
Future perspectives: IRIDEn

## Slide 3: Reactors

## Slide 4
ENEA TAPIRO research reactor
Fast source reactor
Based on the concept of AFSR (Argonne Fast Source Reactor – Idaho Falls)
Designed by ENEA staff
Start-up in 1971
Fuel:
  98.5% U – 1.5% Mo
  18.5 g/cm3 density
  93.5% U235 enrichment
  22107.42 g/U235 operative mass
Cladding: 0.5 mm stainless steel
Reflector:
  Material: Copper
  Cylindrical Inner Reflector: 348 mm diameter
  Outer reflector: 800 mm diameter
  Overall height: 700 mm
  Weight: 2600 kg

## Slide 5
TAPIRO irradiation
Φ ≈ 3∙1012 n/cm2∙s @ 5 kW
Φ ≈ 5∙1011 n/cm2∙s @ 5 kW
Φ ≈ 2∙1010 n/cm2∙s @ 5 kW
Samples ready for irradiation
in the central radial channel

## Slide 6
TRIGA RC-1 Mark II, power 1 MW, thermal reactor
Info: Marco Ciotti
marco.ciotti@enea.it
Position | Flux (n/cm2/s)
Rotary Specimen Rack (40 positions) | 2.00·1012
Pneumatic Transfer System | 1.25·1013
Central Thimble | 2.68·1013
Thermal column collimator | ~1.00·106
Tangential channel collimator | ~1.00·108
Reflector: graphite
Control rods: 3 B4C fuel follower + 1 B4C regulation rod

## Slide 7: Laboratory of Applied Nuclear Energy (LENA) University of Pavia, Italy

## Slide 8
LENA Research Center
Interdepartmental Research Centre of the University of Pavia
(http://www.unipv-lena.it/ )
250 kW TRIGA Mk II Research Reactor
X ray industrial generator
  250kV, 12mA dose 15,6 Gy/min
  350kV, 6mA dose 17,5 Gy/min
Gamma source of Co-60 (0.86KGy/h)
Radiochemistry Laboratory
Cyclotron IBA 18/9
  18 MeV protons (Imax = 80 µA)
  9 MeV deuterons (Imax = 40 µA)

## Slide 9
TRIGA Mark II Nuclear Research Reactor
250-kW light-water Thermal Reactor with an annular graphite reflector cooled by natural convection
offers many positions of irradiation (facilities) with "in-core" neutrons flux from 1012 to 1013 n cm-2 s-1
6 “out-core” irradiation facilities with typical neutron flux from 106 to 1010 n cm-2 s-1
Fuel: 20% enriched Uranium
Moderator/Cooling: light water
Reflector: grafite
3 control rod
Irradiation: 400 hours/year
TRIGA (Training, Research, Isotopes production, General Atomics)

## Slide 10
B
C
A
Thermal Column
109 – 1010 n/s

## Slide 11: Radioactive sources

## Slide 12: IRP: Radiation Protection Institute IRP-DOS: Neutron irradiation hall
“thermal neutron” facility.
A polyethylene moderating cube, 1 m side, with 3 inserted AmBe sources. Characterized and optimized through Monte Carlo calculations, it provides, at the measuring point (the upper face of the cube), a total neutron flux of about 3.104 cm-2 s-1 : 60% neutrons of energy < 0.4 eV; 13% in the range 0.4 eV 100 keV; 27% for energies > 100 keV.
Shadow cone for the scattered contribution to be determined during instrumentation calibration.
“fast neutron” facility
The bank can host 5 sources. Now it contains a 252Cf source providing a total neutron flux of about 105 cm-2 s-1 corresponding to a maximum H*(10) dose equivalent rate of 360 Sv/h.

## Slide 13: Accelerator driven

## Slide 14: The 14 MeV Frascati Neutron Generator - ENEA
The Frascati Neutron Generator (FNG) started operations in Nov. 1992 making available 14 MeV neutrons at a medium intensity (1011n/s) to EU Fusion Community.
It was designed and built by ENEA Frascati for conducting neutronics experiments and to validate nuclear data in the field of thermonuclear controlled fusion.
FNG is a linear accelerator which accelerates a deuterium beam (300 kV and up to 1 mA) onto a tritiated target to produce 14 MeV neutrons via the D+T fusion reaction
The maximum neutron yield is 1.0*1011 n/s. Neutron yield is measured by the associated Alfa particle method with 3 % accuracy. The neutron emission is almost isotropic due to the low acceleration potential (300 KeV maximum) but is characterized by the typical beam-target energy-angle distribution.
During its life FNG has been extensively used for performing a large number of neutronics benchmark and mock-up experiments which covered almost all the most important neutronics aspects related to ITER & Fusion Neutronics.
The FNG facility is also used for qualification, calibration, and radiation damage resistance tests of nuclear detectors and components, and for studies on new neutron (and gamma) detectors.

## Slide 16
DT & DD Target Simulation
Neutron Energy vs emission angle (DT target)
DT Spectrum
classic-relativistic
comparison
DD neutron flux around FNG target
DT neutron flux around FNG target

## Slide 17: Spallation vs. photo-nuclear production
Spallation
Photo-nuclear

## Slide 18: Neutron photo-nuclear production
Why photo-nuclear production from electron beam?
- Competitive costs up to 1016 n/s (at the target)

## Slide 19: Accelerator driven pro and cons

## Slide 20: BTF at LNF
  50-500 MeV electrons or positrons (irrespective from linac primaries)
  Poisson statistics at low intensity
  Few % intensity fluctuations at intermediate intensity (thousands of particles)
  <1% momentum spread
  Few mm beam spot
  Up to 50 Hz [minus 1 bunch/s, used for energy measurement]
From 107-109 positrons or electrons/pulse at 510 MeV from the DAFNE linac…
      …To a finely tuned “single-particle” beam:

## Slide 21: DAFNE Linac
 | Design | Operational
Electron beam final energy | 800 MeV | 510 MeV
Positron beam final energy | 550 MeV | 510 MeV
RF frequency | 2856 MHz | 
Positron conversion energy | 250 MeV | 220 MeV
Beam pulse rep. rate | 1 to 50 Hz | 1 to 50 Hz
Beam macropulse length | 10 nsec | 1 to 10 nsec
Gun current | 8 A | 8 A
Beam spot on positron converter | 1 mm | 1 mm
norm. Emittance (mm. mrad) | 1 (electron) 10 (positron) | < 1.5
rms Energy spread | 0.5% (electron) 1.0% (positron) | 0.5% (electron) 1.0% (positron)
electron current on positron converter | 5 A | 5.2 A
Max output electron current | >150 mA | 350 mA
Max output positron current | 36 mA | 100 mA max
Trasport efficiency from capture section to linac end | 90% | 90%
Accelerating structure | SLAC-type, CG, 2π/3 | 
RF source | 4 x 45 MWp sledded klystrons TH2128C | 

## Slide 22: BTF complex

## Slide 23: BTF electron beam
P = N f E
N = number of particles [Up to 1010 e-/bunch]
f = repetition rate [Up to 49 bunch/s]
E = beam energy [Nominal: 510 MeV]
Maximum rate = N f = 49 Hz × 1010 e-/s = 4.9×1011 e-/s
Pmax = 0.04 kW

## Slide 25: Photon and neutron fluence

## Slide 26: BTF target and shielding

## Slide 27: BTF neutron spectrum

## Slide 28: BTF photon background
1.5 m distance
10-5 photons/cm2/primary

## Slide 30: Neutron source summary
At 1.5 m distance:
Total neutron flux: 8×10-7 n/cm2/pr ±3%
Flux = 4.5×105 n/cm2/s
Equivalente dose = 45 mSv/h
d (m) | ×10-7 n/cm2/pr
0.5 | 58
1 | 15
1.5 | 8
d (m) | ×10-5 n/cm2/pr
0.5 | 63
1 | 5.7
1.5 | 1
Total photon flux = 5×10-5 g/cm2/pr

## Slide 31: New BTF lines?
  Keep using 0° line for ‘standard’ testing
  Use 45° line to drive beam to a new “target area”
    This allows to have a target station dedicated to neutron production and
    A space for neutron experiments
  Add 90° to build a “low energy” line
    This allows to use the Linac groundwork and tunnel as additional shielding

## Slide 33
INFN - Laboratori Nazionali di Legnaro (LNL)
SPES (SELECTIVE PRODUCTION OF EXOTIC NUCLEAR SPECIES) PROJECT
FACILITY GENERAL LAYOUT
Neutron facility 1
thermal neutrons for BNCT
TRASCO-RFQ accelerator
TRIPS proton source
RF wave guides
Klystron
Beam line to LENOS facility
Radiation damage facility
Neutron facility 2 (Optional) epithermal neutrons for BNCT
Current layout of neutron source facilities

## Slide 34: Future facilities

## Slide 35
At the INFN National Labs of Legnaro (LNL), a variable energy (35-70 MeV) high current proton cyclotron (Imax = 750 µA) will soon come into operation (2015).
It will open up the prospect of high flux neutron facilities in Italy that could perform various research activities.
The SPES p Cyclotron at LNL

## Slide 36
ISOL FACILITY
-phase
Expansion for ADS to study GEN4 reactor (-phase)
To ALPI Linac
Experimental hall
Proton and neutron irradiation areas (-phase)
Reaccelerated RIBs
Radioactive Ion Beams are reaccelerated by the superconductive linac ALPI. A normal conductive RFQ placed before ALPI will match the input acceptance beam parameters.
10m
Two ISOL targets
High Resolution Mass Separator
DM/M= 1/40000 (physics design)
ECR-Charge Breeder & Medium Resolution Mass Separator DM/M=1/1000
CYCLOTRON
Radioisotopes for medical applications (-phase)

## Slide 38: IRIDE
Proposal for a new large infrastructure for fundamental and applied physics research.
Conceived as an innovative and evolutionary tool also for multi-disciplinary investigations in a wide field of scientific, technological and industrial applications
A high intensity “particle beams factory”
Based on a combination of
  a high duty cycle radio-frequency superconducting electron linac (SC RF LINAC)
  high energy lasers.
It will be able to produce a high flux of electrons, photons (from infrared to gamma band), neutrons, protons and possibly positrons, that will be available for a wide national and international scientific community interested to take profit of the most worldwide advanced particle and radiation sources.

## Slide 39: IRIDEn: neutrons at IRIDE

## Slide 40: 1 GeV electrons

## Slide 41
IRIDE(expected)
Continuous mode
Be(p/d,n)
(g,n)
spallation
IRIDE (expected)
Short pulse mode
Short pulse
Long pulse
continuous

## Slide 42: Conclusions
Italy has discontinued nuclear power generation since 25 years, still, there are a number of small neutron sources
  Research reactors exist and are routinely used
  Accelerator driven:
    Be/Li/Tritium bombardment with protons/deuterons
    Photo-nuclear production (electron beam)
A growing interest and new impulse to the development of new facilities or upgrade of existing ones
  Complementary to the main European (mainly spallation) sources
  Useful for neutron detectors R&D and industry