## Slide 1: 10B Cathode for thermal neutron
Thermal Neutrons interact with 10B, and alfas are emitted entering in the gas volume generating a detectable signal.
Al Support
Gas gap (Ar CO2)
10B
Thermal neutrons
Alfas
Actually 4% efficiency ... working to obtain 70%. Good candidate as 3He replacement detector
Low Efficiency
Big active area
Beam Monitor and transmission
Side-On detector
cathode
Thermal neutrons
Alfas
High Efficiency
Small active area

## Slide 2: Polyethilene for fast neutron
Fast Neutrons interact with H, and protons are emitted entering in the gas volume generating a detectable signal.
Idrogenate Support
Gas gap (Ar CO2)
Al
Thermal neutrons
Protons
Actually 0.1% efficiency ... working to obtain few %.
Low Efficiency
Big active area
Beam Monitor and transmission
Side-On detector
cathode
Thermal neutrons
Protons
High Efficiency
Small active area

## Slide 3: Why Micro Pattern Gas Detector
MPGDs offer the following advantages
  Very high rate capability (MHz/mm2) suitable for high flux neutron beams like at ESS
  Submillimetric space resolution (space resolution adapted to experimet requirements)
  Time resolution from 5 ns
  Possibility to be realized in large areas and in different shapes
  Radiation hardness and very low neutron-induced discharge probability
  Insensitivity to gamma rays (with appropriate gain)

## Slide 4: Working point
The alfas produce an higher ionization respect to protons
that allow a wider plateau before the gamma background

## Slide 5
Test @ n-tof: measurements
Neutron beam has been reconstructed making an horizzontal scan on the beam.
Horizontal scan
ToF measurements: thermal energy spectrum
Single event
100 events
Slices acquisition: Time spectrum (1ms/bin), 150ms total gate.

## Slide 6: Imaging of Thermal Neutron beam through a cadmium grid (ISIS)
Beam
Online plot
Image realized with a scan
through the beam
Real time image with
30 sec scan with pad dimension of 6 mm pad

## Slide 7: Only limited by alfa/proton path
Image dimension 90x90 mm2
Pressurized chamber ? CF4 ?
Sealed detector ?

## Slide 8: Two prototype of GEMPIX for 10B studies
Head-on detector
Side-on detector
HV Connector
Medipix
DAQ box
3x3 cm2
active area
Pixels of
50x50 µm2
alfas
Compton e lectron
from gamma
Cluster detail

## Slide 9: MPGD possibilities at CERN
Large laminator
1.4m
Large Solvent strip
2m x 0.8m
Large exposure
2.2m x 1.4m
PI etching
0.6m
Large oven
1.4mx 2.3m
Thanks to 9 new equipment and a team of 20 engineer & technicians we have the capability to provide:
-GEM up to 2m x 0.5m
-Micromegas detectors up to 2m x 1m
-THGEMs up to 600mm x 600mm
Equipment are essentially dedicated to prototype production.
Possibilities for medium to high volume productions (but needs formal agreement).
Large developer
Large stripper
Large etcher
Large electro-etch
2m x 0.8m
I
In 107 1m
Now 0.6m
In 107
In 107

## Slide 10: Neutrons converters possibilities
Thermal neutrons
  B4C vacuum deposition : some experience on GEM at CERN
  BN vacuum deposition : some experience on metals
  B10 to be studied
  Large sizes up to 600mm width possible in theory.
Fast neutrons
  PET GEMs with aluminium electrodes (need laser)
  PET THGEMs with aluminium electrodes feasible
    Polycarbonate THGEMs have already been produced

## Slide 11: Main issue for future developments
Boron / converter depositions
  Mecchanical resistence, radiation hard
  type of suports and shapes ... large surface !
Fluxed or Sealed and/or pressurized detectors
Radiation Hard Front End Electronics
  Channels high density for a better resolution
Pixelated detector to match High Rate capability
  2D imaging and fast DAQ
Several neutron surces for detector characterization