Time Calibration with nanobeacons in KM3Net Italia
Christophe Hugon
INFN Genova

---
Overview and objectives
- Context and last result of data analysis reminder
- Technical description of the analysis software

---
Timing measurement in the detector
LED of the OM 11 was used (runs 681 684 & 687)
LED mean wavelength at 470 nm
LED flash at 2 kHz
 => peaks observables within a modulo 500 us timing plot
Floor 8
Floor 7
Floor 6
Floor 5
80 m
Floor 4
Floor 3
Floor 2
Floor 1
3
0
2
1

---
Timing measurement in the detector
LED of the PM 11 was used (runs 681 684 687 1359)
LED mean wavelength at 470 Hz
LED flash at 2 kHz (and 500 Hz for OM time check)
 => peaks observables within a modulo 500 us timing plot
Floor 8
Floor 7
Floor 6
Floor 5
80 m
Floor 4
Floor 3
Floor 2
Floor 1
3
0
2
1

---
Timing plotting for all floors
The distribution gives a good time distribution.
But the intensities in function of distance are not as expected
LED positioning ?
LED homogeneity ?
Floor to floor shadow
The timing profile only can be used for the water properties studies

---
Fit function time improvement
Pmt pulse
30 %
Given by a 3 parts mathematical approach
Permit to take in account the full pulse
Can decrease the resolution from 5 ns to less than 1 ns (see examples)

---
Timing results with pulses at 1 ns of resolution
Floor number (N)	Measured propagation time with floor 1 (floor N-1)	Theoretical time with floor 1 (floor N-1)	Differential time with floor 1 (floor N-1)
1	0 +/- 0.5	0	0
2	174 (174) +/- 0.9	186 (186)	12 (12)
3	354 (179) +/- 0.5	371 (185)	17 (5)
4	550 (195) +/- 0.4	558 (187)	8 (-9)
5	740 (189) +/- 0.3	744 (186)	4 (-4)
6	929 (188) +/- 0.5	931 (187)	2 (-2)
7	1113 (182) +/- 0.72	1118 (187)	5 (-6)
8	1302 (175) +/- 0.75	1305 (187)	6 (1)
As a cross check a lower intensity run was used for first floors. It correspond to
The fitting confirm the last results. It brought a better error to the measure.
Floor number (N)	Propagation time with floor N-1
2	172 +/- 1.1
3	180 +/- 0.9
4	197 +/- 0.8
2.5 ns <=> 20 cm

---
Scattering process
b_P=1.34%nu_S({550 nn} over {%lambda})^{1.7}+0.312%nu_l({550 nm} over {%lambda})^{0.3}
Clancy W. James
Km3 internal note
2 components to the scattering :
On molecule (isotropic angular distribution)
On particles (Forward going angular distribution)
The both processes depend on the wavelength on a different exponent.
They imply a delay in time arriving
In function of distance
In function of wavelength
Need to know the timing to deduce the water properties.
The fit method can help to extract the timing delay to the ns.

---
Example of fitting:
Measure of the scattering
The function fit is a convolution between a Gaussian and an exponential.
Mean is the mean of the Gaussian
Lambda correspond to the “tail length”
The fitting method allow to extract the scattering information

---
Secondary measurement : SPE measurement

---
SPE measure low intensity

---
Analysis conclusion
The LED can be used for time calibration, even at high light intensity (first floors)
The fitting method:
Improved the resolution to the ns
I need the positioning to go further.
The scattering can be studied, needs the simulation (see tomorrow slides)
Checked up to 320 m distance

---
Data Analysis software
- Nreader NReader/documentation
- Started from Tommaso pt data reader
- Has a complete and modulable event model
Features :
Read a PTFile and store it;
Uncompress the channels. Conversion in a NEvent object model;
serialize and save it in multiple formats;
Give human readable xml output format;
on the fly compression in gz or bz2 format;
Very Extensible for the user.
LED run (681 PM 31)

---
Data Analysis software
- Nreader NReader/documentation
- Started from Tommaso pt data reader
- Has a complete and modulable event model
Features :
Read a PTFile and store it;
Uncompress the channels. Conversion in a NEvent object model;
serialize and save it in multiple formats;
Give human readable xml output format;
on the fly compression in gz or bz2 format;
Very Extensible for the user.
LED run (681 PM 31)
Testable and usable at Lyon CC,
check out on the documentation

---
Schematic descripion
PT data file
RawReader
RawData
Exhaustive
NCalibrator
Nreader data file
Readable
Or data
Compressed
Raw2N
NEvent
RunInfo
NHit
Id
Charge
Trigger time
Channels
NEvent
RunInfo
NHit
Id
Charge
Trigger time
Channels
Amplitudes
Calibrated charge
NIO
Third part work

---
Output data and extensibility :
The properties and serialization
- Each Nreader data object inherit of Nserializable :
  - Use the boost serialization and filters to save/compress a part of the attributs
  - Has maps of int/double/string to contain extensible data
- Example (from the fitting result saving) :
  hit->SetDoubleProperty (“FitPar1”, Par [1]);
  [continue, save file, reopen]
  Par [1] = hit->GetDoubleProperty (“FitPar1”);

---
Project on the Analysis software
- Third person use/cross check/complement of the current analysis
- Complete it with finer elements
  - Ideal detector definition
  - Calibrated detector definition (compass/positioning data)
- Try to bind to the track reconstruction ?

---
Timing results with pulses at 5 ns of resolution
Floor number (N)	Fit mean time (gaus on mod 500us distribution)	Diff with floor 1 (floor N-1)	Offset with floor 1 (floor N-1)	Propagation time with floor 1 (floor N-1)	Theoretical time with floor 1 (floor N-1)	Differential time with floor 1 (floor N-1)
1	250,320 +/- 5	0	9	0	0	0
2	250,210 +/- 5	110 (110)	294 (285)	175 (175)	186 (186)	11 (11)
3	250,000 +/- 5	210 (110)	574 (280)	355 (180)	371 (185)	16 (5)
4	249,895 +/- 5	315 (105)	875 (301)	551 (196)	558 (187)	7 (-9)
5	249,802 +/- 3	408 (92)	1157 (282)	741 (190)	744 (186)	3 (-4)
6	249,714 +/- 3	496 (88)	1434 (277)	930 (189)	931 (187)	1 (-2)
7	249,627 +/- 1	583 (87)	1714 (280)	1123 (193)	1118 (187)	-5 (-6)
8	249,493 +/- 1	717 (134)	2034 (320)	1309 (186)	1305 (187)	-4 (1)
As a cross check a lower intensity run was used for first floors. It correspond to
As a first approximation the used index for propagation time was taken from the measurement of the group velocity of light in sea water at the ANTARES site (1.38).
Floor number (N)	Propagation time with floor 1 (floor N-1)
1	170 +/- 5
2	182 +/- 5
3	197 +/- 5
2.5 ns <=> 20 cm

---
Timing results with pulses at 5 ns of resolution
Floor number (N)	Fit mean time (gaus on mod 500us distribution)	Diff with floor 1 (floor N-1)	Offset with floor 1 (floor N-1)	Propagation time with floor 1 (floor N-1)	Theoretical time with floor 1 (floor N-1)	Differential time with floor 1 (floor N-1)
1	250,320 +/- 5	0	9	0	0	0
2	250,210 +/- 5	110 (110)	294 (285)	175 (175)	186 (186)	11 (11)
3	250,000 +/- 5	210 (110)	574 (280)	355 (180)	371 (185)	16 (5)
4	249,895 +/- 5	315 (105)	875 (301)	551 (196)	558 (187)	7 (-9)
5	249,802 +/- 3	408 (92)	1157 (282)	741 (190)	744 (186)	3 (-4)
6	249,714 +/- 3	496 (88)	1434 (277)	930 (189)	931 (187)	1 (-2)
7	249,627 +/- 1	583 (87)	1714 (280)	1123 (193)	1118 (187)	-5 (-6)
8	249,493 +/- 1	717 (134)	2034 (320)	1309 (186)	1305 (187)	-4 (1)
As a cross check a lower intensity run was used for first floors. It correspond to
As a first approximation the used index for propagation time was taken from the measurement of the group velocity of light in sea water at the ANTARES site (1.38).
Floor number (N)	Propagation time with floor 1 (floor N-1)
1	170
2	182
3	197
2.5 ns <=> 20 cm

---
Timing results with pulses at 5 ns of resolution
Floor number (N)	Fit mean time (gaus on mod 500us distribution)	Diff with floor 1 (floor N-1)	Offset with floor 1 (floor N-1)	Propagation time with floor 1 (floor N-1)	Theoretical time with floor 1 (floor N-1)	Differential time with floor 1 (floor N-1)
1	250,123 +/- 0.5	0	9	0	0	0
2	250,010 +/- 0.9	111 (111)	294 (285)	174 (174)	186 (186)	12 (12)
3	250,910 +/- 0.5	211 (100)	574 (280)	354 (179)	371 (185)	17 (5)
4	249,805 +/- 0.4	316 (105)	875 (301)	550 (195)	558 (187)	8 (-9)
5	249,713 +/- 0.3	408 (92)	1157 (282)	740 (189)	744 (186)	4 (-4)
6	249,625+/- 0.5	496 (88)	1434 (277)	929 (188)	931 (187)	2 (-2)
7	249,528 +/- 0.72	593 (97)	1714 (280)	1113 (182)	1118 (187)	5 (-6)
8	249,398 +/- 0.75	723 (130)	2034 (320)	1302 (175)	1305 (187)	6 (1)
As a cross check a lower intensity run was used for first floors. It correspond to
The fitting confirm the last results. It brought a better error to the measure.
Floor number (N)	Propagation time with floor 1 (floor N-1)
1	170 +/- 5
2	182 +/- 5
3	197 +/- 5
2.5 ns <=> 20 cm

---
Timing results with pulses at 5 ns of resolution
Floor number (N)	Measured propagation time with floor 1 (floor N-1)	Theoretical time with floor 1 (floor N-1)	Differential time with floor 1 (floor N-1)
1	0 +/- 5	0	0
2	175 (175) +/- 5	186 (186)	11 (11)
3	355 (180) +/- 5	371 (185)	16 (5)
4	551 (196) +/- 5	558 (187)	7 (-9)
5	741 (190) +/- 3	744 (186)	3 (-4)
6	930 (189) +/- 3	931 (187)	1 (-2)
7	1123 (193) +/- 1	1118 (187)	-5 (-6)
8	1309 (186) +/- 1	1305 (187)	-4 (1)
As a cross check a lower intensity run was used for first floors. It correspond to
As a first approximation the used index for propagation time was taken from the measurement of the group velocity of light in sea water at the ANTARES site (1.38).
Floor number (N)	Propagation time with floor N-1
2	170 +/- 5
3	182 +/- 5
4	197 +/- 5
2.5 ns <=> 20 cm

---
Timing results with pulses at 5 ns of resolution
Floor number (N)	Measured propagation time with floor 1 (floor N-1)	Theoretical time with floor 1 (floor N-1)	Differential time with floor 1 (floor N-1)
1	0 +/- 5	0	0
2	175 (175) +/- 5	186 (186)	11 (11)
3	355 (180) +/- 5	371 (185)	16 (5)
4	551 (196) +/- 5	558 (187)	7 (-9)
5	741 (190) +/- 3	744 (186)	3 (-4)
6	930 (189) +/- 3	931 (187)	1 (-2)
7	1123 (193) +/- 1	1118 (187)	-5 (-6)
8	1309 (186) +/- 1	1305 (187)	-4 (1)
As a cross check a lower intensity run was used for first floors. It correspond to
As a first approximation the used index for propagation time was taken from the measurement of the group velocity of light in sea water at the ANTARES site (1.38).
Floor number (N)	Propagation time with floor N-1
2	170 +/- 5
3	182 +/- 5
4	197 +/- 5
2.5 ns <=> 20 cm

---
Raw timing conclusion
The LED can be used for time calibration, even at high light intensity (first floors)
Need a method to improve the error in the timing (especially for the < 5 ns FWHM of time distribution)