## Slide 1: DAFNE beam-test facility
47th LNF Scientific Committee
Frascati, 14th November 2013

## Slide 2: BTF concept
From 107-109 positrons or electrons at 510 MeV from the linac…
…To a finely tuned “single-particle” beam:
  50-500 MeV electrons or positrons
    Independent from linac primaries
  Poisson statistics at low intensity
  Few % intensity fluctuations at intermediate intensity (thousands of particles)
    Limited by Linac energy uncertainty
  <1% momentum spread
    Limited by selection/collimation configuration
  Few mm beam spot
    Limited by emittance and optics
[Mambo BGO]

## Slide 3: BTF history/1
Originally designed in the DAFNE accelerator complex by F. Sannibale and G. Vignola, 1991
Commissioning started, Feb. 2002, by G. Mazzitelli and P. Valente
Users access since Nov. 2002

## Slide 4: BTF history/2
Separation of BTF line from DAFNE injection, 2004, B. Buonomo joins
Photon tagging, 2005, AGILE team collaboration
Pulsed magnet + fast dipole, 2006, L. Quintieri joins

## Slide 5: BTF history/3
Target shielding 2008
Neutron source studies start 2009
2010, L. Foggetta joins

## Slide 6: BTF people
Staff
Paolo Valente, scientific responsible
Bruno Buonomo, technical responsible
  Linac technical staff
Luca Foggetta, operations and run coordinator,
diagnostics, acquisition and controls, services, …
  DAFNE operations team
Maria Rita Ferrazza, administration support
  Luca Ceccarelli, undergrad. student, user support
  Oscar Frasciello, Ph.D. student, simulations
Related projects
AIDA, FP7, beam-test facilities, diagnostics, G. Mazzitelli, F. Murtas, G. Claps
n@BTF, NESCOFI neutron studies, R. Bedogni, A. Esposito
IRIDE-neutrons, A. Pietropaolo, L. Quintieri, S. Bartalucci, ...
!CHAOS, innovative control systems

## Slide 7: DAFNE Linac
 | Design | Operational
Electron beam final energy | 800 MeV | 510 MeV
Positron beam final energy | 550 MeV | 510 MeV
RF frequency | 2856 MHz | 
Positron conversion energy | 250 MeV | 220 MeV
Beam pulse rep. rate | 1 to 50 Hz | 1 to 50 Hz
Beam macropulse length | 10 nsec | 1 to 10 nsec
Gun current | 8 A | 8 A
Beam spot on positron converter | 1 mm | 1 mm
norm. Emittance (mm. mrad) | 1 (electron) 10 (positron) | < 1.5
rms Energy spread | 0.5% (electron) 1.0% (positron) | 0.5% (electron) 1.0% (positron)
electron current on positron converter | 5 A | 5.2 A
Max output electron current | >150 mA | 350 mA
Max output positron current | 36 mA | 100 mA max
Trasport efficiency from capture section to linac end | 90% | 90%
Accelerating structure | SLAC-type, CG, 2π/3 | 
RF source | 4 x 45 MWp sledded klystrons TH2128C | 

## Slide 8: DAFNE Linac
B
A
C
D

## Slide 9: Bunch selection and timing
Three-way selection installed in Spring 2004
Fast-dipole 3° + Pulsed dipole 3° can drive bunches at
  0° to damping ring
  3° to BTF line
  6° to Linac spectrometer
  Linac
  spectrometer
  BTF line
  to/from DR

## Slide 10: Beam attenuation
Copper target
  Optimized shielding to reduce e.m. background

## Slide 11: Beam attenuation
Copper target
  Variable depth: 1.7, 2.0, 2.3 x0

## Slide 12: Energy selection
Linac
spectrometer
Tungsten collimators
42° momentum selection dipole

## Slide 13: Intensity fine tuning
A fine adjustment of the number of particles can be achieved:
  Without changing the momentum resolution:
    Modulating the Linac current [not possible in ‘parasitic mode’, very rough]
      Act on transport optics or modulators power/phase
    Choosing another target depth [step change but reproducible]
    Closing/Opening the down-stream vertical collimators [fine but small range]
    Closing/Opening the up-stream vertical collimators
  Also changing the momentum resolution:
    Closing/Opening the horizontal collimators

## Slide 14: BTF line
Straight line
More background
Used mainly for high-intensity;
  neutron photoproduction
  equipped with fluorescence flag
45° line
Equipped with detector testing gadgets:
  Remote-control table
  Beam spot and intensity diagnostics for medium and low intensity beam

## Slide 15: BTF complex

## Slide 16
Linac tunnel
Modulators
hall
BTF
control room
BTF
hall
DR hall
DAFNE hall
DR
power
DR pumping
KLOE
Nuclear Physics
building

## Slide 17: Diagnostics
Medium-low intensity
Scintillating fibers hodoscope
Silicon micro-strip detectors (currently under maintenance]
GEM Time-projection chambers
High intensity
Integrating current toroid
Fluorescence flag

## Slide 18: Triple GEM scheme

## Slide 19: GEM TPC
Gain
Readout
Particle
conversion
Gain
Readout
Particle
conversion
Standard Triple-GEM detector
Triple-GEM as time-projection chamber
tdrift

## Slide 20: GEM TPC
Horizontal
4 cm
5 cm
Front
Vertical
5 cm
Top
Side
4 cm

## Slide 21: GEM TPC example: channeling
Positron beam, 477 MeV
- No channeling
- Channeling

## Slide 22: Control system
calorimeter
‘old’ online monitor of BTF diagnostics integrated in the DAFNE general control system
XY beam profile
detector
Significant work already done and still under way on controls, in close collaboration [or by] the !CHAOS project
The BTF line (magnets, controls, diagnostics, tools) will be the first real application of !CHAOS
First commissioning going on this week
No nice picture to show, but we expect a brand new [working] system soon
Many additional bits and pieces added during the last years and have to be integrated:
  New remotely controlled motorized table
  GEM TPC acquisition system
  Slits/collimators/target motors and encoders
  WCM’s oscilloscope readout

## Slide 23: Beam parameters
Parameter | Value
Maximum rep. rate | 1-24 Hz [49 Hz]
Pulse duration | 1 / 10 ns
Linac frequency | 2,856 GHz
Parameter | Value
Maximum allowed intensity | 3×1010 e-/s
Maximum energy | 510 MeV [650 /550 MeV e-/e+]
[AMY microwave antenna]
[AMY microwave antenna]
10 ns

## Slide 24: Beam parameters
Measured emittance:
  <x2>=4 mm
  <x’2>=1.7 mrad
  (<x>2<x’>2-<xx’>2)=4 mmmrad
[508 MeV, Pepper pot]

## Slide 25: Beam parameters
[UA9 Medipix detector]
FWHM 2.4 × 1.8 mm
2 mrad RMS
1.4 mrad RMS

## Slide 26: Photon tagging/1
dipole magnet
silicon tagging
target
silicon detectors
Be window
Bremsstrahlung
photon
Incoming electron
Designed and built in close collaboration with the AGILE collaboration with the main purpose ot the AGILE scientific payload calibration:
  Silicon trackers + calorimeter

## Slide 27: Photon tagging/2
10
100
200
500 MeV
20
50
400× Crab Nebula

## Slide 28: Photon tagging/3
Some issues of this system
In order to have useful tagged photons, need to select clean single electron tracks:
  Offline reconstruction mandatory
  Low beam intensity, below 2-3 electrons/bunch
  Low useful rate, <0.5 Hz after selection (few % efficiency)
    At low energy:
      Low efficiency due to not linear “binning” in energy
      Cut-off due to acceptance of tagging modules (detectors outside the vacuum pipe)
    At high-energy
      Low efficiency due to 1/E spectrum
      More sensitive to spurious events due to off-momentum or off-angle electrons
Due to the peculiar geometry, uneven distribution of photon energies, in particular issue with:
  Geometric overlap of electrons radiating an intermediate energy photon and off-central electrons

## Slide 29: Neutron source/1
Why photo-production? Because it’s more convenient up to 1016 n/s (at the target)
Number of neutrons proportional to the electron beam power:
  P = rate×energy =[N×f]×E
    N = number of particles per bunch (let’s consider 1×1010)
    f = frequency (up to 49 Hz)
    E = beam energy (usually 510, up to 800)
  Maximum power: 40 W at 510 MeV
  Very simple estimate of neutron yield from Swanson’s empirical formula
    1011 n/s for Tungsten
    -20% on Lead, +50% on Uranium
  500 MeV

## Slide 30: Neutron source/2
n@BTF project
Simulated and designed an optimized target (W cylinder d=70 mm, l=60 mm) and shielding system (lead and polyethylene)
Preliminary measurements of the neutron field and photon background
1 MeV
100 MeV
1 keV
10 eV
Isolethargic fluence

## Slide 31: Neutron source/3
At 90° better n/g ratio

## Slide 32: Neutron source/4
Bonner Sphere Spectrometer equipped with Dysprosium activation foils (Dy-BSS)
Response matrix previously tested in reference neutron fields, ±2% overall uncertainty

## Slide 33: Neutron source/5
Good data/simulations agreement

## Slide 34: Neutron source summary
At 1.5 m distance:
Total neutron flux: 8×10-7 n/cm2/pr ±3%
Flux = 4.5×105 n/cm2/s
Equivalente dose = 45 mSv/h
d (m) | ×10-7 n/cm2/pr
0.5 | 58
1 | 15
1.5 | 8
d (m) | ×10-5 n/cm2/pr
0.5 | 63
1 | 5.7
1.5 | 1
Total photon flux = 5×10-5 g/cm2/pr

## Slide 35: BTF users/1
Mainly, two kinds of users:
  Test of detectors or beam diagnostics
    Any kind of detector: calorimeter,s scintillators, fibers, drift chambers, micro-pattern gas detectors (GEM, MSGC), RPC, diamond, silicon pixels, silicon micro-strips, fluorescence detectors, Cerenkov, RICH, …
  Real experiments using the electron or positron beam
    Thermo-acoustic expansion of materials due to ionizing particles (RAP)
    Absolute air and Nitrogen fluorescence yield (AIRFLY)
    Microwave emission from e.m. showers (AMY)
    Electron and positron channeling, parametric radiation

## Slide 36: BTF users/2
Year | Beam-days
2002 | 30
2003 | 150
2004 | 282
2005 | 364
2006 | 244
2007 | 224
2008 | 193
2009 | 256
2010 | 230
2011 | 105
2012 | 316
2013 | 160
40% of rejection in 2013
At least 20 teams/year
Average of 10 days/team
Average of 200 beam-days/year
Typically, two calls/year (November and May)
TARI funding in FP7 (HadronPhysics)

## Slide 37: BTF users/3
C

## Slide 38: BTF users/4
C

## Slide 39: BTF impact
References to BTF
A simple search on google scholar
Not easy to track all publications: many users do not cite or acknowledge the facility in the correct way
Year

## Slide 40: BTF costs

## Slide 41: More info…
LNF committee, since Oct. 1st 2012:
  G. Bencivenni, P. Branchini, Prof. A. Di Ciaccio (chair), E. Cisbani, G. Mazzitelli
  P. Valente, B. Buonomo – ex officio
Database and schedule:
http://www.lnf.infn.it/acceleratori/btf/php/schedule.php?year=2013&acc=1

## Slide 42: Where do we go from here?

## Slide 43: First “upgrade”: constant improvement
2012-2013
Remotely controlled motorized table (AIDA) operational
Improved beam position diagnostics under commissioning (GEM TPC, AIDA)
Improved shielding for high intensity
Neutron beam monitors (servizio FISA) for high intensity
Gas system refurbished
Network, DAQ and controls revised and fully operational
Vacuum system improved (2×10-9 mbar)
New remote YAG flag
New end-flange with WCM and protection
Beam transport and timing optimized: 1.4, 3 and 10 ns shots now avalialable

## Slide 44: Constant improvement: an example
Beam exit flange:
At the beginning:
  Standard flanges with thinned ‘window’, 1.5 mm Aluminum
    Necessary because BTF vacuum in direct connection with Linac main vacuum (with a ‘fast’ safety valve)
  BTF vacuum sectioned, for a long period we used Kapton exit window
    Low pressure (not real vacuum): 10-3, 10-4
Now:
  Independent BTF vacuum system and pump
  New flange with Berillium thin window, 0.5 mm thick
  Integrated ceramics and WCM for beam charge measurement

## Slide 45: Lessons from 10+ years of BTF
The idea was there since from the beginning (Vignola, Sannibale), the commissioning required two youngsters enthusiasm and ingenuity (and relatively few resources)
A process of constant improvement with many small modifications/add-ons
A few larger upgrades, requiring more significant resources:
  Decoupling from DAFNE injection: large effort from the entire Accelerator Division
  High efficiency and long-term running: not transparent to the DAFNE operations, impacts on resources of the AD
  Tagged photon beam: difficult to handle, maintain, not really competitive with continuous sources
  Neutron beam:
    More interesting, more difficult wrt diagnostics, beam control
    But offers wider opportunities
Enlargement of user community/beam usage:
  Interested remains in single particle for detector testing but…
  … increasing interest in low energy with low background
  … increasing interest in high intensity electron and positron beams

## Slide 46: Possible perspectives
Large room for improvement in the field of innovative detectors:
  Extend energy range:
    Towards lower energy for detector testing
    Towards high energy for
      Higher neutron yield and more fast neutrons
      Lower multiple scattering, better spot
  Improve diagnostics quality (good upgrades thanks to AIDA, but more can be done)
  Exploit time structure of beam (and even improve it?)
  Exploit the possibility of high intensity and more particles, especially neutrons
  Exploit the flexibility and ease of use (and improve it)
  And…

## Slide 47: … improve access possibilities
Since duty-cycle is already quite high:
  Increase the number of beam lines
  Enlarge the experimental area
  Improve beam quality
    Background: more/better shielding
    Beam divergence: more/better collimation
    Beam size: better/more flexible optics

## Slide 48: Future plans/1
Three main lines:
  1. Low-energy electron/positron beams
    Improve low-energy diagnostics (LYSO calorimenter, AIDA)
    Improve background
  2. Electron/gamma beam for detector-testing
    Improve high-resolution tracking:
      Silicon micro-strip maintenance
      GEM TPC routinely in operations (AIDA)
    Improve photon tagging resolution
      Change tagging scheme
  3. Neutron source
    Increase linac energy
    Install ‘standard’ neutron diagnostics
    Routine operations of neutron source

## Slide 49: New BTF lines
  Keep using 0° line for ‘standard’ testing
  Use 45° line to drive beam to a new “target area”
    This allows to have a target station dedicated to neutron production and
    A space for neutron experiments
  Add 90° to build a “low energy” line
    This allows to use the Linac groundwork and tunnel as additional shielding

## Slide 50: A simpler alternative
  Essentially:
  Keep the neutron target inside the original BTF hall
    No time of flight
    No beam-dump experiments
  Do not modify walls and control room
  Expand experimental hall a bit only along access road

## Slide 51: Future plans/2
More can be imagined…
  4. Micro-divergence beam for channeling experiments
    Change collimation scheme, e.g. like CERN SPS ‘TAX’ dump-collimators

## Slide 52: Future plans/3
More can be imagined…
  5. Exploit the full Linac beam for beam-dump experiments
    Need to improve biological shielding to drive the full intensity beam [>1010 e-] for a significant time
Ne-/109

## Slide 53: Future plans/4
Present BTF hall
Low energy expansion
Neutron facility

## Slide 54: Thank you

## Slide 55: Shieldings

## Slide 56
Shielding
height
Roof
Hot spot

## Slide 59: More ambitious plans are possible…