## Slide 1: Software and TDAQ
Peter Lichard, Vito Palladino
NA62 Collaboration Meeting,
Sept. 2014 Ferrara.

## Slide 2: Straw DAQ
Straw will have 2 operational modes:
  Triggerless
  Standard L0 matching
Triggereless mode: we will record all the data coming from the detector (it might not be suitable for run with full intensity, 148Tb/d of data throughput), and the trigger time stamps, each PC in pc farm will record data coming from 2 SRBs
Standard mode: will send data within a tunable time window (from 0ns to 800ns with 25ns step).

## Slide 3: Possible Solution for TL Mode
Straw 4
Straw 3
Straw 2
Straw 1
SRB8
SRB7
SRB6
SRB5
SRB4
SRB3
SRB2
SRB1
SRB8
SRB7
SRB6
SRB5
SRB4
SRB3
SRB2
SRB1
SRB8
SRB7
SRB6
SRB5
SRB4
SRB3
SRB2
SRB1
SRB8
SRB7
SRB6
SRB5
SRB4
SRB3
SRB2
SRB1
Opt Switch
2x1Gb/s
2x1Gb/s
2x1Gb/s
2x1Gb/s
2x1Gb/s
2x1Gb/s
2x1Gb/s
2x1Gb/s
Switch
Opt Switch
10(+10)Gb/s
PC farm
PC
PC
PC
PC
PC
PC
PC
PC
10Gb/s
10Gb/s
10Gb/s
10Gb/s
10Gb/s
10Gb/s
10Gb/s
10Gb/s
1Gb/s
1Gb/s
1Gb/s
1Gb/s
1Gb/s
1Gb/s
1Gb/s
1Gb/s
Merger
10Gb/s
10Gb/s

## Slide 4: Data Handling (First Step)
SRBs are equipped with 2x1Gb/s Ethernet ports each to transmit data,
UDP packets are assembled in Event manager (data are read from the DDR3) and then forwarded to the physical link,
First (fake) data from SRB have been sent to PC farm (19/08/2014).

## Slide 5: Data Handling (First Step)
SRBs are equipped with 2x1Gb/s Ethernet ports each to transmit data,
UDP packets are assembled in Event manager (data are read from the DDR3) and then forwarded to the physical link,
First (fake) data from SRB have been sent to PC farm (19/08/2014).

## Slide 6: Data Handling (First Step)
SRBs are equipped with 2x1Gb/s Ethernet ports each to transmit data,
UDP packets are assembled in Event manager (data are read from the DDR3) and then forwarded to the physical link,
First (fake) data from SRB have been sent to PC farm (19/08/2014).

## Slide 7: RUN Control
RUN control provides the management of the detector,
SBC will be the bridge between RUN control commands and hardware (SRB and COVER configuration),
The RUN control is not yet implemented:
  Riccardo has already prepared an interface for the LKr that can fit our requirements,
Next week we plan to install the SBCs (the VME bridge) at least for straws 1, 2, and 3,
  At the same time we can install and test the software form the RUN control side

## Slide 8: Monitoring
VME Monitoring:
The SRBs will be able to use the full statistic (in and outside the burst) to generate histograms like the occupancy of each channel (VME online monitoring),
These histograms are stored in the VME manager and than forwarded (to PC farm? Dedicated PC?),
In case of in-spill monitoring we will send the data in accordance to the general rules of the experiment,
PC farm Monitoring:
Monitoring from the data stored in PC farm is also foreseen,
  Inter-station correlations,
  Tracking samples,
  …

## Slide 9: VME Monitoring (in-SPILL)
~
~
~
~
SOB
EOB
~
~
BURST (SRB signal)
Needed to wait “late” data from COVERs (few ms)
Monitoring data sent to SBCs
SPILL (integration time)

## Slide 10: VME Monitoring (off-SPILL)
~
~
SOG (Start Of Gap)
EOB
~
~
BURST (SRB signal)
Tunable integration window (from few ms up to SPS cycle)
EOG (End Of Gap)
~
~
~
~
~
~
~
~
~
~
~
~
Gap between SPS cycle and command to perform off-spill operations

## Slide 11: Software EOB data
Need to add information coming from non-TEL62 based detectors
  i.e. DCS data for the KTAG, LKr calibration settings, Straw eob data, etc.
Basic mechanism discussed, protoype implemented, to be reviewed
  Based on DIM publishing
  Add the data to the EOB event of the various detectors
  Decoding left to detector reconstructions
    Plan to add derived classes to SpecialTrigger class
Riccardo,
02/09/2014 TDAQ meeting

## Slide 12: Viewer
Example to follow:
KTAG on-line monitoring
(Technical Run)

## Slide 13: Database
The final solution of parameters storage is a database,
Emanuele Leonardi (Rome) is working on it
The WG (me) needs to provide the structure of this DB that will store all the information we need to initialize the detector:
  Thresholds
  SRB configuration (timing, delays, eth configuration, hsl configuration, PLL, etc.)
We can start with a simple TXT (or XML) file

## Slide 14: Software
Ethernet controller ✓
Thresholds setting and getting ✓
Noise scan ~ (to be tested)
SRB firmware upload ✗
COVER firmware upload ✓ (working on the old SRB to be tested on the new one)
Run control ✗ (sw from LKr)
Monitoring ✗
Concerning the SRBs, anything to add to the list that you think is needed for the Run…

## Slide 15: Conclusions and Plans
The first (small) step toward SRB integration within the TDAQ system has been done,
Software will be completed within next 2/3 weeks (at least the main parts),
Run control must be tested text week
Monitoring is not in a good shape but we can have something
Next steps toward October the 6th:
Develop the firmware to send realistic (but still fake) data to PC farm,
Installation of the new SBCs is planned for the next week,
Next week is foreseen a first implementation of RUN control,
Real data in PC farm (~ mid Sept.),
  Coarse time ordering (steps of 25ns) not immediately ready,
L0 matching will be next step,
On line monitoring.

## Slide 16: Spares

## Slide 17: Data Formats

## Slide 18: Data Formats
The coarse time (16-MSB) can 1.64 ms time resolution

## Slide 19: Data Throughput (DT)
 | Full luminosity | 20% FL | 1% FL
Average rate per Straw (kHz) | 60 | 12 | 0.6
DT per SRB (Gb/s) | 1.29 | 0.26 | 0.012
Data per SRB per Burst (MB) | 800 | 160 | 8
DT per station (Gb/s) | 10.3 | 2.1 | 0.1
Data whole detector (TB/d) | ~148 | ~30 | ~1.5