## Slide 1: CMS upgrade
Pierluigi Paolucci

## Slide 2: Outline
Phase I (2012-2014) 30 fb-1
  RE4 RPC detector installation
  HCAL upgrade
Phase II pre (2016)
  Pixel installation
  GEM detector at high eta
  RPC consolidation
Phase II (2018-2019) or (2019-2020) 300 fb-1
Phase III (2023-2025) HL-LHC 3000 fb-1
Phase IV (?)

## Slide 3: LHC schedule

## Slide 4: LHC luminosity schedule

## Slide 5: LHC luminosity schedule
By continuous performance improvement and consolidation
By implementing HL-LHC
Almost a factor 3
Goal of HL-LHC project:
  250 – 300 fb-1 per year
  3000 fb-1 in about 10 years

## Slide 6: LHC luminosity schedule
today
“CERN should undertake design studies for accelerator projects in a global context, with emphasis on proton-proton and electron- positron high-energy frontier machines.”
Project
FCC Study : p-p towards 100 TeV
Kick-off meeting: 11th Nov. 2013 (Daresbury)
Kick-off meeting: mid-February 2014

## Slide 7: Ingredients for the future scenario
The present system was designed up to:
L = 1034, pile-up = 40 and Time = 20 years
  First chamber built in the 2007
  Electronic designed in the 2006
  Chamber tested at GIF up to 0.1 C/cm2 (1000 fb-1)
  Component tested up to a neutron fluence of 1012 neutrons/cm2, corresponding to 3000 fb-1
New goals are:
L = 5 1034, pile-up = 60-140 and Time = 30-35 years

## Slide 8: Ingredients for the future scenario
Three bitter enemies:
Time, high luminosity & pile-up 
  Detector Longevity
  Trigger rate (physic case)
  Electronic speed/transmission protocol
  Computing (Filter farm.....)
Natural improvements thanks to the technology constantly developing.

## Slide 9: Ingredients for the future scenario
A lot of physic in the high/very high eta region
Pile-up 140, background and secondary vertexes
Trigger at 1 MHz
Tracker trigger & muon tagger
New muon technology & present system ?
New R&D and test needed to get 3000 fb-1 and 30 years.
But what about glue, bakelite, wires, spacers..... ?
We don’t have experience about an experiment of more than 30 years.

## Slide 10: Detector Longevity - background
Real time background monitor extrapolation
chamber | Rate (Hz/cm2) @ 1035 cm-2 s-1 | Integrated charge C/cm2 @ 3000 fb-1
W-2 RB3 | 2 | 0.0036
W+2 RB1 | 40 - 50 | <=0.07
W+2 RB4 | 30 - 40 | <=0.07
W-2 RB4 S4 | 80-90 | 0.13
RE1_ring3 | 5-10 | 0.01-0.02
RE-2_ring2 | 100-150 | <=0.21
RE-2_ring2_C | 150-200 | <=0.36
At moment, END OF RUN 2012-13, integrated charge is < 3 mC/cm2
In the worst case
Q = 0.36 C/cm2 @ Lint = 3000 fb-1 close to
Barrel chamber tested at GIF (0.1 C/cm2)
But Atlas and LHCb tested up to ~0.4 C/cm2
Test of 40x40 cm2 CMS chamber by korean group > 0.4 C/cm2

## Slide 11: Detector performance
2200 gaps, 250K electronic channels, 1200 DAQ boards, 1K sensors, 1K power system channels, 100 Km cables, 25K connectors.....

## Slide 12: Muon upgrade I & II

## Slide 13: Progetto RPC (2013-2014)

## Slide 14
RPC project overview - CMS retreat Jan 2013
14
14/7/11
Dott. Pigi Paolucci - I.N.F.N. of Napoli (ITALY) - Symposium on Collider Physics at Seoul (Korea)
14
Belgium
CERN
Bulgaria
CHINA | 2
KOREA | 16
INDIA | 4
BELGIUM | 10
COLOMBIA | 2
N. Puebla | 3
PAKISTAN | 6
EGYPT | 3
CERN | 4
ITALY | 28
BULGARIA | 12
Georgia | 2
TOTAL | 90
Barrel | Italy | Bulgaria | China | Colombia | 
Endcap | Korea | Pakistan | China | Belgium | CERN
Upgrade | Italy | Pakistan | India | Colombia | CERN
 | Korea | China | Belgium | Finland | Egypt
 | N. Puebla |  | Georgia |  | 
Georgia
Uniandes
Nueva
Puebla
Italy

## Slide 15: RE4 production sites

## Slide 16: Chamber construction

## Slide 17: 72 RE4 chambers built in the 2013

## Slide 18: RE4 installation (phase I) Today

## Slide 19: RE4 installation (phase I) Today

## Slide 20: But, how much does it cost ?
running

## Slide 21: But, how much does it cost ?
Upgrade I

## Slide 22: Phase II CMS proposal

## Slide 23: Muon upgrade proposal
Phase I: complete the endcap region
Phase II – pre: internal layer of 1 disk of the forward region (up to eta = 2.1)
Phase II: internal layer of the 2°, 3° and 4° disk.
Consolidation of the present system.
REQUIREMENTS
Background rate up to 1 MHz/cm2
Pile-up and secondary vertex
Trigger rate reduction
Background identification with time resolution

## Slide 24: Napoli nell’upgrade
Il gruppo è composto da 14 persone. Attualmente 4 persone sono già coinvolte nell’upgrade.
Napoli è coinvolta nel disegno delle camere a GEM
Napoli è responsabile per la progettazione dei nuovi rivelatori ad RPC per il consolidamento insieme a Bari, Pavia e Ghent
R&D per Elettronica e sistema di potenza sono già stati approvati dall’INFN
Purtroppo mancano giovani con la cultura “giusta”, riflessione tardiva in tutta la collaborazione. Alcune cose andrebbero cambiate e migliorate per consentire all’Italia di essere competitiva (Phd, post-doc….)

## Slide 25: GEM proposal - basic idea
The leading motivation is to improve muon triggering in this region
    Rate reduction from bending angle and increased efficiency from added redundancy

## Slide 26: GEM proposal

## Slide 27: GEM proposal

## Slide 28: GEM proposal

## Slide 29: GEM proposal

## Slide 30: GEM proposal

## Slide 31: iRPC
New “bakelite” and “glass” RPC are under test right now at GIF
  Old and new electronics
  New gas freon-less
  New gas components
A first new detector will be installed in the 2016 in the barrel region.

## Slide 32: Conclusioni
La fase I del progetto muoni sta procedendo benissimo. In schedule e nel budget.
L’upgrade di fase II è in fase di elaborazione e di scrittura. Il TP dovrebbe essere pronto per la fine dell’anno. Molte simulazioni sono ancora in corso.
Per HL-LHC il percorso è secondo me lungo e va capito bene che funzione deve avere il sistema dei muoni quando il tracker trigger sarà in funzione.
Enorme la mole di lavoro necessaria per la parte tecnologica.