## Slide 1: “GPU for trigger applications in HEP”
Gianluca Lamanna (INFN)
On behalf of GAP collaboration
Pisa, 28.1.2014

## Slide 2: Outline
GPU: brief introduction
GAP: GPU Application Project – Real Time
  GPU in low level triggers
  GPU in HLT and Medical Imaging
Examples of GPU in High Energy Physics

## Slide 3: GPU
The technical definition of a GPU is "a single-chip processor with integrated transform, lighting, triangle setup/clipping, and rendering engines that is capable of processing a minimum of 10 million polygons per second.“
First GPU: 31 august 1999 by NVIDIA (GeForce 256)
Revolution in Computer Graphics and Video Games!
1999
2002

## Slide 4: GPGPU
The possibility to use the GPU for generic computing (GPGPU) has been introduced by NVIDIA in 2007 (CUDA)
In 2008 OpenCL: consortium of different firms to introduce a multi-platform language for manycores computing.
At the same time the Moore’s law starts to show saturation: parallel computing is the solution!
Nowadays several supercomputers are based on GPU.

## Slide 5: Supercomputers

## Slide 6: The GPUs are very powerful
The GPU is a way to cheat the Moore’s law
  The PC no longer get faster, just wider.
  Very high computing power for «vectorizable» problems
Impressive derivative
  almost a factor of 2 in each generation
  Continous development
Easy to have a desktop PC with teraflops of computing power, with thousand of cores.
APE1000
APE100

## Slide 7: GPU vs CPU
A GPU is tailored for highly parallel operation while a CPU executes programs serially
For this reason, GPUs have many parallel execution units and higher transistor counts, while CPUs have few execution units and higher clock speeds
A GPU is for the most part deterministic in its operation
GPUs have much deeper pipelines (several thousand stages vs 10-20 for CPUs)
GPUs have significantly faster and more advanced memory interfaces as they need to shift around a lot more data than CPUs

## Slide 8: Different architecture
SMX executes kernels (aka functions) using hundreds of threads concurrently.
SIMT (Single-Instruction, Multiple-Thread)
Instructions pipelined
Thread-level parallelism
Instructions issued in order
No Branch prediction but Branch predication
Large caches
ILP
Brach prediction
Few powerful ALU
Short pipeline
CPU

## Slide 9: Pentium 5

## Slide 10: GK104 - Kepler

## Slide 11: Different pipeline
The data and instruction handling in multicores CPU and GPU are totally different.
Most of the resources in the GPU are in the ALUs.

## Slide 12: Example of performances

## Slide 13: GAP
GAP (GPU Application Project) for Realtime in HEP and medical imaging is a 3 years project funded by the Italian Ministry of research started in the beginning of April 2013.
Several position will be opened to work on GAP. Contact us for further information (http://web2.infn.it/gap ... Under construction).

## Slide 14: GAP and real-time

## Slide 15: Two problems to use GPU at L0
Computing power: Is the GPU fast enough to take trigger decision at tens of MHz events rate?
Latency: Is the GPU latency per event small enough to cope with the tiny latency of a low level trigger system? Is the latency stable enough for usage in synchronous trigger systems?

## Slide 16: GPU processing
NIC
GPU
chipset
CPU
RAM
PCI express
VRAM
Example: packet with 1404 B (20 events in NA62 RICH application)
T=0
0
us

## Slide 17: GPU processing
NIC
GPU
chipset
CPU
RAM
PCI express
VRAM
0
10
us

## Slide 18: GPU processing
NIC
GPU
chipset
CPU
RAM
PCI express
VRAM
0
10
99
us

## Slide 19: GPU processing
NIC
GPU
chipset
CPU
RAM
PCI express
VRAM
0
10
99
104
us

## Slide 20: GPU processing
NIC
GPU
chipset
CPU
RAM
PCI express
VRAM
0
10
99
104
134
us

## Slide 21: GPU processing
NIC
GPU
chipset
CPU
RAM
PCI express
VRAM
0
10
99
104
134
139
us

## Slide 22: GPU processing
NIC
GPU
chipset
CPU
RAM
PCI express
VRAM
0
10
99
104
134
139
us
The latency due to the data transfer from data source to the system is more important than the latency due to the computing on the GPU
It scales almost linearly (apart from the overheads) with the data size while the latency due to the computing can be hidden exploiting the huge resources.
Communication latency fluctuations quite big (~50%).

## Slide 23: First solution: PFRING
PFRING

## Slide 24: Latency measurement
It is not easy to measure (with high precision) the latency between two systems running with uncorrelated clocks
Use an oscilloscope to have a common time reference

## Slide 25: Results: PFRING
Big improvement thanks to the DNA driver
Concurrent data copy – kernel execution

## Slide 26: Results: PFRING

## Slide 27: Second solution: NANET
Nanet

## Slide 28: Results: NANET

## Slide 29: Results: NANET

## Slide 30: Physics case: NA62
Kaon decays in flight
  High intensity unseparated hadron beam (6% kaons).
  Event by event K momentum measurement.
Huge background from kaon decays
  ~108 background wrt signal
  Good kinematics reconstruction.
  Efficient veto and PID system for not kinematically constrained background.
RICH:
  17 m long, 3 m in diameter, filled with Ne at 1 atm
  Distinguish between pions and muon from 15 to 35 GeV.
  2 spots of 1000 PMs each
  Time resolution: 70 ps
  MisID: 5x10-3
  10 MHz events: about 20 hits per particle
  Trigger/DAQ:
  Three levels
  L0 max latency: 1ms
  10 MHz events on main detectors

## Slide 31: What we need?
In HEP there are several approaches to the ring fitting problem:
  Incompleted rings (non symmetric hits distribution)
  Accurate results
  Fast reconstruction
  Multi-rings
  Fit with additional info…
?

## Slide 32: A look at the market: single ring
Geometric fits:
  Gauss-Newton, Levenberg-Marquardt, Spath, Landau, Chernov-Lesort, …
Algebraic fits:
  Kasa, Chernov-Ososkov, Pratt, Taubin, Crawford, …
Statistical fits:
  MLE, GRAF, …
Conformal fits:
  Riemann-Sphere, Inversion-based, Iterative-RTKD, Karimaki,…

## Slide 33: A look at the market: double rings
Multi rings:
  With seeds: Likelihood, Constrained Hough, …
  Trackless: fiTQun, APFit, possibilistic clustering, Metropolis-Hastings, Hough transform, …
?
?
?

## Slide 34: Requirements for an online multi-rings algorithm
Trackless
  no information from the tracker
  Difficult to merge information from many detectors at L0
Multi rings
  Multi body decay in the RICH acceptance
Fast
  Not iterative procedure
  Events rate at levels of tens of MHz
Low latency
  Online (synchronous) trigger
Accurate
  Offline resolution required

## Slide 35: Single ring
domh
tripl
hough
math

## Slide 36: Processing time
Using Monte Carlo data, the algorithms are compared on Tesla C1060
For packets of >1000 events, the MATH algorithm processing time is around 50 ns per event
The performance on DOMH (the most resource-dependent algorithm) is compared on several Video Cards
The gain due to different generation of video cards can be clearly recognized.
“Fast online triggering in high-energy physics experiments using GPUs” Nucl.Instrum.Meth.A662:49-54,2012

## Slide 37: Single Ring Fit - Throughput
constant time to process a varying number of events, activating more processors as the packet size increases
discrete oscillations due to the discrete nature of the GPU
saturation plateau (1.4 GB/s and 2.7 GB/s )

## Slide 38: Single Ring Fit - Latency
A lower number of events inside a GMEP (packet) is better to achieve a low latency
A larger number of events guarantees a better performance and a lower overhead
The choice of the packet size depends on the technical requirements

## Slide 39: A look at the market: double rings
Multi rings:
  With seeds: Likelihood, Constrained Hough, …
  Trackless: fiTQun, APFit, possibilistic clustering, Metropolis-Hastings, Hough transform, …
?
?
?

## Slide 40: Requirements for an online multi-rings algorithm
Trackless
  no information from the tracker
  Difficult to merge information from many detectors at L0
Multi rings
  Multi body decay in the RICH acceptance
Fast
  Not iterative procedure
  Events rate at levels of tens of MHz
Low latency
  Online (synchronous) trigger
Accurate
  Offline resolution required

## Slide 41: Almagest
New algorithm (Almagest) based on Ptolemy’s theorem: “A quadrilater is cyclic (the vertex lie on a circle) if and only if is valid the relation: AD*BC+AB*DC=AC*BD “
Design a procedure for parallel implementation

## Slide 42: Almagest
A
B
C
D
D
D
i) Select a triplet (3 starting points)
ii) Loop on the remaining points: if the next point does not satisfy the Ptolemy’s condition then reject it
iii) If the point satisfy the Ptolemy’s condition then consider it for the fit
iv) …again…
v) Perform a single ring fit
vi) Repeat by excluding the already used points

## Slide 43: A more “complicated” example

## Slide 44: Almagest on GPU
Very high parallelism:
  Huge number of computing cores (>2000)
  Huge memory bandwidth
. . .
Two level of parallelism:
  Several triplets run in parallel
  Several events at the same time

## Slide 45: Implementation: 4 geometrical selected triplets
Tests on Tesla K20
Total computing time order of few us per event (on single GPU).
Efficiency quite good (by using 8 triplets):
  Room for improvement (points reusing, cuts optimization, …)
Further tests on going to study noise immunity, bias, efficiency as a function of the number of hits, …
preliminary
256 events
preliminary
8 triplets
4 triplets

## Slide 46: NA62 GPU trigger system
8x1Gb/s links for data readout 4x1Gb/s Standard trigger primitives
4x1Gb/s GPU trigger
Readout event: 1.5 kb (1.5 Gb/s)
GPU reduced event: 300 b (3 Gb/s)
2024 TDC channels, 4 TEL62
GPU
TEL62
Events rate: 10 MHz
L0 trigger rate: 1 MHz
Max Latency: 1 ms
Total buffering (per board): 8 GB
Max output bandwidth (per board): 4 Gb/s
GPU NVIDIA TITAN:
  2688 cores
  4.5 Teraflops
  6GB VRAM
  PCI ex.gen3
  Bandwidth: 288 GB/s

## Slide 47: GAP-ATLAS
Several groups interested in using GPUs in HLT and EB (Wuppertal, Frankfurt, Bonn, Edimburg, Oxford,…)
Client-server layer to allow heterogeneous computing solution
Encouraging preliminary tests

## Slide 48: GAP-ATLAS

## Slide 49: GAP-ATLAS
Porting of Track reconstruction (same serial algorithm)
Using standard CPUs the processing time is proportional to the pileup
The GPU give a processing time almost independent
Start the porting of the muon trigger algorithm

## Slide 50: GAP-LHCb
The present trigger/daq scheme can’t fit in the luminosity upgrade (need to increase Pt cuts to maintain the 1 MHz L0 output)
Discussion to have full 40 MHz readout
In any case: GPU in first or second HLT stage (several many-cores architecture under study)

## Slide 51: GAP-NMR

## Slide 52: GAP-NMR
From preliminary estimation:
  Assuming 512x512 pixels
  Factor 20-100 including optimization part
With this gain in image reconstruction time, both Kurtosis and stretched exponential techniques would be used in diagnostic.

## Slide 53: GAP-CT
Porting of FDK algorithm on GPU
Big improvement with respect to already parallel version
Big benefit from next generation (already on the market) GPU (K40)

## Slide 54: GAP-PET
Preliminary studies to identify suitable algorithms:
  MLEM (Maximum Likelihood expectation maximization)
  Common points with CT development (retro-projectors)
  Indication of relevant improvement using GPUs, essential for new scanners with higher resolution (more LOR)

## Slide 55: Alice: HLT TPC online Tracking
2 kHz input at HLT, 5x107 B/event, 25 GB/s, 20000 tracks/event
Cellular automaton + Kalman filter
GTX 580

## Slide 56: Mu3e
Possibly a “trigger-less” approach
High rate: 2x109 tracks/s
>100 GB/s data rate
Data taking will start >2016

## Slide 57: CBM & STAR
107 Au+Au collisions /s
~1000 tracks/event
trigger-less
Since the continuos structure of the beam ~10000 tracks/frame
Cellular automaton+KF
Grid=100000 cores

## Slide 58: PANDA
107 events/s
Full reconstruction for online selection: assuming 1-10 ms  10000 – 100000 CPU cores
Tracking, EMC, PID,…
First exercice: online tracking
Comparison between the same code on FPGA and on GPU: the GPUs are 30% faster for this application (a factor 200 with respect to CPU)
1 TB/s
1 GB/s

## Slide 59: Other applications
LQCD simulation on GPU
  Di Giacomo, D’Elia, Bonati et al.
Geant4 on GPU
  Tool for medical simulation
  Particle transportation
  Physical processes
Madgraph on GPU
  Event generator for LHC
  Big improvement using GPU
And many many others
  …Virgo, Fermi, KM3, …

## Slide 60: “GPU in HEP” conference in PISA!
LOC (temp):
Marco Sozzi
Massimo D’Elia
Claudio Bonati
Silvia Arezzini
Alberto Ciampa
Lucia Lilli
Gianluca Lamanna

## Slide 61: Conclusions
The use of GPU for scientific computing is becoming commonplace
  The future will be necessarily parallel!!!
Several possible uses in HEP: data analysis, Monte Carlo, …
…and outside HEP:
  Medical imaging reconstruction
  … http://www.nvidia.com/object/gpu-applications.html (272 applications)
The GPU in the trigger could give several advantages, but the processing performances should be carefully studied:
  Latency
  Throughput
  I/O
Several experiments are thinking about to use GPU in the trigger in future (both in Lower and Higher levels):
  Upgrade: ATLAS, LHCb, ALICE (already used GPU in run1), …
  NA62, PANDA, CBM, STAR, …

## Slide 62: Spares

## Slide 63: Computing vs LUT
Complexity
LUT
processors
2x2=4
Higgs Analysis
Where is this limit?
It depends …
In any case the GPUs aim to shrink this space
Sin, cos, log, …

## Slide 64
performace
Versatility
ASIC
FPGA
GPU
CPU
Where is your application?
why would I do something in such a complicated way if I can just make it simple?
General purpose or dedicated hardware???
It depends on the application i.e. memory speed vs processor speed
GPUs are a good “compromise” …fill the GAP

## Slide 69: Utilità per la fisica in NA62

## Slide 70: Why GPU?
Two main vendors: effort to simplify GPU programing.
Development drived by video editing and video games industry.
Specialized for math-intensive, highly parallel computation.
Very high computing power for «vectorizable» problems.
In the GPU more transistors are devoted to ALU with respect to the standard CPU.

## Slide 71: GPU: parallel structure
Thousand of cores organized in multiprocessor structure.
Multiple memory structure.
2 levels of parallelism:
  For the algorithm
  For the events
Fast connection with the PC (PCI express gen.3)
Concurrent data copy and execution of the “kernel”

## Slide 72: Implementation: Single Ring
Crowford method (“math”):
  Translate in the center of mass
  Least square minimization  linear
Taubin method:
  More efficient: minimize the bias introduced by the Kasa related methods (minimization of simple algebraic distance)
  Resolution slightly better (on identified rings)
N. Chernov
The difference of computing time on the GPU is at level of 10 ns per event

## Slide 73: Implementation: N (=hits) triplets
Number of triplets equal to the number of hits.
Relatively high efficiency.
Computing time depends on number of rings (different number of GPU cores per events)
Results on TESLA C1060 (240 cores, less than 1 Tflops)
Room for optimization

## Slide 74: Implementation: 4 geometrical selected triplets
Only 4 triplets per event are used: left, right, up and down.
Further cuts to avoid too close hits.

## Slide 75: Implementation: 4 geometrical selected triplets
Stability with small noise (studies are ongoing)
Inefficiency due to the order in choosing the rings.
Dependence on the cuts to define the triplets.

## Slide 76: Flange geometry
18 mm

## Slide 77: The NA62 TDAQ system
L0 trigger
Trigger primitives
Data
CDR
O(KHz)
EB
GigaEth SWITCH
L1/L2
PC
RICH
MUV
CEDAR
LKR
STRAWS
LAV
L0TP
L0
1 MHz
1 MHz
10 MHz
10 MHz
L1/L2
PC
L1/L2
PC
L1/L2
PC
L1/L2
PC
L1/L2
PC
L1/L2
PC
100 kHz
L1 trigger
L1/2
L0: Hardware synchronous level. 10 MHz to 1 MHz. Max latency 1 ms.
L1: Software level. “Single detector”. 1 MHz to 100 kHz
L2: Software level. “Complete information level”. 100 kHz to few kHz.

## Slide 78: GPU: where?
RO buffer
L0
HLT
«classical trigger»
RO
HLT
Reduced rate
full rate
«triggerless»

## Slide 79: GPU roadmap
Thanks to video game industry, the GPU technology will be supported for a long long time.

## Slide 80: Processing time stability
The stability of the execution time is an important parameter in a synchronous system
The GPU (Tesla C1060, MATH algorithm) shows a “quasi deterministic” behavior with very small tails.
The GPU temperature, during long runs, rises in different way on the different chips, but the computing performances aren’t affected.

## Slide 81: Data transfer time
The data transfer time significantly influence the total latency
It depends on the number of events to transfer
The transfer time is quite stable (double peak structure in GPUCPU transfer)
Using page locked memory the processing and data transfer can be parallelized (double data transfer engine on Tesla C2050)

## Slide 82: TESLA C1060
On TESLA C1060 the results both in computing time and total latency are very encouraging
About 300 us for 1000 events
Throughput about 300 MB/s
“Fast online triggering in high-energy physics experiments using GPUs” Nucl.Instrum.Meth.A662:49-54,2012