## Slide 1: The Medium and High resolution mass separators for SPES facility
State-of-art and perspectives
Legnaro 26/05/2014
Antonio Domenico Russo

## Slide 2
HRMS preliminary design;
New line to bypass the HRMS;
MRMS design and dipole simulation.
MRMS
HRMS
By-pass
Overview

## Slide 3
To obtain the ions of interest it is necessary :
To remove isobar ions coming from the source with high resolving power mass separator (HRMS);
Clean up the beam from contaminants introduced by the charge breeder with medium resolving power mass separator (MRMS)
Foreword
MRMS
HRMS
Source
Charge breeder
The list of possible SPES element is available on the SPES web site
https://web2.infn.it/spes/index.php/characteristics/spes-beams-7037/spesbeamstable

## Slide 4
Isobars A=140
Stable
FWtM/R16=1/40000
Isobars with similar intensities are well resolved
+DM/M 1/40.000
-M/M 1/40.000
FWtM
Isobaric nuclei table
The difference of relative mass goes from 11500 up to 38500
Ba and La are not resolved
A/∆A =348 000

## Slide 5
5
Multipole
Sextupoles
Selection slits
Quadrupoles
Dipoles
A Scaled up version of the separator designed by Cary Davids for CARIBU project, Argonne
High Resolution Mass Separator
Parameters | CARIBU | SPES-LNL
Bending radius | 500 mm | 1500 mm
Beam Energy | 50 keV | 260 keV
Magnetic field A=20 | 2.9 kGauss | 2.2 kGauss
Magnetic field A=200 | 9.1 kGauss | 6.9 kGauss
Bending angle | 60° | 80°
Entrance/exit angle | 23 | 28.4°
Pole gap | 80 mm | <80 mm
Pole width | 620 mm | <640 mm
Beam entry

## Slide 6
Mass DM/M= 2.5 10-5 1/40000 ΔΕ=0
x
I
I
y
Gios simulations

## Slide 7
By-Pass
The installation of the bypass line is necessary because :
The system can operate even if the installation of the HRMS is not complete;
The line can be used to transport the low energy beam into another experimental hall;
The line bypasses the HRMS when it is not needed.
HRMS

## Slide 8
By-Pass
the beam cooler capabilities are maintained
  Only two bending magnets are required

## Slide 9
This setup shows how it is possible to use the bypass
line to transfer low energy beam to another experimental hall.
By-Pass
Red lines => Low energy beam

## Slide 10
The beam exit the HRMS is injected in the charge breeder
It increases the beam charge state even if some contaminants are introduced.
The MRMS is required to clean up the beam.
Medium Resolution Mass Separator

## Slide 11
Analysis of contaminants introduced by the charge Breeder. Purple cells show the critical resolution value. A resolution of 0.1 % is sufficient.
Courtesy of Alessio Galatà
Medium Resolution Mass Separator
Resolution (%)

## Slide 12
Characteristics of the beam at the entrance of the platform
MRMS Project requirement
Energy Sn19+@3.04 MeV (40KV+120KV extraction +platform voltage);
Normalized emittance in x-xp=0.1 p*mm*mrad;
Normalized emittance in y-yp=0.1 p*mm*mrad;
Twiss Parameter =0.5 =0
Mass resolution 0.1%
Medium Resolution Mass Separator
Designed by M. Comunian
Beam input
Parameters | 
Bending radius | 750 mm
Beam Energy | 3.04 MeV
Magnetic field A=132 | 0.2 Tesla
Bending angle | 90°
Entrance/exit angle | 35°
Pole gap | 70 mm
Pole width | 400 mm
Multipole Eff. Length | 60 cm
Multipole diameter | 30 cm
Multipole
Sextupoles
Quadrupoles
Dipoles

## Slide 13
First order simulation: Resolution and beam envelope
Medium Resolution Mass Separator

## Slide 14
Optimization
A proper shaped dipole face can optimize the available space on the platform.
The corrective sextpole is no longer required.
14
Curvature 1
Rin1= 0.93 m
Curvature 2
Rout2=0.9 m
1
2
Beam entrance

## Slide 15
Further space optimization
The new design reduces the total number of quadrupoles from 6 to 4

## Slide 16
Resolving power
Resolving power  1/1000
Simulation of a beam with ΔM/M= 0.1%
Tracewin input
output

## Slide 17
Rogoswki shape
Preliminary Dipole design

## Slide 18
Radial field profile
Optimization 0.25% => 0.2%
Rogoswki shape solution
This decreasing index field could be useful to the vertical focusing of the beam
Sharp edges
Bz
Bz
Preliminary Dipole design

## Slide 19
Preliminary Dipole design
Longitudinal field profile:
THE UNIFORMITY OF THE FIELD IS GOOD
m
Beam Input

## Slide 20
Conclusions
3 optics studies of bypass line have been studied. One of these will be chosen in the next future;
MRMS study and design are preparatory to the HRMS;
The magnetic simulation of the dipole needs to be improved. Next studies on the errors of the system will determine the level of field uniformity we have to look for