## Slide 1
R A Bark
The iThemba LABS Radioactive Beam Project

## Slide 2: Outline of Talk
A little bit about iThemba LABS
A little bit about Science & Energy in South Africa
Need for a new accelerator
Plans for a RIB facility

## Slide 3: Separated-Sector Cyclotron (SSC)
Rf-system
Sector Magnet
Rf-system
Low Energy In
High Energy Out
Most Powerful Particle Accelerator in Southern Hemisphere (K200)
Notes: This shows the separated-sector cyclotron. It has four separate magnet sectors with a diameter of 13 m. The RF-system consists of two lambda-half resonators that can operate in the frequency range 7 to 26 MHz. The dee voltage is 220 kV at a power level of 80 kW per resonator. Although it has been designed for a maximum proton energy of 200 MeV but has delivered proton beams of 227 MeV. The beam is inflected with two bending magnets and a magnetic channel and extracted with two septum magnets. Typically the cyclotron delivers a 85 µA beam of 66 MeV protons for radioisotope production with 100% transmission through the machine. Higher beam currents are available but better production target cooling is required for reliable operation at higher intensities.

## Slide 4: iThemba LABS: Multi-User Facility
Proton Therapy: 200 MeV p
Neutron Therapy: 66 MeV p, ~ 40mA
Isotope Production: 66 MeV p, up to 350mA
Nuclear Physics: various beams
Notes: 4
This slide shows the layout of our facilities. Beams from the variable separated-sector cylotron, that has a maximum energy of 200 MeV for protons, are directed to vaults for the production of radioisotopes, proton- and neutrontherapy and nuclear physics experiments. Light ions, pre-accelerated in the first solid-pole injector cyclotron with a K-value of 8 are used for therapy and radioisotope production. For radioisotope production and neutrontherapy a 66 MeV proton beam is used and for protontherapy a 200 MeV beam. The second solid-pole injector cyclotron with a K-value of 10 (which you see here) is used for pre-acceleration of heavy ions and polarized protons from these two external sources

## Slide 5: SSC Beam Schedule
◊ Nuclear Physics
© Neutron Therapy
© Proton Therapy
© Energy Change
© Isotope Production
SSC Weekly Beam Schedule
Notes: 5
Beam is delivered to the different users for 24 hours per day and seven days per week. Radionuclide production and neutron therapy run from 16h00 on Mondays until 5h00 on Fridays. Patients are treated during day time and between treatments the beam is switched to the radionuclide production vault and the intensity is increased to 85μA. On Mondays and Fridays a 200 MeV beam is used for proton therapy and over the weekend beams of light and heavy ions as well as polarized protons, pre-accelerated in a second solid-pole injector cyclotron. In spite of this very tight schedule it remains difficult to satisfy the beam requirements of the different users. We are therefore in the process of increasing the beam intensity for the production of radioisotopes as well as installing and planning additional beam lines for the same purpose. It is planned to produce radioisotopes on two different targets simultaneously.

## Slide 6
Proton Therapy

## Slide 7
Paediatric tumours
Tumours close to critical structures
Brain tumours
Gastro-intestinal tumours (rectum, liver, pancreas)
Prostate tumours
Lung tumours
Recurrent tumours
Proton Therapy
Present Schedule Restricted to 2 “Fractions” / week
Brain tumours
If schedule allowed 5 “Fractions” / week

## Slide 8: Radionuclide Distribution Network
Africa 3
Australia 2
Asia 19
Canada 2
Europe 31
USA 12
Sr-82, Ge-68, Na-22…..

## Slide 9
Chart: Revenue, Isotope Sales
| 05/06 | 06/07 | 07/08 | 08/09 | 09/10 | 10/11
 | 3 | 6 | 12 | 12.5 | 18.5 | 24.4
Radionuclide Production
Made Possible by Flat-topping in SPC1 and SSC and splitting 350µA of 66 MeV protons over two target stations

## Slide 10: Nuclear Physics Research
Nuclear Structure
  Pairing Isomers
  Nuclear Clusters
  Tetrahedral Shapes
  Chirality
  Giant Resonances
  Strength Functions
Nuclear Reactions
  Fusion Barrier Distributions
  Incomplete Fusion
  Astrophysical reactions
  Production of intermediate mass fragments
  Reaction Mechanisms

## Slide 11
K600 Spectrometer

## Slide 12
Physics with the K600

## Slide 13: AFRODITE: -ray spectroscopy
9 Compton Suppressed
Clover detectors
8 LEPS detectors

## Slide 14
AFRODITE: “Double Vacuum”
“search for a tetrahedral nucleus”
?

## Slide 15: Some results from AFRODITE: Nuclear Chirality
Best example of chiral doublet
194Tl
Solving Chiral Conundrum
in 106Ag
E. Lieder et al PRL 112, 202502(2014)
P.L. Masiteng et al Phys. Lett. B719, 83 (20130

## Slide 16
Applications of SSC beams
Calibration of detectors for International Space Station
“Radiation Assessment Detector” calibrated at iThemba LABS.
Presently touring Mars on the rover Curiosity
Neutron Metrology
Long standing with collaboration with PTB

## Slide 17: A Nuclear Future
Cabinet approved 20-year Integrated Resource Plan
9.6 GW Nuclear Power
~ 6 ×1600MW Pressurized Water Reactors
Up to R1 000 000 000 000 (Dipuo Peters, Energy Minister)
Human capacity development

## Slide 18
Weekend Beamtime Only (< 80 days/yr)
  Restricts International Collaborations
  Restricts longer (but very interesting) experiments
Stable Beams only
  Latest Physics not accessible at iThemba LABS
Restricts Human Capacity Development

## Slide 19
Applications of SSC beams
South Africas 2nd satellite - Sumbandila Satellite was damaged beyond repair by solar storm
Cosmic rays peak energy distribution around 300 MeV
Proton & neutron beams up to 200 MeV available at iThemba LABS
Radiation hardness testing
Critical for Space Sciences (SANSA)
Tshepiso Sat
Launched from Yasny, Russia
on RS-20B Dnepr rocket

## Slide 20
Astronomy in South Africa
SALT - Southern African Large Telescope
(largest in Southern Hemisphere 11m)
Square Kilometer Array
Largest in World
11 countries involved (including Italy)

## Slide 21
Synthesis of the elements
N = 126
N = 82
rp-process
Pictures:
Univ. of York

## Slide 22
Synthesis of the elements
N = 126
N = 82
Astrophysical r-process
Massive neutron bombardment in
Supernova (Giusseppe Lorusso talk)
Pfeifer et al,
Z.Phys.A 357, 235(97)

## Slide 23
Shell Model of 1949 needs fixing
3 body forces
Importance of Tensor Force in the n-rich!
Takaharu Otsuka et al PRL 87, 082502 (2001); PRL 95, 232502 (2005)
Neutron Skin

## Slide 24
Drastic Changes of Shell Structure far off stability!
Softening of the nuclear potential:
High-l pushed upward and
Spin-Orbit splitting reduced
Neutron Rich: Neutron Skin!
(Giusseppe Lorusso talk)

## Slide 25: Materials Analysis with RIBs
Hyperfine Structure

## Slide 26
Mössbauer Spectroscopy at CERN
57Mn implanted into diamond
decays to 57Fe
Spectral components correspond
to Fe atoms occupying substitutional
and interstitial sites
K. Bharuth-Ram et al

## Slide 27
Electron Emission Channeling

## Slide 28
Solid State Physics at ISOLDE, CERN
Lattice location of Fe in Diamond
K. Bharuth-Ram et al
59Mn (t1/2 = 4.6s) implanted into
Diamond, decays to 59Fe which
β-decays with t1/2 = 45 days
Electron emission channeling
Measurements indicate that
65% of Fe atoms lie within 0.2 Å
From a substitutional site

## Slide 29: A New Cyclotron at iThemba LABS
Isotope Production off SSC and onto new cyclotron
Free SSC for use by Physics and neutron therapy
More than doubles physics beamtime (including stable beams)
Production of radioactive beams using the ISOL method
In-flight production of RIBs (with SSC upgrade)
Proton Therapy to iTHPTC (probably to a hospital)

## Slide 30: C70 General Description
Diameter < 4m
Weight > 120t
Magnetic field: 1.55T
Magnetic Gap: 30mm
Extraction Radius: 1.2m
2 exit ports
Particles: H- / D- / He2+/ HH+
Variable Energy : 15 MeV  70 MeV
extraction Systems:
    Stripper  H- / D-
    Deflector  He2+/ HH+
Performances:
    750µA H-  70MeV Current upgrade up to 1.5mA
    35µA He2+  70MeV
Notes: POSTER  William Beeckman, TUPRA08 Machining & Assembly
Advantage of a commercial solution: fixed time for delivery, performances already tested.

## Slide 31
Making Radioactive Beams at iTL
Proton induced Fission of Uranium
(p,xn), (p,yp,xn), (p, za, xn) ……
H.I. Fusion-Evaporation
In-Flight
Inverse Kinematics

## Slide 32
Additions to the existing facility

## Slide 33
Low-energy
beamlines
Mass analyser
Beam cooler
Target / ion-
source
maintenance
Target storage
Robot
RIB production
stations
To injector/SSC
Charge breeder
RIB Production

## Slide 34: A New Cyclotron at iThemba LABS
Department of Science & Technology
Developing South African Research Infrastructure Roadmap
iThemba LABS upgrade Ranked Highly
National Research Foundation
RIB Project Strongly Supported
R32M Technical Design Study & Low Energy Facility
iThemba LABS
Flagship Project

## Slide 35
RIB Target/Ion-SourceTest Facility & Technical Design Study
Technical Design Study R7M
Test Facility R25M
Funded by NRF
Later to be used for
-decay studies
Materials sciences
Testing fundamental symmetries

## Slide 36
SPES Target/Ion-source
Collaboration with INFN Legnaro, Italy
High-power tests of SPES targets

## Slide 37
Direct Target:
Power in this design
limited to
P = MeV x µA
= 70 x 150
= 7.5 kW
More than doubles the fission yield (2 x 1013)
Collaboration with Legnaro INFN
Upgrade SPES direct target from 40 MeV beam to 70 MeV beam (Alberto Monetti)

## Slide 38: High – Power Test of SiC Target
60 µA, 66MeV = 4 kW
(designed byAlberto Monetti)

## Slide 39: High – Power Test of SiC Target

## Slide 40
High – Power Test of SiC Target
Heater Power Off
Beam Power Increase
Target Temperature
Vacuum
External Safety Beam Dump Temperature

## Slide 41: High – Power Test of SiC Target

## Slide 42
ISOL Beam Intensities

## Slide 43
I(target) = N × ε1+ × εM.S. × εC.B. × εSPC2 × εSSC × εEXP × e-t/τ
1+ ion – source &
mass selector
RIB
Production
target
New
Accelerator
injector
SSC
Experiment
Charge
Breeder
Technical Design Studies
Putting more beam on target
Without using more beam....
Lifetimes
Efficiencies

## Slide 44
Present SPC2 inflector unsuitable for heavy-ions
Double-drift buncher in injection line before SPC2
  Puts 80% of beam within phase acceptance
Presently have Variable Frequency Flat-Topping on SPC1
  Introduce the same to SPC2
Variable frequency flat-topping on SSC
Upgrade Vacuum
Overall transmission to reach up to 30%
Upgrade SPC2 and SSC:

## Slide 45
Limit due to target diffusion/effusion
Time ~ 1.2s
N-rich intensities ultimately limited by
half lives and diffusion times

## Slide 46
Charge breeding with 14 GHz ECRIS

## Slide 47
Evgeny E. DONETS
Joint Institute for Nuclear Research, Dubna, 141980, Russia
edonets@jinr.ru
iThemba Laboratory, Cape Town, South Africa
January 30, 2012
Status report on physics research and technology developments of Electron String Ion Sources of multicharged ions
Charge Breeding EBIS ?

## Slide 48
Element Xe M=129.0 |  |  |  |  | 
Charge state q | Binding energy E_b; Optimal e-beam energy ≥2.0KeV E_e≈2.5xE_b | Relative abudance in charge state spectrum | Ionization time at J= 300 A/cm2 | Ionization time at J= 500 A/cm2 | Ionization time at J= 1000 A/cm2
Xe26+ q/M≈0.201 | E_b=0.86 KeV; E_e=2.0 KeV; | 30% | 24 ms | 14 ms | 7 ms
Xe42+ q/M≈0.326 | E_b=3.07 KeV; E_e=7.5 KeV; | 33% | 528 ms | 317 ms | 160 ms
Xe43+ q/M≈0.333 | E_b=3.25 KeV; E_e=7.5 KeV; | 40% | 840 ms | 500 ms | 250 ms
Xe44+ q/M≈0.341 | E_b=3.34 KeV; E_e=7.5 KeV; | 60% | 1.0 s | 630 ms | 315 ms
 |  | 70% | 1.3 s | 800 ms | 400 ms
 |  | 80% | 1.7 s | 1.0 s | 500 ms
8M
8 MeV/U
20 MeV/U
Beam
Energy
ESIS - type of EBIS

## Slide 49
Major Instrumentation:
-decay
Coulomb Excitation
Transfer Reactions
Deep Inelastic
High-efficiency -ray array
  ability to Doppler correct -“track”
Large Acceptance Spectrometer
Active Target

## Slide 50: Upgrade of experimental facilities
n-rich ISOL beams (p,f)
p-rich ISOL beams (p,xn) (p,ypxn) (p,za,xn)….
Transfer reactions on light-ion targets e.g. (d,p)
Concept: HELIOS Argonne National Lab.
Lighthall et al NIMA622(2010)97

## Slide 51: Upgrade of experimental facilities
n-rich ISOL Beams (fission fragments)
Transfer reactions on heavy-ion targets (Deep-inelastics)

## Slide 52: Upgrade of experimental facilities
In-flight
In-flight production of n-deficient beams
Fusion-evaporation; inverse kinematics
Beam A ~ 120
1 pµA; 6 MeV/A
A ~ 20
Products A ~ 140
~ 4MeV/A 107 pps
Coulex

## Slide 53
Probably can be done for:
€44M New Accelerator & Isotope Production (pink)
+€33M RIB ISOL facility (RIBS) (yellow)
+€12M Instrumentation
~ €90 M Total
Over 8 – 10 years
Cost Estimates

## Slide 54
Thank You