## Slide 1
Status of ESRF Upgrade Phase II
The Accelerator Project – J.L. Revol
On behalf of the Accelerator Project Phase II Team
Low Emittance Rings 2014 Workshop
Frascati, 17 & 19 September 2014

## Slide 2: Objectives
Design, procurement, preassembly, construction and commissioning of a new low emittance storage ring to reduce the horizontal equilibrium emittance
from 4 nm down to 150 pm
Re-use the same tunnel and infrastructure
Maintain the existing insertion device and bending magnets beamlines
Preserve the time structure operation and a multibunch current of 200 mA
Keep the present injector complex
Reuse, as much as possible, existing hardware
Minimize the energy lost in synchrotron radiation
Minimize operation costs and maintain operation reliability
Minimize the impact on User Operations due to the downtime
for installation and commissioning

## Slide 3: Time scale
  Operation 2013: Accelerator and Source
Start shutdown:
October 2018
Nov 2012 White paper (conceptual design)
Nov 2012- Dec 2014 Technical Design Study
June 2014 Project approved by the Council
Jan 2015 – Oct 2018 Detailed design and procurement
Oct 2018 – Sep 2019 Shutdown for installation
Sep 2019 – Jun 2020 Commissioning
June 2020 User Mode Operation
4 years
Notes: 3

## Slide 4: Optical functions of a standard cell
Space between dipoles 1&2 and 6&7  beta-functions and dispersion grow to high values sextupoles more efficient.
Central part, four high-gradient horizontally-focusing quadrupoles and three high-gradient bending magnets providing also vertical focusing.
At each side of the cell, two dipoles with longitudinally varying bending field  reduce emittance and increase dispersion.
7 bends hybrid achromats to replace the existing DBA

## Slide 5: Main parameters
Lattice parameters | Present | New
Lattice type | DBA | HMBA
Circumference [m] | 844.390 | 843.979
Beam energy [GeV] | 6.04 | 6.00
Natural emittance [pm•rad] | 4000 | 147
Vertical emittance [pm•rad] | 4 | 5
Energy spread [%] | 0.106 | 0.095
Damping times H/V/L[ms] | 7/7/3.5 | 8.5/13/8.8
Energy loss /turn [MeV] | 4.88 | 2.60
Tunes (H/V) | 36.44/13.39 | 75.58/27.62
Chromaticity (H/V) | -130/-58 | -100/-84
Momentum compaction | 1.78 10-4 | 0.87 10-4

## Slide 6: Bending magnets source: 3-Pole wiggler
Field Customized
Large fan with flat top field
2 mrad feasible for 1.1 T 3PW
2 mrad difficult for 0.85 T version
Mechanical length ≤ 150 mm
All new projects of diffraction limited storage rings have to deal with:
Increased number of bending magnets / cell => BM field reduction.
Conflict with hard X-ray demand from BM beamlines.
ESRF will go from 0.85 T BM to 0.54 T BM.
The BM Source can be replaced by a dedicated 3-Pole Wiggler:
Half
assembly

## Slide 7: Brilliance from various sources
I = 200 mA
x 30

## Slide 8: Coherent fraction of the photon flux
x 30
I = 200 mA

## Slide 9: Non Linear dynamics
Amplitude-dependent tune shifts
Momentum-dependent tune shifts
Transverse acceptance at injection
Longitudinal acceptance at injection
Tune shift with amplitude and momentum are minimized by:
-Identity phase advance transform between sextupoles
sextupole tuning
introduction of octupoles.
Transverse and longitudinal acceptance at injection, compatible with a conventional injection scheme and the present injector complex.
Multibunch lifetime in the order of 5-10 hours according to the error seed.

## Slide 10: Special Injection cell
S3 septum
K2
K3
K1
K4
S1-S2
High horizontal beta at septum 18.4 m
Phase advance identical to the standard cell
Optical function identical in most of the cell
Slight local chromaticity differences
Geometry and requirements close to the present injection scheme (4 kickers, 2 in-air septa, 1 in-vacuum septum)
No sextupoles within the injection kicker bump
 | Present Booster | Upgraded Booster
Injected beam emittance [nm] | 120 | 60
Booster RF voltage [mV] | 7.3 | 11
Bunch length [mm] | 23 | 17
Septum thickness [mm] | 2 | 1.5
Beam distance from septum [mm] | 1 | 0.5
Max. efficiency [%] | 70 | 95

## Slide 11: Injector Upgrade
Nominal decay with vertical beam blowup to increase lifetime
Injector upgrade for Top-up operation is a deliverable of Phase I (End2015)
Test with users are on going during machine time
Improvements for reliability are ongoing
  New ramped power supply (4Hz)
  Two additional cavities in the booster
  Linac
Bunch cleaning in the booster under development
Emittance reduction under study
Specific requirement for the new storage ring
Slight reduction of the circumference to compensate the shorter length of the SR (+171 kHz RF frequency)
New injection layout
16 Bunch mode

## Slide 12: Magnets (more details in Gael’s talk)
128 Permanent magnet dipoles
longitudinal gradient 0.16  0.65 T, magnetic gap 26 mm
1.8 meters long, 5 modules
Hybrid Sm2Co17 / Strontium Ferrite
96 Combined Dipole-Quadrupoles
0.54 T / 34 Tm-1 & 0.43 T / 34 Tm-1
64 Octupoles
51.2 103 T/m3
192 Sextupoles
Length 200mm
900-2200 Tm-2
Also used as dipole and skew quad correctors
128 High gradient Quadrupoles
384 Moderate gradient quadrupoles
Gradient: 85 T/m
Bore radius: 12.5 mm
Length: 390/490 mm
Power: 1-2 kW
Gradient: 51 T/m
Bore radius: 15.5 mm
Length: 160/300 mm
Power: 0.7-1 kW
96 Correctors (H/V)
Length 120mm
0.08 T
All magnets individually powered

## Slide 13: Radiofrequency
RF parameters | Present | New
Energy loss (incl 0.5 MeV/turn for IDs) | 5.4 MeV/turn | 3.1 MeV/turn
Longitudinal damping time | 3.5 ms | 8.86 ms
RF frequency | 352.200 MHz | 352.371 MHz
Harmonic number | 992 | 992
Nominal RF voltage | 8 MV | 6 MV
RF energy acceptance | 2.9% | 4.9%
Number of cavities | 5 five-cell cav’s | 14 mono-cells HOM damped
3 cavity prototypes installed in the SR, powered by SSA
12 cavities ordered

## Slide 14: Vacuum chamber layout
Layout with 12 chambers with aperture defined in 3 regions adapted to the beta functions.

## Slide 15: Vacuum system
Centre
Upstream & downstream
ID
50*20 mm
30*13 mm
(50*13 under design)
(reuse of existing ID chambers)

## Slide 16: Vacuum system
Upstream
Centre
Downstream
3 pole wiggler location
Vacuum system:
Split in12 chambers
Discreet conventional pumping system using antechambers
Additional NEG coating for chambers 1 and 12
Most probably stainless steel material
Lump and crotch copper absorbers
Impedance and beam losses management under study

## Slide 17: Girders and stability
Z legs motorised, X and Y legs are manually adjustable
3 or 4 vertical leg concept under evaluation
Preparation and installation strategy under study (total weight of girder + magnets larger than the capacity crane)

## Slide 18: Prototyping mid 2013-mid2015
No new technologies to be validated,
  No R&D foreseen.
Prototypes needed to:
  Validate the components design.
  Finalise the engineering design of the fully assembled elements.
  Verify required tolerances achievable at industrial level.

## Slide 19: Prototyping mid 2013-mid2015
Magnet
  Prototyping started fall 2013.
  Majority of prototypes ordered by end 2014 and validated by summer 2015.
Vacuum chamber
  Prototyping started at the beginning 2014 (Chamber with 3 new BPMs under test with beam, prototypes launched summer 2014 to validate the realisation of profiles, first central part profile available this month).
  Prototyping will allow validating the design of all components, including bellow shields, absorbers....
Girder
  Prototype ordered before end 2014, girder design finalised by end 2015 in order to validate the stability and tolerances requirements.

## Slide 20
Preparing the Upgrade phase II
Technical Design Study (TDS)
completed and submitted to:
Science Advisory Committee (SAC)
Accelerator Project Advisory Committee (APAC)
Cost Review Panel (CRP)
ESRF Council
All committees
very positive to go ahead

## Slide 21: Organisation and project management
10 Work Packages defined in the TDS:
WP0: Logistics and installation
WP1: Beam dynamics
WP2: Magnets
WP3: Mechanical and Vacuum Engineering
WP4: Power supplies
WP5: Radiofrequency
WP6: Control System
WP7: Diagnostics and feedbacks
WP8: Photon source
WP9: Injector upgrade
Accelerator Project Budget:
103.5 M€ Construction and commissioning of the new storage ring
including infrastructure adaptations and logistics for storage and pre-assembly.
In addition, the ESRF Upgrade Phase II also includes the upgrade of 4 beamlines and the implementation of an aggressive scientific instrumentation roadmap.
ESRF is now preparing the organisation to be in a position to start from 2015 the execution phase of the project.

## Slide 22: Many thanks for your attention