## Slide 1: Longitudinal gradient super-bends and anti-bends for compact low emittance light source lattices Andreas Streun, Paul Scherrer Institut, Switzerland Low emittance rings workshop IV, Frascati, Sep. 17-19, 2014

## Slide 2: Contents
Recall: paths to low emittance
Recall: the TME cell
The LGAB cell
Longitudinal gradient bends
Anti-bends
Application to SLS upgrade
Conclusions
References
  AS & Albin Wrulich, Compact low emittance light sources based on longitudinal gradient bending magnets, submitted to NIM A
  AS, The anti-bend cell for ultralow emittance storage rings, NIM A 737 (2014) 148-154
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 2/18

## Slide 3: Recall: paths to low emittance
Equilibrium beam parameters of a flat lattice
exo natural horizontal emittance
sd rms relative momentum spread, d = Dp/p
DE energy loss per turn
I2 I3 I4 I5 synchrotron radiation integrals
constants
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 3/18

## Slide 4
Optics
 horizontal focus in each dipole
 many small dipoles of angle F << 1 multibend achromat (MBA) lattice
Power
 damping wigglers (DW)
Damping
 gradient bends for vertical focusing (bk < 0)
orbit curvature b = 1/r = B/(p/e)
dispersion’s betatron amplitude
dispersion h , derivative h ’
hor. betafunction b, a = -b ’/ 2
transverse gradient k (k > 0 hor. foc.)
F = 1  TME (theoretical minimum emittance)
MBA lattice without wigglers
MBA & DW need space !
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 4/18

## Slide 5: Recall: the TME cell
Lowest emittance of a conventional lattice cell
  homogenous ( constant b ), short ( F =bL << 1 ) bending magnet
  set ao = ho’ = 0 at bend center (symmetry); find minimum H ( bo, ho ) :
 theoretical minimum emittance (TME) for
periodic symmetric cell: a = h’ = 0 at ends matching problem
TME phase advance m TME =284.5°
  2nd focus, useless
  long cell
  overstrained optics
bx by h
F, L, b
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 5/18

## Slide 6
Deviations from TME conditions
Ellipse equations for emittance
Cell phase advance
real cells: m < 180°  F ~ 3..6
How to get F < 1 and m < 180° ?
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 6/18
Dm = 284.5°
d
r
S. Leemann & AS, Perspectives for future light source lattices incorporating yet uncommon magnets, PR ST AB, 14, 030701, 844 (2011).

## Slide 7: The LGAB cell
Detuned TME cell vs. longitudinal-gradient/anti-bend cell
  both: angle 6.7°, E = 2.4 GeV, L = 2.36 m, Dmx = 160°, Dmy = 90°, Jx  1
TME: F = 3.4, e = 990 pm LGAB: F = 0.69, e = 200 pm
bx by h
bx by h
dipole field
quad field
total |field|
} at R = 13 mm
longitudinal
gradient
bend
anti-bend
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 7/18

## Slide 8: Longitudinal gradient bends
b(s) = B(s)/(p/e)
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 8/18
Longitudinal field variation b(s) to compensate H (s) variation
Beam dynamics in bending magnet
  Curvature is source of dispersion:
  Horizontal optics ~ like drift space:
  Assumptions: no transverse gradient (k = 0); rectangular geometry
Variational problem: find extremal of h(s) for
  too complicated to solve
    mixed products up to h(4) in Euler-Poisson equation...
use special function b(s) = f (s,{ak}) with parameters {ak}: variational problem  minimization problem for {ak}
numerical optimization: find extremal; suggest functions f

## Slide 9: Numerical optimization
Half bend in N slices: curvature bi, length Dsi
Knobs for minimizer: {bi}, b0, h0
Objective: I5 ( or e ~ I5 / I2 )
Constraints:
  length: SDsi = L/2
  angle: SbiDsi = F/2
  [ field: bi < bmax ]
  [ optics: b0 , h0 ]
Results:
  hyperbolic field variation (for symmetric bend, dispersion suppressor bend is different)
  Trend: b0   , b0  0 , h0  0
Results for half symmetric bend
( L = 0.8 m, F = 8°, 2.4 GeV )
homogeneous
optimized
hyperbola fit
I5 contributions
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 9/18

## Slide 10: Analytical optimization
Given function b(s) = f (s,{ak}), parameters {ak}
  I5/b0, I5/h0 = 0  emittance & matching
  {I5/ak} = 0  optimum parameters
Useful simple functions for field profiles:
  high field magnets: hyperbola (parameters h, p)  superbends  hard X-ray photons from field peak!
  low field magnets: step function (parameter m)  most simple design
          numerical optimization results
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 10/18

## Slide 11: Deviations from optimum matching
Numerical optimization of field profile for fixed b0, h0
  Emittance (F) vs. b0, h0 normalized to data for TME of hom. bend
F = 1
F = 2
F = 2
F = 3
F = 3
F = 1
small (~0) dispersion at centre required, but tolerant to large beta function
F  0.3
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 11/18

## Slide 12: Anti-bends
General problem of dispersion matching:
  dispersion production in dipoles  “defocusing”: h’’ > 0
Quadrupoles in conventional cell:
  dispersion is horizontal trajectory: quads treat h and bx in same way.
  over-focusing of horizontal beta function bx
  insufficient focusing of dispersion h
  striking example: the TME cell
   disentangle h and bx !
use negative dipole: anti-bend
  kick Dh’ =  , angle  < 0
  out of phase with main dipole
  negligible effect on bx , by
Side effects on emittance:
  main dipole angle increase by 2| |
  anti-bend located at large H
   in total, still lower emittance
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 12/18
bx by
dispersion: anti-bend off / on
relaxed TME cell, 5°, 2.4 GeV, Jx  2
Emittance: 500 pm / 200 pm

## Slide 13: Half quad anti-bend
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 13/18
Recall: emittance reduction via I4  get  half emittance
2k >> b2, h > 0
 b > 0, k < 0 defocusing gradient bend
 b < 0, k > 0 focusing gradient anti-bend
need horizontal focusing at anti-bend location anyway (out of phase with main bend).
convenient magnet design: anti-bend = half quadrupole

## Slide 14: Application to SLS upgrade
Plans for an upgrade of the Swiss Light Source (SLS)
  SLS emittance now: 5500 pm
 M. Ehrlichman, First studies on a possible SLS upgrade, Wednesday 10:10
SLS constraints: 288 m, 12 straights, 2.4 GeV  rather compact lattice !
 LGAB-HMBA lattice hybrid multibend achromat incorporating longitudinal gradient bends and anti-bends
100 – 200 pm emittance: factor 50 – 25 improvement.
hard X-rays (100 keV) from LG-superbend field peak. SLS-1 normal bend SLS-1 superbend SLS-2 LG superbend
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 14/18
Eg

## Slide 15: a) most aggressive design
 ultra-low emittance: e = 73 pm ! ( 18 m / 30° arc at 2.4 GeV )
  feasible magnets,  sufficient dynamic aperture
 quasi isochronous (MCF a = -510-5) and nonlinear
 too short bunches, insufficient energy acceptance
 large normalized chromaticities -/Q = 3.9 / 4.3
anti-bend
half quad
step-function LG bend
hyperbolic LG superbend
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 15/18

## Slide 16: b) compromise design
 acceptable emittance: e = 183 pm
  feasible magnets,  sufficient dynamic aperture
 large MCF (a = +1.310-4 )  bunch length & E-acceptance 
 large normalized chromaticities -/Q = 4.1 / 6.5
 only partial exploitation of LGAB scheme
hyperbolic LG superbend
homogeneous
bends
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 16/18

## Slide 17: c) negative alpha design
 acceptable emittance: e = 162 pm
 large negative MCF (a = -1.010-4 )
 low normalized chromaticities -/Q = 2.0 / 2.9
 full exploitation of LGAB scheme: relaxed focusing.
 work in progress...
strong anti-bends
hyperbolic LG superbend
S|F| = 500°
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 17/18

## Slide 18: Conclusions
Longitudinal gradient bends ...
  ... provide lower emittance than the TME for homogenous bends.
  ... offer the double use to provide low emittance and hard X-rays.
  ... can be described well by hyperbolae (high field) or step functions (low field).
  ... require very small dispersion at focus,
  ... but tolerate large values of horizontal beta function at focus.
Anti-bends ...
  ... disentangle dispersion and horizontal beta function,
  ... are thus well suited to provide the matching for LG bends.
  ... introduce negative momentum compaction.
The LGAB cell ...
  ... combines longitudinal gradient bends and anti-bends.
  ... offers a lattice solution for compact low emittance rings.
A. Streun, Longitudinal gradient superbends and anti-bends LER-4, Frascati, Sep. 17-19, 2014 18/18