## Slide 1
Tracker “front-end” board
Mauro Citterio

## Slide 2
One PCB for two fiber planes
Fibers connected to SIPM
SIPMs read-out via BASIC 32
To take advantage of the BASIC input channel layout , one PCb every two fiber planes
6 planes
3 PCBs (SIPM on the TOP face, BASIC 32 on the BOTTOM face)

## Slide 3
Cartoon of the PCB
Overall PCB dimensions to be optimized against mechanical constraints.
One board will contains
96 x 2 SIPMs
6 BASIC32 ICs
Distance between SIPM and IC INPUTs minimized (“vias” through the board)
TOP View
BOTTOM View (only three ICs shown)
Data Flow: traces embedded in the PCB
In/out connector(s) area

## Slide 4
Prototype Test Board
Subset of the final board
  Same use of TOP and BOTTOM layers
Additional components included to perform BASIC32 tests
  Injection circuit
  External ADC
  Learn from prototype the criticality of the final board
  HV – LV distribution to be defined on the test-board
Design is ongoing:
  Schematic to be reviewed soon
    Help from Cristoforo and Adalberto
  Layout by first week of April
  Board in house by end of April
    Testing lab in preparation
  External interface for test board: CAEN V1495 board
    BASIC32 controlled via onboard FPGA