## Slide 1: uSOP
A. Aloisio – R Giordano

## Slide 2: uSOP – Ver. B
Cortex A8 uP – 1GHz
Linux OS (Debian)
2 GB Flash
2 GB RAM
General platform for slow-control
Designed for reliability

## Slide 3: Project Status @ Apr. 2014
Design of first version completed
PCB manufacturing started today
Software for ADC read-out via I2C in progress
Software for JTAG programming of Xilinx FPGA tested successfully
Integration in EPICS to be started soon

## Slide 4: Front Side
2x USB device + host
Supply via USB (device)
Board management via an IPMI-like interface
USB device
Ethernet
USB device
IPMI
uSD
LEDs

## Slide 5: Rear Side
Fully Isolated I/O:
  I2C
  SPI
  RS232
  JTAG
  All IOs fail proof
Non Isolated I/O:
  Parallel
  On-chip ADCs
SPI
2x I2C
RS232
RS232
On chip ADC

## Slide 6: ADCs
ADC LTC2499 – 24 bit
Sigma/Delta Architecture
7.5 Hz sampling Rate
VERY high performance