## Slide 1: The FP7-IAPP-FTK project: real-time image reconstruction for Hadron Collider experiments & a possible application to the Artificial Intelligence field
Paola Giannetti
INFN Pisa
Pisa Seminar, May 6 2014

## Slide 2
In this talk:
Highly parallelized, pipelined electronics for Hadron colliders
the technology was born in CDF, exported to LHC
Spinoff of the FTK – IAPP project
Comparison with other technologies when possible

## Slide 3
109
107
105
103
10
10-1
10-3
S1/2 (TeV)
H
Events at L = 1034 cm-2s-1
RARE
EVENTS
Common
EVENTS
p
Event & Underlying event
p
Pile-up:
25 eventi @1034 cm-2s-1
40 MHz coll. Rate
500 eventi @1035 cm-2s-1
20 MHz coll. Rate SLHC
Pile-up:
25 events @1034 cm-2s-1
40 MHz coll. Rate
Hundreds of events
@1035 cm-2s-1
40 MHz coll. Rate HL-LHC
Bunch Crossing
Hadron Colliders
HARD LIFE
High Luminosity →
high P density in the Bunch

## Slide 4
Role of the a high precision Tracker, the most computing power reconstruction
ATLAS Silicon Tracker
ATLAS
Pix2
Pix1
Pix0
SCTs
Hard scattering!
P
P
Pile-up

## Slide 5: The Trigger at ATLAS
L3: CPU farm
Full event reconstruction
with speed optimized offline code
L1 pipeline
42 clock cycles
L1
L2
L2 buffer
4 events
DAQ buffers
L3 Farm
L1
7.6 MHz Synchromous
Pipeline
5.5 s Latency
30 kHz accept rate
L2
Asynchronous 2 Stage Pipeline
20 s Latency
1 kHz accept rate
Mass Storage
(~100 Hz)
7.6 MHz Crossing rate
L1 pipeline 100 clock cycles
L1
L2
L 2 buffer many events
DAQ buffers
L3 Farm
Level 1
40 MHz Synchromous
Pipeline
2.5 s Latency
75 kHz accept rate
Level 2
Asynchromous
10 ms Latency
6-4 kHz accept rate
Mass Storage
(~800-300 Hz)
40 MHz Crossing rate
ATLAS
CDF

## Slide 6: CDF vs ATLAS TDAQ Architecture
L3: CPU farm
Full event reconstruction
with speed optimized offline code
L1 pipeline
42 clock cycles
L1
L2
L2 buffer
4 events
DAQ buffers
L3 Farm
L1
7.6 MHz Synchromous
Pipeline
5.5 s Latency
30 kHz accept rate
L2
Asynchronous 2 Stage Pipeline
20 s Latency
1 kHz accept rate
Mass Storage
(~100 Hz)
7.6 MHz Crossing rate
L1 pipeline 100 clock cycles
L1
L2
L 2 buffer many events
DAQ buffers
L3 Farm
Level 1
40 MHz Synchromous
Pipeline
2.5 s Latency
75 kHz accept rate
Level 2
Asynchromous
10 ms Latency
6-4 kHz accept rate
Mass Storage
(~800-300 Hz)
40 MHz Crossing rate
ATLAS
CDF
CPUs FARMs
Highly parallelized
Dedicated hardware

## Slide 7: CDF vs ATLAS TDAQ Architecture
L3: CPU farm
Full event reconstruction
with speed optimized offline code
L1 pipeline
42 clock cycles
L1
L2
L2 buffer
4 events
DAQ buffers
L3 Farm
L1
7.6 MHz Synchromous
Pipeline
5.5 s Latency
30 kHz accept rate
L2
Asynchronous 2 Stage Pipeline
20 s Latency
1 kHz accept rate
Mass Storage
(~100 Hz)
7.6 MHz Crossing rate
SVX read out after L1
SVT here
XFT here
L1 pipeline 100 clock cycles
L1
L2
L 2 buffer many events
DAQ buffers
L3 Farm
Level 1
40 MHz Synchromous
Pipeline
2.5 s Latency
75 kHz accept rate
Level 2
Asynchromous
10 ms Latency
6-4 kHz accept rate
Mass Storage
(~800-300 Hz)
40 MHz Crossing rate
ATLAS
CDF
No
Tracking
Late
Tracking
CPUs FARMs

## Slide 8
SVT, The FTK predecessor @ CDF &
Its upgrades (~2000-04)
XFT : 3D Tracks at L1
SVT: Tracks in the silicon at L2
in a average time of 20 ms
with enough precision to see b quarks decays – Exceptional CDF B-physics results
p
p
200 mm
B
p
p

## Slide 9
SVT
2 Wedges
per crate
SVT was installed in 2000.
It was made of 12 processors (one per wedge) made of 5 different 9U VME boards each, for a tot of ~72 boards
CDF Trigger ROOM

## Slide 10
w SVT
Mkkππ
wo SVT
The sample for the Bs Mixing at CDF
Panofsky Price 2009
Efficient collection of
B’s purely-hadronic decays

## Slide 11
But AM survives at LHC inside FTK an exception
to the LHC strategy
Very limited space
For dedicated HW
After 15 years
of discussions &
studies a new addition, a second generation
TRACKER
has been approved

## Slide 12
m
30 minimum bias events + H->ZZ->4m
Tracks with Pt>2 GeV
Where is the Higgs?
m
m
FTK
m
m
m
m
30 minimum bias events + H->ZZ->4m
m
Tracks with Pt>2 GeV
Where is the Higgs?
Help!
HOW FTK WORKS
@LHC (both CMS & Atlas) tracking
is missing @L1 and late @L2

## Slide 13
FTK: a second generation processor
PT
h
High efficiency
Large h coverage
Good
d0 resolution for low pt tracks
Performances are mantained at high luminosity
Low Fakes
No pile-up
High pile-up
PT
NReco Vtx
h

## Slide 14
FTK Physics case: collect high statistics samples of
Higgs purely hadronic decays (but also standard decays)
P
P
High efficiency and short execution time to
Identify the primary vertex & hard scattering
Tag b-jets & tau-jets
………
Online track-corrections for MET & jets
track-based isolation algorithm, not only for leptons…isolated hadrons (one-prong t or highly ionizing particles)
Benchmark channels:
– ZH→nnbb, bbbb, bb tt ; bbH, ttH → bbbb, bbtt ; X → hh → bbbb, bb tt .
– VBF Hqq → ttqq; boosted H → tt
– Calibration channels: Boosted Z → bb & Z → tt
leading PT
track
RISO
RI
RSIG
Jet axis
Hadornic
TAU decay

## Slide 15
PV Z
Resolution
~100 um
Jet b-tagging
Jet tau-tagging
Primary Vertex reconstruction;
right PV identification 98% efficient
Tau signal
cone

## Slide 16
HOW much FAST it is
WH events @31034 average of 40 jets (ROIs) > 70 Gev per event
CPU: 25 ms * 40 = 1 sec → 1 Hz
FTK : ~ latenza 25 msec, event rate 100 kHz → 100 k times faster !
GPU : ~4 times faster than a CPU → 25 k times slower than FTK!
HOW CAN FTK DO IT?

## Slide 17: FTK: Full event tracking in 2 steps
Track fitting
  using full resolution of the detector
Data Organizer
(DO)
Hits
Tracks parameters
(d, pT, , h, z)
Roads
Pattern matching
(Associative
Memory - AM)
SSIDs
Roads + hits
Track
Fitter
(TF)
Super
Strip (SS)
  Find coarse Roads first (Pattern Matching with Associative Memory, AM)
  From those Roads extract the full resolution Hits
  Combine the Hits to form Tracks, calculate χ2 and parameters (Track Fitter)

## Slide 18
~80 FTK_IM: Clustering in parallel
~380
ROLs
@2 Gb/s
100 GB/s
32 DF: cross-point for clusters -
SSB: Final Fit-HW
Board-board
Connector
AMBoard
AMBoard
4 DOs
AMBoard
4 TFs
4 HWs
4 DOs
4 TFs
4 HWs
4 DOs
4 TFs
4 HWs
128 PUs =
512 pipelines
SSB: Final Fit-HW
32
boards
ROS
RODS
ROS
FLIC: FTK-to-Level-2 Interface Crate
fibers
PU
AUX CARD
ATCA
ATCA
8 VME core crates
To
TDAQ
ROS
1860 large FPGAs
8200 AM-Chips (ASICs)
Thousands of 2Gb/s Serial Links
Only one AMB
750 Slinks
~200 GB/s
Only AMBs ~25 TB/s
8
8x128 Slinks@6Gb/s
~800 GB/s

## Slide 19
~80 FTK_IM: Clustering in parallel
32 DF: cross-point for clusters -
SSB: Final Fit-HW
Board-board
Connector
AMBoard
AMBoard
4 DOs
AMBoard
4 TFs
4 HWs
4 DOs
4 TFs
4 HWs
4 DOs
4 TFs
4 HWs
128 PUs =
512 pipelines
SSB: Final Fit-HW
32
boards
ROS
RODS
ROS
FLIC: FTK-to-Level-2 Interface Crate
fibers
PU
AUX CARD
ATCA
ATCA
To
TDAQ
ROS

## Slide 20
The Event
...
The Pattern
Bank
TRACKING WITH
PATTERN MATCHING
We need a Highly
Parallelized Comparison
AM: ACE in the Hole

## Slide 21
pattern
Bus_layer0 Bus_layer1 Bus_layer2 …….. Bus_layer7
layer0
layer1
layer2
layer7
pattern0
pattern1
pattern2
pattern3
layer0
layer1
layer2
layer7
….
- very parallelized ASIC x pattern matching
AM COMPUTING
POWER
Each pattern:
4 32 bits comparators
128 kpat *4 = 500 K comparisons
→ 500 K * 100 M/s = 50 106 MIPS/chip
MIPS → note: only comparisons!
+ readout tree
+ 128 k *100 M/s 8-bits-coincidences w majority= 1 1015 bit-coincidences/s
AM CONSUMPTION:
~ 2.5 W for
128 kpatterns
AM Memory Accesses:
128 k * 4 * 32 bits *100 M/s=
1.6 * 1015 accesses/s
1 COMPARATOR between
the BUS & 1 stored
16-bits-WORD

## Slide 22
History
90’s Full custom VLSI chip – 0,7 mm AMS (INFN-Pisa) 128 patterns, 6x12 bit words each (F. Morsani et al., The AM chip: a Full-custom MOS VLSI Associative memory for Pattern Recognition, IEEE Trans. on Nucl. Sci.,vol. 39, pp. 795-797 (1992).) 25 MHz clock
1998 FPGA (Xilinx 5000) for the same AMchip (P. Giannetti et al., A Programmable Associative Memory for Track Finding, Nucl. Intsr. and Meth., vol. A 413/2-3, pp.367-373, (1998) ).
1999 first standard cell project presented at LHCC
2006 AMChip 03 Standard Cell UMC 0,18 mm, 5k patterns in 100 mm2 for CDF SVT upgrade total: AM patterns (L. Sartori, A. Annovi et al., A VLSI Processor for Fast Track Finding Based on Content Addressable Memories, IEEE TNS, Vol 53, Issue 4, Part 2, Aug. 2006). 50 MHz clock
2012 AMchip04 (Full custom/Std cell) TSMC 65 nm LP technology, 8k patterns in 14mm2 Pattern density x12. First variable resolution implementation. (F. Alberti et al, 2013 JINST & C01040, doi:10.1088/1748-0221/8/01/C01040) 100 MHz
2013 AMchip05, 4k patterns in 12 mm2 a further step towards final AMchip version. Serialized I/O buses at 2 Gbs, further power reduction approach. BGA 23x23 package.
2014 AMchip06: 128k patterns in 180 mm2. Final version of the AMchip for the ATLAS experiment.
ATLAS
CDF
Associative Memory (AM)

## Slide 23
  Measures:
  Jitter Analysis
  BER
  Eye diagram
  Good results
Input Measure
Output Measure
AMBSLP: Tests
Notes: We went to the National Lab of Frascati to check the quality of the serial links. We performed measures of the jitter, we checked the bit error rate and the quality of the signals with the eye diagram.
We did this analysis in different point of the data path, the most important result that I want to show you are on the input of the miniASIC and at the output. The result show that we have a very good input data path but no so good output links.

## Slide 24
Track fitting – high quality helix parameters and 2
  Over a narrow region in the detector, equations linear in the local silicon hit coordinates give resolution nearly as good as a time-consuming helical fit.
      pi’s are the helix parameters and 2 components.
      xj’s are the hit coordinates in the silicon layers.
      aij & bi are prestored constants from full simulation or real data tracks.
        The range of the linear fit is a “sector” which consists of a single silicon module in each detector layer.
      This is VERY fast in FPGA DSPs.
Nucl.Instrum.Meth.A623:540-542,2010
doi:10.1016/j.nima.2010.03.063
14D coord. space
5D surface
8 TMACs/chip top line
~625 GBs/chip top line

## Slide 25: DO+TF: FPGA firmware - overview
Full resolution stored in a smart DB, while SSID of each hit is sent to the AM
AM performs pattern recognition and provides the ID value for each road (RoadID)
The RoadIDs get decoded in SSIDs for each layer, using an external RAM
Database retreives all hits for each SSID of the detected Roads
Combiner unit computes all possible permutations of the hits to form tracks
A very fast full resolution fit it is done for each possible track, fits are accepted or rejected according to x2 value
DO
TF
XC7K325T-900ffg-3

## Slide 26: FPGA implementation (device floorplanning view)
4 Track Fitter instances
Local clock routing for the Track Fitters

## Slide 27: Speed and latency
225MHitsper layer
50MRoads
Units are per second
@550MHz
2200Mfits
@450MHz
450-1800 Mhits per layer/event
576MBit RLDRAM3
57.6Gb/s 10ns tRC

## Slide 28: Track Fitting: 5 scalar products
Very fast FPGA implementation was developed for the fitter
All multiplications are executed in parallel, giving 1 fit per clock
With dedicated DSPs, the frequency of the fitter is 550MHz→1 fit/2 ns
4 such fitters run in parallel in the device →2 fits/1 ns
One DSP
Pipeline
of
DSPs
Set of 14 Constants
Set of 14 hits

## Slide 29: Device utilization & power
Power estimation of 15.5W is the absolute worst-case figure
Simple improvements to the design and use of Xilinx UltraScale new devices are expected to reduce this by 30% or more.
96%

## Slide 30
4500 GF/s
300 GB/s
Theoretical GFLOP/s
Theoretical GB/s
In HEP there
is preference for CPUs/GPUs

## Slide 31
BUT FPGA and Asic’s advancement is also
impressive ….. and they
are more flexible
Up to 96
in the top
line Virtex7
~150 GB/s

## Slide 32
 | Spartan-6 | Artix-7 ~150 € | Kintex-7 | Virtex-7 | Kintex UltraScale | Virtex UltraScale
Logic Cells | 147,443 | 215,360 | 477, 760 | 1,954,560 | 1,160,880 | 4,407,480
BlockRAM | 4.8Mb | 13Mb | 34Mb | 68Mb | 76Mb | 115Mb
DSP Slices | 180 | 740 | 1,920 | 3,600 | 5,520 | 2,880
DSP Performance (symmetric FIR) | 140 GMACs | 930 GMACs | 2,845 GMACs | 5,335 GMACs | 8,180 GMACs | 4,268 GMACs
Transceiver Count | 8 | 16 | 32 | 96 | 64 | 104
Transceiver Speed | 3.2 Gb/s | 6.6 Gb/s | 12.5 Gb/s | 28.05 Gb/s | 16.3 Gb/s | 32.75 Gb/s
Total Transceiver Bandwidth (full duplex) | 50 Gb/s | 211 Gb/s | 800 Gb/s | 2,784 Gb/s | 2,086 Gb/s | 5,101 Gb/s ~635 GB/s
Memory Interface (DDR3) | 800 | 1,066 | 1,866 | 1,866 | 2,400 | 2,400
PCI Express® Interface | x1 Gen1 | x4 Gen2 | x8 Gen2 | x8 Gen3 | x8 Gen3 | x8 Gen3
Analog Mixed Signal (AMS)/XADC | - | XADC | XADC | XADC | System Monitor | System Monitor
Configuration AES | Yes | Yes | Yes | Yes | Yes | Yes
I/O Pins | 576 | 500 | 500 | 1,200 | 832 | 1,456
I/O Voltage | 1.2V - 3.3V | 1.2V - 3.3V | 1.2V - 3.3V | 1.2V - 3.3V | 1.0 – 3.3V | 1.0 – 3.3V
Please refer to the device data sheets for the latest product information. |  |  |  |  |  | 
20-16 nm
28 nm
45 nm

## Slide 33: PU evolution: integration of many FTK functions in a small form factor
Main goal is to integrate the FTK system in a more compact form
First step will be to connect an AMChip, an FPGA and a RAM in a prototype board
In the future the devices could be merged in a single package (AMSiP)
That AMSiP will be the building block of the new processing unit, to be assembled in an ATCA board with new mezzanines
AMSiP

## Slide 34: FTK SPINOFF /www.plosone.org/article/info%3Adoi%2F10.1371%2Fjournal.pone.0069154 M. Del Viva, G. Punzi
AM: a filter to detect the IMAGE relevant features
HEP
FILTERING NATURAL IMAGES: edge detector
 AM as neurons?
Filtered images are clear to
human eyes

## Slide 35
B/W ... 29=512 patterns: 101-010-100, ……. , 111-011-001
4 gray level ... 218= 256 Kpatterns: 00,00,01-00,01,00-11,00,10 …..
B/W + time 227= 128 Mpatterns: 111,000,000 - 000,111,000 - 000,000,000 …
Training: Calculate the frequency of each pattern in the image
SELECT the RELEVANTs
to be PUT in the AM BANK
Accepting only
these 50 patterns
Accepting only
these 16 patterns
9.8%
5.5%
4 grey level:
218 patterns
Stored N=2000
= 1/64 di 1 chip
= 50 mW
HOW we use the AM to filter images?
We build small arrays of pixels (3x3 for static images or 3x3x3 for movies) that are AM patterns - M. Del Viva, G. Punzi

## Slide 36
How we select the relevant patterns to be
stored in the AM bank?
Patterns that are
efficient carriers
of information
given the bandwidth (W)
&memory limits (N),
All 512 patterns
W=0.5, N=50
W=0.5, N=16
Low p
under real constraints
M. Del Viva e G. Punzi (Universita’ di Firenze e Universita’ di Pisa)

## Slide 37
Michela Del Viva e Giovanni Punzi (Universita’ di Firenze e Universita’ di Pisa)

## Slide 38: Possible applications: smart cameras
DreamCam is a modular smart camera built with the use of an FPGA like main processing board. The core of the camera is an Altera Cyclone-III EP3C120 associated with a CMOS imager and six private Ram blocks.
The main novel feature of our work consists in proposing a new smart camera architecture and several modules (IP)
to efficiently extract and sort the visual features in real time.
2000 patterns ~ 1/64 Amchip~50 MW

## Slide 39: AM-based Coprocessor a unit with PCI-express and ethernet
~ 8 chips = 1 Mpatterns → good for Movie filtering

## Slide 40
Conclusions
Optimal partitioning of complex algorithms on a variety of computing technologies (ASICs - FPGAs – CPUs) demonstrated to be a very powerful strategy.
Hardware dedicated highly parallelized systems offer extremely powerful computing power and I/O and have been demonstrated to be necessary for tasks like tracking in very high occupancy detectors at LHC.
Expertise in the ASIC and FPGA field is extremely important and should be kept alive to be able to achieve extreme performances, when necessary.

## Slide 41: COFUND application
SMART SYSTEM Integration (SSI): Real Time Image and Sensor Data processing – large interest argument into our Institute:
ATLAS, CMS, LHCB, NA62… (trigger @GR1), fisica medica, gruppo 2….
Ditte che potrebbero essere interessate:
EMC (Ponsacco) avrebbe gia' detto di si' per una smart camera che incorpori la AM
Alkeria (polo tecnologico): ha dei bellissimi sistemi embedded con FPGA attaccati a videocamerine ad altassima risoluzione, dove gli FPGA eseguono trasformate di Fourier per fare tomografia all'occhio (OCT)
CAEN (Viareggio) potrebbe entrare con i suoi sistemi di monitoring di Aeroporti e porti per ricerca di sostanze radiattive.
Microtest (Altopascio): lavora con noi per tests dei chip di memoria associativa
Kaiser (Livorno): fa tanti progetti, specialmente per lo spazio, potrebbe partecipare sul tema di sistemi embedded per processamento di immagini o dati da sensori. Antonio Bardi lavora li’
Prisma Electronics (Grecia) ha un sistema embedded per monitoraggio di sensori nelle sale macchine di navi.

## Slide 42
pattern
Bus_layer0 Bus_layer1 Bus_layer2 …….. Bus_layer7
layer0
layer1
layer2
layer7
pattern0
pattern1
pattern2
pattern3
layer0
layer1
layer2
layer7
….
- very parallelized ASIC x pattern matching
AM COMPUTING
POWER
Each pattern:
4 32 bits comparators
Each 10 ns
128 kpat *4 = 500 K comparisons
→ 500 K * 100 M/s = 50 106 MIPS/chip
MIPS → note: only comparisons!
+ readout tree
+ 128 k *100 M/s 8-bits-coincidences w majority= 1 1015 bit-coincidences/s
AM CONSUMPTION:
~ 2.5 W for
128 kpatterns
AM Memory Accesses:
128 k * 4 * 32 bits *100 M/s=
1.6 * 1015 accesses/s
1 COMPARATOR between
the BUS & 1 stored
16-bits-WORD

## Slide 43: Speed and minimum latency
There are ideas to further improve performance, if needed
~40ns
Speed and latency are data dependent, further system simulation needed for precision
~10ns
~50ns
~70ns
Figures represent latency from last incoming hit to first output track
System latency (from last hit to first computed parameters) <0.3us

## Slide 44
VIRTEX 5: 65 nm- 550 MHz devices
XC5VSX95T: 160 x 46 CLB Array (Row x Col)
Each Slice:
4 6-input Luts or RAM or SR
4 FFs
Wide MUXs
Carry logic
160
46
244 39kbits BlockRams or Fifos+ 640 DSP Slices (organized in columns)

## Slide 45
5 CLBs (like Block RAM): 32 into each column x 20 colonne
DSP SliCEs

## Slide 46
Michela Del Viva e Giovanni Punzi (Universita’ di Firenze e Universita’ di Pisa)