## Slide 1: Backgrounds simulations (*), SVD radiation protection system and environmental monitoring L.Lanceri Univ. Trieste & INFN Belle2 – Italia Meeting, Roma, June 9 - 10, 2014 (*) Summary from B2GM and BPAC presentations

## Slide 2: Backgrounds simulations
From B2GM, BPAC summary talks

## Slide 3: Backgrounds: SuperB TDR
SuperB TDR, detailed simulations:
  radiative Bhabha (BBBREM):
  pairs production (BDK, DIAG36, GP++):
  Touschek (STAR, MAD)
  beam-gas (Coulomb, inelastic)
  synchrotron radiation: smaller contributions
Sub-detectors: rates, occupancy, doses (Bruno)
  SVT (pairs production dominates)
  DCH (radiative Bhabha, pairs)
  FTOF, FDIRC (radiative Bhabha)
  EMC (radiative Bhabha)
  IFR (radiative Bhabha; neutrons)

## Slide 4: Backgrounds: Belle2 TDR
Qualitative statements on bkgd sources
  radiative Bhabha: new IR, expect 1/40 x KEKB (?);
  pairs production: 45 - 670 MHz in PXD
  Touschek: HER dominates, 20-30 x KEKB expected
  beam-gas: depending on beam currents (x2), vacuum, magnets…
  synchrotron radiation
Subdetectors: rates, occupancy, doses…
  PXD (pairs production: BDK, KoralB, Racoon; occupancy < 0.5%)
  SVD (specs: bkgd up to 30x KEKB, dose up to 10 Mrad)
  CDC, TOP (…)
  ECL (endcap upgrades: pure CsI, BSO, etc.)
  KLM (extrapolations from KEKB: endcap scintillators upgrade)

## Slide 5: Backgrounds: on-going simulations
New working group (simulations + BEAST)
  Hiroyuki Nakayama (KEK) + Sven Vahsen (Hawai’i)
  Subsystems reps., in particular for simulations:
  SVD: Peter Kvasnicka, ECL: Sam de Jong, TOP: Marko Petric
Simulation “campaigns”
  6th- 8th: reported at the February B2GM & BPAC
  9th: in preparation for the June B2GM;
  HN, private communication: 9th should also include updates on Touscheck and beam-gas from the accelerator group
Slides from Sven (B2GM) & Hiro (BPAC):
  Latest IR loss distributions of each BG source
  Full detector simulation (6th – 8th campaigns)
  NB: problem with rates, in particular pair production ??

## Slide 6
Neutrons (rad. Bhabha)
Background picture
SR
Touschek LER
RBB LER
Coulomb HER
Touschek HER
RBB HER
Ver. 2013.6.12
HER
LER

## Slide 7: Beam BG simulation
 | Touschek | Beam-gas Brems | Beam-gas Coulomb | Radiative Bhabha
Phase 1 No QCS Vacuum baking | READY | READY | READY | No collision
Phase 2 Detuned optics | READY | Not ready | Not ready | READY (x1/80 of phase 3)
Phase 3 Full luminosity | READY | READY | READY | READY
Y.Funakoshi, Y.Ohnishi (KEKB)
Loss distribution
Geant4
Belle II+ Beam Pipe + Shielding
Belle II / BEAST II detector digitization

## Slide 8: 8th background MC campaign
New in 8th campaign:
  Spent e+/e- from 2-photon process
    included for the first time for sub-det except PXD
  QCS cryostat design update: type 1 or type 2?
    More tungsten structure on QCS-R head?
    Quick study shows more tungsten increase CDC rate but decrease TOP PMT rate
  Conclusions: Tungsten on QCS-R head preferred from BG point of view
~nakayama/basf2_output/release_201312_8th/Work_Mcgen/output/output_*.root
Nakayama

## Slide 9: Summary for 6th campaign
 | (5th) 6th campaign result | limit | SF
PXD occupancy | 2photon:0.8%, SR:1.1+-0.3% | < 2~3% | 1
CDC wire hit rate | (200)120kHz | <200kHz | 2
CDC Elec.Borad n-flux* | (2.6)2.1 | <1 | 0.4
CDC Elec.Board dose | 30Gy/yr | <100 Gy/yr | 3
TOP PMT rate | 2MHz/PMT | <1 MHz/PMT | 0.5
TOP PCB n-flux* | 0.5 | <1 | 2
ARICH HAPD n-flux* | (2.0)1.4 | <1 | 0.7
ECL crystal dose | (12)6 Gy/yr | <10 Gy/yr | 2
ECL diode n-flux* | (2.2)0.9 | <1 | 1
ECL pile-up noise | 4/1MeV | 0.8/0.2MeV at Belle-I | ?
SF=Safety Factor
*neutron flux in unit of
1011 neutrons/cm2/yr,
NIEL-damage weighted
KLMs are not included
showing SF<5 only
With “combined” shield inside ECL
FIXME: not updated for 8th campaign - yet!
All sub-detectors groups except KLM delivered results from 8th campaign

## Slide 10: Sub-detector BG summary
PXD occupancy close to limit
CDC FPGA
  >1x1011 neutrons/cm2/year, but SEU rate is still acceptable
TOP PMT lifetime
  New PMTs has super-long lifetime (~x10 improvement)
  Low-gain operation could help old PMTs
    TTS is OK, need to check timing resolution with readout electronics
  Last resort: replace PMTs every few years

## Slide 11: VXD Radiation Monitoring and Beam Abort
(Trieste)

## Slide 12: Conceptual Design
8 + 8 sensors
on SVD L3
support rings
4 + 4 sensors
PXD-beam pipe
3+15 m (3+40 m) triax cables
Voltage sources (150÷500 V)
picoAmmeters
Shielded
diamond
sensors

## Slide 13: Diamond sensors and metallization
Offers and working prototypes from:
  Micron (UK): sensors from E6 + metallization
  Cividec (Austria): sensors from E6 + metallization
Other options under investigation:
  Bare sensors directly from E6
  Metallization by Elettra/Trieste (or ZM Fraunhofer ?)
  EDP (Japan):
    beginning to produce electronic grade diamond crystals
    To be investigated if time constraints are more relaxed

## Slide 14: Measurements
Single particles (MIPs)
  Tests on 9 p/scCVD sensors
  Charge collection efficiency
  Beta source + beam test
Currents measurements for dosimetry and beam abort
  collaboration with Elettra, Electronics Division
  AH501 fast picoammeter
  Noise measurements and optimization(see next slide)
  Digital filtering studies (see next slide)
Sr90 e-, “2 MeV” selection
DESY e- beam, 3 GeV

## Slide 15: Grounding, cabling, digital filtering tests (TS)
Noise measured in different configurations, with AH501 picoammeter
  grounding scheme
  Cables types and layout: optimized
    3 m two small coaxial (HS SM47LSFH)
    15 m two coaxial HS S_04162-B60, double shield
    Or 15m one tri-axial (HS BNT-50-3-1)
Noise characterization and filtering, results:
  Noise dominated by 50Hz and multiples
  Down to few pA level, with 3+15m cables
  Digital filtering algorithms can further reduce noise (5-10x)
    Moving average (or “sliding sums”), CIC sum (sum of sums)
    Good compromise on bandwidth: reachable by further waveform subtraction
Next:
dosimetry tests, with
90Sr beta source:
mechanics in preparation

## Slide 16: Mechanics: compact package
very small multi-layer package in Rogers laminate
12 x 20 x 3.1 mm3 with copper extra shielding
Designed and produced, now under test

## Slide 17: Electronics: preliminary specs
Modules with 4 input channels, for monitoring and abort
  Evolution of AH501 front-end + Altera Cyclone IV FPGA
  Functionality similar to the FermiLab BLM system
  http://beamdocs.fnal.gov/AD-public/DocDB/ShowDocument?docid=1410
Common logics: features
  Timing synchronized to SuperKEKB revolution period (10 μs)
  “SuperKEKB status” register, to select appropriate thresholds
  Programmable masks and majority logics: abort signal (output)
  Circular buffer for timing information, in parallel with data buffers
  Circular data buffers “freeze” upon external or internal abort
  Ethernet interface for programming and data read-out
    “slow” readout of averaged radiation dose monitoring data (< 100 Hz, typical 1 Hz)
    Full data buffers readout for post-abort diagnostics

## Slide 18: Rad.Mon+Abort, 4-channel module
ADC + 3 Sums
+ 4 Abort Levels
4 Circular
Buffers
Ethernet I/O
Timing (100 kHz)
Machine status
Timing buffer
Timing
Control
Abort
HV
Thresholds
etc
(for each
input channel)

## Slide 19: Electronics: preliminary specs
For each of the 4 input channels (diamond sensors)
  Individual HV supply
  Effective bandwidth: 100 kHz (revolution period = 10 μs)
  Selectable current range: 0-50 μA or 0-2 mA
  16 (24?) - bit ADC; over-sampling possible
  4 circular data buffers, updated every 10 μs:
    “Raw data” and 3 levels of "sliding sums” over programmable numbers of cycles
     different digital filtering levels and time responses, from "immediate" (10 us) to "very slow" (typically 1 s)
  4 levels of abort signals
    from the comparison of raw data and sliding sums with the programmable thresholds, selected according to the “SuperKEKB status”
In collaboration with G.Cautero, D.Giuressi, and R.H.Menk from Elettra - Sincrotrone Trieste S.C.p.A.

## Slide 20: Temperature & Humidity Monitoring
(Trieste)

## Slide 21: Temperature and humidity
System characteristics
  PXD+SVD Front End power dissipation: 360+700 W
  CO2 cooling pipes (-20oC); dry air / nitrogen flow (20oC)
Requirements
  Temperature monitoring:
    near heat sources and at the inlets/outlets of cooling pipes
    about 1oC (0.1oC) absolute (relative) accuracy
  Interlocks on temperature and humidity (stand-alone, VXD)
    Temperature above threshold, or dew point approaching -30oC
Current activities and preliminary design
  Conventional NTC thermistors for cross-calibration and interlocks
  Fiber Optical Sensors (FOS) and laser interrogators
    Based on Bragg grating reflection of specific wavelengths
    Can monitor stress, temperature, humidity (with humidity-sensitive coating) at several points
  Humidity interlock: “sniffers” plus chilled mirror hygrometer outside

## Slide 22: NTC temperature sensors
At least 28 x 2 = 56 NTC thermistors
  12 sensor pairs attached to the 12 half-rings supporting the SVD ladders
  16 sensor pairs on the inlets and outlets of the CO2 cooling pipes
  A few positioned near fibers for cross-calibration
We adopted rad-hard sensors and readout, largely used by LHC experiments
  One ELMB board + Betatherm NTC thermistors: borrowed from CMS
  2 motherboards and 10 adapter mini-cards procured (public CERN design)
  Procurement of more Betatherm thermistors
  Read-out via CAN bus interface, implemented

## Slide 23: ELMB boards, CAN bus read-out
Embedded Local Monitor Board
CAN node, CANopen protocol
ATmega128 processor
128k flash, 4k SRAM, 4k EEPROM
64 chan. MUX, 16 bit ADC
General purpose motherboard
Interconnections, signal adapters
PC – CAN bus interface
hardware
software
CAN interface drivers
CANopen OPC Server
OPC Clients
Server Explorer
N.I. LabVIEW DSC
(Data Logging & Supervision Control)
Installed and working
in our lab !

## Slide 24: FOS Technique
Where:
neff is the effective refractive index of the fiber,
Λ is the grating pitch and
λB is the reflected Bragg wavelength.
TEMPERATURE CHANGE
Thermal expansion for
Thermo-optic effect for
STRESS
Elasto-optic effect for
Direct Strain for

## Slide 25: FOS set-up, preliminary design
45 fibers, one fiber per ladder (layers 3-6)
  Embedded in Airex, with several measurement spots (at each wafer)
Preliminary design: result of discussions with
  PXD FOS monitoring experts (D.Moya, I.Vila / IFIC)
  Rappresentanza italiana di Micron Optics (B.Griffoni / GHT Photonics)
Option A
  SM225-800 interrogator, 16 channels (Micron Optics)
  3 SM041-008 4x8 couplers/multiplexers (8 dB attenuation)
  1 SM041-016 4x16 coupler/multiplexer (16 dB attenuation)
Option B
  SM225-800 interrogator, 16 channels
  10 1x4 passive couplers (5-6 dB att.)

## Slide 26: Initial plan for humidity
  Humidity interlock: “sniffing pipes” plus Chilled Mirror Hygrometer outside the detector
    See CMS developments for their tracker upgrade: 3-fold approach
      “sacrificial” expendable radiation-soft sensors for initial calibrations
      Combination of FOS fibers measuring temperature and humidity
      26 sniffer lines and Vaisala hygrometers in accessible positions
    To start: lab tests using an hygrometer purchased with committed dot.1 funds
    Mechanics, pipes, valves, etc: to be understood !
Some FOS fibers sharing the same interrogator with temperature FOS fibers

## Slide 27: Humidity: CMS “sniffer” approach

## Slide 28: Timeline, first guess (Feb. 2014)
Temperature & humidity | 2014 |  |  |  | 2015 |  |  |  | 2016 | 
What | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2
T&H Specifications, sign up |  |  |  |  |  |  |  |  |  | 
Fibers, mechanical layout |  |  |  |  |  |  |  |  |  | 
Fibers, assembly tests (SVD) |  |  |  |  |  |  |  |  |  | 
Fibers, multiplexing scheme |  |  |  |  |  |  |  |  |  | 
Fibers design sign up |  |  |  |  |  |  |  |  |  | 
Procurement, assembly |  |  |  |  |  |  |  |  |  | 
installation (PXD & SVD) |  |  |  |  |  |  |  |  |  | 
Thermistors, lab tests |  |  |  |  |  |  |  |  |  | 
Mechanics & cabling design |  |  |  |  |  |  |  |  |  | 
Procurement |  |  |  |  |  |  |  |  |  | 
assembly, installation |  |  |  |  |  |  |  |  |  | 
Radiation | 2014 |  |  |  | 2015 |  |  |  | 2016 | 
What | 1 | 2 | 3 | 4 | 1 | 2 | 3 | 4 | 1 | 2
Specifications, sign up |  |  |  |  |  |  |  |  |  | 
Simulations |  |  |  |  |  |  |  |  |  | 
Dosimetry, characterization |  |  |  |  |  |  |  |  |  | 
Diamond sensors choice |  |  |  |  |  |  |  |  |  | 
Mechanics & cabling design |  |  |  |  |  |  |  |  |  | 
Electronics specifications |  |  |  |  |  |  |  |  |  | 
Electronics design & proto. |  |  |  |  |  |  |  |  |  | 
Overall design, sign up |  |  |  |  |  |  |  |  |  | 
Components, procurement |  |  |  |  |  |  |  |  |  | 
"final" prototypes (4 ch.) |  |  |  |  |  |  |  |  |  | 
BEAST, 1 preliminary tests |  |  |  |  |  |  |  |  |  | 
BEAST, 2 complete test (4 ch) |  |  |  |  |  |  |  |  |  | 
electronics production & test |  |  |  |  |  |  |  |  |  | 
sensors installation & cabling |  |  |  |  |  |  |  |  |  | 
electronics installation |  |  |  |  |  |  |  |  |  | 

## Slide 29: Back-up

## Slide 30
PXD
Pit Vanhoefer

Yuri Soloviev
SR LER: 0.1% at one half ladder in #1 layer
SR HER: Should be updated with the latest optics,
but it was 0.5%+-0.3% with previous optics
Close to limit (2~3%)

## Slide 31
SVD
Peter Kvasnicka

Well below 10%. OK

## Slide 32
TOP



- New PMTs has good lifetime (>10C/cm2) but we still need to use old PMTs (~1C/cm2)
- Charge on PMTs can be 1/2 with half-gain operation
(timing resolution with half-gain operation should be checked)
Marko Petric
half gain, old PMTs
full gain, old PMTs
* Note that TOP assumes 50/ab, while the other detectors assume80/ab(=full luminosityx10year)
Notes: “TOPSimHits” = “detected photon” = photon * QE * CE = photoelectron * CE Marko’s MHz/PMT number counts “detected photon”. Is QE*CE in BASF2 is realistic? for new PMT, old PMT, respectively. (2MHz, full gain) 2MHz/PMT, 2.25cmx2.25cm,10^6 gain, 1.6e-19C, 10^7sec/year --> 0.63C/cm2/year 2e6/(2.25*2.25) * 1e6 *1.6e-19 * 1e7 = 0.63C/cm2/year 80/ab (full luminosity*10year) --> 6.3C/cm2 50/ab-> 4.0C/cm2 (2MHz, half gain) 80/ab -> 3.2C/cm2
50/ab -> 2.0C/cm2

## Slide 33
ECL
Sam de Jong
Crystal radiation dose/ diode Neutron flux becomes OK,
with “combined” shielding option.







## Slide 34: Radiation Monitoring and Beam Abort
Requirements
  Measurement of instantaneous dose rates & integrated doses
    sensitivity O(1 mrad/s = 10 μGy/s), sampling rate O(10 KHz)
  Beam Abort for excessive beam losses affecting PXD, SVD
    “Fast” (10-100 μs) and “slow” (minutes) Beam Abort triggers
    Programmable “intelligent” thresholds, depending on accelerator conditions
Conceptual design
  Based on experience from Belle, BaBar, CDF…
  Diamond sensors, measurement of currents
    Typical pCVD sensor (10 × 10 × 0.5) mm3: 1 nA = 7 mrad/s = 70 μGy/s
    Noise should be limited to a few pA, in current measurements
  up to 4 + 4 sensors near PXD
  up to 8 + 8 sensors near SVD

## Slide 35
From M.Iwasaki (KEK), 2014-05-23: KEKB – Belle2 cables

## Slide 36: Reminder: FOS Monitor proposal
FC vs. LC connectors
Recent idea, under discussion:
1 fiber per ladder (45 ladders),
inserted in the Airex foam
R&D completed,
successfully tested
at the DESY beam test