## Slide 1: Electron accelerator for the AWAKE experiment at CERN
Experimental requirements
Accelerator design
Expected performance
Outlook and conclusions

## Slide 2
AWAKE layout

## Slide 3: Awake electron beam requirements
Parameter | Baseline Phase 2 | Range to check
Beam Energy | 16 MeV | 10- 20 MeV
Energy spread (s) | 0.5 % | < 0.5 % ?
Bunch Length (s) | 4 ps | 0.3-10 ps
Beam Focus Size (s) | 250 mm | 0.25 – 1mm
Normalized Emittance (rms) | 2 mm mrad | 0.5 - 5 mm mrad
Bunch Charge | 0.2 nC | 0.1 - 1 nC

## Slide 4
PWA-simulations
Injection of realistic electron beams into realistic density plasma
with a = 5 mm (orifice radius)
Beam phase portrait taken from simulations of Ulrich Dorda
Plasma density slope along 10 m
Oblique electron injection
presented by K.Lotov at 11th AWAKE Physics Board Meeting, CERN 26.06.2015

## Slide 5
Beam parameters against acceptance at z=-40cm
Electron energy distribution
Trapping is good even for twice larger size and angular spread of the electron beam
Injection parameters can be further optimized for more narrow energy spread
The result is not very sensitive to injection parameters
PWA-simulations
presented by K.Lotov at 11th AWAKE Physics Board Meeting, CERN 26.06.2015

## Slide 6
AWAKE electron source schematic
Length ~ 4 m
FC
E, DE
MS
BPT
Laser +Diagnostics
RF GUN
Emittance
Incident, Reflected Power and phase
Spectrometer
Corrector
MTV
VPI
FCT
Accelerator
MTV,
Emittance
Matching triplet
BPT
Incident, Reflected, transmitted Power
Klystron
A,f

## Slide 7
Electron source layout

## Slide 8
Load lock cathode system
Decided to use the load lock cathode system to allow for different type of cathodes:
Baseline: copper cathode Qe ~10-4
Option: CsTe Qe ~ 10-2
 Flexibility in future beam parameters

## Slide 9
Laser requirements
650 mJ amplifier
atten
Vacuum compressor
Compressor
THG
Splitter
Mechanical pulse selector
2.5 mJ
25 mJ amplifier
atten
Requirements to Amplitude | 0.1 nC | 0.2 nC | 1 nC
Pulse duration | 0.3 ps | 10 ps | 10 ps
Pulse energy to the Cu-cathode in UV | 50 uJ | 100 uJ | 500 uJ
IR laser output | 2.5 mJ | 2.5 mJ or 25 mJ | 25 mJ
To plasma
UV to e-gun
Wavelength : 262 nm
Phase 2
Phase 1
Phase 1
Main limitation: ablation threshold on copper cathode

## Slide 10
Beam instrumentation
Instrument | How many | Resolution | Who
BPMs | 3 | 50 mm | TRIUMF, new
Screens | 2 | 20 mm | CERN, partly existing
Pepper pot | 1 | < mm mrad | Cockcroft, new
FCT | 1 | 10 pC | CERN, existing
Faraday Cup | 1 | 10 pC | TRIUMF, new
Spectrometer | 1 | 10 keV | CERN, MTV
Streak Camera | 1 | < ps | CERN, merging point
Instrumentation contributed by TRIUMF (Canada) and Cockcroft (UK)

## Slide 11
Beam instrumentation
Strip line BPM’s developed by Triumf for electron beam line and common beam line
Pepper pot diagnostic developed by University of Manchester/Liverpool

## Slide 12: Graeme Burt and Ron Apsimon, The university of Lancaster
Constant gradient 2p/3 travelling wave structure at 2.99855 GHz
30 cells is just under 1 metre long
9.6 MW input power gives 15 MV
Average group velocity is 1.23% c. The filling time is equal to 273 ns
Booster structure

## Slide 13
Parmela simulation with r= 0.5mm, E=100 MV/m, Q=0.2 nC
 e = 1.3 mm mrad
Electron Beam Dynamics

## Slide 14
PHIN Emittance measurements for Awake 22.8.2014
Laser size: ~ 1 mm sigma, Charge 0.2 , 0.7, 1.0 nC, Energy 5.5 – 6 MeV
Normalized emittance for 0.2 nC: 3.2 mm mrad ( big errors !)
En (1nC): 5.5 mm mrad
En(0.7 nC): 4.6 mm mrad
PHIN emittance
measurements
Qe measurement for copper cathode: 5 10-4, surprisingly good

## Slide 15
Laser PLL
Fiber receiver/transmitter
3 GHz master
GPS receiver
Fiber receiver/
transmitter
SPS synchro crate
88.2 MHz (laser)
2997.9 MHz
(reference)
10 MHz (reference)
9.97 Hz, 8.68 kHz, 400.4 MHz, 10 MHz
Fractional divider SPS
Main RF divider
400.4 MHz
Fast pulse triggers
Buffer amplifiers
Electron
LLRF
Various frequencies distributed (many!)
Fast pulse triggers (~20 adjustable)
Laser
Buffer amplifiers
Fast pulse triggers
176.3 MHz
Timing
Timing
200.2 MHz
Proton LLRF
Extraction and bunch rotation triggers
BA4
TSG40
BA3/Faraday Cage
Timing and Synchronization
Goal: ~ 100 fs jitter

## Slide 16: Outlook
Shorter pulses: to better probe the wake fields ?
Higher current: yield, efficiency, beam loading ?
Higher Energy: for better injection ?
Positrons: proof of principle
Anticipate future electron beam parameters for the AWAKE experiment
What will be needed to advance towards a plasma accelerator for high energy physics ?

## Slide 17
Awake simulations
Phin gun, 20 MV/m structure, 0.2 nC, 1 mm laser,
1 ps laser

## Slide 18
Awake simulations
Phin gun, 20 MV/m structure, 0.1 nC, 0.25 mm laser

## Slide 19: Conclusions
The electron accelerator for AWAKE has been defined and construction started
We are working towards installation and commissioning in 2017
Have to start thinking about the future evolution of AWAKE and the necessary equipment and developments
Collaborations: Cockcroft (University of Lancaster, Liverpool, Manchester), TRIUMF, CLIC

## Slide 20: End

## Slide 21
Electron source design
Oznur Mete, Cockcroft

## Slide 22
Thales TH2100
Parameters | Specifications
RF frequency | 2998.5 MHz
Peak RF power | 45 MW
RF gain | 54 dB
Efficiency | 43 %
Anode voltage | 307 kV
Beam current | 340 A
High voltage pulse length @75% | 7.6 us Needed : 1-2 us
Total height | 1.7 m
Klystron and modulator

## Slide 23
Laser requirements

## Slide 24
Parmela simulation with r= 1mm, E=85 MV/m, Q=0.2 nC
 e = 3.2 mm mrad ( by chance)
PHIN to AWAKE