## Slide 1: Aggiornamento sullo sviluppo di una nuova versione del chip CASIS per CALOCUBE
Valter Bonvicini, Giulio Orzan, Nicola Zampa, Gianluigi Zampa
INFN Trieste
CALOCUBE meeting
Firenze, 20 giugno 2014

## Slide 2: Front-end electronics
Scientific interest: direct measurement of the cosmic-ray fluxes above the TeV region. Examples:
Direct observation of cosmic-ray electrons
up to 10 TeV
Measurement of cosmic-ray nuclei flux and
elemental composition up to the “knee”
( 1014 – 10 15 eV)
A major concern: dynamic range!!!
(with sensitivity down to fractions of a MIP)
(a big challenge…)

## Slide 3: Front-end electronics
R&D carried on in Trieste through the CSN 5 experiments CASIS and CASIS2
Several prototypes designed, realized and tested
CASIS1.2A ASIC (used for the prototypes of calorimeters realized in Florence):
  Double-gain (double-range) CSA
  Double-correlated sampling, MUX and output buffer
  Input calibration circuit (with arbitrary channel pattern)
  16 channels
  Noise: 2700 e- + 8e-/pF
  Power consumption: 2.8 mW/channel
  Dynamic range (low gain): 53 pC

## Slide 4
5300 µm
4000 µm
16 FE channels with A/D conversion
function integrated in the ASIC;
1 12-bit cyclic ADC /channel with
capacitor averaging and digital
correction;
Design submitted in August 2013
(prototypes arrived at the end of 2013);
Next step: CASIS1.2B

## Slide 5
2970 µm
250 µm
CASIS1.2B: layout of a complete channel

## Slide 6: CASIS1.2B
Details of one chip (AMS 0.35 um CMOS C35B4 technology)

## Slide 7: CASIS1.2B
Detail of the test boards designed and realized in Trieste for the characterization
of the new ASIC

## Slide 8: CASIS1.2B
CASIS1.2B chip in
CQFP120 package
“Daughter board”
“Mother board”

## Slide 9: CASIS1.2B
Test set-up in Trieste