## Slide 1: MC simulations for the improvement of hadronic energy resolution using Cherenkov signal
M. Bongi, S. Bottai
1st Calocube collaboration meeting - 20th June 2014 - Firenze

## Slide 2
Fluka-based MC simulation
  3,6cm CsI Scintillating crystals Scintillation Light collection efficiency and PD quantum efficiency
  Photodiode Energy deposits in the photodiodes due to ionization are taken into account
  Carbon fiber support structure (filling the gaps between crystals)
  Number of crystals passed via parameter
  New dedicated versions for Cherenkov and Neutrons detection added recently (to be finalized and eventually ‘unificated’ with standard version)
THE SIMULATION & RECONSTRUCTION TOOL
Developed by florence groups (Paolo Papini) for internal use
mori@fi.infn.it to get the code (via GIT)
CaloFlukaSim
( CaloPrototypeFlukaSim ; a version with prototype geometry)
C++ reconstruction tools
  Noise
  Shower axis reconstructed by fit
  Lateral and longitudinal profiles respect to axis
  Point of first interaction along axis
  Length from first interaction to end of calorimeter
  ............................................................................
No MC truth is needed
in the analysys

## Slide 3: Proton energy resolution
100 – 1000 GeV
1 TeV
10 TeV
32%
35%
39%
100 TeV
40%
( Measured Energy – Real Energy ) / Real Energy

## Slide 4
IF THE ELECTROMAGNETIC FRACTION IS GIVEN FOR EACH SHOWER IT CAN BE
USED TO IMPROVE THE RESOLUTION fem=Eem/E
for 1 TeV vertical proton the resolution scale from 35% to 15%
PERFECT fem CORRECTION
Slices
has lower RMS

## Slide 5
The DREAM concept : USE CHERENKOV LIGHT [ Q ]
2 equation, 2 variables
As far as ηS ≠ ηQ
Otherwise we have only 1 equation
Degeneration !

## Slide 6
Preliminary simulation studies seems to indicate that in the standard CsI CALOCUBE
ηS ~ ηQ
small calorimeter thickness for pure hadronic component ?
Index of refraction ?
TO BE STUDIED
Is it possible to improve the situation using the high segmentation
to combine topology and Cherenkov ? TO BE STUDIED
S/E
Q/E
In such configuration the method can’t work !

## Slide 7: TOTAL ABSORPTION CALORIMETER
In order to compare with published results:
20 x 20 x 20 BGO cubes
side of each cube = 18 cm
>16 interaction lengths (for vertical tracks)
E=100 GeV, 1000 events
Signal integrated for t<20ns
hs=(h/e)S 0.64 hc=(h/e) C 0.45
LET’S SIMULATE SIMPLER CONDITION AND COMPARE TO LITTERATURE

## Slide 8
Without corrections
TOTAL ABSORPTION CALORIMETER
BEST METHODS : SEE CORRELATION S versus C/S

## Slide 9: “A. PARA-LIKE” CORRECTION
A better result can be obtained taking into account the shape of the distribution
Correct the scintillation signal with a function Fcorr obtained from a polynomial fit (e.g. 3rd grade) of the profile-X histogram of the scatter plot

## Slide 10: “A. PARA-LIKE” CORRECTION
With correction
Scorrected/E
C/S
Without corrections

## Slide 11: NORMALIZED ENERGY DISTRIBUTION
improvement of energy resolution:
Here ~ 40%
~34% (DREAM)
~44% (PARA)
Resolution Improvement ~ 40%
We controll the
method !
consider blue line
Scorrected/E

## Slide 12: LET’s come back to CALOCUBE
More realistic case:
20 x 20 x 20 CsI cubes
side of each cube = 3.6 cm
~ 1.9 interaction lengths (for vertical tracks)
E=100-300 GeV, 10000 events
selecting events interacting in the first layer, and shower > 70 cm
“hS=(h/e)S" 0.18 " hc=(h/e)C" 0.07
SCINTILLATION
CHERENKOV

## Slide 13: Apply the ‘standard’ correction to CALOCUBE
Vertical protons E=100 GeV, interacting in the first layer
S/E
C/S
C/S
Scorrected/E
RMS=22%
RMS=20%
IF WE GET A SAMPLE OF SHOWERS INTERACTING DEEPER AND HENCE WITH MORE LEAKAGE THE IMPROVEMENT IS AGAIN
~ 10%
35% 31%
RESOLUTION IMPROVEMENT ~ 10%

## Slide 14
ACCESS CALORIMETER : THIN SAMPLING CALO
Vladimir Nagaslaev, Alan Sill, Richard Wigmans
~ 10%
IMPROVEMENT DUE TO DUAL REDOUT ~ 10% IN ACCORDANCE TO WHAT WE FIND !
FOR THEM IS A GOOD RESULT
FOR US ????? (personally I think not)
TEST BEAM ANALYSIS

## Slide 15
USING CHERENKOV WE CAN MEASURE QUITE WELL Shad and Sem
EE
Eh
Sem ~Ee
p+/-
Shad
Shad is strongly correlated with
S-C=scintillation-Cherenkov
Shahd
S-C
S=Sem+Shad
Scintillation and Cherenkov give direct info only on Sem and Shad (not on Eh)

## Slide 16
BUT WE DO NOT KNOW fem WITHOUT ERRORS ! (fem=Eem/E )
Fem(reconstructed)= Sem /[Sem +Shad*<1/h>]
Each slice DS/S~10%
S/E
Fem=Eem/E
SUPPOSE TO HAVE AN IDEAL DUAL DETECTOR !
MEASURE WITHOUT ERRORS separately Sem and Shad (Visible Em and had energy deposited )
Each slice DS/S~20%
EE
Eh
Sem ~Ee
p+/-
Shad
E=Ee+Eh=Sem+Shad*<1/h>
<1/h>=<1/ht>*<1/hleak>
Nuclei Excitation,
neutrons
Pions leakage
Fem(reconstructed)
S=Sem+Shad
S/E

## Slide 17: LEAKAGE fluctuations prevent cherenkov correction !
Even if we suppose to have perfect access to the scintillation signal produced by e.m. particles Sem and separately tp the scintillation signal produced by hadrons Shad…
Sem(GeV)
Ee (GeV)
Shad(GeV)
Eh(GeV)
Sem, Shad = Energia Ionizzazione Depositata effettivamente (em , had)
EE
Eh
Sem ~Ee
p+/-
Shad
E=Ee+Eh=Sem+Shad*<1/h>
<1/h>=<1/ht>*<1/hleak>
Nuclei Excitation,
neutrons
Pions leakage
<ht>~ 0.85
<hleak>~ 0.25
RMS ~ 40% !
100-300GeV protons
interacting first layer
100-300GeV protons
interacting first layer
DE/E ~ 20%

## Slide 18: CAN the spatial distribution of signals help?
Shad/Eh
Eh = energy of hadrons
Shad = energy of hadrons deposited by ionization in the calorimeter
    ‘SHAPE’ VARIABLES
COGS and COGh: center of gravity of scintillation (S) and hadronic (S-C) signals
along the longitudinal development (expressed in fraction of total length)
Shad/Eh

## Slide 19: CAN the spatial distribution of signals help?
fracLASTh: fraction of hadronic energy (S-C) released in the last two layers
Shad/Eh
hoped distribution

## Slide 20: conclusion
Simulations indicate that the possibilities to improve energy resolution
using Cherenkov light are only marginal !
10-15% improvement
Chenrenkov light is also very important for cross-calibration and
Cross linearity-check