## Slide 1
Accelerator Division Activities
Andrea Ghigo on behalf of
INFN-LNF Accelerator Division

## Slide 2
Accelerator Division Main Projects
DAFNE
SPARC-LAB
SPARC-Premiale
CHAOS-Premiale
ELI-NP (Romania) / STAR (Cosenza)
Collaborations: LC/CLIC, HL-LHC, FCC, ESRF, CNAO…
FP7 European projects
  FEL
  Plasma acceleration
  Thomson Scattering
  FLAME
  TeraHertz
!
  KLOE
  Beam Test Facility
  Synchrotron Radiation

## Slide 3
Dipendenti:
38 Laureati
48 Tecnici
2 Coll.Amm.
+ 3 Ass.Ric
+3 borse diplom.
+ Dottorandi
9 Servizi
16 Reparti
24 TD

## Slide 4
DAFNE
LINAC
BTF
DAFNE-light
The DAFNE -Factory complex
LNF

## Slide 5
DAFNE – LNF - FRASCATI
e+ e-
Ecm = 1.02 GeV
L = 1.5 1032 cm-2 sec-1

## Slide 6
DAFNE IR for the KLOE-2 run

## Slide 7
The new KLOE detector layers have been wired
Whole structure has been inserted inside the experimental apparatus

## Slide 8: New KLOE vertex detector

## Slide 9
Third carbon fiber support installed
IR branches outside the detector reassembled and aligned
Shut-down activities completed by mid July

## Slide 10
DAFNE shut-down was intended mainly to upgrade the experimental detector (KLOE became KLOE-2), and it has been very useful to consolidate the entire collider.
December 16th 2012 ÷ mid July 2013
Activities involved almost all the components of the DAFNE accelerator complex:
  IR mechanical structure and IP vacuum chamber
  auxiliaries’ automation and control system
  Control system
  Vacuum installation (windows, scrapers)
  Cooling system
  Cryogenic plant
  Magnets and power supplies
  Modification of the LLRF controllers
  Linac
  E-cloud electrode power supplies
  new horizontal kicker for the MRe feedback
  Additional BPMs and improved tools for beam profile measurements
DAFNE Consolidation Activities

## Slide 11
Commissioning
Commissioning started mainly by the end of January 2014, but it has been severely slowed down by 3 main interruptions due to external circumstances causing, in total, two and half months of inactivity.
Transverse betatron coupling all skew QUADs off:
  k+~ 0.4%
  k- not yet optimal
Tuning the skew QUADs:
  0.2% < k < 0.3% (both beams)
working points adopted
  nx- = 5.098 ny- =5.164
  nx+ = 5.102 ny+ = 5.139
according LIFETRAC simulations should provide good luminosity
e- ring optics

## Slide 12
Beam Dynamics
Highest currents stored, so far, in 98 bunches spaced by 2.7 ns are:
I- = 1.7 A I+ = 1.15 A
These currents are the highest ever achieved after installing the new IR for the KLOE-2 detector, based on the Crab-Waist collision scheme.
The three independent bunch-by-bunch feedback systems installed on each ring are essential for high current multi-bunch operations.
The e+ vertical feedback is now using a new ultra-low noise front-end module, designed in collaboration with the SuperKEKB feedback team, aimed at reducing the noise contribution to the transverse vertical beam size in collision.

## Slide 13
Beam dynamics in the e+ ring is dominated by the e-cloud induced instabilities which are kept under control by:
  powerful bunch-by-bunch transverse feedback systems
  solenoids wound all around the straight sections
  electrodes installed inside dipole and wiggler vacuum chambers.
Electrodes effectiveness has been already proved in 2012 polarizing the stripline with a positive voltage in the range 0÷250 V
Simulations indicate that a factor two higher voltage is required to completely neutralize the e-cloud density due to a e+ current of the order of 1 A
e+ Beam Dynamics

## Slide 14
Integrated luminosity
L∫1 hour = 0.415 pb-1
L∫day ≈ 10. pb-1
KLOE is taking data
Acquired and delivered L are comparable
L∫1 hour is the highest measured with KLOE-2
27/11/2012

## Slide 15
 | DANE CW upgrade SIDDHARTA (2009) | DANE KLOE (2005) | DANE (CW) KLOE (2012) | DANE (CW) KLOE-2 (2014)
Lpeak [cm-2s-1] | 4.53•1032 | 1.50•1032 | 1.52•1032 | 1.70•1032
I- [A] | 1.52 | 1.4 | 0.93 | 0.96
I+ [A] | 1.0 | 1.2 | 0.72 | 0.89
Nbunches | 105 | 111 | 100 | 100
Lpeak exceeds by a 13% the best luminosity ever achieved, at DAFNE, during operations for an experimental apparatus including high field detector solenoid.
Peak Luminosity
Background presently has been reduced to levels almost compatible with the detector data-taking
100 bunches
L∫1 hour = 0.4 pb-1
moderate injection regime

## Slide 16
Vertical beam-beam Luminosity scan
Smeasy is still considerably high since the transverse betatron coupling in the e- ring is not yet properly corrected

## Slide 17
Crab-Waist Sextupoles
Crab-Waist Sextupoles effectiveness has been tested on the e+ ring
ICS = 210 A
ICS = 150 A
DAFNE luminosity monitor
Crab-Waist Sextupoles strengths are 30% and 50% lower than the nominal ones for e+ and e- respectively.

## Slide 18
10 Bunches Luminosity
Lpeak ~ 2.5 1032 cm-2 s-1 might be achieved by using 100 bunches
  Beam-beam is not a limiting factor
  Crab-Waist Sextupoles work (even at lower strength)
This result can be improved by:
  optimizing dynamical vacuum
  perfecting colliding beams parameters
  tuning multi-bunch and high current operations
Aiming at minimizing the impact of collective effects on L

## Slide 19
Pushing luminosity further
Higher luminosity might be attained by:
  Improving the transverse betatron coupling correction in the e- ring
  optimizing the present rings optics and working point
  Setting the CW-Sextupoles to the nominal values
  improving dynamic vacuum
  Increasing stored currents and number of colliding bunches

## Slide 20: Beam Test Facility (BTF) Infrastructure @DAFNE Linac
The Frascati Beam Test Facility infrastructure is a beam extraction line optimized to produce electrons, positrons, photons and neutrons mainly for HEP detector calibration purposes. The quality of the beam, energy and intensity is also of interest for experiments (~ 20% of the users) studying the electromagnetic interaction with matter

## Slide 21: BTF LAYOUT – Primary beam
Positron Beam
6×109 e+/bunch
Electron Beam
3×1010 e-/bunch
TO BTF
PRIMARY
PRIM conditioned
4x single-axes SCRAPERS
Forward Magnetic Line
LINAC Energy is conserved

## Slide 22: BTF LAYOUT - Secondary Beam
Positron Beam
4×109 e+/bunch
Electron Beam
3×1010 e-/bunch
TO BTF
PRIMARY
SECONDARY

## Slide 23
BTF LAYOUT - Secondary Beam
3-selectable thickness Copper Showering TARGET (Targhettone…)
1.7, 2.0 or 2.3 radiation lengths
Energy [MeV]
1010
510
Mult
∫∫
For 10^8 e+/e- primary particles
Mult
∫∫
Primary Beam
YAG:Ce FLAG
Secondary Beam
2cm2 MEDIPIX

## Slide 24
LNF
FLAME
SPARC-LAB
The SPARC-LAB complex

## Slide 25
COMB
THz Source
FEL
(2colors)
EOS
Thomson X-ray
FLAME
EXIN
SPARC_LAB
Sources for Plasma Accelerators and Radiation Compton with Lasers And Beams

## Slide 26
Ti:Sa FLAME laser
Stretcher
Amplifiers
Compressor
LWFA
Electron Self Injection
And
Protons

## Slide 27
S-band Gun
Velocity Bunching
Long Solenoids
Diagnostic and Matching
Seeding
150 MeV S-band linac
12 m
Undulators
u = 2.8 cm
Kmax = 2.2
r = 500 nm
15 m
Spectrometer
Linac and FEL

## Slide 28
HB photo- injector with Velocity Bunching

## Slide 29
Free Electron Laser

## Slide 30: TWO COLORS SASE FEL
two bunches with
a two-level energy distribution
and time overlap (Laser COMB tech.)
produce two wavelength SASE –FEL radiation
with time modulation
1 MeV
18 nm
110 fs

## Slide 31: Tunable X-ray radiation source based on Thomson Scattering

## Slide 32: SL-Thomson Source at SPARCLAB
FLAME
SPARC

## Slide 33
Thomson back-scattering source

## Slide 34
Thomson back-scattering source

## Slide 35: SPARC_LAB synchronization system
SPARC HALL
FLAME AREA
FLAME oscillator
In 2856MHz
Out 79.33MHz
PC laser
Oscillator
79.33MHz
RF reference
2856MHz
Main RF Reference oscillator
  RF system and laser oscillators locked to the reference through PLL
  Electrical signal distributed through coaxial cable
  Single sub-system VS reference time jitter <50fsRMS
  Interaction laser VS electrons time jitter (estimated) <200fsRMS

## Slide 36: Electron Beam Experimental Studies
Thomson backscattering experiments
  Flame transport
Max energy: 7J
Max energy on target: ̴ 5J
Min bunch duration: 23 fs
Wavelength: 800 nm
Bandwidth: 60/80 nm
Spot-size @ focus: 10 µm
Max power: ̴ 300 TW
Contrast ratio: 1010
e- beam at IP
σx=0.16±0.01 mm
σy=0.24±0.01 mm

## Slide 37
Weak blowout regime with resonant amplification of plasma wave by a train of high Brightness electron bunches produced by Laser Comb technique?
Ramped bunch train configuration to enhance tranformer ratio?
High quality bunch preservation during acceleration and transport?
Resonant plasma excitation by a Train of Bunches

## Slide 38
Sezione Banda C
Gruppo Pompe Vuoto
Permanent magnet actuator
YAG/OTR/EOS crystal actuator
Camera interazione e
Sistemi ancillari di pompaggio e iniezione gas
YAG/OTR actuator
COMB plasma interaction chamber

## Slide 39: LWFA acceleration of externally injected electrons in a gas-jet plasma

## Slide 41: Interaction Layout
e-beam
EOS chamber
Interaction chamber
Gas: Hydrogen
Gas cell and/or capillary
CL - Preventivi Frascati, 1 Luglio 2014

## Slide 42: The SPARC_LAB THz beam lines
CTR source
CTR and CDR sources
Linac-based source: Coherent Radiation from an aluminum-coated silicon screen (Coherent Transition Radiation, CTR) and from a rectangular aperture in the metallic screen (Coherent Diffraction Radiation, CDR).
YAG:Ce screen
Si-Al screen (CTR)
5 mm slit (CDR)
3 mm slit (CDR)

## Slide 43: Broad-band THz radiation: Measurements
Electron beam parameters | 
Energy (MeV) | 100
Charge (pC) | 260
RMS bunch length (fs) | 260
Intensity (arb. units)
Frequency (THz)
Frequency cut limited by the vacuum window quartz
Diamond window to be installed

## Slide 44: Narrow-band THz radiation: 2-bunches train measurements
Current profile as measured at the end of the linac
Measured Longitudinal Phase Space (LPS)
Electron beam parameters | 
Energy (MeV) | 122
Charge/bunch (pC) | 80
RMS bunch 1 length (fs) | 150
RMS bunch 2 length (fs) | 165
Time distance (ps) | 0.91 (0.019)
Autocorrelation measurement
of CTR with
a Michelson interferometer
0.9 ps
40%

## Slide 45: Achieved THz Performances
Radiation parameters | SPARC (single bunch) | SPARC (4-bunches/train)
Energy per pulse (J) | 40 10-6 | 0.6 10-6 (@ 1 THz)
Peak power (MW) | > 100 | 3 (@ 1 THz)
Average power (W) | 1.8 10-4 | 6 10-6
Electric field (kV/cm) | 500 | > 10
Pulse duration (fs) | 160 | < 100
Bandwidth (%) | broadband | < 25
Electron beam parameters | Single bunch (VB mode: max compression) | 4-bunches per train (VB mode + laser comb)
Charge/bunch (pC) | 300 | 50
Energy (MeV) | 130 | 100
Bunch length (fs) | 160 | 200
Rep. Rate (Hz) | 10 | 

## Slide 46: ELI-NP proposal INFN – CNRS – STFC – ALBA +European High Tech firms

## Slide 49
Laser Optical multipass ricirculator
LAL-Orsay

## Slide 51
Thanks for your attention