## Slide 1: Performances of the SDHCAL technological prototype for future lepton collider experiments
Imad Laktineh
IPN de Lyon
On behalf of the SDHCAL groups of the CALICE collaboration

## Slide 2
For future colliders, jet energy resolution will be a determinant factor of
understanding high energy physics.
Exemples:
Trilinear Higgs self coupling measurement
WW scattering measurement
To improve on the jet energy resolution
PFA is a promising solution to reduce the
confusion term.
But PFA needs high granularity Calorimeters
Resolution
Tracking
Leakage
Confusion
30%/E
Motivations
Different solutions of such calorimeters are being followed within the
CALICE international collaboration. The option we are investigating is the
Digital and Semi-Digital Hadronic CALorimeter using GRPC as sensitive medium

## Slide 3
Calice calorimeters
Several R&D on calorimeters are followed within the CALICE collaboration in order to
apply successfully particle flow analysis.
High granularity but also compactness and hermeticity are the key words of this development.

## Slide 4
1- Detector choice
Gaseous detectors: homogenous, cost-effective and highly transverse and longitudinal granular.
GRPC : is an adequate candidate for ILC.
2- Electronics readout choice
At high energy the shower core is very dense
 Simple binary readout will suffer saturation effect
 Semi-digital readout (2-bit) can improve the energy
resolution.
Simulation
1 cm2 pad
Avalanches
SDHCAL concept
30 GeV

## Slide 5
The structure proposed for the SDHCAL-ILD :
Is self-supporting
Has negligible dead zones
Eliminates projective cracks
Minimizes barrel / endcap separation
(services leaving from the outer radius)
SDHCAL for ILD
The SDHCAL-GRPC is one of the two HCAL options proposed
in the ILD Letter Of Intention (LOI). Modules are made of
48 RPC chambers (6λI) equipped with
power-pulsing electronics readout.
SDHCAL Prototype
- Come as close as possible to the ILD module
and be able to study hadronic showers
-48 units (active layer + absorber)
fulfilling the ILD requirements.
Challenges
-Homogeneity for large surfaces
-Thickness of only few mms
-Services from one side
-Embedded power-cycled electronics
-Self-supporting mechanical structure

## Slide 6: GRPC development
Max. deformation: 44μ
Dead zones minimized
Deformation studies
Genuine gas distribution
New resistive painting was developed

## Slide 7: Electronics readout development
6mm(active area) + 5mm(steel) =
11 mm thickness
4.7 mm
4.3mm
ASIC: HARDROC
64 channels, trigger less mode, memory depth:
127 events
2-bit readout : 3 thresholds
Dynamic range: 10 fC-15 pC
Gain correction  uniformity
Power-pulsed  reduced power consumption
Printed Circuit Boards (PCB) were designed to reduce the x-talk with 8-layer structure and buried vias.
Tiny connectors were used to connect the PCB two by two (the 24X2 ASIC are daisy-chained).
DAQ board (DIF) was developed to transmit fast commands and data to/from ASICs.

## Slide 8
SDHCAL acquisition system
Acquisition software was developed to deal with the output of large
number of electronics channels (> 460 000).
Oracle database used for ASIC configurations and slow control.
 CMS Xdaq used to provide the DAQ framework.

## Slide 9: Cassette development
6mm(active ara) + 5mm(steel) =
11 mm thickness
144 ASICs= 9216 channels/1m2
 To provide a robust structure.
 To maintain good contact
between the readout electronics
and the GRPC.
 To be part of the absorber.
 It allows to replace detectors
and electronics boards easily.
The cassettes are built of no-magnetic stainless steel walls 2.5 mm thick each  Total cassette thickness = 6mm (active layer)+5 mm (steel) = 11 mm

## Slide 10
10
HV : 7.4 kV
The homogeneity of the detector and its readout electronics were studied
Power-Pulsing mode was tested in a magnetic field of 3 Tesla
Beam spot position
Efficiency
Multiplicity
The Power-Pulsing mode was
applied on a GRPC in a 3 Tesla
field at H2-CERN
(2 ms every 10 ms)
No effect on the detector
performance
Test Beam validation
Notes: 10
10

## Slide 11
High-Rate GRPC may be
needed in the very forward
region
Semi-conductive glass (1010 Ω.cm)
produced by our collaborators
from Tsinghua University was
used to build few chambers.
4 chambers were tested
at DESY as well as standard
GRPC (float glass)
Performance is found to be excellent at high rate
for GRPCs with the semi-conductive glass and can be used in the very forward of ILD region if the rate exceeds 100 Hz/cm2 in future ILD upgrades
High-Rate GRPC

## Slide 12
10500 ASIC were tested and calibrated using a
dedicated robot that was used by CMS (IPNL, OMEGA)
(ASICs layout : 93% ).
SDHCAL prototype construction
310 PCBs were produced, cabled and tested (IPNL).
They were assembled by sets of six to make 1m2
ASUs
50 detectors were built and assembled with
their electronics into cassettes. Cassettes were tested
by sets of 6 using a cosmic test bench (IPNL).
The mechanical structure was built in CIEMAT.
HV, cooling services were built by UCL, Gent.
Full assembly took place at CERN.
170 DIF(LAPP), 20 DCC(LLR) were built and tested.

## Slide 13
Prototype @TB
TB in 2012, 2014 and 2015 (6 weeks)
Thresholds choice
optimization;
Muons run calibration;
 Pion, electron runs
to study EM and
hadronic showers;
No particle identification detector was used.
Power-Pulsing Triggerless modes

## Slide 14
Data collection
All hits of all sorts are recorded while the power-pulsing is on ( during the spill duration)
Efficiency
Pad multiplicity
Mean : 0.76 hits
RMS : 0.70 hits

## Slide 15
10 GeV pion
10 GeV electron
50 GeV pion
50 GeV electron
X
X
Y
Y
Z
Z
Z
Z
Z
Z
Z
Z
units in cm
Event display
TriggerLess
Power-Pulsed
Colours correspond to the three thresholds: Green (100 fC), Blue (5 pC), Red (15 pC)
Raw data, no treatment except time hit clustering

## Slide 17
Mean number of hits for each threshold versus energy

## Slide 18
Energy estimation
The thresholds weight evolution with the total number of hits obtained by minimizing a χ2
Χ2 = (Ebeam-Erec)2/Ebeam
Erec = α (Ntot) N1 + β(Ntot) N2 + γ(Ntot) N3
N1,N2 and N3 : exclusive number of hits associated to first, second and third threshold.
α, β, γ are quadratic functions of the total number of hits (Ntot)
For instance α = α0 + α1 Ntot +α2 N2tot
Events of September runs corresponding to energies : 5, 10, 30 , 60 and 80 GeV were used to fit the 9 parameters. This represents more than 50 k events.

## Slide 19
Semi-digital improvement with respect to the binary version.
Calice note CAN-037

## Slide 20
SPS-H6
SPS-H6
SPS-H2
SPS-H2

## Slide 21
High-granularity impact
Hough Transform is an example to extract tracks
within hadronic showers and to use them to control
the calorimeter in situ
ρxz = z sin(θ) + x cos(θ)
Excellent agreement with results obtained from direct methods

## Slide 22
Improvement of energy resolution

## Slide 23
Raw data
Pion
Selection
Shower separation
Comparison
E1 – E3 ?
E2 – E4 ?
Overlay
Excellent separation down to 10 cm of distance between 2 close-by h.showers

## Slide 24
Build few very large GRPC detectors (2-3 m2) : gas circulation system, thickness…;
Test the new version of electronics (I2C, roll mode..) ;
Design a new ASU capable to read the large GRPC (up to 3 m2);
Develop a new DIF ( low consumption, reduced size, new functionalities);
Build a small mechanical prototype to host the few large chambers and test it.
Road map in the 2-3 coming years

## Slide 25
New version of the readout electronics
The new version brings improvements on the previous one:
Independent channels and
zero suppression
Independent ASICs (I2C)
Better dynamic range
(up to 50 pC).
successfully tested;
600 ASIC have been produced
ASU
connectors
FPGA
Large enough to embed processor if needed
Power supply
DIF and ASU
Goldcaps to handle power pulsing ?
Current/voltage monitoring
TTC electrical layer
(ADN2814)
WatchDog
Temp
SFP cages
RJ-45 (Data)
Spare I/Os
Clock in/out
Power out
Power in
Micro USB
USB2
External Network chip
RJ-45 (TTC)
Fiber/copper
(future use)
New features in
the DAQ boards
Only one DIF per plane. For the maximum
length plane (1x3m) the DIF will handle
432 HR3 chips;
Slow control through the new HR3 I2C bus;
 Data transmission to DAQ by Ethernet using commercial switches for concentration;
Clock and synchronization by TTC;
Synergy with R&D on fast links R&D of LHC (GBT)
Funded essentially by CIEMAT
New ASU design for large detectors under study

## Slide 26
2 m
1 m
inlet
outlet
Prototype circulation system
New circulation system
Detector improvement : to achieve same performances with very large GRPCs
Mechanical structure : to be built with EBW techniques and to host few large detectors GRPCs

## Slide 27: Conclusion and prospects
-The SDHCAL prototype is the first and up-to-now the unique technological
calorimeter prototype built for ILC future experiments.
-SDHCAL with its fine granularity is an excellent tool to develop and exploit
PFA algorithms;
-Fine granularity is also an excellent tool to study hadronic shower;
-The project has led to several spin-offs (TOMUVOL, CMS,..);
-Work on complete validation of the SDHCAL concept is on-going.
-Adapting the SDHCAL to CEPC, FCCee are also on-going (active cooloing, timing….)