Performance simulation studies for the ALICE TPC GEM Upgrade
Martin Ljunggren on behalf of the ALICE Collaboration
Lund University
- From run 3 of the LHC (2019) and on, an expected Pb-Pb collision rate of 50 kHz is foreseen
- The ALICE Time Projection Chamber (TPC) will be upgraded with Gas Electron Multiplier (GEM) readout to allow continuous operation
- The buildup of positive space charge will cause large distortions to the measured tracks.
- The goal of the simulations is to characterize these distortions.
The ALICE TPC
Distortion in measured r-coordinate for electrons drifting from the middle of the TPC (z=0)

---
Simulation and results
- Simulation:
  - Use HIJING to generate 5.5 TeV Pb-Pb events
  - Simulate track propagation and electron + ion drift with distortions. Distortions are taken into account by solving Poisson's equation and the Langevin equation.
  - The resulting ion distribution is binned in 3D
  - Evolution of space point distortion in a specific point shown to the right:
- Calibration
  - Simulations show that the ideal momentum resolution (without space point distortions) is recovered after corrections
Distortions in a point close to the inner field cage of the TPC (r=100cm, z=0cm) as a function of time
Momentum resolution in the ideal case (left), after a first reconstruction stage (middle) and after a second, more precise, reconstruction stage (right)