## Slide 1: Cylindrical Micromegas An innovative solution for central trackers.
PISA Meeting – elba island
May 2015
Maxence Vandenbroucke – CEA saclay - IRFU

## Slide 2: Overview
Micromegas Principle, Bulk
Cylindrical Micromegas
Large radius resistive cylindrical Micromegas for CLAS12
  Overview
  Performances
  Resistive technology features
Small Radius detectors : The ASACUSA Micromegas Tracker
Future project at an Electron Ion Collider

## Slide 3: Micromegas Principle
~100 mm
thin gap
Fast ions collection

## Slide 4: Bulk Technology (2006)
Embedded of the MicroMesh on the readout electrode
Goal : Make the Production of Micromegas an Industrial process
Robust, Cheap
Simplified and light mechanical structure
Ability to use thin PCBs and produce different shapes (cylindrical detectors !)
Notes: ToDo add transition toward Barrel

## Slide 5: Cylindrical Micromegas
Electric leak test
Segmentation and preparation
Gluing of the side carbon ribs on circular shape
Gluing of additional ribs
Setting drift plane
Gluing of the drift plane

## Slide 6: CLAS12 Central Tracker
CLAS12 experiment at J-LAB
High Rate 10 MHz
High magnetic field (5 T)
Deported electronics
6 Disks after the target (Forward Det.)
  Resistive strips divided in 2 zone inner/outer
  1024 strips, pitch 525 µm
  Dimensions: 430 mm diameter disk with a 50 mm diameter hole at the center
Cylindrical Barrel
  Resistive Detectors
  Phase 1 : 2 Layers (6 Det. Of 120º)
  Phase 2 : 6 Layers (18 Det.)
Notes: ToDo Barrel intro + CLAS12 logo + dream

## Slide 7: CLAS12 Barrel Detectors
“C” Barrel
“Z” Barrel
1152 “C” strips
221 mm radius
Pitch from 0.67 to 0.33 mm
PCB thickness 100 µm, Drift thickness 250 µm
0.3% of X0
Drift Field 2.4kV on 3 mm gap
Resistive strips technology
“C” Barrel
“Z” Barrel
768 “Z” strips
225 mm radius
0.529 mm pitch
PCB thickness 200 µm, Drift thickness 250 µm
0.37% of X0
Drift Field 2.4kV on 3 mm gap
Resistive strips technology
Notes: To do reoder bullets to have symetry

## Slide 8: CLAS12 Barrel : Geometry
How well a self support cylindrical MM hold its shape ?
Minimal mechanical support
3D probing machine measuring points :
  270 points on top (drift side)
  120 points under (readout side)
List of measured points |  |  | 
 | X | Y | Z
PT-Arceau1_1 | -3.588 | 231.995 | -0.005
PT-Arceau1_2 | 28.993 | 231.995 | 33.071
PT-Arceau1_3 | 64.992 | 231.994 | 57.126
…
Mechanical precision up to ~2mm in radius (only one measurement)
Crosscheck using cosmic ray data reconstruction
Notes: Motivation + self supporting + 0.40 % of x0 + “Frist time mm, don’t know

## Slide 9: CLAS12 Barrel : Performances
Z Barrel Efficiency Map
Cosmic rays characterization at Saclay
Barrel efficiency >98% :
Typical event
C Barrel Efficiency Map
Efficiency Plateau
Resistive Barrel Nominal performances :
  Great signal to noise
  Fully efficient
  2500V on drift electrode ok
  ~200µm spatial resolution
  (limited by track resolution)
  ~25ns time resolution

## Slide 10: High current on resistive detectors
Zoom on a part of the CLAS12 Barrel pre-series #2 with thermal cam, with HV on and current of about 300 mA
Happens when a default enters in the amplification gap
Not possible to burn using sparks
Not a barrel related issue, also observed in the forward detectors
Large problem when the current flows over the detector surface to the nearest ground
Solutions :
  No resistive interconnection (ladders)
  Aluminum frame at the gas inlet
  More ground connections
    “C” Barrel detectors had no problem !
  Fixing is possible by filing the area with a drop of polymer
Efficiency Map
without current
with current
position of the noisy strip
position of resistive contacts

## Slide 11: Time resolution
Time Resolution with resistive detectors is ~25ns instead of ~15ns (depending on the conditions)
Inhomogeneities over the detector surface observed
Time Vs Det. X
2D Time distribution
Solutions :
  Electronic parameters optimization (~3ns)
  1D (2D?) corrections under investigation (~5ns)
  Currently under investigation

## Slide 12: CLAS12 Barrel - Status
4 Full scale prototype detectors assembled and tested
“Z” pre-series CLAS12 Detectors :
  CR6Z-1 -> High current, sent back to CERN
  CR6Z-2 -> Fixed ! OK !
“C” pre-series CLAS12 Detectors
  Drift electrode to be changed (production issue)
  CR6C-1 -> missing channels (to be repaired soon) 92% efficiency
  CR6C-2 -> OK !
All problems found a solution and we are ready for production for this summer !
Drift Electrodes not thermally treated

## Slide 13: The ASACUSA Micromegas Tracker
ASACUSA experiment : spectroscopy of anti-H at the Anti-Proton Decelerator (AD) at CERN
Goal : Vertex reconstruction inside the EM trap where the anti-H is produced with ~1cm resolution
Overall thickness of the full system limited to ~2.5cm
4T magnetic field (from -2T to 4T in the active area)
Annihilation rate: ~10-50 kHz
2 Cylindrical layers = 4 MM with 2D readout
Magnet Trap

## Slide 14: The ASACUSA Micromegas Tracker
Phase I : Half Cylinder Instrumented (2 MM)
2D metallic Micromegas “C” – “Z” pattern
Internal Layer RMIN : 60cm x 85 mm radius
External Layer RMAX : 60cm x 95 mm radius
Intermediate support pillars
DREAM electronics using 2m Hitachi cables from CLAS12 R&D
3D printed structure (white)
Cutout flaps for a better deformation at the connector level
Gas distribution through aluminum frame
0.87mm pitch: 250 longitudinal Z strips, 500 circulars C strips
“C” strip
“Z” strip
Readout pattern (top)
Readout pattern (bot)

## Slide 15: The ASACUSA Micromegas Tracker
Characterization at Saclay :
6 Months of smooth data taking ! (technical paper submitted)
Effect of the magnetic field (80º Lorentz angle at low drift field)
B Field ON
B Field OFF
Notes: Small plateau – Review of scientific instruments – pictures todo - Can’t show physics data - > micro tpc

## Slide 16: AMT – MicroTPC Algorithm
Resolution Vs Track Angle
Antiproton distribution
(calibration data)
Filtered distribution
Fitted signal in the drift space
The MicroTPC algorithm uses the time information on multi-strip clusters to extrapolate the track angle :
MicroTPC algo on anti-p data :
Track angle from a single layer barrel
time
space
µTPC
Cut
Notes: TO REDO WHILE SPPEAKING 3mm drift, only only one layer

## Slide 17: Barrel Micromegas for an Electron-Ion Collider (EIC)
A solution based on a TPC + Barrel detectors is considered for an EIC detector
Internal (~20cm) and external (~2m radius) 2D cylindrical layers
Establish <100 µm spatial resolution in a 3T field
Deliver reliable “vector” measurement
Fast measurement layer between MAPS and the TPC
Minimized material budget
Internal layers
External layers
EIC GEMs : See B. Surrow Poster
Notes: Bernd –posrter’s

## Slide 18: Outlook
Large Cylindrical Micromegas has been developed thanks to the bulk technology for the CLAS12 experiment after a long R&D
Cylindrical Micromegas allows fast and precise measurements on light weight layers
4 full scale CLAS12 Barrels using resistive technology have been produced and tested
Pre-series production issues understood, ready for production !
Great performances measured on the barrel CLAS12 detectors
  Full efficiency
  0.3% of X0
  Below 200µm spatial resolution
  20 to 25 ns time resolution in Ar/iC4H10 95/5
First use of small radius cylindrical detectors in the ASACUSA experiment
4x2D AMT operational det. produced, 2 used for data taking
Vector measurements with a single layer successfully tested in experimental conditions
R&D for an EIC started for a mixed Si/TPC/Cylindrical MM tracker

## Slide 19: CLAS12 TEAM AT SACLAY
D. Attie, S. Aune, J. Giraud, R. Granelli, C. Lahonde-Hamdoun, I. Mandjavidze, O. Meunier, S. Procureur, M. Riallot, J-Y Rousse, F. Sabatie, M. Vandenbroucke

## Slide 20: Spares

## Slide 21: Detector characterization at Saclay : The Cosmic Test Bench
to the
trigger
Coincidence
module
Scintillator
Top reference
detectors
Prototype
Down reference
detectors
Setup to characterize in 2D the prototypes
Tracking detectors : MultiGen 2D x4 (8 Connectors)
Fully equipped with DREAM FEE
24 Positive + 24 Negative HV
Gas mixing system + pre-mixed bottles
Trigger control module, trigger time resolution below 3 ns, Projected track resolution of ~100 µm
6 Hz trigger rate, >90% track reconstruction efficiency
1h to get one efficiency point

## Slide 22: The ASACUSA Experiment
Antimatter spectroscopy at CERN
ASACUSA Micromegas Tracker

## Slide 23: CLAS12 Operating Conditions

## Slide 24: Material Budget

## Slide 25: CLAS12 Barrel : Geometry
OUTER (4 ribs)
R= 211.3 +/- 1.8
INNER(4 ribs)
R= 207.3+/- 2.1
=> Mechanical precision up to ~2mm in radius (only one measurements)
Using cosmic ray data reconstruction
Notes: Maybe suppress X0 to avoid Q?

## Slide 26: Forward disk for CLAS12: issue with resistive ladders
2 pre-production detector tested, One not ok :
  High current due to a contact in the active area (can’t burn it with sparks)
  Large impacted zone due to ladders
  Drift electrode glued
Production detectors
  No ladders
  Re-openable design with screws
Before the current appaered
With current

## Slide 27
Some defects observed with the Mitutoyo along a noisy strip.
Zoom on a part of the CLAS12 Barrel pre-series #2 with thermal cam, with HV on and current of about 300 mA
Investigation of the cause of the short
The defect has not been identified
Observation of the current with infra-red camera made

## Slide 28: List of detectors tested
10 CLAS12 & M-Cube detectors were tested in our cosmic bench
Detector | experiment | resistive | Active area | manufacturer | year | Drift frame
Forward prototype | CLAS12 | Hand, no ladder | R=20 cm | ELVIA | 2013 | Epoxy
Forward preserie | CLAS12 | Screen printing, ladders every 2 cm | R=18.5 cm | CERN | 2014 | ?
Barrel preserie (x2) | CLAS12 | Screen printing, ladders every 8 cm | 45x37 cm² | CERN | 2014 | Carbon ribs
Forward Tagger prototype | CLAS12 | no | R=14.6 cm | CERN | 2013 | Epoxy
MultiGen 2D (4x) | M-Cube | Screen printing with ladders | 50x50 cm² | CERN | 2014 | Aluminum
MultiGen 2D | M-Cube | Screen printing with ladders | 50x50 cm² | CERN+ELVIA | 2014 | Aluminum
→ 9 resistive + 1 non resistive
→ Detectors without current between resistive strips and mesh are perfectly fine…
talk by S. Bouteille
M-Cube