## Slide 1: The drift chamber with a new type of straws for operation in vacuum
Yu. POTREBENIKOV on behalf of CERN-JINR straw working group of the NA62 Collaboration
NA62 main goal: measuring K+→p+nn,
~100 events with 10% precision
in 3 year of data taking
BR x 1010 | SM prediction | Experiment
K+ → p+nn | 0.781 ± 0.075 ± 0.029 | 1.73 ± 1.10
KL → p0nn | 0.243 ± 0.039 ± 0.006 | < 260
Spatial resolution 130 mm per coordinate, 80 mm per space point
≤ 0.5% of a radiation length (X0) for each chamber
Working in vacuum (P=10-5 mbar) with minimum gas load for the vacuum system 10-1 mbar l/s
Operation in high rate environment (up to 500 kHz/channel) with a mean rate 60 kHz/channel
signal signature : one K+ track, one p+ track
kinematic variable : m2miss = (PK – Pp )2
momentum measurement + particle
identification + veto
DPp/Pp ≤ 1%; DqKp ≤ 60 mrad
Region I
Region II
Region I: 0 < m2miss < 0.01 GeV2/c4
Region II: 0.026 < m2miss < 0.068 GeV2/c4
Design of straw
view
Straw chamber (2 straw modules)
2 independent pairs of layers, each for registration of min 1 hit of particle with up to 3o angle;
< 15% more material than in 2 closed layers (< 5% for straws with effective Ø= 9.4 mm);
All tracks with 2 or more hits in effective (Ø= 9.4 mm) straw volume;
Up to 35% track with 3 hits in a view
Design
Straw module
Chamber

## Slide 2: New type of straws for operation in vacuum
36 mm PET
20 nm Au
50 nm Cu
Over 8000 straws have been produced
(more than 20 km of ultrasonic welded tubes).
97.58% straws are good after all quality tests
  2.7 m long tube with a diameter of 9.8 mm
  The base material is Poly Ethylene Terephthalate (PET) or Mylar (Hostaphan), 36 mm thickness
Straw module assembling
Resolution
of the +0 peak
5*10-3 GeV2/c4
( vs. 3*10-3 GeV2/c4
in MC)
module sealing;
straw support by 2 spacers;
straw gluing with a pretension 1.8 kg;
wire crimping with 90 g tension;
electrical connection (HV and signal, 16 straw granularity) by flexible circuit board (WEB);
gas manifold covers by front-end electronics board – 2 CARIOCA+ALTERA chips;
2 straw read-out board (SRB) per module
straw position test by optical rangefinder – ±100 mm from the nominal (17.6 mm)
distance between straws;
straw pretension test - 1.6 ÷ 2.1 kg;
wire position test by “visible light” -
±35 mm from the nominal position;
vacuum test - < 0.8 mbar l/min CO2 per module;
gas used - Ar(70%) CO2(30%);
and test
Integration of the straw chamber Into NA62 setup
First results
Hit time distribution
m2miss = (PK – Pp )2
+0
3
mn
Kaon selected in time with CHOD and Spectrometer track + geometrical acceptance
Vertex in fiducial region
15 < P < 35 GeV/c
Preliminary