## Slide 1
The RD53 effort towards the development of a 65 nm CMOS pixel readout chip for extreme data rates and radiation environments
RD53 was organized to tackle the extreme and diverse challenges associated with the design of pixel readout chips for the innermost layers of particle trackers at future high energy physics experiments (LHC – phase II upgrade of ATLAS and CMS, CLIC)
Valerio Re (INFN-Pavia) on behalf of the RD53 collaboratios
ATLAS and CMS Phase 2
Pixel Detector Requirements:
Small pixels: 50x50 mm2 (or 25x100 mm2)
Large chips: > 2cm x 2cm ( ~1 billion transistors)
Hit rates: ~3 GHz/cm2
Radiation: 1 Grad, 1016 n/cm2 (unprecedented)
Trigger: 1 MHz, 10 ms (~100x buffering and readout)
Total power budget: ≤ 1 W/cm2
Minimum threshold: 1000 electrons
RD53 institutions
    ATLAS: CERN, Bonn, CPPM, LBNL, LPNHE Paris, Milano, NIKHEF, New Mexico, Prague, RAL, UC Santa Cruz.
    CMS: Bari, Bergamo-Pavia, CERN, Fermilab, Padova, Perugia, Pisa, PSI, RAL, Sevilla, Torino.

## Slide 2
95% digital, Charge digitization
~256k pixel channels per chip
Pixel regions with buffering
Data compression in End Of Column
Chip must work with large pixels for outer layers
Global architecture of the chip
New challenges of the RD53 collaboration
Detailed understanding of radiation effects in 65 nm
Development of a simulation and verification framework with realistic hit generation
Design and test of small/medium size pixel readout chip prototypes
Design of a shared rad-hard IPs library
Design, characterization and test beam of a full sized pixel array chip > 1cm2 from a common engineering run
RD53 Goals
65 nm CMOS is the candidate technology to address the RD53 requirements for the ATLAS/CMS pixel readout chip