## Slide 1: Tracking software of the BESIII drift chamber
Linghui WU
For the BESIII MDC software group

## Slide 2: Outline
Introduction
Tracking algorithms
  PAT algorithm
  TSF algorithm
  CurlFinder algorithm
  Track fitting with Kalman filter
Tracking efficiency
Alignment
Summary

## Slide 3: Introduction
2.6m long cylindrical chamber
It consists of an inner chamber and an outer chamber
With an inner radius of 59mm and an outer radius of 810mm
Filled with He/C3H8(60/40)

## Slide 4
Inner chamber
Outer chamber
Sense wires:
  f25mm gold-plated tungsten
  at a potential of 2100V for the inner chamber and 2200V for the outer chamber
Field wires:
  f110mm gold-plated aluminum
  at ground

## Slide 5: Cell geometry
Square cell
6796 sense wires and 21884 field wires.
The average half-cell size is 6mm for the inner chamber and 8.1mm for the outer chamber
Half cell staggering to resolve the left-right ambiguity
12 or 16.2 mm

## Slide 6: Layer Configuration
43 sense layers
  The inner most 8 layers are located in the inner chamber and the other 35 layer are in the outer chamber.
Layer | Number of cells per layer | type | Stereo angle（degree）
1 － 4 | 40/44/48/56 | stereo (-) | 2.9 ~ 3.3
5 － 8 | 64/72/80/80 | stereo (+) | 3.4 ~ 3.9
9 － 20 | 76/88/100/112/128/140 | axial | —
21 － 24 | 160 | stereo(-) | 2.4 ~ 2.7
25 － 28 | 176 | stereo(+) | 2.7 ~ 3.1
29 － 32 | 208 | stereo(-) | 3.0 ~ 3.3
33 － 36 | 240 | stereo(+) | 3.3 ~ 3.6
37 － 40 | 256 | axial | —
41 － 43 | 288 | axial | —

## Slide 7: Flow diagram of reconstruction
MdcFastTrkAlg
EsTimeAlg
Track finding
(PAT/TSF/CurlFinder)
Track fit
(KalFitAlg)
MdcDedxAlg
Track
extrapolation
&
matching
TofRec
EmcRec
MucRecAlg

## Slide 8: Track parameters
dr
  Signed distance in x-y plane from the pivot to the helix
f0
  Azimuth angle of the Poca (point of closest approach in the x-y plane)
k
  q/Pt
dz
  z position of the Poca
tanl
  Tangent of the dip angle

## Slide 9: Tracking algorithms
PAT algorithm
  Based on template matching
TSF algorithm
  Conformal transformation
CurlFinder algorithm
  For low momentum tracks
Track fitting with Kalman filter

## Slide 10: PAT algorithm
Read MDC raw hits
Find segments in super layers based on template matching
Combine axial segments to circle
Track fit in x-y plane
Combine stereo segments
Helix track fit

## Slide 11: Segment Finding Method
Tracking in the MDC is based on segments
Search for patterns in the super layer
4
3
2
1
0
7
6
5
1
0
1
0
1
0
0
1
0
1
2
3
4
5
6
7
Pattern No.0
One segment pattern
Cells for pattern
(2,0)
(2,1)
(2,2)
(2,3)
(2,4)
(2,5)
(1,0)
(1,1)
(1,2)
(1,3)
(1,4)
(1,5)
(3,0)
(3,1)
(3,2)
(3,3)
(3,4)
(3,5)
(0,0)
(0,1)
(0,2)
(0,3)
(0,4)
(0,5)
clockwise
We have 8 4-hit patterns
and 20 3-hit patterns
An example of the pattern

## Slide 12: 4-hit patterns
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
00101101
01010101
10010101=0225
01001101
10010110
01010110
01001110
00101110

## Slide 13: Combination of segments
Link axial segments
Link stereo segments

## Slide 14: Track fit
Least squares fitting without consideration of NUMF, multiple scattering, energy loss
dmeas is the measured drift distance
dtrack i.e. doca, distance of closest approach

## Slide 15: TSF algorithm

## Slide 16: Conformal transformation
A hit position (x, y) in x-y plane is transformed into a position (X, Y) in the conformal plane.
  X = 2x/(x2+y2), Y = 2y/(x2+y2)
A circle which passes through the origin (0, 0) is transformed into a line.
  xcX + ycY = 1
  (xc, yc) is the center of the circle
A circle which does not pass through the origin in x-y plane is transformed into a new circle which still does not pass through the origin in the conformal plane.

## Slide 17: Track segment finding
If the hit belongs to the track, its drift circle in the conformal plane is tangent to the line of the track
Left-right ambiguity is kept after conformal transformation
Require that at least 3 layer are fired in each super layer
Patterns
Four-layer pattern in the conformal plane
Four candidates of track segment
The best candidate after matching the middle layers

## Slide 18: CurlFinder algorithm
An algorithm for low momentum track finding
Super layer | Stereo/ axial | Radius (cm) | pT (MeV/c)
1 | stereo | 11.5 | 17
2 | stereo | 16.2 | 24
3 | axial | 24.6 | 37
4 | axial | 31.0 | 47
5 | axial | 37.5 | 56
6 | stereo | 44.8 | 67
7 | stereo | 51.4 | 77
8 | stereo | 57.9 | 87
9 | stereo | 64.2 | 96
10 | axial | 71.6 | 107
11 | axial | 77.1 | 116
Outer tube | -- | 81.0 | 122

## Slide 19: Flow diagram

## Slide 20: Axial segment finding
More than one hit in the same layer
Find consecutive hits in each axial super layer
  Fired cell  find neighbor  find neighbor’s neighbor …
Definition of neighbor

## Slide 21: 3-D track finding
Find stereo hits near the circle
Line fit in s-z plane
Helix fitting

## Slide 22: Track fitting with Kalman Filter
A standard track fitting with Kalman Filter method
Initial track parameters and hits from track finding
Track parameters obtained by in iterations: …predictionfilter with a hitupdate…
Considered effects: nonuniform magnetic field, energy loss and multiple scattering
5 hypothesis: e, m, p, K, p
Inwards filter: provide track parameters at IP
Outwards filter: provide track parameters seed for extrapolation (expected TOF, reconstruction with TOF/EMC/MUC)

## Slide 23: Momentum distribution
sP=11.3MeV/c
sP=28MeV/c
Track finding
Kalman fitting

## Slide 24: BESIII Drift Chamber Tracking
Runge-Kutta fitting
Kalman fitting
MdcPatRec
  limited by segment pattern coverage, rec. for high pt tracks (PT > 250MeV/c)
MdcTsfRec
  PT : 120~250MeV/c
CurlFinder
  PT <120MeV
PAT
TSF
Curlfinder

## Slide 25: Tracking efficiency with PT
proton
anti-proton
J/psi  pppp

## Slide 26: Tracking efficiency with PT
p+
p-
J/psi  pppp

## Slide 27: Tracking efficiency with cosq
proton
anti-proton
J/psi  pppp

## Slide 28: Tracking efficiency with cosq
p+
p-
J/psi  pppp

## Slide 29: Alignment
Alignment with tracks is the only possible strategy to estimate positions and orientations of components of a track detector with sufficiently high precision
16 independent components in total.
  Inner chamber (×2)
  Ring ×6 (×2)
  big endplate (×2)
For each component, 3 alignment
parameters (dx, dy, qz) are considered
Methods:
  Residual fit
  Millepede Matrix method
dx
dy
qz

## Slide 30: Pre-alignment
Alignment method: Residual fit
Tracking algorithm: PAT algorithm
Big endplates are fixed to BESIII mechanical measurements
Use cosmic tracks fitted by hits in the outer sections to align the inner and stepped sections

## Slide 31
Translation in x causes dependence of residual on sinφ
Translation in y causes dependence of residual on cosφ

## Slide 32
Rotation in z causes shift of residuals which are independent of φ
So rmean = c0 -c1∙sinφ + c2∙cosφ
where
  rmean is the mean value of residuals
  c1 and c2 are estimated values of δx and δy, respectively
  θz = c0 / Rlayer
    ( Rlayer is the radius of the layer )
Misalignment effects (MC)

## Slide 33
Before alignment
After alignment
Residual vs f
(The first stepped section in the east)
Results of the cosmic-ray

## Slide 34: Results (dimu in May 2012)
P vs j
P vs cosq
Before alignment
After pre-alignment

## Slide 35: Precise alignment
In order to improve the alignment of MDC sub-endplates, Millepede matrix method is introduced.
  Global fit: simultaneous fit of all alignment and track parameters
Big endplates are free
Data sets: dimu + cosmic rays

## Slide 36: Results (dimu in May 2012)
P vs j
P vs cosq
Pre-alignment
Precise alignment

## Slide 37: Resolutions
m+m- invariant mass
sJ/psi = 16.74 ±0.01 MeV
M(m+m-)(GeV/c2)
Momentum distribution
sP= 12.13 ±0.01 MeV/c
Dimu from J/psi in 2012

## Slide 38: Spatial resolution (Bhabha)
Residual distribution
(from XYZ in 2014)
Data | Spatial resolution (mm)
Before HV optimization (J/psi in 2009) | 123
After HV optimization (XYZ in 2014) | 115

## Slide 39: Momentum resolution (Bhabha)
From XYZ data in 2014
no serious misalignment
sP = 18.5MeV/c @ 2.3GeV/c
P vs f
P vs q
Run35320

## Slide 40: Summary
MDC tracking Algorithms
  Track finding
    High momentum: PAT, TSF (tracking efficiency 98~99%)
    Low momentum: CurlFinder
  Track fitting
    Kalman filter
Alignment
  Pre-alignment: residual fit using cosmic tracks
  Precise alignment: Millepede matrix method using cosmic and dimu tracks
Performance of Bhabha events (from XYZ in 2014)
  Spatial resolution: 115mm
  Momentum resolution: sP = 18.5MeV/c @ 2.3GeV/c