## Slide 1: Progress of CGEM software
Yue GUO, Jingran HU,
Liangliang WANG, Linghui WU

## Slide 2: Outline
Garfield Simulation
Reconstruction
  CGEM cluster reconstruction
  Track fit
Summary

## Slide 3: Garfield simulation
  Motivation
    To understand the drift property in magnetic field and implement more realistic digitization model
Use Garfield++
Construct the detector
and calculate the field
map using Ansys

## Slide 4: CGEM of a hexagonal geometry
The basic cell,which is used to construct the whole detector by periodic arrangement in X and Y

## Slide 5: Electric field from Garfield
3mm
2mm
2mm
2mm
-3190V
-2740V
-2350V
-2050V
-1670V
0
Cathode
Anode
GEM3
GEM2
GEM1
Drift
Transfer2
Transfer1
Induction
-1370V
-1000V
A typical voltage from 300 to 500V is applied between the two sides of the foil.
The field reaches 100kV/cm in the hole.
The expected gain should be around 10^4.
-0.5
cathode
-0.2
gem-1
0
gem-2
0.2
gem-3
0.4
anode

## Slide 6: Simulation of the avalanche
AvalancheMicroscopic
  Accurate simulations of electron trajectories in small-scale structures
  Detailed calculations of ionization and excitation processes
  Transporting electrons on a microscopic level
  Time consuming
AvalancheMC
  Calculate Ds=vdDt in the direction of Vd at the local field
  A random diffusion step is sampled from Gaussian distributions
  Time consuming but Faster than AvalancheMicroscopic

## Slide 7: AvalancheMicroscopic
Get gain about 103
Set the limit of size of an electron avalanche to 1000
Time consuming
Need more study

## Slide 8: AvalancheMC
Without magnetic field
Get the gain about 104
Half of generated electrons are absorbed by the 3rd GEM

## Slide 10: Reconstruction flow for CGEM + DC
Cluster reconstruction for CGEM: fired strips  cluster (preliminary algorithm finished)
Track segment finding in CGEM (not started)
Track segment finding in DC (exist)
Combination of track segments (need modification)
Global fit (need modification)
Kalman filter (in progress)

## Slide 11: Cluster reconstruction for CGEM
Search for continuous fired X strips
Search for continuous fired V strips
Intersections
as clusters
Charge weighted geometrical center
Correction to the position on track
Package: CgemClusterCreate
rec_x
rec_v

## Slide 12: Variables in RecCgemCluster
RecCgemCluster |  | 
type | item | Description
int | m_layered | ID of CGEM Layer
int | m_sheeted | ID of CGEM sheet
int | m_flag | Type of cluster: 0-X, 1-V, 2-XV
double | m_energydeposit | Total energy deposit
double | m_recphi | X position (phi)
doulbe | m_recv | V position

## Slide 13: Distribution of number of fired strips in each cluster
single muon MC sample 1.0 GeV |cosq|<0.93
Average number of strips that each cluster contains is 2~3 in either direction
Number of fired X strips
Number of fired V strips

## Slide 14
Resolution for 2D readout in drift layer
σρ= 134.9μm
σv= 146.7μm
Xrec – Xtruth (mm)
Vrec – Vtruth (mm)

## Slide 15: Track fit using Kalman filter
Obtain track parameters and covariance matrix under different hypothesis (e,μ,π,K, p)
Reconstructed tracks (with MDC outer chamber hits ) as input
Use MDC hits and CGEM clusters to update the track parameters from the outermost point to the origin
Take into Account the multiple scattering, energy loss and NUMF

## Slide 16: Difference between the fit and truth
zfit – ztruth (cm)
phifit – phitruth (rad)
z
phi

## Slide 17: Momentum resolution
1GeV/c m-
pfit – ptruth (GeV/c)
1GeV/c m+
pfit – ptruth (GeV/c)

## Slide 18: Summary
Garfield simulation
  Get some preliminary results
  CPU consuming is a big problem
Reconstruction
  A preliminary cluster reconstruction package is developed
  The Kalman filter based track fitting with full simulation of CGEM + outer DC is in progress

## Slide 19: Backup

## Slide 20
Data
e-
Data
e+
Drift time (ns)
Drift time distribution
Garfield
e-
Garfield
e+
Drift distance (mm)

## Slide 21: X-T relations of MDC
Drift behavior from Garfield simulation are comparable with data
Data
Garfield sim