## Slide 1
Introduction to the
String
DAQ/Read-out
part 2
Tommaso Chiarusi
Carmelo Pellegrino
INFN - Sezione di Bologna
KM3NeT-Italy Collaboration Meeting |
Catania, November 26-27 2014 |
Notes: Before to start talking about the Trigger and data acquisition system, I’ll introduce the physics case, the neutrino telescopes and in particular km3net. The aim of a neutrino telescope is to study high energy cosmic events by revealing neutrinos.

## Slide 2: Trigger and Data Acquisition System (TriDAS)
Notes: That’s the solution we adopted: here is sketched the data acquisition system

## Slide 3: DataQueue
The DataQueue (DQ) is the software component of the KM3NeT-EU TriDAS which provides the data aggregation and distribution layer for both acoustic and optical data.
Read-out of the KM3NeT-EU data frames (UDP) from a predefined number of CLBs
Reassembling of the Time Slice (TS, which is compiled by the off-shore electronics)
Distribution of the TSs to the proper DataFilter

## Slide 4: Two flavours
Route the data collected from all DQs referring to a precise Time Slice to the very same oDF.
Acoustic data must be sent in a continuous stream, addressing all data from one DQ to a single aDF.
Optical World
Acoustic World

## Slide 5: Optical DataFilter
The main task of the optical DataFilter (oDF) is to reduce the data-stream coming from the DOMs' PMTs by selecting events that are interesting for physics analyses.
Apply algorithms that find space-time correlations between hits.
Keep a buffer of raw data for dumping in case of an external alert (i.e. GRB alert)
Send data to the Data Writer

## Slide 6: Algorithms serving Physics
Motivation | T-Trigger | Simple Causality Trigger | Sky Scan Trigger | Tracking | Stack-Analysis | Vertex / Inertia
muon | ✔ | ✔ | ✔ | ✔ | ✔ | ✔
showers | ✔ | ✔ | ✔ | ✔ |  | ✔
slowly moving particles | ✔ | ✔ | ✔ | ✔ |  | ✔
sources | ✔ |  |  | ✔ | ✔ | ✔
But other algorithms are under development...

## Slide 7: DataWriter
The DataWriter collects the filtered data coming from the various oDFs and performs write operation on permanent storage media in a ROOT compatible data format.

## Slide 8: Acoustic DataFilter
The acoustic DataFilter (aDF) performs online calculation of the Time-Of-Arrival (TOA) of the acoustic signals emitted by the ground-based acoustic beacon array.
Calculate the TOA using the data from all the sensors (piezo + hydrophone) collected on-shore by a DQ
Send data directly to the DB Writer

## Slide 9: Control Unit
The Control Unit (CU) is composed of several elements:
Detector Manager (DM):
  Perform complete configuration of the CLBs (PMT HV, instruments, etc…)
  Record all parameters and the occurring events
  Provide online monitoring of sensible parameters/measurements
Tridas Manager (TM):
  Operate the TriDAS computing farm
SC Gate:
  Read-out of the SlowControl data
DB Writer
  Perform write operation to the remote Data Base
Slides from C. Bozza

## Slide 10: DM GUI
Slides from C. Bozza

## Slide 11: Control Unit features
High flexibility
Customizable GUI via HTML files
Easy read-out of the parameters via HTTP/JSON
  http://<mysrv>:1302/mon/clb/outparams/pmt_threshold@/1/1/2
Manual mode (authorization required)
    http://<mysrv>:1302/override?inp=pmt_highvolt&inv=-1500&du=1&dom=2&pos=3&scope=0
Security
Authentication required
  Local Authentication Provider + DBInterface
«Jolly token» to be used in test benches
  To be configured at Detector Manager start-up
Slides from C. Bozza

## Slide 12: DAQ Kit
CLBSwissKnife, which allows to have fast debugging, monitoring and raw data dump on file (still developing, but already usable and very helpful);
DAQ chain, i.e. DataQueue + DataFilter + DataWriter;
ROyWeb, which is the powerful, web-based, monitoring server;
Detector Manager (still developing, see C. Bozza’s talk) and JavaGUI, which allow the operation of the CLB.
Please, find the documentation about how to install and use here:
http://wiki.km3net.de/index.php/CLB_Swiss_Knife
http://wiki.km3net.de/index.php/Jpp
https://github.com/tamasgal/royweb
http://wiki.km3net.de/index.php/DAQ_kit_for_integration_tests

## Slide 13: Thank you for your attention!