## Slide 1
  Benno List
  DESY –IPP–
  XVII Roma Tre Topical Seminar on Subnuclear Physics: The Higgs potential and physics at future colliders.
  Dec 10, 2014
The International Linear Collider

## Slide 2: The International Linear Collider
A linear e+e- collider with 500GeV CM energy, upgradeable to 1TeV
Acceleration with superconducting RF cavities
Polarized beams
Designed by a worldwide collaboration
About 31km long
For more information: www.linearcollider.org

## Slide 3: Running Scenarios
Joint Parameters WG (Physics/Detectors and Machine) studies many running scenarios -> work in progress
Investigated time evolution of physics results
~25 years of running before 1TeV upgrade, incl. lumi upgrades
Baseline: Start with “500GeV” machine (no long 250GeV run)
Example: “D500” scenario: 0.5ab-1 @250 and 300, 5.5ab-1 @ 500GeV

## Slide 4: Running Scenarios
Joint Parameters WG (Physics/Detectors and Machine) studies many running scenarios -> work in progress
Investigated time evolution of physics results
~25 years of running before 1TeV upgrade, incl. lumi upgrades
Baseline: Start with “500GeV” machine (no long 250GeV run)
Example: “D500” scenario: 0.5ab-1 @250 and 300, 5.5ab-1 @ 500GeV

## Slide 5: Three Questions
Why?
How?
When?

## Slide 6: WHY
… international?
… linear?
… e+e- collider?  physics case
… superconducting?  how?

## Slide 7: Why International?
ILC is too large for a single country, or even a single region
New paradigm:
No central host lab
Truly global cooperation

## Slide 8: Why Linear?
N. Walker, ICHEP 2014, Valencia
Circular e+/e- accelerator: Limiting factor is energy loss by synchrotron radiation
Synchrotron radiation power: P ∝ E4 / R if circumference ∝ E2 -> cost scales as ∝ E2
  For a linear accelerator: cost ∝ E
  Increasing the energy: Just make tunnel longer!
  Beyond the top pair threshold, there are only linear colliders!

## Slide 9: Why an e+e- Collider?
pp and e+e- colliders are complementary, we need both:
  Energy reach and precision
  Strong and electroweak interactions
e+e- strong points:
  Pointlike interaction
  No debris from witness quarks
  Known energy and polarization of initial state
  Flavour democracy: no bias towards up/down, i.e. proton constituent flavours

## Slide 10: Why an e+e- Collider?
To measure the Higgs properties
To measure the Top properties
To constrain SUSY / BSM by precision measurements
To look for new particles: Discovery potential is complementary to LHC, not inferior

## Slide 11: Why a Higgs Factory?
Establish the Higgs mechanism:
  Measure the branching ratios and absolute width model independently  recoil mass method: e+e-  Zh  𝓁+𝓁- X  Includes invisible decays!
  Measure mass: input to branching ratio prediction
  Measure Top-Higgs coupling in e+e-  tth
  Measure Higgs self-coupling: e+e- Zhh – needs energies >= 500 GeV
  Measure CP quantum numbers
Le Diberder et al, arXiv:1210.0202 (2012).

## Slide 12: Why a Higgs Factory?
Establish the Higgs mechanism:
  Measure the branching ratios and absolute width model independently  recoil mass method: e+e-  Zh  𝓁+𝓁- X  Includes invisible decays!
  Measure mass: input to branching ratio prediction
  Measure Top-Higgs coupling in e+e-  tth
  Measure Higgs self-coupling: e+e- Zhh – needs energies >= 500 GeV
  Measure CP quantum numbers
Quantum
numbers
Le Diberder et al, arXiv:1210.0202 (2012).
Mass and Zh coupling
Branching Ratios

## Slide 13: Higgs Couplings: SM or other Higgs?
ILC 250: Lumi 417 fb-1, sqrt(s) = 250 GeV
ILC 500: Lumi 833 fb-1, sqrt(s) = 500 GeV
ILC 250up: Lumi 1920 fb-1, sqrt(s) = 250 GeV
ILC 500up: Lumi 2670 fb-1, sqrt(s) = 500 GeV
ILC 1000up: Lumi 4170 fb-1, sqrt(s) = 1 TeV
Measure couplings directly, model independent, and separately!
Standard Model

## Slide 14: Higgs Couplings: SM or other Higgs?
ILC 250: Lumi 417 fb-1, sqrt(s) = 250 GeV
ILC 500: Lumi 833 fb-1, sqrt(s) = 500 GeV
ILC 250up: Lumi 1920 fb-1, sqrt(s) = 250 GeV
ILC 500up: Lumi 2670 fb-1, sqrt(s) = 500 GeV
ILC 1000up: Lumi 4170 fb-1, sqrt(s) = 1 TeV
Measure couplings directly, model independent, and separately!
Standard Model
Supersymmetry
(MSSM)

## Slide 15: Higgs Couplings: SM or other Higgs?
ILC 250: Lumi 417 fb-1, sqrt(s) = 250 GeV
ILC 500: Lumi 833 fb-1, sqrt(s) = 500 GeV
ILC 250up: Lumi 1920 fb-1, sqrt(s) = 250 GeV
ILC 500up: Lumi 2670 fb-1, sqrt(s) = 500 GeV
ILC 1000up: Lumi 4170 fb-1, sqrt(s) = 1 TeV
Measure couplings directly, model independent, and separately!
Standard Model
Supersymmetry
(MSSM)
Composite Higgs
(MCHM5)

## Slide 16: Why top physics after LHC?
Top mass: Fundamental SM parameter, leading contribution to radiative corrections
Threshold scan measures mass in a theoretically very clean way  gets rid of QCD uncertainties (~0.5 GeV)
Input for radiative correction measurements!
Top performance:
Mass*: 27MeV (0.019%)
Width: 22MeV (1.7%)
Seidel et al., EPJ C73(2013)2530

## Slide 17: Interesting Energies
Higgs recoil: 250GeV
Higgs and tt threshold: 350 GeV
Htt coupling, Higgs self coupling: ≥ 500 GeV – 1000 GeV
⇒ Higgs + Top provide physics case for machine with initial ~500 – 550GeV energy reach → the ILC!

## Slide 18: Energy Reach
Htt coupling has a very sharp threshold at 475GeV
Need to reach >=500GeV with high confidence
A machine that delivers 500GeV at 95%CL can most probably reach 550GeV or more (may require some funds though…)
Discussions about performance reserve are ongoing: stay tuned

## Slide 19: Why continue precision physics?
Radiative corrections gave us
  the Top mass before the Top discovery
  bounds for the Higgs mass before the Higgs discovery
With known Top and Higgs masses, we constrain whatever lies beyond the SM!

## Slide 20: ILC Precision: Gfitter Projection
Gfitter group, EPJC 74(2014)9.

## Slide 21: ILC Precision: Gfitter Projection
Gfitter group, EPJC 74(2014)9.

## Slide 22: Beyond the Standard Model?
Cahill-Rowley, Hewett, Rizzo
Dark Matter: Wino / Higgsino-like
pMSSM with low fine-tuning
Models with small NLSP/LSP mass diff.
ILC 500 GeV
ILC 1 TeV
Berggren et al., EPJ C73 (2013) 2660

## Slide 23: Beyond the Standard Model?
Cahill-Rowley, Hewett, Rizzo
Dark Matter: Wino / Higgsino-like
pMSSM with low fine-tuning
Models with small NLSP/LSP mass diff.
ILC 500 GeV
ILC 1 TeV
Berggren et al., EPJ C73 (2013) 2660
Plenty to do, even after HL-LHC!

## Slide 24: Why Superconducting?
Linear accelerator: Accelerate electrons in a long string of Rfcavities
Gradient: 31.5MV/m  need 15.8km for 500GeV!
For given total power (electricity bill!), luminosity proportional to efficiency
ILC: ~160MW @ 500GeV
Superconducting cavities maximise RF-to-beam efficiency
http://www.supraconductivite.fr/media/ images/Applications/image037.png
RF efficiency
RF power

## Slide 25: HOW
… will it look like?
… can one get the energy?  Superconducting RF technology
… can one get the luminosity?  low emittance beams, final focus
… can one do measurements?  the experiments
… much will it cost?

## Slide 26: How will the ILC look like?
200-500 GeV Ecm e+e- collider L ~2×1034 cm-2s-1
Superconducting “TESLA” Technology
30km long main tunnel
  21km Main Linac
  4.5km interaction region
Positron production from undulator radiation (polarized source!)
3.2km central damping ring
14mrad crossing angle

## Slide 27: How to get the energy
Parameter | Value
Av. field gradient | 31.5 MV/m
Length | 1.3026 m
Frequency | 1.3 GHz
Quality factor Q0 | > 1010
# 9-cell cavities | 16024
# cryomodules | 1855
1.3m
Superconducting “TESLA” Cavities

## Slide 28: “ILC-Type” Cryomodules around the World
DESY FLASH: in operation for 15 years!
100 Cryomodules for European XFEL – installation has started
35 cryomodules for LCLS-II at SLAC
STF2: Test Facility at KEK

## Slide 29: Module Performance: Recent Results
Cavities in Cryomodule CM-2 (FNAL)
Harms, TTC meeting, KEK 2014
Module series production for E-XFEL
Reschke, TTC meeting KEK 2014

## Slide 30: The Luminosity Challenge
Design: L=1.74･1034 cm-2s-1 requires a very small beamspot
1000nm
12nm
DNA: 2.5 nm
ILC Beam Spot
Small Emittance
CESR-TA Facility at Cornell: Validate Damping Ring design
Sharp Focus
ATF2 Facility at KEK: Validate Final Focus
ATF2: 50nm Beam Size at 1.3GeV!
K. Kubo, IPAC14 (WEZA01)

## Slide 31: How to detect the particles?
Two Detectors: ILD and SiD, sharing one interaction region
Clean e+e- environment permits low-mass, precision trackers  Excellent performance expected
ILD
SiD

## Slide 32: Detectors: Challenges and Opportunities
W+W-  4 jets
Z0Z0  4 jets
Jet energy resolution -> particle flow calorimetry
Jet flavour tagging -> super-thin pixel detectors
Extremely good tracking -> TPC or thin silicon tracker
M. Thomson, Calor 2010

## Slide 33: How much does it cost?
Estimate in 2013 Technical Design Report: 7.8 ･109 $ + 14k years labor (7% increase)
Dominated by Main Linac
Also read the fine print: This number does not include costs for accelerator, lab, site activation

## Slide 34: WHEN
When can ILC be built?
… and Where?

## Slide 35: The ILC Timeline
Expecting ~ (2+ 4) year
Being re-studied
Preparation Phase
We are here, 2014
Japan: MEXT Review
Apr 2016

## Slide 36: Candidate Sites in Japan
Preferred Site http://ilc-str.jp/topics/2013/08281826/

## Slide 37: ILC on the World’s Roadmaps
Japan, Oct 2012 Statement by JAHEP panel
European Strategy for Particle
Physics, Update 2013
http://cds.cern.ch/record/1551933/
http://www.usparticlephysics.org/p5/pdf/ BuildingForDiscovery_P5Report2014_BriefSummary.pdf
America: Report of the Particle Physics Project Prioritization Panel (P5)

## Slide 38: Take Home Message
ILC has a strong physics case as precision machine:
  Complementary to LHC
  Ideal to study light Higgs and Top
  Explores what lies behind the Standard Model, by indirect constraints, additional measurements, or discoveries
  Energies above the Top threshold are vital for that programme
ILC is ready to be built today
Strong movement in Japan in favor of ILC, supported by European and US roadmaps!

## Slide 39: Acknowledgements
Many thanks to Karsten Büßer, Eckhard Elsen, Brian Foster, Jenny List, Gudrid Moortgat-Pick, Nicholas J. Walker and Georg Weiglein for their help in the preparation of this talk.
Additional Material taken from talks by J. Brau, F. Simon, K. Fujii, T. Tanabe, and many others.