## Slide 1: Preliminary data analysis on 16x16 modules
Francesco Pennazio on behalf of the Torino INSIDE group
INSIDE meeting, Roma, December 18th 2014

## Slide 2
Lutetium 176 decay scheme
INSIDE meeting, Roma, December 18th 2014
Conversion into 55 keV

## Slide 3
Experimental setup
INSIDE meeting, Roma, December 18th 2014
fan
Temperature control (50°C)
Matrices
(15 years old) Na22 source

## Slide 4
Coincidences map
INSIDE meeting, Roma, December 18th 2014
… channel map?
We then can analyze just few channel – channel coincidences

## Slide 5
Energy spectrum
INSIDE meeting, Roma, December 18th 2014
TOFPET ASIC measures energy with TOT technique ( log(E))
Acquisition system has already implemented a conversion system to try to linearize the TOT (TOTraw->TOTcorr)
TOT detailed MC and Simulink model, Marco Boretto master thesis, Apr. 2014

## Slide 6
Energy spectrum
INSIDE meeting, Roma, December 18th 2014
Chip 0 channel 11 TOT spectrum
TOT raw
TOT corrected
22Na 511 keV
176Lu 307 keV
176Lu 202 keV
Background

## Slide 7
Energy resolution
INSIDE meeting, Roma, December 18th 2014
Chip 0 channel 11 TOT spectrum
TOT raw
TOT corrected

## Slide 8
Coincidence energy spectrum
INSIDE meeting, Roma, December 18th 2014
Chip 0 channel 11 TOT spectrum
TOT raw
TOT corrected
22Na 511 keV 11% ∆E/E
176Lu 307 keV 14% ∆E/E
176Lu 202 keV 18% ∆E/E*
Background
* ∆E/E with gaussian fit sigma

## Slide 9
Coincidence energy spectrum
INSIDE meeting, Roma, December 18th 2014
Chip 0 channel 11 TOT spectrum
TOT raw
TOT corrected

## Slide 10
Coincidence time resolution
Lu-176 decays emitting b and 3g (2 detectable) -> CTR can be studied with different energy selection windows, since the 401 keV b spectrum overlies the g photopeaks
Data with TOFPET shaping ON
22Na 511 keV 0.35 ns s
176Lu 307 1.05 ns s
Analysis procedure -> 2 channels selection
Energy window on single acquired data around selected photopeak
8 ns time window to find coincidences
INSIDE meeting, Roma, December 18th 2014

## Slide 11
511 keV coincidence time resolution
INSIDE meeting, Roma, December 18th 2014
chip 2 channel 29 vs chip 5 channel 41
Coincidence Time Resolution 330 ps s
chip 0 channel 11 vs chip 5 channel 51
Coincidence Time Resolution 370 ps s

## Slide 12
176Lu-only coincidence time resolution
Lu-176 decays emitting b and 3g (2 detectable) -> CTR can be studied with different energy selection windows, since the 401 keV b spectrum overlies the g photopeaks
Data with TOFPET shaping OFF
No 22Na source available for this dataset
22Na 511 keV ?
176Lu 307 keV 0.66 ns s
Analysis procedure -> 2 channels selection
Energy window on single acquired data around selected photopeak
8 ns time window to find coincidences
INSIDE meeting, Roma, December 18th 2014

## Slide 13
Software development
As the INSIDE PET detector size increases, number of histograms needed is becoming huge: an interface is being developed to increase data analysis efficiency and to evaluate overall chip and detector behavior.
INSIDE meeting, Roma, December 18th 2014
In- and inter-spill values
Chip “health” analysis (Tcoarse, Ecoarse, Tfine, Efine)
Overall system (512 channels)
Single-channel interactive selection

## Slide 14
Software development
As the INSIDE PET detector size increases, number of histograms needed is becoming huge: an interface is being developed to increase data analysis efficiency and to evaluate overall chip and detector behavior.
INSIDE meeting, Roma, December 18th 2014
In- and inter-spill values
Number of events per frame

## Slide 15
Software development
As the INSIDE PET detector size increases, number of histograms needed is becoming huge: an interface is being developed to increase data analysis efficiency and to evaluate overall chip and detector behavior.
INSIDE meeting, Roma, December 18th 2014
Single-channel figures of merit
TOT and CTR behavior of channels of the same chip are about uniform, chip by chip calibration and channel-by-channel fine calibration is needed, feasible off-line via software

## Slide 16
Software development
As the INSIDE PET detector size increases, number of histograms needed is becoming huge: an interface is being developed to increase data analysis efficiency and to evaluate overall chip and detector behavior.
INSIDE meeting, Roma, December 18th 2014
Coincidences figures of merit

## Slide 17
Conclusions and outlook
INSIDE meeting, Roma, December 18th 2014
Preliminary data shows that the modules fully meet the project requirements in terms of time and energy resolution.
Analysis software is stable and flexible (it analyses both simulated and acquired data).
Data analysis graphical interface is available.
Future work:
Channel-by-channel equalization to extend the single channel vs channel results to module vs module
Energy calibration
Data analysis optimization:
  Analysis of binary data
Extension of GUI functionalities