## Slide 1
CMS Muon detector from LHC to HL-LHC
Pigi Paolucci
INFN Napoli

## Slide 2: Gruppo di Napoli
S. Buontempo (DR)
N. Cavallo (PO)
F. Fabozzi (PA)
O. Iorio (AR)
L. Lista (PR)
S. Meola (PA)
M. Merola (AR)
P. Paolucci (PR)
F. Tyssen (Post-doc)
Project Manager (Pigi)
Technical Coordinator (Salvatore)
Rapr. Nazionale della fisica (Luca)
Single Top Convener (Orso)
Attività Hardware
Sistema presente
Rivelatori ad RPC
DAQ – realizzato a Napoli
Software Trigger/DAQ
Sistema di potenza
Upgrade Phase II
Rivelatori iRPC: bakelite
Rivelatori iRPC: design
Meccanica GEM/RPC
Sistema di potenza
GIF++ construction
L. Parascandolo
A. Vanzanella
F. Cassese
L. Roscilli
G. Passeggio
Servizi

## Slide 3: RPC project
Belgium
CERN
Bulgaria
CHINA | 2
KOREA | 16
INDIA | 4
BELGIUM | 10
COLOMBIA | 2
N. Puebla | 3
PAKISTAN | 6
EGYPT | 3
CERN | 4
ITALY | 28
BULGARIA | 12
Georgia | 2
TOTAL | 90
RE4 | Italy | Pakistan | India | Colombia | CERN
 | Korea | China | Belgium | Finland | Egypt
 | Mexico |  | Georgia |  | 
R&D phase II | Italy, CERN, Korea, Belgium, Pakistan, Mexico |  | Georgia Egypt | Colombia India | 
Georgia
Uniandes
Nueva
Puebla
Italy
Authors
Notes: Very good control of the dominant ZZ background
Cntrolla sia ultimo plot …

## Slide 4: Organization Chart 2014
DPG
A. Ocampo
P. Verwilligen
Technical Coordination
S. Buontempo
A.Dimitrov
Project Manager
P. Paolucci
G. Pugliese – M. Tytgat
Resource manager H. Hoorani
Upgrade
Coordinator
M. Abbrescia
A. Sharma
Run Coordinator
M. Maggi
A. Cimmino
Steering committee
W. Van Doninck, M. Maggi
H. Hoorani, A. Colaleo,
A. Sharma
(PM+DPM+RC+TC+DPG+UP)
Institution Board
L. Litov
Conference Committee
B. Pavlov
Editorial board
S. Qian, D. Piccolo,
M. Abbrescia

## Slide 5: Attività 2013-2014 Manutenzione

## Slide 6: RPC present system
RPC present system
Covers 0 < |h | < 1.6
1056 chambers
110,000 electronic channels and 3500 m2 of active area
Double gaps gas chamber: 2 mm gas width
Bakelite bulk resistivity: r = 2 - 5 x 1010 cm
Strip width: 1 − 4 cm.
Gas mixture: C2H2F4 + isoC4H10 + SF6 (40% of H)
95.2% 4.5% 0.3%
Operated in avalanche mode
CMS muon upgrade
Completion of the 4th station in 2013-14:
144 chambers

## Slide 7: 2013-2014 actvities
2011
2012
RPC Maintenance 2013-2014
Power system
DAQ
Front-end
Gas leak
Fully recovered now
Area 4000 m2
8.000 m2 di gap
18.540 Gas connections
840 HV channels
20 km HV cable
8.000 HV connectors
120.000 strips
6.448 front-end boards
934 Distribution boards

## Slide 10: Attività 2013-2014 Upgrade RE4

## Slide 11: Muon system

## Slide 12: Upgrade phase I - RE4
RE4 installation 2013-2014
144 new chambers
DAQ-Trigger
Commissioning
4.2 millions CHF
20 institutions
100 people

## Slide 14: RE4 – chamber construction
Very low current
High efficiency
Construction
Commissioning

## Slide 16
The only phase-I project
completed on schedule and within the budget

## Slide 17: Upgrade Phase II GEM and iRPC

## Slide 18: Muon system

## Slide 19: High eta region

## Slide 20: Muon system Upgrade

## Slide 21: Where we arrived in the 2013
Maximum rate (Barrel) = 7 Hz/ cm2
Maximum rate (Endcap) = 14 Hz/cm2
Average rate (Barrel) = 2 Hz/cm2
Average rate (Endcap) = 5 Hz/cm2
Q = rate Teff <q> = 3 mC/cm2
Present CMS results
Maximum rate capability 1 kHz/cm2
10 years of LHC at 200 Hz/cm2
Total integrated charge = 100 mC/cm2
(ATLAS up to 300 mC/cm2 )
RPC certified by CMS at
Max rate vs time
Endcap rate Map
rate vs lumi

## Slide 22: GEM upgrade
Two GEM station will be installed in the inner disk to improve the PT assignment and reduce the trigger rate.

## Slide 23: Extrapolation to HL-LHC
 | Max (Hz/cm2) | Average ( Hz/cm2) | Qmax (C/cm2)
Barrel | 125 | 25 | 0.15
Endcap | 250 | 60 | 0.30
RE3/1 & RE4/1 | 500 (CSC & Fluka) see backup slide | < 250-300 (CSC & Fluka) | 1.2
For 10 years of HL-LHC – 3000 fb-1
The main requirements for the high eta region of the disk 3 and 4 can be summarized as follow:
Maximum rate of 1 kHz/cm2 (safety factor included)
Integrated charge of about 1 C/cm2
Eco-gas (C2H2F4 and SF6 to be replaced)
Fitting the space available (up to η 2.4) similar to RE4 space

## Slide 24: RPC history
* First batch failed for high temperature (27-30 oC). Then oiling procedure was improved a lot
** very maximum rate (safety and energy factor included)
Collaboration with ATLAS is going on
1992 1996 2003 2013 2019
LEP/L3 | BaBar | CMS/ATLAS | RE4 | Phase II
10 years | 5 years* | 10 years |  | 
1011-12 Ωcm | 1011-12 Ωcm | 2-5 1010 Ωcm | 1-2 1010 Ωcm | 7-8 1009 Ωcm
300 m2 | 2000 m2 | 7000 m2 | 300 m2 | 200 m2
streamer | streamer | avalanche | avalanche | avalanche
Heavy mechanic | Gap Industrial prod. (Italy) | 2nd Gap company (Korea) | improved HPL prod. (Italy) | Light detector
Few leaks | eco gas mix | Oiling procedure improved a lot |  | new eco gas mix
FE chip Napoli | FE chip Napoli | FE chip Bari | FE chip Bari | New FE chip
0.3 Hz/cm2 | < 3 Hz/cm2 | < 15 Hz/cm2 | 150 Hz/cm2 | 1000 Hz/cm2**

## Slide 25: From phase I (RE4) to phase II
To go up to 1 kHz/cm2 for 10 HL-LHC years at 5 1034 cm-2s-1
We need to optimize: the bulk resistivity of the Bakelite electrodes and, eventually, the average charge generated by the avalanche.
The role of these parameters can be explained looking at the three following equations, obtained using simple electrostatic model:
The time constant of an elementary cell involved in the avalanche process:
τ = e0 (er + 2) ρ
The area of the “cell” concerned in the discharge
S = 2<q>/e0E = 2<q>d/e0Vd
The rate capability of the single cell
r = 1/Sτ
Where <q> is the average charge per avalanche (C), r is the rate (Hz/cm2), ρ is bulk resistivity (Ωcm), E is the electric field inside the gas, Vd is the voltage drop that stop the avalanche in the cell and d is the gas gap width.
τ can be reduced of a factor 2-3 (ρ= 9-10 × 109 Ωcm)
Rate can increase of 3-5 times

## Slide 26: From Phase I (RE4) to phase II
To increase the rate capability and reach the kHz/cm2* needed need to decrease the resistivity of the Bakelite electrode and reduce the average charge <q> associated to the avalanche. A resistivity of 9-10×109 Ωcm (factor 2-3 in the rate) can be easily produced taking into account that for the RE4 region we were already able to reach the 1-2×1010 Ωcm.
 | RE4 | RE4/1 & RE3/1
Electrode | ρ= 1-2 × 1010 Ωcm | ρ= 6-7 × 109 Ωcm
Gap | 2 mm | 1 or 1.5 mm
Power system | < 1% fault | New connectors
Gas system | some leaks | New distribution
A thinner gap/bakelite (from 2 mm to 1.5-1.0 mm), a more performing front-end chip and new gas is a possible aspect to be investigated to reduce the average charge produced in an avalanche and at same time the power consumption of the detector.

## Slide 27: Multigap bakelite (Korea)
The standard double gap configuration used in CMS has been modified by adding an additional thin gap, with a thickness reduced to 1 mm, on both sides of the read out strips. Standard HPL and front-end electronics
Plateau for cosmic rays muon with and without irradiation (γ-ray at 3 kHz/cm2 on the whole chamber). The chamber reaches full efficiency and has a streamer-free plateau of several hundreds Volts.

## Slide 28: Glass RPC
Resistivity few 109 Ωcm
Thin plates could be used (< 1mm) .
Small gas gaps (≤1 mm) and with standard gas mixture Charge/mip ≤ few pC.
This explains why one can achieve higher rate capabilities with respect to other materials 10 kHz/cm2 (to be verified)
Timing performance ≈ 1 ns for single gap and less than few tens of ps in case of multi-gap.
Constraint : Size of low-resistivity glass is limited. Largest surface is 30X30 cm2
Source OFF
(CO2)
Source ON
(Isobutane)
Preliminary
After 8 months of exposure
Test at GIF++ will be performed by the Lyon group with the help of the RPC collaboration.
Standard radiation tests to be performed at GIF++.

## Slide 29: Glass RPC test beam
Time Resolution < 40ps
Beam Test@HZDR June, 2012
HV scan
Rate scan

## Slide 30: Eco-gas studies
The European Community has limited the industrial production and use of gas mixtures with Global Warming Power
This is valid mainly for industrial (refrigerator plants) applications
C2H2F4 is the main component of the present RPC gas mixture:
  C2H2F4 and SF6 Crucial to ensure a stable working point in avalanche
On the physical and chemical properties of this components we:
  Designed FE electronics and chambers
  Did all performance, ageing and calibration tests
Gas mixture was already modified during the LEP time for a similar European request. No problem in the change at all

## Slide 31: RE4 test at GIF & GIF++
31
Current monitoring vs. integrated charge
  Integrated charge up now: ≈ 0.05 C/cm2 gap with current stable
  Plan to integrate 10 years LHC and then HL-LHC at GIF++ in about 1 year.
Bakelite resistivity monitoring vs. integrated charge
  HV scan with argon and source ON every month.
  Resistance gap (not only Bakelite) ≈ 1-2 1011 W cm to be used for stability.
  Stable in time

## Slide 32: Conclusioni
I goal principali dei prossimi anni sono:
  Running del sistema presente 2015-2018
  Sviluppo del rivelatore a GEM per il 2018-2019
    Sistema di potenza
    Meccanica del rivelatore
  Progettazione di un “futuro” rivelatore ad RPC 2022-2023
    Leggero, sottile e che possa lavorare a tensioni inferiori
    Pronto per il 2019 (dimostratore)
    Test in laboratorio a Napoli per rivelatori con piccole gap e a bassa resistività
  Grazie a tutti per il lavoro originale e professionale svolto nel 2014