## Slide 1: Particle ID with emphasis on Cherenkov detectors

## Slide 2: OUTLINE
Introduction
    PID (Particle IDentification)
    The Cherenkov effect in brief
Cherenkov Counters
    Historical background
    The role of the radiator
    Different Cherenkov Conter types:
      Threshold
      Differentail
      RICH
The photondetectors
Cherenkov counter optics, an example
The RICH family
    A (non exhaustive ) gallery
    The most recent approaches
RICHes & Physics

## Slide 3: PID

## Slide 4: PID: how ?
PID, 2 ways:
  Based on the specific features of particle interactions, examples
    High energy muons, penetration
    Intermediate energy muons, range
    Low energy p, range
    E.m. particles vs hadrons: calorimetry (shower development)
    …
  Measurement of the particle mass
    Direct measurement from decay products
    m from the equation
  E2 = (mc2)2 + (pc)2
    2 measurements have to be combined
    p (deflection in magnetic field) v (TOF, Cherenkov)
    E (range) v (TOF)
      p (deflection in magnetic field) dE/dx (for instance TPC)
      p (deflection in magnetic field) E/m (transition radiation e)
      p (deflection in magnetic field) E (range)

## Slide 5: PID by measuring p & v
Resolution:
Assuming p is measured with fine resolution, the resolution in Dm/m becomes a specific request concerning the resolution of the b measurement:

## Slide 6: THE CHERENKOV EFFECT

## Slide 7: INTUITIVELY
bpart∙c < phase velocity of the light in the medium
Symmetric configuration 
Destructive interference
bpart∙c > phase velocity of the light in the medium
No longer a Symmetric configuration a coherent interference front is created
phase velocity of the light in the medium :
1/n ∙ c

## Slide 8: CHOC WAVE
Analogous phenomena (mechanical waves):
  Boat wake
  Supersonic plane
Phenomena taking place above a given threshold

## Slide 9: The coherent interference
threshold: nb = 1
saturation: b  1
The Cherenkov photons are linearly polarized:
E vector is orthogonal to the cone surface
H vector is tangent to the cone surface

## Slide 10: A FEW EQUATIONS
Frank e Tamm, photon spectrum:
  Photons are in the infrared, visible
  and UV range
Fixing the radiator length L:
Integrating the spectrum:
  1 - 1/(b2n2) = 1 - cos2qC = sen2qC
When b = 1, L = 1 and DE = 1 :
Always:
  N is a mean value: Poisson statistics  v from a direct measurement of qC , not from N !!!
N ≈ 1-1/(bn)2 = sin2qC

## Slide 11: EQUATIONS OF PRACTICAL INTEREST
In detectors photon losses, QE and photoelectron detection efficiency have to be accounted for
N0 – FIGURE OF MERIT of a Cherenkov Counter
  e – photoelectron detection efficiency
  QE – quantum efficiency
  T – transparency
  R - reflectance
NPE – mean value of detected photoelectrons (here assuming Z=1)

## Slide 12: THRESHOLD & SATURATION
th
Near threshold:
A moderate angular resulution is enoght
Limited number of photons
Towards saturation:
Very fine angular resolution needed
More photons

## Slide 13: REMINDER
Photons, E vs l
[ E= hc/l l (nm) = 1240 / E(eV) ]
N-photons vs l
Chart: 
visible light
Chart: 
Chart: 
n = 1.333
n = 1.000297

## Slide 14: THE CHERENKOV EFFECT, A BIT OF HISTORY
1892: Oliver Heaviside – prediction based on the e.m.: particle with velocity > light velocity in the medium emit e.m. radiation con with propagation front at fix angle respect to the particle trajectory
1919: Marie Curie – feeble blue light observed from water radium solutions
1934: Pavel Cherenkov – experimental proof that the observed light is produced by the movement the Compton electrons; the equation linking the Cherekov angle and the refractive index of the medium is formulated [PMT not yet invented !!!]
1937: Frank and Tamm - classical theory of the Cherenkov effect and shape of the photon spectrum
1940: Ginsburg - quantistic theory of the Cherenkov effect
1958: Nobel award to Cherenkov, Frank and Tamm
Pavel Cherenkov

## Slide 15: CHERENKOV COUNTER, GENERAL ELEMENTS

## Slide 16: CHERENKOV COUNTERS, A BIT OF HISTORY
1937: Pavel Cherenkov mentioned the possibility of using the Cherenkov radiotion for PID
early 1940 years: PMTs are there !
1951: J.V.Jelly builts the first Cherenkov Counter
1955: a Cherenkov counter in the setup of the experiment that discovred the anti-p
1960: A. Roberts – the measurement of qC to perform PID – first RICH(*) scheme
1977: T. Ypsilantis e J. Seguinot first working RICH
1982: first RICH used in an experiment, E605 at Fermilab
(*) RICH - Ring Imaging CHerenkov
Setup sperimentale dell’esperimento che scoprì l’anti-p
O. Chamberlain et al., Phys. Rev. 100 (1955) 947

## Slide 17: CHERENKOV COUNTERS, THE COMPONENTS
RADIATOR
  The Cherenkov light is produced and
  transmitted here
  The detector design originates from the choice of
  the radiator
PHOTODETECTORS
  The ranges of transparency in the radiator and
  efficiency in the photodetector must match
  Provide position information when needed
( FOCALIZATION OPTICS )
  when NEEDED
E-691 C1
D.Barlett et al.,
NIMA 260 (1987) 55
COMPASS RICH-1
Photo CERN
MAPMT
Hamamatsu R7600-03-M16

## Slide 18: THE DETECTOR DESIGN ORIGINATES FROM THE CHOICE OF THE RADIATIOR

## Slide 19: RADIATORs
Choice based on:
  Threshold g (gth), namely the p-range of interest
  Transparency range
  Chromatic dispersion (intrinsic limit of the resolution in imaging counters)
Radiator families
  1 < n < 1. 12 (gth >2.15)
    Gas
    Cryogenic liquids (He, Ne)
    Silica aerogel (only visible light)
  1.12 < n < 1.35 (1.49 < gth < 2.15)
    Liquid fluorocarbons
      CF4, C2F6, C4F10 at low temperature
      C5F12, C6F14 at room temperature
  n > 1.33 (gth < 1.52)
    Transparent liquids (water, alcohol, glycerin, hydrocarbons)
  n > 1.46 (gth < 1.37)
    Solids with transparence in the visible range (glass, plastics)
    Solids with transparence in the UV range (fused silica, namely quartz, NaF, CaF2, LiF)
E. KRAVCHENKO
@ RICH2007

## Slide 20: TRASMISSION
WINDOWS
RADIATORS

## Slide 21: THE CHROMATIC DISPERSION
dn / dE:
Lorentz-Lorenz equation
f(E) - molar reflectivity, in general well reproduced by a 2-pole fit (Sellmeier):
In a gas ( n-1 << 1 ): n-1 ≈ P / T

## Slide 22: CHROMATIC DISPERSION & No OF PHOTONS
At 5 eV
quartz
quartz

## Slide 23: To work in the VUV range
transmission
through 1,87 m,
corresponding to:
H2O: ~1 ppm,
O2: ~3 ppm
COMPASS RICH-1, typical
wavelength (nm)
transmission
filters
liquid
storage
tank
liquifier
compressors
PLC and
electrical
installation

## Slide 24: CHERENKOV COUNTER TYPES

## Slide 25: CHERENKOV COUNTER TYPES
THRESHOLD CHERENKOV COUNTERS
  nb > 1
DIFFERENCIAL
  p is given, an n ∙ Db – range is selected (by selecting a Dqc range)
  Cherenkov IMAGING counter (RICH) - qc is measured
  With focalization
  Proximity focusing
  DIRC

## Slide 26: THRESHOLD CHERENKOV COUNTERS
Typical scheme
efficiency
  Poisson statistics
  Inefficiency
  Efficiency

## Slide 27: THRESHOLD CHERENKOV COUNTERS
Secondary beam of
negative particles
at 1 GeV/c
Radiator:
quartz, 96.4 cm
Counters with gas radiator to tag
particles species in secondary
beams
  By P regulation, gth is modified
  to tag different particles spieces
  A couple of counters is often
  used to suppress
  the background due d-rays
Experimental Setup of the experiment that discovered the anti-p
O. Chamberlain et al., Phys. Rev. 100 (1955) 947
I contatori CE1 e CE2 counters, PS Est Hall at CERN – in this example e- are tagged for rejection

## Slide 28: THRESHOLD CHERENKOV COUNTERS
E-691 at Fermilab ( studies of the photoproduction of charmed particles)
2 hugh threshold Cerenkov counters
at atmospheric P  K/p, K/p sep. 5-35 GeV/c
PMT coupled to Winston cones
Average number of collected photons:
  ~ 2-3 in C1, inefficienza P(2.5) = 8%
  ~ 3-4 in C2, inefficienza P(3.5) = 3%
Radiator - N2
L = 3755 cm
Radiator - N2 : He =20:80
L = 6604 cm
PMT
Winston cone
L  p p
w/o C1, C2
with C1, C2

## Slide 29: THRESHOLD CHERENKOV COUNTERS
A more recent counter: TIC, CERN-NA44 (heavy ions at CERN SPS)
hadron identification in the 3-8 GeV/c momentum range by the TIC (Threshold Imaging Cherenkov)
Localization of the photon blob: correlation of the blob to the specific particle in multiparticle events

## Slide 30: DIFFERENCIAL CHERENKOV COUNTERS
Charged particle discrimination in secondary beams
DISC - Differential Isochronous Self Collimating
The useful phase space is very narrow (it can be used only along beam lines)
World record in beta-resolution
efficiency (coincident of k PMT) < 90%
J. Litt and R. Meunier, Ann. Rev. Nucl. Sci. 23 (1973)

## Slide 31: RICH, THE PRINCIPLE
Proposed by Roberts, 1960 [ A. Roberts, Nucl. Instr. and Meth. 9 (1960) 55 ]
Ideal geometry:
  Spherical mirrors and detectors, detectors at the focal surface, particle source (target) at the sphere centre
2 options:
  The particle trajectory is MEASURED, a qC measurement by each ph.
  Image centre is NOT KNOWN, the ring pattern must be recognized
// trajectories & same p 
Identical image
Photon detectors with good space resolution

## Slide 32: PHOTODETECTORS

## Slide 33: PHOTODETECTORS
single photon detectors :
the CENTRAL QUESTION since the beginning of the RICH era
3 groups (with examples, not exhaustive lists)
Vacuum based PDs
PMTS (SELEX, Hermes, BaBar DIRC)
MAPMTs (HeraB, COMPASS RICH-1 upgrade)
  Flat pannels (various test beams, proposed for CBM)
Hybride PMTs (LHCb)
MCP-PMT (all the studies for the high time resolution applications)
Gaseous PDs
Organic vapours - in practice only TMAE and TEA (Delphi, OMEGA, SLD CRID, CLEO III)
Solid photocathodes and open geometry (HADES, COMPASS, ALICE, JLAB-HALL A)
Solid photocathodes and closed geometries (FENIX HBD, even if w/o imaging, COMPASS second upgrade)
Si PDs
Silicon PMs (only tests)
USED SO FAR IN EXPERIMENTS

## Slide 34: PMTs

## Slide 35: PMT
For a long while only single channel devices (limited space resolution)
To equip large surfaces: costs!

## Slide 36: PMT – THE PHOTOCATHODES
STANDARD:
peak QE ~ 25%
The LHCb-production example:
  The necessity of deeper contacts and positive feedback loops with industry
- recent HAMAMATSU photocathodes with peak-values above 40% !
RMS of
batch spread
<QE> per delivery batch
QE [%]
Batch number
  <QE @ 270nm> = 30.8%
UBA
SBA
0
40
20
QE (%)
0 20 40
BIALKALI
HAMAMATSU
400 600
wavelength (nm)
  LHCb HPD
  production by
  DEP

## Slide 37: PMT – the architectures
STANDARD
MULTIANODE
- HYBRID
MAPMT
HAMAMATSU R7600-M16
16 anodes
time resolution << 1 ns
Flat PANNEL
HAMAMATSU H8500
64 anodes
(256 ch.s also available)
HPM, LHCb custom
1024 anods

## Slide 38: MCP – PMT

## Slide 39: MCP - PMT

## Slide 40: MCP-PMTs 1/3
good
response
in magnetic
field
good
time
resolution
B. Seitz @ TIPP09
the rate response
is still a concern
[… another serious concern is life time … ]

## Slide 41: MCP-PMTs 2/3
K. INAMI @ TIPP09
Gain vs B TTS vs B TTS vs Gain
HPK6 BINP8 HPK10 Burle25
Diameter: 6mm
Diameter: 8mm
Diameter: 10mm
Diameter: 25mm

## Slide 42: MCP-PMTs 3/3
Enough life-time?
K. INAMI @ TIPP09

## Slide 43: HUNTING THE ps
MCP: 10 mm Photonis Planacon, with 10+3 mm radiator
SiPM: Hamamatsu MPPC 3 x 3 mm2 with 6 x 6 x 16 mm3 poly radiator
resolution: 47 ps
PSEC Timing – T979
Erik Ramberg @ TIPP09
the need of adequate electronics
the synergies with PET
for MCP detectors : the intrinsic resolution
limit due to TTS from the photocathode

## Slide 44: Si PM

## Slide 45: Si-PM, GENERAL COMMENTS
First large-scale use of SiPMs in
a physics experiment : T2K
D. ORME @ TIPP09

## Slide 46: Si-PM FOR Cherenkov imaging counters
ISSUES:
Low V operation (10-100 V)
Peak PDE (QE x ε_geiger x ε_geo ) up to 65% (@400nm Hamamatsu data sheet), but …
Gain ~ 106
time resolution ~/<100 ps
Works in magnetic field
Small size  light guides
High noise rate ~ 100 kHz/mm2 (noise pulse = pe pulse) +
Noise rates varying with environmental conditions (T) and aging
Radiation damage (p,n)
Cross-talk
Afterpulsing and cross talk
should be taken into account.
(H. Haba, RICH2007)
Otono @PD07
Measured with
photocurrent.
From HPK
catalogue:
HC100
HC050
HC025

## Slide 47: Si-PM in an AEROGEL RICH
TEST BEAM
test w/o and w/ light guides:
Noise rate: 2.4 MHz/ch.
Noise & signal (5 ns time window)
N_ph, meas. / exp.~ 50-60%
S. KORPAR @ TIPP09
Module:
8 x 8 MPPC HC100
Pad size: 5.08 mm
4 mm2 active (15.5% w/o LG)
background

## Slide 48: GASEOUS PHOTODETECTORS

## Slide 49: WHY GASEOUS PHOTDETECTOR?
In spite of critical aspects and technical challenges,
gaseous photon detectors offer:
operation in magnetic field
the most effective solution for what concerns the cost of large detector area application
minimum material budget when the photon detectors have to seat in the experiment acceptance
third generation of gaseous photon detectors

## Slide 50: GASEOUS PHOTODETECTORS, WHERE ARE WE?
photoconverting vapours are no longer in use, last example: CLEO III
(rates ! time resolution !)
the present is represented by MWPC (open geometry!) with CsI
  the first prove (in experiments !) that coupling solid photocathodes and gaseous detectors works
  Severe recovery time (~ 1 d) after detector trips ion feedback 
  Aging after integrating a few mC / cm2 CsI ion
  Moderate gain: < 105 (effective gain: <1/2) bombardment
The way to the future: photon & ion blocking architectures
  GEM/THGEM allow for multistage detectors
    With THGEMs: High overall gain ↔ pe det. efficiency!
    Good ion blocking (up to IFB at a few % level)
  IBF control by Micromegas

## Slide 51: GASEOUS PDs, THE PAST
Gaseous photon detectors, the first generation: converting vapours
OMEGA
DELPHI
TMAE
(Tetrakis-Dimethylamine-Ethylene)
TEA (Tri-Ethyl-Amine)
SLD - CRID
CLEO III
E605

## Slide 52
TMAE
QE,
NIMA 323 (1992) 351
TMAE
DELPHI barrel RICH, NIMA 273 (1988) 247
Chart: 
| 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70
 | 120.5318 | 86.8881 | 63.3447 | 46.6776 | 34.7476 | 26.1185 | 19.8142 | 15.1644 | 11.7034 | 9.105 | 7.1378 | 5.6367
DELPHI barrel RICH
Photosensitive volume:
5 cm thick
cloisons
Anode wire
thick photosensitive volume (slow photon
detectors, parallax error)
heating and temperature control
(T _bubbling <T_operation)
photon feed-back from amplification region
(protections)
chemically extremely reactive
GASEOUS PDs, THE PAST

## Slide 53
GASEOUS PDs, THE PAST
TEA
NIMA 554 (2005) 147
CLEO III, NIMA 441 (2000) 374
technical challenges of the far UV domain
large chromatic dispersion in far UV region:
  Proximity focusing (the Chromatic dispersion is not the major resolution limitation)
  He, a radiator gas with extremely reduced chromatic dispersion

## Slide 54
GASEOUS PDs, THE PRESENT
MWPCs with solid state photocathode (the RD26 effort)
TIC, NA44
COMPASS,
RICH-1
CsI area > 5 m2
JLAB-HALL A
ALICE-HMPID
CsI area > 10 m2
STAR
HADES
A solid state photocathode exposed to
a gaseous atmosphere in an effective PD:
a success !

## Slide 55
GASEOUS PDs, THE PAST
Photocathode - the most robust
one in gaseous atmosphere: CsI
Structure of the PDs
@ 2 kV (typical):
E (CsI surface) ~ 7 kV/cm
P. Abbon et al, NIM A 577 (2007) 455.
The best quartz cuts here
A. Di Mauro, NIM A 525 (2004) 173.
COMPASS,
RICH-1 PDs

## Slide 56
GASEOUS PDs, THE PRESENT
Reflective versus semi-transparent photocathodes
REFLECTIVE - larger photoelectron collection :
  Semitransparent photocathode - the application of a thin metallic film, which absorbs photons, on the entrance window is required
  the probability of photoelectron absorption is lower in a reflective photocathode than in a semitransparent one as the conversion probability is the highest at the entrance surface of the photo-converter
the thickness of the photo-converter layer is non critical in the reflective configuration, contrary to the semitransparent one:
this aspects is very relevant for large area detectors

## Slide 57
GASEOUS PDs, THE PRESENT
Photoelectron extraction from a CsI film, the role of gas and E
M. Alexeev et al., NIM A 617 (2010) 396
Breskin et al.,
NIM A 367 (1995) 342
VACUUM
C. D. R. Azevedo et al., 2010 JINST 5 P01002

## Slide 58: Large surface photocathodes, the technology
coating

## Slide 59: Large surface photocathodes, the technology
photocathode
storing
glove box for
photocathode
mounting
photocathode
transportation
system
PDs CH4 gas
system,
semiclosed
loop with O2
and H2O
filters
CsI: hygroscopic,
water degrades QE
never
exposed
to air
(max
50 ppm O2 ,
routinely:
10 ppm)

## Slide 60
GASEOUS PDs, THE PRESENT
MWPCs with CsI photocathode, the limits
Severe recovery time (~ 1 d) after detector trips
  Ion accumulation at the photocathode moderate gain: ≈ a few times 104
Feedback pulses (effective gain: <1/2)
  Ion and photopns feedback from the multiplication process not fast
Aging after integrating a few mC / cm2
  Ion bombardment of the photocathode
H. Hoedlmoser et al., NIM A 574 (2007) 28.
1 mC/cm2
0.2 mC/cm2
MWPCs  slow signal formation
  + low gain  “slow” electronics (signal
  integration, low noise level)
  Gassiplex FE : integration time ~ 0.5 ms, time res> 1 ms
  APV (COMPASS RICH-1 upgrade) : resolution ~ 400 ns
   Detector memory, i.e. not adequate for high rates

## Slide 61: GASEOUS PDs, THE FUTURE
TWO REQUESTS
Reduced photon and Ion BackFlow (IBF)
  Reduced aging
  High gain  high photoelectron detection efficiency
Intrinsically fast gaseous detectors (signal due to electron motion)
  Short integration time
  High rate environments
MICROPATTERN GASEOUS DETECTORS

## Slide 62: PD A GAS, IL FUTURO
First developments …
GEM-based PDs
A. Breskin and R. Chechwik, NIM A 595 (2008) 116
Semi-transparent PC
Reflective PC
e- avalanche
ion avalanche
No photon feedback!

## Slide 63: GASEOUS PDs, THE FUTURE
70 µm
55 µm
5 µm
50 µm
Induction gap
e-
e-
I+
Electrons
Ions
60 %
40 %
foglio di poliimmide metalizzato,
foratura con attacco chimico
S. Bachmann et al., NIMA A479(2002)294

## Slide 64: GASEOUS PDs, THE FUTURE
… and applications:
PHENIX HBD,
a threshold Cherenkov counter
(window-less)
Central message for any similar application
Reversed bias cuts the MIP signal !
Aspects non exportable to imaging devices:
detection of >> 1 photon per pad: low gain (5000)
non negligible noise level (~20% single photon signal)
detect photons with l down to ~110 nm: chromaticity !
~ 1 m
Cherenkov
blobs
e+
e-
B≈0
Standard Bias
Reverse Bias
MIP
HV
CsI
Transparent mesh 90%
A. Milov et al. J. Phys. G34, S701 2007
I. Tserruya, RICH2010

## Slide 65: GASEOUS PDs, THE FUTURE
Thick GEM – THGEM
PCB technology, thus:
robust
mechanically self supporting
industrial production of large size
boards
economic
Comparing to GEMs
Geometrical dimensions X ~10
  But e- motion/multiplic. properties do not!
  Larger holes: dipole fields and
  external fields are strongly coupled
About gain:
Large gains are easily obtained (rim !)
introduced in // by different groups:
L. Periale et al., NIM A478 (2002) 377.
P. Jeanneret, PhD thesis, Neuchatel U., 2001.
P.S. Barbeau et al, IEEE NS50 (2003) 1285
R. Chechik et al, .NIMA 535 (2004) 303
RIM
About PCB geometrical dimensions:
Hole diameter : 0.2 – 1 mm
Pitch : 0.5 – 5 mm
Thickness : 0.4 – 3 mm

## Slide 66: GASEOUS PDs, THE FUTURE
Tripple THGEM: Ion Back Flow
by staggering plates
0.1 mm rim
no rim
M. Alexeev et al., JINST 7
(2012) C002014
Gain vs time
M. Alexeev et al.,
NIMA 617 (2010) 396
The first phase of the
systematic studies is entirely
due to the Weizmann group
R. Chechik et al., NIMA 553 (2005) 35
THGEM

## Slide 67: GASEOUS PDs, THE FUTURE
THGEM-PD & Cherenkov
photons
THGEMs
Dim: 0.4 mm
Pitch: 0.8 mm
Thickn.: 0.4mm

## Slide 68: GASEOUS PDs, THE FUTURE
MICROMEGAS has intrinsic IBF blocking properties
e-
ioni +
x = Ea/Ed
transmission (%)
x = Ea/Ed ~ 50 
trasparenza per gli e-
soppressione del
ritorno degli ioni +
Y. Giomataris et al, NIMA A376 (1996) 29
R-O strip
(anodo)
mesh
(catodo)
Parallel Plate
(gap ~ 100 mm)
↑ Ea
↑ Ed
Ionizzazione e drift
(gap ~ 3-5 mm)
IBF ~ 1% e meno !
S. Mukhopadhyay, N. Majumdar
12th RD51 Collaboration meeting

## Slide 69: GASEOUS PDs, FUTURE is here
Hybrid approach:
THGEM + MICROMEGAS
On the floor in 2016
radiator:
C4F10
5 m
6 m
3 m
MWPC’s + CsI
UV mirror
wall
radiator gas: C4F10
PMTs
beam pipe
THGEMs + CsI
COMPASS RICH-1
Staggered THGEMs

## Slide 70: A FEW WORDS ABOUT OPTICS

## Slide 71: COMPASS RICH-1, THE MIRROR SYSTEM 1/2
‘VUV mirror wall’,
21 m2,116 mirrors
radius: 6.6 m
average on 126 mirror
units at production
2000 = @ COATING
reflectance
reflectance stable in time
2002
2001
2000

## Slide 72: COMPASS RICH-1, THE MIRROR SYSTEM 2/2
mirror wall mechanics,
assembled
the elements of this
modular structure
mirror wall
mechanics,
assembling
assembly jig
mirror rear side
individual
mirror support
regulation
for angular
alignment,
2 orthog.
movements
THICKNESS
mechanics: 2.5 % X0
mirrors ~5.5 % X0
STABILITY:
after an initial deformation ~1 mrad, stable: 0.1 mrad over ~ 3.5 y

## Slide 73: THE RICH FAMILY

## Slide 74: THE RICH FAMILY
With focalization
Extended radiator
(gas)
the only approach
at high momenta
(p > 5-6 GeV/c)
EXAMPLES: SELEX,
OMEGA, DELPHI, SLD-CRID, HeraB, HERMES, COMPASS, LHCb
Proximity focusing
thin radiator
(liquid, solid)
Effective
at low momenta
(p < 5-6 GeV/c)
EXAMPLES: STAR,
ALICE HMPID, HERMES, CLEO III
DIRC
Quartz as radiator and as light guide
Effective at low momenta
(p < 5-6 GeV/c)
The only existing DIRC (so far) was in operation at BABAR

## Slide 75: RICHes WITH FOCALIZATION: HISTORICAL EXAMPLES

## Slide 76: SELEX
SELEX (E 781) at Fermilab
Studies of charmed baryons
RICH
10 m He
n_ph (b=1) : 13.6

## Slide 77: OMEGA
OMEGA
Multipurpose spectrometer at SPS, CERN
(exp.s WA 69, 82, 89, 94)
H spectroscopy (s,c)
Heavy ions
OMEGA RICH
radiator: N2; N2 + C2 F6
Spherical mirrors, f = 5 m
TPC a 40 oC
  CH4 + C4H10 + TMAE (15 oC)
  C2H6 + TMAE (30 oC)
p-K separation 15-100 (150) GeV/c
<n_ring> = 16 - 20

## Slide 78: RICHES WITH FOCALIZATION: A RUNNING DETECTOR

## Slide 79
COMPASS RICH-1
p
K
p
in operation
at COMPASS
since 2001
PERFORMANCES:
photons / ring (b ≈ 1, complete ring in
acceptance) : 14
sq-ph (b ≈ 1) : 1.2 mrad
sring (b ≈ 1) : 0.6 mrad
2s p/K separation @ 43 GeV/c
PID efficiency > 95% (q particLe > 30 mrad)
5 m
6 m
3 m
mirror
wall
vessel
radiator:
C4F10
photon
detectors:
CsI MWPC

## Slide 80: COMPASS RICH-1 – UPGRADE 1/2
Large uncorrelated background
in the forward direction
(m beam halo)
UPGRADE
overlap
of event
images

## Slide 81: COMPASS RICH-1 – UPGRADE 2/2
Technical data
Hamamatsu 16 anode PMTs
(R7600 – UV extended glass)
quartz optics
surface ratio 1:7 ($ !)
wide angular acc. (± 9.5 degrees)
high sensitivity pre-amplifier
fast, high time resolution digital electronics
dead zone: 2% even with 46 mm pitch
About performance
photons / ring (b ≈ 1, complete ring in
acceptance) : 56
time resolution better than 1 ns
sq-ph (b ≈ 1) : 2 mrad
sring (b ≈ 1) : 0.3 mrad
2s p/K separation @ 55 GeV/c
PID efficiency > 95% (also < 30 mrad)
online event
display
photons
MAPMT
concentrator
field lens

## Slide 82: COMPASS RICH-1 UPGRADE, EVENTS (ON-LINE IMAGES)
The same event, two different time windows
100 ns 10 ns
n_ph ~ 60 PHOTONS / RING

## Slide 83: COMPASS RICH-1 UPGRADE, a typical event

## Slide 84: PROXIMITY FOCUSING RICHes

## Slide 85: THE DEVELOPMENT OF THE TEA-BASED FAST RICH
Proposed and developed for a (never built) B-factory at PSI (Switzerland)
Basic ingredients:
  TEA: a 20 oC, absorption length: 0.56 mm  very short electron drift  fast with good time resolution
  PAD read-out  fast
prototype
  scheme: proximity focusing
  p-K separation (3s) up to
  3.5-4 GeV/c
  radiatore: LiF, CaF2
  Dedicated read-out electronics

## Slide 86: CLEO III
Upgrade of CLEO II
at CESR – asymmetric B-factory
  Matrix CKM
  CP violation
  Rare B decays
p-K separation at 4 s level up to 2.65 GeV/c
Proximity focusing
  LiF saw-shaped to let the light by normal incident particles getting out
CH4 + TEA at 18 oC

## Slide 87: CLEO III, events
Plane radiator
Saw-shaped
radiator

## Slide 88: ALICE HMPID
EXPECTED PID:
K/π up to 3 GeV/c
p/π up to 5 GeV/c
Confirmed by STAR RICH :
an HMPID prototype

## Slide 89
ALICE HMPID
12% occupancy
.5<p<.75 GeV/c
1.5<p<1.75 GeV/c
p

## Slide 90: DIRC
A single one developed, built and used in the experiment BABAR (ended)

## Slide 91: WHAT IS A DIRC ?
A fraction of the produced light is guided to the PMT system at one of the bar ends
Thanks to the very fine mrchanical accuracy of the bar, the light direction is preserved (left/right ambiguity)
Reconstruction is based on the PMT coordinates and the signal time

## Slide 92: BABAR DIRC
BABAR
At PEP-II B-factory, SLAC
Study of CP violation in the B sector
DIRC
144 bars, 4.9 m long (4 parts glued together), kept in constant N2 flux
purified water at an end to let the photons out
n_ph (b = 1) = 23
Algebraic reconstruction of the image (it is not a ring !)
separation p/K at 2 s level up to 4 GeV/c

## Slide 93: BABAR DIRC
The only DIRC ever built and operated !
p/K separation power
K ID efficiency
p miss- Id as K

## Slide 94: RICHes with MULTIPLE RADIATORS

## Slide 95: DELPHI (prototype, barrel, forward)
DELPHI at LEP (e+ e- circular collider), CERN
Systematic study of the weak force vector bosons
+ much more in physics
in particular, RICHes used for the study of the heavy quark spectroscopy
separation p,K,p in the range 0.3-40 GeV/c  dual radiator
Long drift path of the pe (=photoelectrons) : up to a 1.6 m
  Crucial calibration and monitoring : drift velocity, alignments
  Slow response
Photoconversion, drift and multiplication in CH4 +TMAE
  Crucial calibration and monitoring : refractive indexes, transparency, temperature, pressure
In the following, DELPHI BARREL RICH

## Slide 96: DELPHI _ BARREL RICH
Liquid radiator: 1 cm, C6F14
Gaseous radiator: C5F12 (@ 40 oC)
E_drift = 0.6 kV/cm (100 kV in total !)
Max drift time: 25 ms
Multiplication and detection: camera multifili a elettrodi ciechi

## Slide 97: DELPHI _ BARREL RICH, events

## Slide 98: DELPHI RICH BARREL, q vs p
Liquid radiator
Gaseous radiator

## Slide 99: RICHes WITH DUAL RADIATOR: THE RICHes of HERMES
First RICHes using aerogel
HERMES: 2 identical RICH counters

## Slide 100: RICHes WITH DUAL RADIATOR: THE RICHes of HERMES
at saturation:
<n.ph.s_aerogel>: ~8
K ID efficiency
K missID efficiency
p missID efficiency
p: no ID efficiency
Calculation:
effective range
of separation
DATA
DATA

## Slide 101: MULTIPLE RADIATORS
Another example:
LHCb RICHes
Aerogel
(RICH1)
C4F10
(RICH1)
CF4 (RICH2)

## Slide 102: LHCb
B-PHYSICS at LHC
2 RICH
radiators
  aerogel + C4F10
  CF4
Double reflection to limit the spherical abberation
photodetectors
  HPD
RICH 1
RICH 2

## Slide 103: MULTIPLE RADIATORS
LHCb - RICHes

## Slide 104: “FLYING” RICHes
Experiments: CAPRICE stratospheric balloons (ended) AMS, on the Shuttle (active)

## Slide 105: CAPRICE, AMS
CAPRICE
Cosmic radiation
Separation of pbar, e-, m-, p- 1-5 GeV/c
Radiator
  NaF
  C4F10
Photodetector:
  MWPC at 45 oC: C2H6 + TMAE (38 oC)
  MWPC with CsI
AMS
Cosmic radiation
Separation of relativistic ions (A≤15), 1< p/A<10 GeV/c
Radiator
  NaF + aerogel
  C4F10
photodetector:
  MAPMT
Photodetector plane (680 MAPMTs)
Radiator(s)
Conical mirror

## Slide 106: RICHes TO IDENTIFY RELATIVISTIC HEAVY IONS
EXPERIMENTS: CAPRICE stratospheric balloons (ended) AMS 2, on the Shuttle (active) HIRICH at GSI (ended)

## Slide 107: RELATIVISTIC HEAVY IONS
N_photon proportional to Z2 !
 Here photon counting pays !
Z
2
3
6
>~16
>16
He
Li
C
Si-P ?
~Fe ?
AMS test beam (at CERN, heavy ion beam): 20 GeV/N Cherenkov rings

## Slide 108: NOVEL ARCHITECTURES AND APPROACHES

## Slide 109
For future applications
  The new concepts of DIRC family
  COMPLEMENTING or ALTERNATIVE possibilities with TOF
  Multiple refractive index Aerogel for proximity focusing RICH (FARICH, BELLE upgrade)
t resolution
required ~ 10 ps
A breakthrough
in the next future?

## Slide 110: FOCUSING DIRC
A general upgrade of the DIRC concept:
Future DIRC needs to be smaller and faster
Focusing (to remove the bar thickness
dependence) and smaller pixels can reduce the
expansion volume by a factor of 7-10
Faster PMTs to remove chromatic dependence
and reduce sensitivity to background.
Photon detectors
Hamamatsu H-9500 MaPMTs
Burle-Photonis MCP-PMT
θc (mrad)
θc (mrad)
θc (mrad)
θc (mrad)
All pixels:
3mm pixels only:
Correction off:
Correction off:
Correction on:
Correction on:
σ=10.4mrad
σ=6.9mrad
σ=7.5mrad
σ=5.5mrad
Position 1
Lpath≈10m
mineral oil
J. Schwiening @ RICH2007

## Slide 111: THE TOP CONCEPT
TOP
DIRC: large screen !
Second coordinate from time measurement:
due to the different Cherenkov angle
the light path has a different length
simulation
test beam
K. Inami @ RICH2007

## Slide 112: TOF vs CHERENKOV IMAGING
J. Va’vra
@ RICH2007
TOF, 1 ps
TOF, 5 ps
TOF, 10 ps
TOF, 15 ps
TOF, 20 ps
Babar
DIRC
Aerogel
(Japan)
Test beam
Aerogel
(Novosibirsk)
MC
dE/dx, 100 meas.s
Key points:
fast Cherenkov light
rather than a scintillation
new detectors able to provide
s ~/< 10 ps
Fast electronics
Adequate for low momenta

## Slide 113: AREOGEL WITH MULTIPLE REFRACTIVE INDEX
Multiple Radiators
sc=14.4mrad Npe=9.6
2 layers of 2cm thick
n1=1.047, n2=1.057
  (Recall: pmaxns ~ 1/√sring )
Conventional
4cm thick aerogel
n=1.047
sc=22.1mrad Npe=10.7
p/K separation with focusing configuration
~ 4.8s @4GeV/c
T. Iijima @ RICH2007

## Slide 114: RICHes & PHYSICS

## Slide 115: RICHes FOR PARTICLE AND NUCLEAR PHYSICS

## Slide 116: CHERENKOV COUNTERS IN ASTROPARTICLE PHYSICS
Flying spectrometers to study CR composition
  Caprice, AMS, CREAM
(Solar and) cosmic n telescopes
  Super-K , Tunka, Amanda, Antares,
  Nemo, KM3Net
High energy gamma-ray astonomy
  Auger, HESS, MAGIC,
  VERITAS observatory, CANGAROO-III
These experiments are totally based on
the detection of the Cherenkov radiation!

## Slide 117: THANK YOU !