## Slide 1: The SPARC_LAB Thomson source
C. Vaccarezza
on behalf of the SPARC_LAB team

## Slide 2: Outline
General layout
Thomson Source design parameters
Laser & electron beam parameters
Source optimization & reference WP
Experimental results
What’s next

## Slide 3
SPARCLAB

## Slide 4: Thomson source design parameters
Photon Energy (keV) | 20÷500
Photon number per shot | 109
Source rms radius (μm) | 10
Bandwidth (%) | 10
X-ray beam characteristics

## Slide 5: APPLICATIONS @ 20-500 keV
Mammography
Identification of fissile materials
Cristallography
Microdensitometry 3D for cultural her.
Single Shot Imaging at psec time scale
(not accessible to FELs for hn > 20 keV
precluded to Sync. Light Sources, CW)

## Slide 6: Thomson Source Parameter List
FLAME Laser
Wavelength 800 nm
Compressed pulse energy 1-5 J
Pulse duration/bandwidth 6 ps
Rep.Rate 10 Hz
Beam quality M2 <1.5
Energy stability 10%
Pointing stability < 2 µm
Synchronization with SPARC photoinjector clock < 1 ps
SPARC Electron Beam
Bunch charge 100-800 pC
Energy 30-150 MeV
Length 15-20 ps
εn x,y 1-3 µ rad
Energy spread <0.1 %
Spot size at IP 5-20 µm
Rep.Rate 10 Hz

## Slide 7: A TS source driven by high-quality electron beams can work in different operating modes, e.g.:
High-flux-moderate-monochromaticity mode(HFM2) suitable for medical imaging when high-flux sources are needed
Moderate-flux- monochromatic-mode (MFM) suitable to improve the detection/dose performance
Short-and-monochromatic-mode (SM) useful for pump-and- probe experiments e.g. in physical-chemistry when tens of femtosecond long monochromatic pulses are needed.

## Slide 8: From theory
*-P. Tomassini et al Appl. Phys. B 80, 419-36 , 2005
-P. Tomassini et al. IEEE Trans. on Plasma Sci. 36,n.4, 2008

## Slide 9: HFM2 operating mode
For the first experiments the source has been optimized for applications in medical imaging, mammography in particular.
Highest X-ray flux at about 20 keV, with a relative radiation energy spread < 20% and keeping as low as possible the high harmonics contribution.

## Slide 10: The Thomson Interaction laser
Spectra of the collected radiation for pulses of duration 3, 6, 9, and 12 ps.
for
Spectral–angular (integrated in the azimuthal angle φ) distribution of the collected radiation for the optimized parameters w = 15 μm and duration T = 6 ps, where ϑM = 8 mrad

## Slide 11: The nominal case injector : 30MeV, 840pC
2007 measured beams
εx,y= 2.7 mm-mrad (at first TW Cavity entrance)
120 MV/m
(S2)=90°
(S1)=0°
t [ps]
Int.
Measured Laser-profile
εth=1.2 mm-mrad (norm. σx= 1 mm)
σt = 6.5 psec
Qbunch = 840 pC
σx,y = 0.57 mm
Energy Spread Correction
11.0 MV/m
2.0 MV/m
Off
sol. embedded
sol. embedded
z [m]
εx [mm-mrad]
0
12
6
3 mm-rad
emittance
A.Bacci

## Slide 12: e-beam envelope evolution down to IP
Twiss parameters and envelope evolution from the linac exit to the Thomson IP obtained with the TRACE3D code

## Slide 13: Source spectra simulations
q=1 mrad
q=6 mrad
Spettro
Ee=30 MeV
Ntot=1,69 109
Dw/w (FWHM)=10.5 %
Dw/w rms=5.2 %
div (FWHM)= 22 mrad
div rms= 5.3 mrad
V.Petrillo

## Slide 14: BEATS 2 experiment
I phase: Experimental verification of possible applications to breast diagnostic of the X Thomson beam produced in the laboratories of Frascati LI2FE
Scattering chamber setup – X-ray beam line setup (collimators, beam monitors, photon flux measurement) Electron beam and laser beam alignment. Collision parameter optimization for 20keV energy: stability ( flux, jitters) and spectral distribution. Imaging line installation. Topographic characterization of 20 keV X beam. Characterization of focal spot (effective area of collision). Preliminary tests of absorption and phase contrast radiography.
II phase: Monochromatic absorption radiography experiments w human tissue equivalent samples and dosimetry at 20 keV. Contrast phase radiography experiments w human tissue equivalent samples and dosimetry at 20 keV. Collision parameter optimization for 40 keV energy. Topographic characterization of 40 keV X beam. Contrast phase radiography experiments at 40 keV. Radiography experiments at the two energies and dosimetry. Collision parameter optimization at the iodine k-edge (33 keV) Differential radiography experiments at k-edge and dosimetry

## Slide 15: 1st commissioning phase configuration

## Slide 16: 50 MeV Working point 1
Charge (daily avrg):Qav= 200 ± 20 pC
Energy (daily avrg):Eav= 50.6 ± 0.2 MeV
  Launch phase: Φ= + 30°
  Laser pulse length = 8.3 ps
  S1 phase: Φ= - 20°
  S2 phase: Φ= + 65°
  S3 phase: Φ= - 90°
  Bunch length rms = 3.1 ps

## Slide 17: 50 MeV WP Emittance (best) 2
  Linac meas:
    Emittance90% emitny=1.53736 mm mrad std_emitny=0.0917644 mm mrad betay_in=35.3509 m std_betay=2.16708 m alphay_in=-2.52296 std_alphay=0.184184 sigmaX @ PTL=0 mm sigmaY @ PTL=0.74157 mm
    Emittance90% emitnx=1.20039 mm mrad std_emitnx=0.0527792 mm mrad betax_in=21.4779 m std_betax=1.10179 m alphax_in=-2.53342 std_alphax=0.171565
  PLX meas:
    Emittance90% emitny=2.39145 mm mrad std_emitny=0.118678 mm mrad betay_in=59.046 m std_betay=3.60262 m alphay_in=40.1767 std_alphay=2.4532 sigmaX @ PTL=0.540578 mm sigmaY @ PTL=1.19534 mm
    Emittance90% emitnx=1.50711 mm mrad std_emitnx=0.0688194 mm mrad betax_in=17.8999 m std_betax=0.883045 m alphax_in=-0.982182 std_alphax=0.11063

## Slide 18: e-beam envelope evolution in the linac
Electron beam emittance (blue curves) and envelope evolution (black curves) from the photocathode to the linac exit calculated with the Astra code.
The dots represent the beam spot measurements taken in this configuration at screen locations along the linac.

## Slide 19: 50 MeV WP Emittance 3
  Thomson meas:
    Emittance90% emitnx=4.82406 mm mrad std_emitnx=7.12887 mm mrad betax_in=3.41413 m std_betax=1.37934 m alphax_in=1.82552 std_alphax=2.21207
  IP beam size w solenoid:
  X Sigma (mm) 8.913322E-2 (2.688746E-3)
  Y Sigma (mm) 8.826175E-2 (3.250392E-3)
  X centroid (mm) 1.634655E+1 (5.039738E-2)
  Y centroid (mm) 1.007501E+1 (2.500132E-2))

## Slide 20: Beam size at IP w photon signature
X Sigma (mm) 2.374734E-1 (8.227418E-3)
Y Sigma (mm) 1.597200E-1 (1.249213E-2)
X centroid (mm) 1.341996E+1 (6.399130E-3)
Y centroid (mm) 1.236400E+1 (8.072908E-2)

## Slide 21: The synchronization system

## Slide 22: The synchronization system

## Slide 23
Front view (shielding)
Rear view (PMT)
Detector: PMT+CsI scintillator

## Slide 24
We also checked that the signal is absent if only FLAME is on (no e- beams)

## Slide 25
The signal is (almost) completely attenuated by 0.5 mm of Pb.
This is in agreement with the attenuation characteristics of the expected X-rays

## Slide 26: Since July 2014:
  To recover the most critical issues: background and beam-beam overlap:
  Dumping dipole installation (delivered Jan 2014) w tapered pipe to the flag.
  Parabolic mirror Chamber & Interaction cross alignment
  Solenoid cooling system decoupling from RF system

## Slide 27: New IP configuration:

## Slide 28: 2015 Activity
Thomson Source low-high energy characterization
Beats2 experiment completion
Electron energy distribution after interaction study