## Slide 1: HoW Fast an Earthquake Early Warning can Be Issued
Gaetano Festa, Aldo Zollo, Simona Colombelli,
Matteo Picozzi, Alessandro Caruso
Dipartimento di Fisica; Università di Napoli Federico II

## Slide 2: Summary
Earthquake Early Warning
Concepts
Methods
Southern Italy application
Next generation of ew systems

## Slide 3: Time scales of seismic hazard
decades
years
days
Early
Warning
Long-Term
Forecasting
Short-Term
Forecasting
& Prediction
Long-term
Hazard
Mapping
ShakeMaps
&Rapid Loss Assessment
0
minutes
Earthquake
seconds
days/
months
Aftershock
Hazard
From REAKT
REAL-TIME SEISMOLOGY
Notes: 3

## Slide 4: Fundamentals of EW
Based on the difference between the propagation velocity of the seismic waves and radio signals or cable
The information about earthquake ground shaking can reach a target “potentially at risk” from a few to tens of seconds before the arrival of the largest amplitude seismic waves.

EPIC
S-wave velocity:
around 3.5 km/sec
TARGET
Light speed:
around 3x105 km/sec
Notes: -

## Slide 5
 |  |  |  | 17 | 15 | 13 | 11 | 9 | 7 | 5 | 3 | 1
0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24
SECS AVAILABLE TO TARGET
NAPLES
85 km
C
TARGET
Early Warning Time-Line – PRESTo PLUS
SECS FROM ORIGIN TIME
Origin Time
P-Waves at
1st Station
P
On-Site
Alerts
Probabilistic
Location
Bayesian
Magnitude
Regional Scale
Peak Ground Motion
PDZ - Probable
Damaged Zone
S-Waves
At Target

## Slide 6: Worldwide EWS

## Slide 7: Regional vs Onsite EW
Epicentral Area
✹
Warning (Light/connection Speed)
Early Warning
~ 10- 30 s
Postevent
~ 10 min
Telemetry
Event detection
TP
TStarget
Time
T0
P Waves (5-6 km/s)
S/Surface Waves (3,3.5 km/s)
Regional
Onsite
S/Surface Waves (3,3.5 km/s)
target
Lead-time
(S-target)- (first-P network )
(P-target)- (S target )

## Slide 8: P-wave based Early Warning
Objective:
estimating fast and reliably the earthquake’s damage potential

## Slide 9: Lead-times for P-wave based EWS
The expected lead-time of Regional system increases with distance and is larger than for On-site systems for d>50 km.
On-site systems can provide fast warning to targets close to the epicenter.

## Slide 10
In a dense network accurate location can be obtained within 3-4 s from OT
Events in the network outskirts require a longer time for the location to converge (6-10s)
Real Time Earthquake Location (RTLOC)
Satriano et al., BSSA,2008

## Slide 11: Magnitude: an empirical approach
Pd = peak displacement
τc = average period
log Pd = A + B * M + C log R
log τc = A' + B' * M
Data from Japan,Taiwan, and Italy
Data from European SM data-base

## Slide 12: Real Time Magnitude
Basic Concepts
Use of information carried out by early P- and S-waves recorded at a dense, high dynamics network deployed in the source area of earthquakes
Determine empirical regression laws between real-time measured ground motion parameters (dominant period, peak displacement) and magnitude
At each time step after first P, evaluate the magnitude using an evolutionary approach and combining P and S information at all recording stations
Notes: The real time magnitude: basic concepts
- Information from few seconds of initial P- and S-wave signals
- Empirical regression laws relating the measured parameter and magnitude
- Probabilistic and Evolutionary combining the available P- and S- information

## Slide 13: Offline application: The 1995 Kobe Eqk
Probability to exceed M 6.5 and M 7.0 thresholds as a function of time
M 6.5
M 7.0
Magnitude vs Time
Lancieri & Zollo, JGR, 2008
P(m|d) vs Time
Notes: We show the time evolution of the PDF and related magnitude as a function of time, with uncertainty. The initial magnitude from the closest station largely underestimate the earthquake size, while the arrival of P- and S data from distant stations 6-7 seconds after the first arrival contribute to improve the accuracy on the magnitude estimation. The available PDF allows to compute the probability to exceed a given magnitude threshold as a function of time. We observe that after about 6 sec the probability for the event to exceed M 6.5 become stable with time, thus providing with a usefull information for alert notification.

## Slide 14: Prediction of peak ground motion at the target site
Use of existing Ground Motion Prediction Equations (GMPE) for PGV,PGA, …
At each time step, the instantaneous attenuation curve can be built given the estimated values of M.
The map of predicted PGX is obtained by calculating the expected value of ground motion parameter, given the estimated Magnitude and Distance (from eqk location)
Increasing Magnitude
Log( Epicentral distance)
Log( Peak Motion amplitude)
D1
D2
M1
M2

## Slide 15
T0
PRESTo PLUS Playback of L’Aquila 2009, ML 5.9 Eqk
Epicenter
Vulnerable Site
S-Waves
Station
Alert Level
Magnitude
Accelerograms
P- and S-waves Windows
Depth
Notes: Off-line application and testing of PRESTo+ for the 2009, Mw 6.2, L’Aquila earthquake in Central Italy

## Slide 16: Issuing an EW alert: Can we by-pass the Magnitude estimation?
Observed correlation between PD and PGV (Wu & Kanamori, 2005)
For moderate to strong eqks PGV is related to seismic intensity
Using PD and Tau for setting up an alert decision table
From Kanamori, 2005

## Slide 17: A Threshold-Based Early Warning
Initial P-peak displacement (Pd) correlates with whole-record Peak Ground Velocity.
Pd>0.2 cm  PGV > 16 cm/sec  IMM> VII : DAMAGING EQK!
Initial P-period parameter (tc) correlates with final magnitude. tc > 0.6 sec  M> 6
Japan
Taiwan
Central Italy
Alert levels |  |  | 
Damages nearby & far away from the station | Damages only nearby the station | Damages only far away from the station | No damages
3 | 2 | 1 | 0
Alert levels and threshold values for Pd and tc
Zollo et al., GJInt,2010

## Slide 18
PGV  IMM
IJMA
PDZ
Colombelli et al., 2011, Test of a threshold-based Earthquake Early Warning method using Japanese data, Bull.Seism.Soc.Am.
Test of the Threshold Method on Japanese Eqks
Qualitative comparison of the
Threshold Early Warning method
with IMM maps of
three Mw>6 earthquakes in Japan occurred during the last decade

## Slide 19: Southern Italy –ISNet & INFO

## Slide 21: Toward next EWS generation
Real time GPS application
Low-cost sensors
NEW
EWS
Different initial Pd slope
Early Warning for
Mega-Earthquakes

## Slide 22: Future challenges
Robustness
Time
Actual
Future
Blind
zone
Past
Future
Real time continuous
data processing
A-priori
Bayesian
combination
HPC
Evolutionary
Ground shaking