## Slide 1: Results of the 1st EUSO-Balloom flight
Hiroko Miyamoto
for the JEM-EUSO Collaboration, EUSO-Balloon Collaboration
Universita' degli studi di Torino/INFN
SIF 2015 September

## Slide 2
Extremely High Energy Cosmic Ray (EECR) observatory onboard of International Space Station (ISS)
Observing Extensive Air Shower (EAS) produced by the EECRs
wide FoV (+-30°)
Near UV: 300 ~ 400 nm
Temporal resolution: 2.5 us
Spatial resolution: 500 m on the ground
JEM-EUSO telescope
Nadir mode
JEM-EUSO schematic view
Fresnel lens #2
Precision Fresnel lens
Iris
Fresnel lens #1
Focal surface detectors
Support of focal surface
Electronics
~140 PDMs (0.3 M pix) on 2.3 m diameter
Focal Surface. ±30° large Field of View (FoV)
~140 PDMs
64ch-MAPMTs
x ~5000
1PDM
7
Coverage between lattitude of ±51.6°
Noth to Southof the earth by ISS orbit

## Slide 3
1. EUSO-BALLOON:
1st balloon flight from
Timmins, Canada
(French Space Agency
CNES) 2014
2. TA-EUSO:
Ground detector at
Telescope Array site:
2015-
3. MINI-EUSO
(ASI/INFN/Roscosmos)
2017
4. EUSO-SPB
(NASA) 2017
5. JEM-EUSO
(>2020+)
The EUSO program
MINI-EUSO
(2017)
400km
30°
JEM-EUSO
250 km
5
About 300 researchers from 88 institutions of 16 countries !
EUSO-SPB(2017)/

## Slide 4: EUSO-Balloon
A balloon-borne fluorescence telescope, pathfinder of JEM-EUSO
1 PDM with electronics and mechanics as close as possible to JEM-EUSO
DAQ & BG study
Detection EAS > ~1018eV from an altitude of 40km (optinal. expected 0.2-0.3events with E>2×1018 eV during 10 hours night-flight)
Projects CNES (Le Centre national d’études spatiales) supported
by the whole JEM-EUSO collaboratio
(88 institutets from 16 countries)
Italiy supported by INFN
 | JEM-EUSO | EUSO-BALLOON
Height [km] | 420 | 40
Diameter [m] | 2.5 | 1
FoV/pixel [deg] | 0.08 | 0.25
Pixel@ground [m] | 580 | 130
FoV/PDM [deg] | 3.8 | 11-12
PDM@ground [km] | 28.2 | 8.4
Signal Ratio | 1 | 17.6
BG Ratio | 1 | 0.9-1.8
S/√N | 1 | 20-10
Eth [eV] | 3×1019 | 1.5-3×1018
# of PDM | 137 | 1
1st launch was successfully carried out on August 24-25th 2014, Timmins, Canada!!

## Slide 5: EUSO-Balloon Instrument
Instrument
• Mechanical structure (gondola)
• Optics: 2 flat Fresnel lenses (L1&L3)
• 1 Photodetector Module (PDM)
• Data acquisition system (DAQ)
• Monitoring controlled by House Keeping system (HK)
• A set of power supplies (LVPS) powered by onboard batteries (Power Pack)
• An IR camera for atmospheric monitoring

## Slide 6: EUSO-Balloon Data Acquisition (DAQ) Chain
Front-end (FE) electronics
PMT
• Hmamatsu 64-ch MAPMT
• BG3 filter
EC-Unit
• 4 PMTs (256-ch)
readout cables
• HV board
• potting
Sensor (photodetector)
EC-ASIC
• 6 x ASICs
• readout
• counter
PDM-Board
• Slow control
CPU
• Run control, config. FE electronics
• Console & GUI, remote access, etc.
• Data processing
• managing Mass Memory for data
storage
CCB
(Cluster Control Board)
• Receive data
from 9 PDMs
Data Processing (DP)

## Slide 7: EUSO-Balloon Data Acquisition (DAQ) Chain
Front-end (FE) electronics
PMT
• Hmamatsu 64-ch MAPMT
• BG3 filter
EC-Unit
• 4 PMTs (256-ch)
readout cables
• HV board
• potting
Sensor (photodetector)
EC-ASIC
• 6 x ASICs
• readout
• counter
PDM-Board
• Slow control
CPU
• Run control, config. FE electronics
• Console & GUI, remote access, etc.
• Data processing
• managing Mass Memory for data
storage
CCB
(Cluster Control Board)
• Receive data
from 9 PDMs
Data Processing (DP)
PDM
• 9 EC-Units (36 MAPMTs, 1024 pix)

## Slide 8: EUSO-Balloon Data Acquisition (DAQ) Chain
Front-end (FE) electronics
PMT
• Hmamatsu 64-ch MAPMT
• BG3 filter
EC-Unit
• 4 PMTs (256-ch)
readout cables
• HV board
• potting
Sensor (photodetector)
EC-ASIC
• 6 x ASICs
• readout
• counter
PDM-Board
• Slow control
CPU
• Run control, config. FE electronics
• Console & GUI, remote access, etc.
• Data processing
• managing Mass Memory for data
storage
CCB
(Cluster Control Board)
• Receive data
from 9 PDMs
Data Processing (DP)
HK, LVPS
IR camera
PDM
• 9 EC-Units (36 MAPMTs, 1024 pix)

## Slide 9: The realization

## Slide 10
Balloon
EUSO
detector
8 km
~38 km
Testing EUSO-Balloon
Fly one aircraft equipped with
three types of calibrated pulsed UV light sources.
Point Test: Fly airplane in field of view and fire flash lamp and UV LED. Light travels directly from lamp to detector
Track Test: Fly airplane outside field of view and shoot a UV pulsed laser across field of view. Light scatters out of the beam to the detector.
(15 mJ Laser ~100 EeV Cosmic Ray)
Fly aircraft at altitudes between 3.1 km.
Field of View
Helicopter equipped with
YAG laser, UV LED and Xenon flasher
EUSO-BALLOON ‘‘in flight’’ calibration
11°
scattered light
3.1 km
Calibrated
Flash lamp

## Slide 11: The Flight Campaign
Aug 12th : equipment arrived in Timmins (Ontario)
Aug 19th : EUSO-Ballon en configuration for the flight
Aug 24th : Ideal flight (40mn + 5h10 flight)
Aug 25th : recover of the instrument

## Slide 12: Balloon Flight Trajectory
Data acquisition with HV: started at 2:54 UTC, ended at 8:07 UTC
Total flight duration: 5h10 + 40mn

## Slide 13: Balloon Flight Trajectory (altitude included)
Balloon stayed at ~38km altitude during the measurement

## Slide 14: First Light (images of Timmins city light)
2hrs after launch (2:54~2:55 UTC) Balloon altitude 33.5km
GoPro image
PDM SCURVE data
PDM CPU_TRIGGER data

## Slide 15: Balloon Flight Trajectory
Helicopter Trajectory

## Slide 16: Laser flasher event

## Slide 17: Laser flasher event

## Slide 18: Laser track
Event profile

## Slide 19: Analysis Ongoing
UV background measurement
Trigger study
Reconstruction of laser tracks

## Slide 20
Simon Mackovjak: Progress of UV background analysis from EUSO-Balloon data

## Slide 21: Results on UV background
10 km
S. Macovjak et al. (JEM-EUSO collaboration), ICRC #1302 (2015)

## Slide 22
UV Background and Atmospheric Conditions
S. Macovjak et al. (JEM-EUSO collaboration), ICRC #1302 (2015)

## Slide 23
Important for JEM-EUSO:
Best conditions for measuring EAS
S. Macovjak et al. (JEM-EUSO collaboration), ICRC #1302 (2015)

## Slide 24: Typical LED-laser-Xe_flasher event
Image of one helicopter event obtained by integrating the counts in each pixel for the whole packet=1960 of RUN=043202 (128 GTUs). A threshold is applied to the minimum signal level to emphasize the location of the track. The UV-led and Xe-flasher signals are centered around pixel (X=5;Y=26).
G.Suino (INFN-TO) et al. (JEM-EUSO collaboration), ICRC #0925 (2015)

## Slide 25: Time evolution of the signal in the underlined 3x3 pixel box
Triggers in this packet in the entire PDM
Number of counts recored in the 3 3 pixel-box
centered around (X=5;Y=26) during the entire packet.
Sequence of trigger alerts in the different ECs where
the pixel (X=5;Y=26) is located during the entire packet.
EC4
EC5
EC6
The minimum signal required to trigger should exceed the average background level by 2.1 + 0.3 times.
G.Suino (INFN-TO) et al. (JEM-EUSO collaboration), ICRC #0925 (2015)
LED
laser
Xe flasher
afterpulse Xe flasher

## Slide 26: Data Analysis
B. Panico & F. Guarino (INFN-NA) et al. (JEM-EUSO collaboration), ICRC #1155 (2015)
OffLine

## Slide 27: Reconstruction of laser tracks
J. Eser et al. (JEM-EUSO collaboration), ICRC #0860 (2015)

## Slide 28
Summary
~2560000 packets (128 GTU/packet) acquired during the flight in 5 configs
8 GB transferred to ground during the flight while 83GB of data registerd on the disks
Telemetry data (voltages, currents and temperatures) transferred to ground during the flight
Trigger modes:
  CPU trigger .OR. GPS 1 pulse per second
  GPS 1 pulse per second .OR. 20 Hz clock
Demonstrated almost all the functions of equipment as intended including water tightness which was not expected this time
Conclustions
EUSO-Balloon 1st flight helped raising the TRL (Technical Rediness Level) of JEM-EUSO system and proved that the technique works!
The UV intensity was measured on many different conditions: grass, forest, lakes, city light, clouds with excellent spatial and temporal resolutions! Results in general agree with expectations.
It was proved that such a system can see and track EAS-like events.

## Slide 29: Landing and recovery

## Slide 30: Thank you for your attention!

## Slide 31: Thank you for your attention!

## Slide 32: Backup slides

## Slide 33: Trigger behavior on different background levels
Nominal Background | ~8.5 s |  | 
Method | Laser | Others | rate others
Box-bckg | 128 | 56 | 6.6 Hz
Pixel-bckg | 126 | 17 | 2.0 Hz
Urban-like Background | ~6.5 s |  | 
Method | Laser | Others | rate others
Box-bckg | 149 | 1941 | 299 Hz
Pixel-bckg | 148 | 59 | 9.1 Hz
The two methods provide comparable results on laser events
The Pixel-box method is more powerful in rejecting high-level background conditions
G.Suino & M. Mignone (INFN-TO)
33

## Slide 34
34
I. Tabone (INFN-TO)

## Slide 35
Entries : 33
Distribution of (counts-noise)/(counts-noise)_3x3
vs size of boxes
Results more compatibile with RMS spot size: ~3x3 box
 |  |  |  |  |  |  |  |  |  | Z9 | 
 |  |  |  |  |  |  |  |  | Z7 |  | 
 |  |  |  |  |  |  |  | Z5 |  |  | 
 |  |  |  |  |  |  | Z3 |  |  |  | 
 |  |  |  |  |  | Z1 |  |  |  |  | 
 |  |  |  |  | Z2 |  |  |  |  |  | 
 |  |  |  | Z4 |  |  |  |  |  |  | 
 |  |  | Z6 |  |  |  |  |  |  |  | 
 |  | Z8 |  |  |  |  |  |  |  |  | 
 | Z10 |  |  |  |  |  |  |  |  |  | 
M. Rouissat & L. Conti (INFN-RM2)

## Slide 36
36
I. Tabone (INFN-TO)

## Slide 37: Summary
~2560000 packets (128 GTU/packet) acquired during the flight in five configurations
83 GB of data registered on the disks
8 GB transferred to ground during the flight
Telemetry data (voltages, currents and temperatures) transferred to ground during the flight
Trigger modes:
  CPU trigger .OR. GPS 1 pulse per second
  GPS 1 pulse per second .OR. 20 Hz clock
Demonstrated almost all the functions of equipment as intended including water tightness which was not expected this time (possibility was low, prepared mainly for soil landing)

## Slide 38: CNES Flight Chain
valve
covering
Discharge sleeve
Remote separator
Parachute tension
Operational servitude pod (NSO)
Radar refector
Beacon
Alticoder radar
responder
dampers
(EUSO-BALLOON main frame)
Scirnetific equipment
Scirnce telemetry pod
Main elements
of an open
Stratospheric
balloon
100 m
~ 150 m
20 m
~ 180 m

## Slide 39: Other instruments onboard
Infrared Camera (IR Camera)
NIST photodiode
Geiger counter
GPS
Attitude sensor
GoPro camera
Independent of data acquisition systems
Offline synchronization (UTC time stamps)

## Slide 40: Complementary and/or anecdotal data
  Temperature eveolution
  Cosmic ray intensity (Geiger)
  Light intensity (NIST)
  Infrared data