## Slide 1: PADME ecal studies
Mauro Raggi
PADME Kick-off meeting Frascati, 20th-21st April 2015

## Slide 2: Outline
Ecal and the gamma measurement
Possible Ecal materials
Ecal geometry constraints
Ecal in the PADME MC
Ecal Read out schematics
Conclusion and prospects

## Slide 3: Aims of the PADME Ecal
PADME Ecal is the heart of the PADME invisible experiment
Calorimeter performance reflects on the M2Miss resolution which is a crucial ingredient of the invisible decay sensitivity
Ecal is supposed to measure E, position and time of the cluster
  Dx,Dy ~ 2-3 mm
  s(E)/E ~ 1-2%/sqrt(E) for energy as low as 50-100MeV
  DT < 500 ps on single cell
Need a very dense, high light yield, good timing crystal and a segmentation at the cm2 level in the readout

## Slide 4: The calorimeter geometry
Cylindrical shape: radius 150 mm, depth > 200 mm
  Inner hole 4 cm radius
  Active volume 13120 cm3 total of 656 crystals 10x10x200 cm3
Material LSO(Ce): high LY, high r, small X0 and RM, short tdecay
Material BGO: high LY, high r, small X0 and RM, long tdecay, (free form L3?)
Expected performance for LYSO ECAL:
  s(E)/E =1.1%/√E ⨁ 0.4%/E ⨁1.2% superB calorimeter test at BTF [NIM A 718 (2013) 107–109]
  s(q) = 3 mm/1.75 m < 2 mrad
  Angular acceptance 1.5-5 degrees
30 cm

## Slide 5: LYSO performance
NIM A 718 (2013) 107–109
M. Cordelli, G. Corradi, F. Colao, S. Giovannella, F. Happacher, M. Martinia, S. Miscetti, L. Morescalchib, G. Pezzullo, I. Sarra, and S.R. Soleti
Mu2e DocDb # 5377
Courtesy of Mu2e INFN group.
Preliminary
Mu2e LYSO matrix time resolution
SuperB prototype
constant term due to trigger
Obtained in a test beam at BTF

## Slide 6: PADME calorimeter simulation
15 cm long LYSO crystals
20 cm long LYSO crystals

## Slide 7: MC calorimeter performance
Missing mass resolution in agreement with toy MC using
  s(E)/E =1.1%/√E ⨁ 0.4%/E ⨁1.2% [NIM A 718 (2013) 107–109]
  Differences are ~ 10%
Resolution is the result of combination of angular resolution energy resolution and angle energy correlation due to production
Mmiss2(MeV)

## Slide 8: Cost of a LYSO calorimeter
Official quote from Saint Gobain for more than 250 LYSO crystals of 10x10x200 mm3 650 euro/pcs
  Tolerance 0.1 mm in side and 0.2mm in length.
  10-12 weeks after acceptance of order by Saint Gobain
Scaling the price to the full calorimeter ~700 pcs ~455Keuro
Opportunity to have even smaller crystals explored can reach 4x4x210 mm increasing spatial resolution of the ecal.

## Slide 9: L3 BGO calorimeter performance

## Slide 10: PADME ecal using L3 BGO crystals
What about collecting the L3 calorimeter BGO?
We collected ~80 BGO crystal from L3 calorimeter.
Negotiation started by INFN and DOE to get more crystals ~200 pcs.

## Slide 11: Cutting the L3 BGO crystals
On 13 of April we went to Silo (FI) to start crystal cutting procedures
We already have 3 crystals in @ Silo firm to get back:
  4 crystals 10x10x200 mm optically polished
  4 crystals 10x10x220 mm optically polished
  4 crystals 10x10x220 mm raw surfaces
We expect to get the crystals back for the end of April
Present cost of the cutting is 200+VAT per original L3 crystals
  4 PADME crystal per 250 euro
  Cutting order 200 L3 crystals will cost 50Keuro to be compared with 450K

## Slide 12: Missing mass and Ecal resolution
LYSO
L3 BGO
Are we able to get the same figure of merit with PADME Ecal?

## Slide 13: Calorimeter photosensors
The basic solution for the photo sensors is APD S8664-55
  High gain
  Linear on full range
  Price 120 euro/pcs (~1000 pcs)
SiPM Hamamatsu: MPPC S12572-010P, -015P, -025P
  3x3mm2 MPPC 1.3x105 gain
  Number of cells: 90000, 40000, 14400
  Is it linear for 10x10x200 mm3 BGO crystals up to 300-400 MeV?
  We have few of them to try linearity at the BTF in may
  Price 17 euro/pcs.
Cost of photo sensor solution is ~10 times smaller with SiPM

## Slide 14: QE and GAIN APD vs SiPM
MPPC
APD

## Slide 15: BGO and LYSO with APD

## Slide 16: Ecal front-end electronics?
- Charge or Transimpedence preamp and detector
- Voltage regulator programmable.
TOP side View
Detector linear voltage regulator
BOTTOM side View. Charge preamp View.

## Slide 17: Calorimeter readout
Minimum effective threshold < 12 mV
Small dispersion (RMS = 1.3 mV)
High and Low threshold channels can be swapped reducing the minimum threshold
Threshold (mV)
A3818
PCI Express CONET2 Controller
PCIExpress x8 card 4 independent optical links
CONET2 CAEN Proprietary Optical link Compatible
Up to 32 CAEN CONET2-compliant Optical slave cards (CAEN VME Bridges or Waveform Digitizer) controlled by a single A3818
Data Transfer rate up to 85MB/s per link
12-bit @ 5 GS/s, 1024 samples per event
5, 2.4,1 GS/s selectable sampling frequencies
VME64/VME64X (32 ch.)
Special analog inputs 2 ch.
1 Vpp input dynamic range with programmable DC offset adj.
16 programmable LVDS I/Os
Daisy chain capability
V1742
PCI Express CONET2 Controller

## Slide 18: Calorimeter readout model
Needs 21 V1742 to collect a total of 656 channels
All the board receive the trigger from BTF in daisy chain (50 Hz)
  On each trigger all the boards digitize all channels and send data to optical links
4 V1742 digitizers connected on each of the 4 optical receiver on A3818 installed in the server
  16 V1742 boards per A3818 on a single server
A3818
Server
CAEN V1742
All the chain already available test will start in May for the PADME test beam.

## Slide 19: Calorimeter readout data load
Data transfer rate per each A3818 optical link with 4 V1742
  Max samples per channel: 1024
  Nbits per sample: 12
  Number of channel per link = 32x4 =128ch
  Without zero suppression = 128x12x1024x50 = 78Mbit/s ~1/8 of the A3818 nominal bandwidth
Total Ecal data transfer to server
  Without zero suppression = 656x12x1024x50 = 403 Mbit/s

## Slide 20: Calorimeter readout cost
Item | Npieces | Unit cost | Total cost
VME 6U crate | 2 | 5000 | 10K€
VME 1742 | 22 | 8000 (CAEN quote 2pcs) | 176K€
A3828 | 2 | 2500 (CAEN quote 1pcs) | 5K€
Servers | 2 | 4000 (already have 1) | 8K€
Total |  |  | 200K€+44K€ I.V.A
Electromagnetic calorimeter readout
  656 channels required for digitization
  2 VME 6U crates
  21 boards V1742 = 672 channels
  2 A3818 = 4 boards on each optical link (4Boards/link x 4links/board x 2boards = 32 boars max)
  2 server PC with 2 PCIExpress x8

## Slide 21: Global Ecal cost estimate
Item | Solution BGO | Solution LYSO
Crystals | 50Keuro | 450Keuro
ReadOut | 250Keuro | 250Kero
Front End | 100Keuro?? | 100Keuro??
Photo sensors | 80K APD/12K MPPc | 80K APD/12K MPPc

## Slide 22: SPARE SLIDES