## Slide 1: High intensity electron beam and infrastructure
Paolo Valente*
INFN Roma
*On behalf of the BTF and LINAC staff

## Slide 2
BTF
BTF
control room
Damping
Ring
transfer line
transfer line
Main rings
LINAC
Power supplies
The DAFNE complex

## Slide 3
The DAFNE LINAC
 | Design | Operational
Electron beam final energy | 800 MeV | 510 MeV
Positron beam final energy | 550 MeV | 510 MeV
RF frequency | 2856 MHz | 
Positron conversion energy | 250 MeV | 220 MeV
Beam pulse rep. rate | 1 to 50 Hz | 1 to 50 Hz
Beam macropulse length | 10 nsec | 1.4 to 40 nsec
Gun current | 8 A | 8 A
Beam spot on positron converter | 1 mm | 1 mm
Normalized Emittance (mm mrad) | 1 (electron) 10 (positron) | < 1.5
rms Energy spread | 0.5% (electron) 1.0% (positron) | 0.5% (electron) 1.0% (positron)
electron current on positron converter | 5 A | 5.2 A
Max output electron current | >150 mA | 500 mA
Max output positron current | 36 mA | 85 mA
Trasport efficiency from capture section to linac end | 90% | 90%
Accelerating structure | SLAC-type, CG, 2π/3 | 
RF source | 4 x 45 MWp sledded klystrons TH2128C | 

## Slide 4
DAFNE LINAC gun
Pulse charge: gun
During parasitic operation, pulse duration is fixed at 10 ns for the injection into the damping ring
Bunched structure at 2856 MHz is visible with a good enough timing resolution
Typical charge: 1–2 nC for e-, 0.5–0.8 for e+
  i=100 mA current corresponding to 1 nC/10 ns
10 ns, 100 mA
40 ns, 150 mA
10 ns, 100 mA
10 ns
4

## Slide 5
Increasing the charge: pulse width
Scales linearly up to 40 ns: 4×
E = 725 MeV
Standard setting
Present gun pulser: from 1.5 to 40 ns in 0.5 ns steps
Working to further extend the pulse width (see presentation on positron beam for PADME)
In principle, the gun cathode produces a current, thus no limitation expected in emitted total charge increasing the pulse width!
Of course, cathode consumption will be also much faster

## Slide 6
Increasing the charge: gun voltage
Scales more than linearly up to 420 V: 3×
E = 725 MeV
10 ns
Standard setting
Present gun pulser: from 300 to 750 V in steps of 30 V
More measurements needed in dedicated mode

## Slide 7
Increasing the charge
E = 725 MeV
10 ns
Decreasing the “stopping” voltage applied to the grid should increase the extracted charge
Standard setting
Increasing the pulse width and the gun voltage at the same time: saturation of current monitors at 16 nC
More measurements needed in dedicated mode

## Slide 8: Possible beam parameters for electron dump experiments
Measured maximum energy: E=725 MeV
Conservative value: Q=25 nC
  40 ns pulses
  8.5 nC ×3 gain using grid and gun pulse height
  Ne = 1.6·1011 e/pulse× 49 pulse/s= 0.784·1013 e/s
  P = 0.9 kW
  0.784·1013 e/s × 3·107 s = 2.4·1020 eot
Further increase by enlarging the pulse time width to >100 ns
  Gun extraction saturation and beam loading effects to be checked
Full gain extrapolation: Q=50 nC
      Single factors well measured
      But the combination of pulse height, length and grid voltage has to be tested
      As a comparison, the design intensity on positron converter is 1.44·1013 e/s at 10 ns
        Efficiency of the acceleration & transport has to be considered

## Slide 9
Maximum intensity in BTF hall
Authorization limit is 3.125 1010 particles/s
1 Hz operation
No more than 1018 eot/year
Where to dump the maximum available electron charge?

## Slide 10
Beam dump at the end of LINAC to damping ring transfer line
LINAC beam dump

## Slide 11
LEALE, “Sala pioni”, “Cella calda”, drawings of 1964-1969

## Slide 12
LEALE line, drawing sent to authorities in 1991
The ADONE LINAC beam dump

## Slide 13
130 cm
100 cm
40 cm
200 cm
75 cm
[dimensions estimated from drawing scale]
The ADONE LINAC beam dump

## Slide 14
“Livello 1”

## Slide 15
DHPTT01
Check depth/exact composition of the dump and the wall behind
Move or dismantle pumps in order to use the pump hall behind the wall
Build (two-exits) new vacuum pipe for DHPTT01
Check doses vs. beam intensity
A possible location for dump experiments
DR Pumps hall

## Slide 17
Conclusions
The DAFNE LINAC can provide >1011 e-/bunch in 40 ns long pulses at 49 Hz
There is room for a further increase of the delivered charge, both increasing the pulse width and pushing the gun emission
  Limits of this charge increase to be checked experimentally
  New hardware for longer pulses is needed
It is possible to dump the electron beam at the end of the transfer line towards the damping ring
Room for an experimental installation downstream of the dump is available (but work is needed to make it available)
Radio-protection is the primary issue