## Slide 1: Controls and Computing First Ideas
PADME Kick-Off Meeting – LNF, April 20-21, 2015
Emanuele Leonardi
INFN Roma

## Slide 2
DAQ Data Rate - Preliminary estimate
Tentative setup: all channels read with Fast ADC
1024 samples, 12 bits per sample → 1536 Bytes per channel per event
Beam rate: 50 Hz
Data source | # channels | Data rate (MiB/s)
Active target | 32 | 2.3
Hodoscope | 200 | 14.6
Calorimeter | 656 | 48.0
SAC | 4 | 0.3
Positron veto | 50 | 3.7
Total |  | 69.0
Preliminary DAQ L0 Rate

## Slide 3
After L1 (zero suppression)
Data source | # channels |  | Data rate | 
 | Total | 0-supp | MiB/s | TB/y
Active target | 32 | 6 | 0.44 | 14.5
Hodoscope | 200 | 5 | 0.37 | 12.1
Calorimeter | 656 | 25 | 1.83 | 60.6
SAC | 4 | 4 | 0.29 | 9.7
Positron veto | 50 | 5 | 0.37 | 12.1
Total |  |  | 3.30 | 109.0
Notes:
Occupancies from MC studies
1 year = 365 days of data taking
No event selection: all events are written to disk
ROOT can give a 30-50% data compression factor when writing data to disk
RAW data keeping full
ADC samples

## Slide 4
Reconstruction format (RECO)
Energy/Time per Channel
Physics objects (Clusters/Tracks)
O(10 TB/y)
Analysis format (ANAL)
Physics objects only
O(1 TB/y)
RAW data
L2

## Slide 5
Storage requirements
~2 TB/Production Unit
Monte Carlo production - Storage
Production Unit
1013 e+ i.e. 2x109 bunches of O(5000) e+
N.B. 1 bunch = 1 MC event
Event size: O(1KB/event)
Includes only E,t for
each active channel
If we want 10x statistics each year: ~20 TB/y

## Slide 6
Full GEANT4 simulation of the experimental setup
Running on a HP Proliant DL560 server
  4 Intel Xeon E5-4610v2 @ 2.3GHz (32 cores)
  128 GB ECC RAM
Monte Carlo production - CPU
Use of GRID for MC production under investigation
Current MC production rate:
3 Hz/core (3 bunches per second per core)
10 production units per year → 37 days per production
CPU power needed: 210 cores, i.e. 7 servers.

## Slide 7
Disk costs: 0.2 K€/TB
Tape costs: 0.1 K€/TB
CPU: 6K€ per server (32 cores)
All data (RAW+RECO+ANAL) written to tape
10% RAW + 100% RECO + 100% ANAL kept on disk
Costs
 | Disk |  | Tape | 
 | TB/y | K€/y | TB/y | K€/y
Data | 20 | 4 | 120 | 12
MC | 20 | 4 | 40 | 4
CPU: 7 server → 42 K€
Accessories: racks, networking, cables, … → O(10 K€)

## Slide 8
Informal preliminary meeting with Massimo Pistoni, head of the LNF IT services, on April 1st.
Space, power, cooling, UPS, network are available.
No technical problems to host computing resources for PADME.
IT @ LNF – Central services
Computing Center
Allocate computer room resources for PADME ASAP
BTF
Caveat
New collaboration INFN-INAF
LNF will be asked to host computing resources for the CTA/SKA project.

## Slide 9
Cloud-based storage is being investigated by INFN (CNAF, LNGS, To)
Good scaling properties (PB and beyond)
Automatic and configurable redundancy (not RAID-based)
Lower cost per TB → SAN ~200€/TB vs. Cloud ~100€/TB
IT @ LNF - Disk
A Storage Area Network (SAN) exists
EMC2 CX500 (120 disks) + CX300 (60 disks)
Hitachi-Storagetek 9985V (up to 240 disks)
2 Switch FC Brocade DS4900B
  2x32 ports @ 4 Gbps
It can host storage for PADME but the current SAN infrastructure (servers and switches) is close to saturation
  Bottlenecks are possible
  Might need an upgrade

## Slide 10
Two tape libraries are available.
IBM 3494
  1000 slot
  4 Magstar 3592, 300 GB/tape, 40 MB/s
StorageTek L1400
  700 slot (max 1400)
  2 STK 9940, 200 GB/tape, 30 MB/s
Both have spare cartridge slots and can be upgraded with TB-class tape drives.
Alternative: buy a new LTO tape library
Format | Capacity (unc.) | Transfer rate (unc.) | Cost per tape | Cost per TB | Availability
LTO-6 | 2.5 TB/tape | 160 MB/s | 50 € | 20 € | Now
LTO-7 | 6.4 TB/tape | 300 MB/s | (?) | (?) | End 2015
IBM 3494
STK L1400
IT @ LNF - Tapes
Cost of tape storage: ≤100 €/TB (less for LTO)
Need to evaluate cost of new tape drives/library for different solutions

## Slide 11
IT @ LNF - Networking
Internal
BTF control room close to LAT room
  Existing single-mode fiber link @ 10 Gbps
BTF experimental area: currently connected @ 1 Gbps
  No upgrade planned. Should we require one?
Geographical
ATLAS T2 has a dedicated 10 Gbps link
Other traffic on a 1 Gbps link → will be upgraded to 10 Gbps soon
Computer room
Central switch with 40 ports @ 10 Gbps

## Slide 12
IT @ LNF - Services
Batch system
LSF is commonly used
Central license administered by CNAF
@LNF: batch farms are managed by each collaboration with “some support” from IT
Uses AFS to manage clients’ common area
DataBase
MySQL available. Currently used for LNF web services.
Oracle used by INFN central services
Cloud-based DB-as-a-service being investigated
GRID Computing
Used (and managed) by ATLAS T2
  M.Antonelli, E.Vilucchi

## Slide 13
Controls
Investigate solutions used by other experiments
Slow control
DAQ monitoring
Long data taking
Small collaboration
Unattended DAQ
Remote alarm system
Automatic recovery

## Slide 14
Conclusions
Data production
  Preliminary estimate of DAQ rate: ~70 MiB/s
  Data production close to 100 TB/y
MC production
  G4 simulation already quite advanced
  Storage requirements close to 40 TB/y
  Investigate use of GRID for MC production
LNF IT resources
  Well suited to host PADME computing
  Allocate computer room resources ASAP
  Investigate use of existing SAN and alternatives
  Investigate use of existing tape libraries and alternatives
Controls
  Controls must allow automatic and unattended run of the experiment