## Slide 1: New Detectors Ideas for a Possible Class of Experiments
A short list of theoretical motivations
New Possible Low Energy Active Detectors:
Ideas and Facts
Electron / Nuclear Spin Detection
Preliminary Results
G. Carugno – INFN & Padova University

## Slide 2
Processi Fisici e Basse Soglie di Energia
Emissione a 2 neutrini
Assione-Effetto Primakov
Scattering coerente di neutrino
Via EM e Debole su Nuclei
Lattice displacements
Yoshimura
Sikivie

## Slide 3: Axion Electron interaction
The interaction of the axion with the a spin ½ particle
In the non relativistic approximation
The interaction term has the form of a spin - magnetic field interaction with playing the role of an effective magnetic field

## Slide 4
ZEEMAN TRANSITION RATE With 1 Mole of Polarized Electrons
Hz Rate

## Slide 5: Neutrino Nuclear Spin Interaction
Forward Neutrino Scattering
Michael,Stodolsky,Langacker,Gelmini,Dyson
I neutrini esercitano un torque sulla particella di spin s data da :
Un Flusso di una specie di neutrino Su Materia Polarizzata e’ come se producesse
un Campo Magnetico Efficace B costante
Per flusso da reattore e spin 1/2h allora =10^-33 eV

## Slide 6: A New Class of Detectors
Rivelatori bassa energia dal KeV all’eV
basati su Mezzi Attivi:
a)Quantum Counter
b)Maser detector
Magnetometria EPR = LODER
Quantum Limited Parametric Amplifier

## Slide 7: Stato Attuale Rivelatori Basse Soglie
( Fano Factor , Quenching Factor,…)
Scintillatori : Kev (40 ph/KeV) Q.F. elevato alle basse energie , F.F. alto
Semiconduttori : 400 eV ( 1 e/h /3,6 eV Si , 100 elettroni rumore a bassa Capacita’)
MicroBolometri : 1 eV (Capacita termica totale, basse soglie MA piccole masse e mK)
Shockley

## Slide 8
Infrared Quantum Counter Idea
Bloembergen ( Nobel Prize ) suggested to detect IR photons with large Q.E. where No Phototube are available at IR wavelenght (PRL ‘59 )
Quantum Efficiency for 20 micron IR photons almost at 100% level
GAS and CRYSTALS

## Slide 9
Laser Cooling of Solid
Densita’ Fononica Cristallo KT= 25 meV
Promuove stati eccitati a bassa energia
I quali sono portati su stati eccitati elevati
Da laser tunato su opportune transizioni.
Fotone Fluorescenza emesso = Fotone laser + Fonone Reticolo

## Slide 10
Optical Cooling
Now the lowest temperature: 119+_ 1 K ( ~ -154 C)!
Opt. Letters 38 (2013) 1588-1590
Nature Photonics 4 (2010) 161-164
Opt. Express 18 (2010) 18061-18066
ab = ~ 10-4 cm-1

## Slide 11
A New Detector Approach for Low Energy Release
-Radiazione in Attraverso dE/dx o Nuclear Recoil Promuove atomi su stati eccitati
-Maggior probabilita’ P(E) = 1/E^2 su stati di bassa energia
-Campo Cristallino Mezzo Attivo rimuove la degenerazione sullo stato
Fondamentale , generando primi stati eccitati a livelli dei meV
SATURATION VALUE

## Slide 12
Scattering elettroni su Fononi Ottici
BETHE -BLOCH

## Slide 13
Tracce Elettrone Compton in Elio Liquido CCD

## Slide 15: Laser Based Scintillation: Alfa Detection NIM 2002
Neon 100Torr
Diam. Laser beam 2 mm
DE/Dx =10 KeV/mm
Tau = microsecond
Transizione saturata a 10 W/cm2

## Slide 16: Rivelatore Particelle = Sistema a 3 livelli

## Slide 20
X Rays Facility @ Legnaro
PRELIMINARY RESULTS: ( PD – PI – CA )

## Slide 21
0.5 eV
0.75 eV
Nd:YAG IR Transitions and Spectra
At Room Temperature
IR Emission Efficiency larger than 15%

## Slide 22
4I13/2 --4I15/2
Erbium:Yag Emission Spectrum
0,4% Er

## Slide 23: Double Laser Resonance Experimental Apparatus PISA
\
Monochromator
Lock-in amplifier
Detector
Crystal
Laser
Diode
Laser
Diode
lens
lens
collecting lens
chopper
fluorescence
LASER PUMP
X Rays Source
UP CONVERSION
LASER PROBE

## Slide 24
A
B
C
A:Pump @ 780 nm
B: Pump @ 635 nm
C: Emission @ 480 nm
BaY2F8: 8% Tm3+,
Tm population density: 1023 ions/cm3
Excitated populations
3F4: 8x1020 ions/cm3

## Slide 25
Double Resonace Spectrum
Pump : 3F4 ----- 1G4 ( 633 nm)
Emission: 1G4 ---- 3H6 (480 nm)

## Slide 26
Tunable CW Titanium:Zapphire Laser @ LNL
from 740 nm to 920 nm , Power higher than 100 mW

## Slide 27
MASER AS LOW RF MICROWAVE FIELD AMPLIFIER
AND NEUTRAL PARTICLE DETECTOR
Bloembergen Paramagnetic Maser 4 Level System

## Slide 28
Power Stimulated Emission :
Where
Quantum Maser Noise :
Minimum Detectable B field:
or
Minimum Cross Section Attainable:
WEAK CROSS SECTION SEEMS ATTAINABLE 10-43 cm2

## Slide 29: ESR / MR magnetometry
We exploit the Magnetic Resonance (MR) inside a magnetized material (Electron Spin Resonance - ESR)
ESR/MR resonances inside a magnetic media can be tuned by an external magnetizing field and lies in the multi GHz range (radio frequency)
1 T -> 28 GHz

## Slide 30: Experimental parameters
Axion /Photon/Neutrino En.
Equivalent RF magnetic field
Working frequency
Electron Larmor Frequency
Measurement at the quantum limit
;
Magnetizing field
Working temperature

## Slide 31: Detection issues
The working frequency lies in a region at the interface of two different regimes for best detection sensitivity
Frequency
Above 40 GHz
Below 40 GHz
FIELD DETECTION
(Linear detection)
ENERGY DETECTION
(Square detection)
- EPR Magnetometry
- MASER Amplifier
- QUANTUM COUNTER
(ZEEMAN Transitions)
In either case to reach quantum limit sensitivity 1/100 -1 mole of a magnetized sample at cryogenic temperature is necessary

## Slide 32: The Bloch equations
The evolution of the electron spin (spin precession) under the influence of external fields is described by a set of coupled non-linear equations due to Bloch (Magnetizing field H0 along z-axis)
T1 – longitudinal relaxation time
T2 – transverse relaxation time
Radiation Damping to be investigated
At low temperature T < 1 K
T1 ~ 10-6 to 10 s
T2 ~ 10-6 to 0.1 s
depends on spin density
Magnetization
N0 – spin density
mB – Bohr magneton
Ts – sample temperature

## Slide 33: Longitudinal detection of axion field
H0
We magnetize the sample along the z-axis and orient the sample in order to have the equivalent axion field ha in the transverse direction
H0 amplitude matches the searched value of the axion mass
We drive the sample with a pump field Hp at the Larmor frequency
The total driving radio-frequency field is then
ha
Hp
Also Present

## Slide 34: Longitudinal detection of axion field II
The relevant Bloch equations
A stationary solution can be obtained.
The magnetization along the z-axis (longitudinal component) shows a term modulated at the difference frequency wD.
for
Saturation parameter s
Hp, ha in Tesla M0 , mz in A/m

## Slide 35: Longitudinal detection of axion field III
If we put some relevant numbers (already published)
find the right material
power dissipated in the cryogenic system
noises in the system
T1 = 10-3 s
T2 = 3 x 10-7 s
M0 = 200 A/m
We can define some sort of gain Gm for the low frequency field component m0 mz with respect to the high frequency one ha
We obtain Gm > 1
for a pump field of Hp ~ 1 nT
Can we get enough gain Gm to be able to reach a measurable low frequency value from the axion field ha ~ 10-22 T?

## Slide 36: Detection of Low Frequency Field
The most sensitive device for measuring magnetic field is the DC squid.
Squid measures magnetic flux F, the best sensitivity Fs obtainable is:
Fs = 10-22 Wb/√Hz
The flux that can be obtained at low frequency is:
Flf= Gm ha A
where A is the area covered by the sample.
For A ~ 10-4 m2, the gain necessary to obtain a signal 1/100 x Fs is:
Gm ~ 100
To reach this gain, given the material (T1, T2), the free parameter is the pumping field.

## Slide 37: Pumping field
The pumping field Hp is limited by two factors:
- saturation of the spins in the material
- power dissipated into the lattice (having volume Vs)
The most stringent limitation comes from the power dissipation, which must be lower than the cryogenic power available.
@ 100 mk Pcryo ~ 1 mW
@ 1 K Pcryo ~ 300 mW

## Slide 38: Noise
Supposing to reach the limiting sensitivity for the detector, residual intrinsic noise will be present as magnetization noise dmz in the sample.
A first guess of its level can be calculated using Fluctuation-Dissipation theorem. This is in general correct for system at the equilibrium, which in principle is not our situation (stationary system).
Gd2Si5O2 @ 100mK + 1 Tesla SQUID , Noise @ 10^-15 T/Hz^0,5
The noise level must be measured experimentally!
(A/m)

## Slide 39: Calibration
We have illustrated a technique which is not new (Pescia 1965, Ablart and Pescia 1980), however it has been normally used with very small values of relaxation times: t1, t2 < 1 ms.
Moreover, the theoretical framework is correct for paramagnets with small spin density N0 ~ 1022 m-3. For higher densities radiation damping mechanisms and coupling to the pumping cavity must be taken into account.
In order to reach the necessary gain Gm, we will need t1 ~ 10-100 ms, N0 ~ 1024-1025 m-3.
The system must be verified, both from an experimental and a theo-retical point of view, in this extreme regions. Calibration is possible:
Provide ha with a second RF generator

## Slide 40: First prototype at Legnaro
Using an old EPR magnet we have set-up an apparatus to test the measurement scheme at room temperature.
The equivalent axion field ha was generated using a second RF generator frequency locked to the pump Hp.
As a magnetized sample we used DPPH (2,2-diphenylpicrylhydrazyl) at 300 K.
T2 = 24 ns (measured by us)
T1= 60 ns (from literature)
M0 = 3.7 A/m (N0 ~ 1022 m-3)

## Slide 41: Detection scheme

## Slide 42: Cavities
TE102 mode
2.5 GHz
5.0 GHz
At critical coupling
From Poole 1967
B in Tesla

## Slide 43: Cavities
300 mm thick wall to allow low frequency magnetic field to pass

## Slide 44: Magnetic samples
Material | Spin density | M0 | T1 | T2 | Size
DPPH | 2.1 x 1027 [1/m3] | 8 A/m | 60 ns | 60 ns | Cylinder 8 mm diameter 8 mm length
YIG | 2.1 x 1028 [1/m3] | 1.4 105 A/m | 0.16 ms |  | Sphere 2 mm radius
All values at room temperature
YIG
DPPH box
DPPH box
DPPH box

## Slide 45: DPPH @ 5.0 GHz

## Slide 46: DPPH linewidth @ 5 GHz

## Slide 47: Prospettive a Breve Termine (2015)
Dimostrare Quantum Counter per Particle Detection
Magnetometro EPR a 4 Kelvin Bmin = 10-14 T @ 10 GHz - NO SQUID
Studiare soluzioni numeriche Equazioni Bloch con radiation Damping e accoppiamento con Cavita’ ( Esercizio da svolgere per R.Barbieri )
- Esplorare Approccio QC per rivelare B a 10^-21 Tesla
Assieme a : PISA , LENS , NAPOLI ( cristalli/Gas Freddi )
- Dettagliare Calcoli Per Maser come Detector attraverso SiC.N

## Slide 48
FINE

## Slide 49
ZEEMAN TRANSITION RATE With 1 Mole of Polarized Electrons
Hz Rate

## Slide 50
Infrared Quantum Counter Idea
Bloembergen ( Nobel Prize ) suggested to detect IR photons with large Q.E.
where No Phototube are available at IR wavelenght (PRL ‘59 )
Actual Quantum Efficiency for few 100 GHz Photons at 10-5 level

## Slide 51: Short term perspectives
Build up a prototype apparatus capable of working at low temperature (at 4 K)
Find a material with long T1 and large magnetization at low temperature
In a first step: use as low frequency detector a resonant pick up coil.
We will integrate a SQUID into the system in a second step/phase.
One year goal: reach a sensitivity at 10^-14 Tesla
Study numerically the solution of the Bloch equations with radiation damping and coupling to external cavity.
- Esplorare diversi approcci per rivelare B tra 10^-21 e 10^-22 Tesla
Assieme a : PISA , LENS , NAPOLI

## Slide 55
Infrared Quantum Counter Idea
Bloembergen ( Nobel Prize ) suggested to detect IR photons with large Q.E.
where No Phototube are available at IR wavelenght (PRL ‘59 )
Actual Quantum Efficiency for 10 micron IR photons almost at 100% level

## Slide 56
BLOCH EQUATION FOR ELECTRON SPIN PRECESSION
MAGNETIZATION
T1=Longitudinal Relaxation
T2=Transverse Relaxation
At low temperature < 1K
T1 larger than a seconds
T2 depends on spin density
from micros to sec

## Slide 57: Particle Detector = 3 Levels System

## Slide 59: FASE A : Activity 2015 @ 4 Kelvin
1)Caratterizzazione materiali a 4 Kelvin in Cavita' e misura di rumore di magnetizzazione nelle micronde
2) Misura di parametri di alcuni materiali magnetici fatta dai
colleghi 4 K dell' INRIM di Torino + Simulazione Sistema
3) Misura Temperatura Rumore Amplificatore LNA a 4 Kelvin CON e SENZA Cavita’ ( Q cavita’ e Tnoise @ 4 Kelvin ) ( 58 Keuro )
5) Progettazione magnete da usare nell'esperimento.
Le richieste finanziarie per il 2015 sono in realta' ridotte
perche' utilizzeremo :
a) Un Magnete di polarizzazione in prestito dal CNR o dall'INFN di
Frascati o dal CERN.

## Slide 60: Particle Detector = 3 Levels System

## Slide 61: FASE A : 4 Kelvin R&D Activity
1)Validazione schema proposto per la misura della componente longitudinale della magnetizzazione utilizzando cavita’ risonanti e misure di rumore di magnetizzazione.
2) Misure di parametri di materiali magnetici a 4K in collaborazione con i colleghi dell' INRIM di Torino
3) Esplorare diversi approcci per rivelare B tra 10^-21 e 10^-22 Tesla
Assieme a : PISA , LENS , NAPOLI
IN ATTESA DI : FINANZIAMENTI / MAGNETE / SPAZIO LABORATORIO

## Slide 62: Short term perspectives
Build up a prototype apparatus capable of working at low temperature (at 4 K)
Find a material with long T1 and large magnetization at low temperature
In a first step: use as low frequency detector a resonant pick up coil.
We will integrate a SQUID into the system in a second step/phase.
One year goal: reach a sensitivity at 10^-14 Tesla
Study numerically the solution of the Bloch equations with radiation damping and coupling to external cavity.

## Slide 63: The strong CP problem
The QCD lagrangian contains a term that foresees CP violation
The parameter q is unprescribed by the theory, it is expected to be q ~ 1. QCD interaction actually depends on q through its difference with the phase of the quark mass matrix:
VERY FINE TUNING! -> STRONG CP PROBLEM

## Slide 64: ADMX Haloscopes – Galactic axions
Search for cold dark matter constituent
Original proposal by P. Sikivie (1983)
DM particles converted into photons inside a magnetic field (Primakoff)
The mass of the DM particle determines the frequency of the photons to be detected. For axions we are in the microwave range.
ba~10-3 axion velocity
Use a microwave cavity to enhance signal. Cavity must be tuned to axion mass. Being this unknown, tuning is necessary: very time consuming experiment!
meV <-> GHz

## Slide 65: Haloscope detectors
Pilot experiments in Brookhaven (1988) and University of Florida (1990)
Second generation experiments:
  ADMX @ Lawrence Livermore employing low noise amplifier detectors
  CARRACK @ Kyoto employing Rydberg atom detectors
ADMX – Axion Dark Matter eXperiment
High Q microwave cavity inside an 8.5 T magnet
Almost Quantum Limited SQUID detector
Reached sensitivity for probing DM axion:
If all galactic DM is all made of axion
If we assume KSVZ model right
If the axion has the right mass, i.e. resonant with the cavity

## Slide 66: ADMX recent progress and prospects
http://www.phys.washington.edu/groups/admx/future.html
The experiment goes to a second stage with a collaboration between University of Washington Berkeley JPL and Yale
New scheme to employ SQUID at higher frequency
New type of amplifier at frequencies above a few Ghz
Use higher order modes in the resonant cavity
Optimize cavity material to obtain higher Qs – hybrid superconducting cavities
Photonic band gap cavity in the multi-GHz range

## Slide 67
Tale effetto e’ presente per le interazioni deboli ed e’ stato osservato
Sia sul neutrone ( Ramsey) che sugli Atomi (Bouchiat)
= 10^-7 rad/cm
L’effetto per il neutrino :
Michael,Stodolsky,Langacker,Gelmini
I neutrini esercitano un torque sulla particella di spin s data da :
( 1 )
Su Materia Polarizzata e’ come se fosse presente un Campo Magnetico Efficace
Attualmente si misurano Campi di 10-^20 T
I neutrini esercitano un torque sulla particella di spin s data da :

## Slide 68: Processi Fisici e Basse Soglie di Energia
- Neutrino Scattering Coerente via Zo su Nuclei
(Neutrini Solari o da Reattore rilasciano 10 – 100 eV)
Neutrino Momento Magnetico su Nucleo
Materia Oscura : Assioni e WIMPS Ridurre Energia Soglia
Electron Capture Enhancement under Atom-Laser Illumination
Sezione d’urto differenziale neutrini Vs elettroni (nuclei)
Forward Scattering dei Neutrini e Campo Magnetico Efficace
Violazione di CP attraverso esperimenti di EDM e Assioni
Accoppiamenti Gravito-Magnetici su Particelle Elementari

## Slide 69: Axion interactions
Axion interactions are model dependent
Axion photon photon
gg = 0.36 (DFSZ)
gg = - 0.97 (KSVZ)
Axion electron electron
ge = 10-3 (KSVZ)
(DFSZ)
All couplings are extremely weak!

## Slide 70: Low Energy Particle Detector: Laser Induced DORELAS
Fisica vs Rivelatori a Bassa Soglia di Energia
Da KeV a eV Breve sguardo d’insieme e prospettive
Pompaggio Laser su “ Mezzo Attivo “ : RIVELATORE
Progetto di Ricerca
Richieste :Finanziarie ,Sezione, F.T.E.

## Slide 71
Infrared Quantum Counter Idea
Bloembergen ( Nobel Prize ) suggested to detect IR photons with large Q.E.
where No Phototube are available at IR wavelenght (PRL ‘59 )
Actual Quantum Efficiency for 10 micron IR photons almost at 100% level

## Slide 72
Infrared Quantum Counter Idea
Bloembergen ( Nobel Prize ) suggested to detect IR photons with large Q.E.
where No Phototube are available at IR wavelenght (PRL ‘59 )
Actual Quantum Efficiency for 10 micron IR photons almost at 100% level

## Slide 75: Axion interactions
Axion interactions are model dependent
Axion photon photon
gg = 0.36 (DFSZ)
gg = - 0.97 (KSVZ)
Axion electron electron
ge = 10-3 (KSVZ)
(DFSZ)
All couplings are extremely weak!

## Slide 76: Does the axion exist?
While the standard Peccei Quinn Weinberg Wilczeck (PQWW) axion was soon ruled out ( Electro Weak Scale F = 250 GeV ), the other axion (DFSZ, KSVZ) continues to evade all current experimental limits
A reduced window of possibilities is actually left for discovery
Excluded
Searches
Hint
From G. Raffelt talk in Vistas in Axion Physics, INT, Seattle, 23–26 April 2012

## Slide 77: Axion Electron interaction
The interaction of the axion with the a spin ½ particle
In the non relativistic approximation
The interaction term has the form of a spin - magnetic field interaction with playing the role of an effective magnetic field

## Slide 78: QUAX Beam Pattern
EFFETTO DIREZIONALE
SPIN ELETTRONE -ASSIONE

## Slide 79: QUAX goal
Reach the axion model coupling constant within a 5 year development in a narrow axion mass range
Major issue is to demonstrate that noise sources are under control in reasonable amount of time, thus allowing to extend the mass range in a larger apparatus

## Slide 80
Infrared Quantum Counter Idea
Bloembergen ( Nobel Prize ) suggested to detect IR photons with large Q.E.
where No Phototube are available at IR wavelenght (PRL ‘59 )
Actual Quantum Efficiency for few 100 GHz Photons at 10-5 level

## Slide 81: Magnetic detection
A possibility is to exploit the axion electron coupling
Due to the motion of the solar system in the galaxy, the axion DM cloud acts as an effective RF magnetic field on electron spin
This field excites magnetic transition in a magnetized sample
( Larmor frequency ) and produce a detectable signal
MS
Axion
Wind
Measurable signal
Idea comes from several old works:
L.M. Krauss, J. Moody, F. Wilczeck, D.E. Morris, ”Spin coupled axion detections”, HUTP-85/A006 (1985)
L.M. Krauss, ”Axions .. the search continues”, Yale Preprint YTP 85-31 (1985)
R. Barbieri, M. Cerdonio, G. Fiorentini, S. Vitale, Phys. Lett. B 226, 357 (1989)
A.I. Kakhizde, I. V. Kolokolov, Sov. Phys. JETP 72 598 (1991)
MS – Magnetized sample

## Slide 82: Frequency prescriptions
The general solution for the variable component of the magnetization is:
T1
T2
wD(rad/s)
This has to be taken into account in order to keep the largest gain-bandwidth.
For large values of T1 and T2 ( T1 > T2 ) the gain drops off as 1/w above w1 ~ 1/T1.

## Slide 83: Pick – up coils
Before using squids the system can be studied with a pick-up coil.
A pick-up coil surrounding the magnetized sample will produce an induced voltage which is:
Which has now the form:
there is a different frequency behavior, but sensitivity is in general much worse than squids
wD(rad/s)

## Slide 84
e

## Slide 85: Longitudinal detection of axion field
H0
We magnetize the sample along the z-axis and orient the sample in order to have the equivalent axion field ha in the transverse direction
H0 amplitude matches the searched value of the axion mass
We drive the sample with a pump field Hp at the Larmor frequency
The total driving radio-frequency field is then
ha
Hp

## Slide 86: Longitudinal detection of axion field
The relevant Bloch equations
A stationary solution can be obtained.
The magnetization along the z-axis (longitudinal component) shows a term modulated at the difference frequency wD.
for
Saturation parameter s
Hp, ha in Tesla M0 , mz in A/m

## Slide 87: Longitudinal detection of axion field
If we put some relevant numbers (already published)
find the right material
power dissipated in the cryogenic system
noises in the system
T1 = 10-3 s
T2 = 3 x 10-7 s
M0 = 200 A/m
We can define some sort of gain Gm for the low frequency field component m0 mz with respect to the high frequency one ha
We obtain Gm > 1
for a pump field of Hp ~ 1 nT
Can we get enough gain Gm to be able to reach a measurable low frequency value from the axion field ha ~ 10-22 T?

## Slide 88: Results