## Slide 1: Neutron imager and flux monitor based on Micro Channel Plates (MCP) in electrostatic mirror configuration
Vincenzo Variale INFN-Bari, Italy
MCP detector features
Neutron detection with MCP
Proposal of a new Neutron Beam Monitor based on MCP
Monitor design
Conclusion

## Slide 2: The Micro Channel Plate (MCP) features
MCP behavior scheme
Gain = exp(k .L/d) (k=channel e- emission factor)
L
d
The MCP consists of a two-dimensional array with a great number of very small glass channels bundled in parallel and formed into the shape of a thin disk. Each channel has an internal diameter ranging from 6 to 20 microns with the inner wall processed to have the proper electrical resistance and secondary emissive properties.
Each channel acts as an independent electron multiplier 

## Slide 3: Advantageous MCP features for detection
fast time response (rise time ˞ 300 ps, fall time 600 ps)
high spatial resolution (up to 6 mm for single MCP, 25 mm for a 2-stage MCP)
Very low dead time (depending on d, for a d ≈ 6 mm, about 100 ns)
High Counting rate (more than 108 s-1)
Low dark current (for a vacuum < 10-6 mbar, < 1Hz/cm2)
Detection efficiency (up to 85% depending on the radiation type  see following )

## Slide 4: MCP detection efficiency
Types of Radiation | Energy or wavelength | Detection Efficiency (%)
Electrons | 0.2 keV to 2 keV 2 keV to 50 keV | 50 to 85 10 to 60
Ions (H+, He+, Ar+) | 0.5 keV to 2 keV 2 keV to 50 keV 50 keV to 200 keV | to 58 60 to 85 4 to 60
UV | 300 Å to 1100 Å 1100 Å 1500 Å | to 15 1 to 5
Soft x-rays | 2 Å to 50 Å | 5 50 15
Hard x-rays | 0.12 Å to 0.2 Å | to 1
High energy particles (r,p) | 1 GeV t 10 GeV | to 95
Neutrons | 2.5 MeV to 14 MeV | 0.14 to 0.64
For e- around 1 keV is ≈ 80%
Very low efficiency
From Ref.[1]

## Slide 5: Neutron detection with MCP: past proposal
Fast neutron detection proposed by D. W. MacArthur, Los Alamos [2]
In analogy with Multi Wire Proportional Chamber (MWPC) detector
In 1987 
Polyethylen layers for fast neutron  proton recoils
MCP for proton detection
Frazer and Pearson proposed to dope directly the MCP with 6Li atoms [3] to detect thermal neutron.
Some years later, Tremsin et al used 10B [4]
In 1990 
Behavior scheme
Note: 157Gd or 155Gd have been also used as doping element
Position sensitivity 10 mm
Time accuracy about 100 ps
Detection efficiency ~21% (low)
 The detection efficiency depends on 10B doping percentage ( < 20%)

## Slide 6: In 2012 
The 10B doping concentration is limited by production process of the MCP glass
 low neutron detection efficiency .
They used Atomic layer deposition (ALD) technique to implement the natGd2O3 film
coating process. In [5] about 100nm of natGd2O3 film on the inner surface of MCP pores
has been realized. Simulations show a detection efficiency of 60 ÷ 70 % can be reached
in this way.
Note: The ALD technique can give uniform layer also for large values of L/D (~37) but that technique is not easy to realize.
In order to increase the neutron detection efficiency, a natGd coating has been
proposed by Nianhua Lu et al. in ref [5] on the MCP channel

## Slide 7: Commercially available Neutron detector with image intensifier (MCP inside)
The radiation converter is doped with 157Gd
luminescent screen + multialkali photocathode
MCP
Note: the detection device and the read-out system is on the same axis of the neutron beam
Neutron beam

## Slide 8: Neutron beam monitor with a MCP in an Electrostatic Mirror
Note :as detection readout it can be used a phosphor screen instead of a anode and in this way
we could obtain a neutron beam profile
Neutron
To detect the neutrons a Carbon foil with
a 6Li deposit could be used
Grids at ~1,2kV
Note: The Secondary electrons (SE) are emitted with few eV (black arrow) and then they are
accelerated by the 1kV grid towards the grids placed at 45° in such a way
that they are deflected towards the MCP in CHEVRON configuration.
Stainless steel
Plastic
In this configuration the neutron beam profile image is obtained in the transverse
plane (the plane parallel to the beam) 
6Li
t
a
e-
e-

## Slide 9: The neutron detection efficiency: neutron counting
The detected neutron number will depend essentially on the cross- section reaction used:
n + 6Li  t + a (con Q = 4.7 MeV)
Note: assuming a carbon foil of about 20 mg/cm2 we get a corresponding tickness of lc = 9 mm
which allows the 100% transmission of t ions but stops all the a .
For the conservation law: mt/ma=Tt/Ta
Tt = 2.7 MeV
Ta= 2.0 MeV
Note: for the above energies , the range of a is about 5 mm In the C foil and 22 mm in the Li
the range of t is about 30 mm in C and i 120 mm n the Li )

## Slide 10
Note: However a neutron flux , usually, do not have a unique energy but a very large energy distribution then a more
realistic capture reaction rate evaluation can be done only through MC simulations. The MCNPX code has been used for that.

## Slide 11: MCNPX simulations for Nt evaluation
MCNPX Geometry:
Transverse
section
6Li deposit depth
Carbon foil
Parameters used in the simulations:
r = 2. cm
l1 = 1, 2, 3, 4, 5 mm ; l2 = 9 mm
dn = 4. cm
As source  CERN n_TOF neutron flux
Nt are the Triton exiting by the C foil (x p pulse)
r
dn
l1
l2
Nt /cm2
l1
Note : to get the effective neutron counting, Nt should be
multiplied for the intrinsic 1 keV electrons MCP detection
efficiency shown before.

## Slide 12: Neutron position uncertainty evaluation
The reaction 6Li(n,t)a is isotropic  triton coming out from C foil are uniformly
spread out through a cone angle f up to 90° (see fig.)
l
neutron position uncertainty = Dx = l tgf  few tens of mm
Note: the most part of t should be emitted with angle f < ~85° (corresponding to a Dx < ~100m).
Furthermore the beam profile image precision will depend also on the SEE trajectories  Simulations with SIMION

## Slide 13: SE trajectory simulations in the Electrostatic mirror
Trajectory simulations for f ≠ 0 (blue-lines); Ekn = 4 eV for all SE
xi’ final positions of n_th SE for
dxi  xi’ – xi  (deformation)
 SE trajectories with f =0 (green lines) are shown for comparison
Trajectory simulations of 8 equidistant SE :
yn  initial positions of the n_th SE
Ekn  initial kinetic energy (increasing from 1 to 8 eV)
 emission Cone angle =0 for all SE)
xn  final positions of th n_th SE (xn remain equidistant)
y
x
Note: for fn = 20°  dyi= 80%
this maximum deformation results
is due to the high initial kinetic
energy used.
z
Note: the initial SEposition differences are maintained
on the MCP plane  Dy = Dx
 That means the beam image in (y,z) is
preserved in (x,z) plane (MCP plane).
Dx
Dy
fn increasing up to 20°

## Slide 14
Note: SE with emission cone angle, f < 10°, and
initial kinetic energy of ≈2 eV can be considered
good SE initial conditions 
Tajectories simulation with a large number of SE
have been also considered 
(fn increasing up to 20°
By reducing the initial kinetic energy to 1 eV
a deformation, dy, of ≈ 20% is obtained 
SE tajectories with Ek =2 eV Seand increasing cone angle with
a maximum f =10°  maximum deformation, dy, of ≈ 10% .

## Slide 15
SE with Flat distribution in f and Ek
Simulations of ≈ 1000 SE trajectories which have a square shaped initial position (Dy=Dz=8mm) and a flat distribution in the emission cone angle and initial kinetic energy.
Further initial conditions used:
Eki= 2 eV with PERCENT_ENERGY_VARIATION = 50%
SE Emission Cone_Angle = 10° (max. value)
Dyi = 8 mm
3D view
 deformation: <dx’> = 6%

## Slide 16: Summary of simulation results
The beam profile in the (y,z) plane (perpendicular to the beam axis) is reproduced on the MCP, the (x,z) plane (the one parallel to the beam axis).
The image quality depends strongly by the SEE initial conditions
Good quality beam image can be obtained for SE with initial conditions having Eki= 2 eV and Fi< 10°.
It is important evaluate the SEE initial conditions to evaluate the beam image
quality and then the spatial resolution

## Slide 17: Initial condition features for SE Emission
Forward and backward SEE Yield measurements carried out on
ions hitting a Carbon foil target, with different energies.
The SEE depend on the stopping power of the particles impinging or exiting from the foil surface.
The forward SEE can be greater than the backward SEE up to a factor 1.55.
The SEE energy distribution, due to ions with energy of about few MeV, has a peak around a value of few eV.
Ref.: - N Nickles, R. E. Davies and J. R. Dennison, ”Applications of
Secondary Electron Energy and angular distribution to space
Charging”, 6th SPACE CHARGING CONFERENCE, AFRL-VS-TR 20001578 (1998).
- h. Rothard and B. Gervais, “Electron Emission from Solids Irradiated with Swift Ion Beams”, in ION BEAM SCIENCE; Solved and unsolved problems, Ed. By P. Sigmund, Royal Danish Academy of Scienc and Letters, Copenhagen 2(006).
- A. Billeband et al. “Ion by ion measurements secondary electron emission of carbon foils under theimpact of MeV H+, H0, H- projectiles” on Phys. ReV. A , vol. 55, N. 2 Feb. 1997.

## Slide 18: Angular distribution of the SEE
SEE angles can be reduced by applying a negative bias to the emitting surface
The SEE angular distribution probability
Can be given by:
In first approximation theory
emission angle could not
be considered.

## Slide 19: Energy distribution of SEE
CONCLUSION: the SE initial conditions used in the trajectory simulations shown in the slide 15
That is: Ek ≈ few eV and the emitted cone angle f <10° have been reasonable assumptions.

## Slide 20: Monitor construction
The phosphor screen is of P47 type (It has an afterglow time very short (0.11 ms) and a light emission in the range 430 nm 
A CCD camera with a high sensitivity in that light wavelength is needed.
MCP assembly (vacuum side)
MCP phosphor window (Air side)
Not enough funds obtained, but we had in our lab. a MCP + phosphor screen assembled
on the vacuum flange (Hamamtsu) used in the past.
Note: it need to be regenerated and will be ready in 3 month

## Slide 21: That vacuum flange which will be mounted on a Cross shaped vacuum chamber  The MCP will be about 8 cm away from the neutron beam axis where the electrostatic mirror must be placed 
The beam profile image quality shown in
previous simulations will be still
maintained?
MCP Assembly (vacuum side)
n
Flange with MCP
Electrostatic mirror
Vacuum chamber
d
Device mechanical drawing
 New simulations of the modified electrostatic mirror design are needed

## Slide 22: Further SE trajectory simulations for the modified electrostatic mirror configuration 
MCP
Note: the 2 arrow indicate neutron beams entering the 6LiC foil from 2 different positions.
 The vacuum chamber walls are on the ground then the beam profileimage on MCP results deformed 
dF
Equipotential lines
Electrons
Neutrons
Vacuum chamber walls(V5)
MCP (V4)
By shielding the vacuum chamber
wall with the electrode 1
Note: in this case, however, we have
a Dy/Dx ~ 1.35 instead of 1.04
Dy
Dx

## Slide 23
In order to reduce the SE divergence the input
MCP surface can be put to a higher voltage than
the electrode 1 to obtain a focusing lens as
shown in the simulations 
Inside the vacuum is shown the Electrostatic mirror
mechanical design:
Cross vacuum chamber
Reflecting grids
Shielding electrode
MCP
Grids with C foil
Electrostatic lens
Support bar
insulators

## Slide 24: The Phosphor screen coating the Fiber Optic Plate (FOP) window present on the vacuum flange is of P47 type. It emits in a wavelength range peaked at 430 nm (UV) but has also a long tail in the visible light region.
The phosphor light will be detected by a CCD camera (of type Kodak KAF 1400, sensivity in wavelength range 400 ÷ 1000 nm, it has 1317x1070 pixels of 6.9 mm and a resolution of 40 line-pair/mm ( 25 mm)).
Phosphor screen
MCP- Chevron configuration
V=+6kV max.
2 MW
4 MW
Read out system
CCD camera
Lens
PC

## Slide 25: CERN n_TOF facilty
n_TOF is a spallation neutron source based on 20 GeV/c protons from the CERN PS hitting a Pb block (~360 neutrons per proton).
Experimental area at 200 m.
Main feature: very high instantaneous neutron flux (105 n/cm2/pulse):
high resolution in energy (DE/E = 10-4)
wide energy range (25 meV<En<1GeV)
low repetition rate (< 0.8 HZ)

## Slide 26: Electrostatic Mirror in construction:

## Slide 27: Conclusion
A new kind of neutron beam imager with minimal perturbation of the
beam based on the 6Li(n,t) reaction is being considered for various applications.
It uses a MCP assembled with a phosphor screen and an electrostatic mirror
that reflects the neutron beam profile image on a plane off the beam axis.
The Computer simulations show that the device could have a very good spatial
resolution (up to few hundreds of mm) and good efficiency.
The device is under construction and will be tested at the CERN n_TOF facility
the beginning of the next year.
References: [1] Hamamatsu MCP assembly data sheets; [2] Report LA- 11039-MS ; [3] NIM A293 (1990) 569; [4] NIM A539 (2005) 278;
[5] Physics Procedia 26 (2012) 61.