## Slide 1: Next Generation Muon (g-2) Goal dam ~ 140 ppb
David Hertzog, University of Washington
for the E989 Muon (g-2) Collaboration
FCCP2015 Flavor Changing and Conserving Processes

## Slide 2
A Case for Challenging the Standard Model
Momentum
Spin
e
The experiment compares how fast a muon spin rotates in a magnet compared to the predictions from theory
am(Expt) = 116 592 089 (63) x 10-10 (540 ppb)
BNL result 

## Slide 3: This talk is surrounded by many distinguished g-2 experts. I will assume we know why we are all here
“Five numbers” needed to test for New Physics
  … and many others that are known “too well” to enter the discussion
What do the g-2 experiments provide?
Design and status of efforts
  FNAL
  JPARC
See review: Precision Muon Physics, T.P. Gorringe and D.W. Hertzog , Prog. Part. Nucl.Phys. 84 (2015) 73-123

## Slide 4
Fermilab E989: 34 Institutes; >150 Members
Domestic Universities
  Boston
  Cornell
  Illinois
  James Madison
  Kentucky
  Massachusetts
  Michigan
  Michigan State
  Mississippi
  Northern Illinois
  Northwestern (thy)
  Regis
  Texas
  Virginia
  Washington
  York College
National Labs
  Argonne
  Brookhaven
  Fermilab
Italy
  Frascati,
  Roma 2,
  Udine
  Pisa
  Naples
  Trieste
China:
  Shanghai
The Netherlands:
  Groningen
Germany:
  Dresden (thy)
England
  University College London
  Liverpool
  Oxford
Korea
  KAIST
Russia:
  Dubna
  Novosibirsk
g-2 Physics Week 2015
Seattle

## Slide 5: J-PARC E-34 g-2/EDM

## Slide 6: 5 Numbers to establish the “g-2 Test” (that is, 5 that have relevant uncertainties to keep watch on)
++
am(New Physics) ≡ am(Expt) – am(SM)



am(Expt)
Dam(Expt) ~ 140 ppb
Dam(SM) < 220 ppb
Goals:
Discussion today
Discussion today
Expression in BNL PRD
Essentially experimental; limited at 120 ppb by mm/mp

## Slide 7: am(SM): There are really 2 numbers in play here

## Slide 8: am(SM): Historical

## Slide 9: am(Expt) is extracted from several measurements
am(Expt)
-2.002 319 304 361 53(53) [0.26 ppt]
Electron g-2 + QED
206.768 2843(52) [25 ppb]
-.001519270384(12) [8 ppb]
~
In E821 ≡ [0.54 ppm]*
CODATA #s
*0.46 ppm statistical; 0.28 ppm systematics
Muonium HFS experiment(s)
Need to measure DnMu

## Slide 10: Muonium* HFS to determine mm/mp and mm/me
*We’ll need this again to understand the J-PARC muon source
DnMu
In, sum of n12 and n34 intervals in strong field

## Slide 11: wa – What FNAL g-2 plans to deliver
    dwa(statistics) at 100 ppb level
  ~ 1.5 x 1011 events in the final fit
    Multiple independent blind analyses
    Multiple sorting and fitting methods
    Net Systematics error to 70 ppb (x 3 improvement)
    Leading issues
      Pileup
      Gain (energy scale) stability
      Muon losses
Correction for Electric Field and Pitch
    Dwa(E) = +470(50) ppb
    Dwa(Pitch) = +270(40) ppb
BNL numbers;
(errors will be reduced)
Typically ~4-5 analyzers here

## Slide 12: p – What FNAL g-2 plans to deliver
Stored muon optics parameterized in azimuthally averaged multipole expansion
      NEW in-vacuum Tracker detectors and modelling
Magnetic field map & multipole expansion vs time
      Trolley mapping of field “daily”
      Calibration of NMR probes from Absolute field (used in Muonium HFS) to Plunging probe to Trolley probe to ~400 Fixed probes
Magnetic field folded with muon distribution and weighted by electron count
    This is the p that appears in the expression
Control systematic to 70 ppb (x2 better than BNL)
    Better inter- probe calibration
    More uniform field preparation
    Modern instrumentation

## Slide 13: Graphically: Present situation and Goals
BNL E821
Theory
3.6 s
x10-11
Future Goals
Goal: 140 ppb
Expected Improvement
>7.5 s if same central values
What is nature trying to tell us?
a exp – a SM | = | (261 - 287 ± 80)  10 –11
 3.3 to 3.6 s |  | 
*
*range of typical SM evaluations

## Slide 14: The coupling C is VERY model dependent
From D. Stockinger (See many of this g-2 presentations about new physics impact)
g-2 feature: Chirality flipping interactions for mass and charge (moment) terms
g – 2
mm
am(New) [10-11]
Radiative muon mass generation
Z’, W’, UED, Littlest Higgs (LHT) …
SUSY (tanb), unparticles
Extra dimensions (ADD/RS)
Goal
Current Dam

## Slide 15: Post LHC Run 1 physics case strong as ever Representative papers –6 weeks in spring – with g-2 in titles are typically refined models of SUSY
Now with more restricted spaces and tanb ranges

## Slide 16: Perhaps something at low scales … not seen at the LHC
Light vector space of dark photon  e+e- (visible decays) largely ruled out now
But, the “invisible” decay space is quite alive; Dark Z model also alive and connects to running of sin2qW vs Q
NA48/2 arXiv: 1504.00607

## Slide 17: How is the experiment done ?
… and how to do it better

## Slide 18: Both experiments will measure the difference between the spin precession and cyclotron motion for a muon moving in a magnetic field, which is
In practice, with E field focusing*
EDM
Magic g
*Not relevant at J-PARC

## Slide 19: 4 Key elements of modern storage-ring g-2 measurements
(1) Polarized muons
~97% polarized for forward p decays
~50% (max) from muonium at rest source
(2) Precession proportional to (g-2)
(3) Pm magic momentum = 3.094 GeV/c
not required in J-PARC approach
(4) Parity violation in the decay gives average spin direction
n p+ m+
µ

## Slide 20: Two frequency measurements are made and both are “blinded”
Precession frequency
  Detectors involved
Muon distribution
  Measured and Simulated
Magnetic field
  In terms of proton NMR
B

## Slide 21: FNAL Requirement and Status
Intense shots of highly polarized 3.094 GeV/c muons,
  21 times data vs. BNL. (backups to explain)
Instrumentation to inject, kick, and store muons into the Muon Storage Ring
  Lessons learned  new hardware
Methods to shim 1.45 T field to high uniformity and to measure it vs time throughout experiment
  Think: comprehensive refinements
Instrumentation to measure decay positron times and energies, and to determine beam parameters
  Entire overhaul
Collaboration is organized around these 4 Teams
Beam
Ring
Field
Detector

## Slide 22: … shots of highly polarized 3.094 GeV/c muons
No hadronic flash
Pions all decay
Protons removed by a DR kicker
Forward muons collected
95% polarized
~800,000 m+/fill (dP/P 2%) at ring
8 GeV Protons
Pions
Muons
4 bunches
All protons are “excess” from those used for NOvA n Program
Possible Cycle: 16 Shots / 1.33 s Cycle
Beam

## Slide 23: Beamline Progress and End-to-End Modeling Significant and on schedule
Beam
M2-M3 beamline
p  m n
Critical for muon capture
M4-M5 into Ring
Handoff to Ring Models
Into and around the DR
Critical for p and p removal
Target working
Beamlines in progress
Ready early 2017
- p. 23

## Slide 24: … inject, kick, and store muons in the Muon Storage Ring
incoming muons
Quads
KICKERs
About 2-3% store

## Slide 25: An in-vacuum Tracker can reconstruct the stored muon distribution from the decay trajectories
Determines beam position vs. time
- p. 25
3 locations
8 UV stations
128 straws per station
Reconstructed decay position
Also EDM measurement: See Becky Chislet’s talk

## Slide 26: Ring Reassembly Complete Cool-down and Power on in progress
6 – 9 Months of Field shimming begins next week
Aim: factor of 2 better than BNL

## Slide 27: What does the shimming process do?
What matters
  The integrated field experienced by the stored muons
  Therefore, azimuthal average plus transverse multipole decomposition
  For both Field and Stored Muon distribution
As you go around, it is pretty lumpy
But very smooth in transverse average
Final BNL measurements
A more uniform (flat) field reduces uncertainties in the mapping and monitoring. But any individual measurement by NMR is very precise

## Slide 28: NMR probes determine field in terms proton precession frequency
- p. 28
FID
trolley
trolley

## Slide 29: The muon precession frequency is revealed as an oscillating rate of high-energy electrons hitting detectors vs. time
e+
1.25 ns samples
N
A
NA2
<A>=0.4
54 PbF2 crystals

## Slide 30
Few billion events
Getting a good c2 is a challenge
Fit to Simple 5-Par Function
N(t) = N0 e-t/t [1+Acos(wat + f)]
Of course, much more challenging because of:
Pileup
Gain changes
Coherent Betatron Oscillations
Muon Losses

## Slide 31
- p. 31

## Slide 32
SiPM boards optimized to produce PMT-like pulses to exploit short pulse duration of Cherenkov crystals (relevant: pileup)
- p. 32

## Slide 33: State-of-the-art Laser-based calibration system
Front Panel Prisms
10-4 / h demonstrated
- p. 33

## Slide 34: What impacts statistical precision for N counts in final histogram
Higher momentum  larger gtm
Higher magnetic field  greater wa
Polarization
Asymmetry
  determined by threshold cut, which also impacts the count rate N

## Slide 35: The J-PARC approach*
*Slides derived from talk by Glen Marshall, July 2015

## Slide 36: What makes them different?
Eliminate electric focusing removes b x E term
 Do need ~zero PT to store muons
 Not constrained to run at the “magic momentum”
Create “ultra-cold” muon source; accelerate, and inject into compact storage ring.
Consequences are quite interesting …
  Smaller magnet; intrinsically more uniform
  Issues related to needed counts
Aim for BNL level precision as an important check

## Slide 37: Ultra-cold Muons
Surface m+
Stop in Aerogel
Diffuse Mu into vacuum
Ionize
  1S  2Punbound
  Max Polarization 50%
Accelerate
  E field, RFQ, linear structures
  P = 300 MeV/c

## Slide 39: Continuous detector system of silicon trackers
Expected data. Note shorter lifetime at this momentum, and lower asymmetry owing to polarization of source

## Slide 42: Comparison
Gorringe and Hertzog, Progress in Nuclear and Particle Physics, Volume 84 (2015) September 2015

## Slide 43: Summary
FNAL: status and the plan going forward …
  Design complete and implementation well along
  Ring cold; Power “on”
  Construction phase for many subsystems
  Beam expected in early 2017
  Goal remains 140 ppb (or 16 x 10-11) on am
  EDM parasitically
J-PARC: novel method being developed*
  Working out key new issues: source; magnet; detectors, etc.
  Concept has greater reach for EDM owing to detector coverage
  Aiming at 2019 Phase 1 start with
    g-2 to ~400 ppb,
    EDM ~10-21 e-cm;
*apologies for any errors in describing E34

## Slide 44: Systematic Errors on wa (ppb)
Ring Team
Detector Team
Detector Team
- p. 44

## Slide 45: Systematic Errors on wp (ppb)
Brookhaven E821
FNAL
- p. 45

## Slide 46: Conceptual idea of calibration handshake …
Absolute probe was used in the Muonium HFS experiment that established mm/mp, which is needed to determine am
A second absolute magnetic field probe is in development at UMass
Field
- p. 46

## Slide 47: Acquiring x21 statistics at FNAL vs. BNL
BNL E821: ~ 4000 m+ / fill using 4 TP of 24 GeV p / fill
FNAL E989: > 10,000 m+ / fill using 1 TP of 8 GeV p / fill
  Many design factors recover lower s and proton intensity / fill
    e.g: target focus, FODO lattice; forward decays; beamline length
  Additionally: 12 Hz fill rate at FNAL vs 4.4 Hz at BNL (factor x 2.7)
    This is a critical advantage
NET: Physics / hour 7 times greater at FNAL compared to BNL.
Beam
- p. 47

## Slide 48: Existing Cross section measurements for e+e- →p+ p-

## Slide 49: Existing Cross section measurements for e+e- →p+ p-

## Slide 51: Prospects if these improvements are successful …
dam(Expt) 16 x 10-11 (140 ppb)
dam(SMa) 36 x 10-11 (309 ppb) dHLbL = 25 x 10-11 (no change)
dam(SMb) 27 x 10-11 (231 ppb) with dHLbL = 10 x 10-11
Dam(Expt - SM) ~ (287±80) x 10-11 (3.6 s)
E821 New Physics Test
E989 + Future SM dHVP  26 x 10-11
E989 in possible* scenarios …
Dam(Expt - SMa) ~ (287±38) x 10-11 (7.5 s)
possible* if central values stay the same …
am(SM) = 116 591 802(49) x 10-11
am(E821) = 116 592 089(63) x 10-11
Dam(Expt - SMb) ~ (287±28) x 10-11 (10 s) !!
Present:

## Slide 52: am(SM): we need 2 more numbers here …
QED: done (amazing, wonderful, wow, etc, but uncertainties tiny)
Weak: done (also amazing, wonderful, etc….and tiny)
Hadronic Vacuum Polarization: 0.42 ppm LARGEST
  See next slide
  Hadronic Light-by-Light: 0.26 ppm (or larger)
  … but what do errors mean here?
  am(HLbL) from models and lattice
  The “theory challenge”

## Slide 53
New results on amHLO 6923(42) x 10-11 (2011)
  BES
    New; 1/3rd data; pp results
    consistent with others
    (arxiv:1507.08188)
  VEPP-2000
    New results this year at ~0.6% on pp
    Aim at ~0.3% by 2017 (the ultimate goal)
  Lattice
    Results on amHLO with 4% error; 4x worse
    than the dispersive approach (~1% uncertainty)
F. Burger et al.
arXiv:1311.3885
✔
More from speakers